## Slide 1: TCP: Congestion Control (part II)
CS 168, Fall 2014
Sylvia Ratnasamy
http://inst.eecs.berkeley.edu/~cs168
Material thanks to Ion Stoica, Scott Shenker, Jennifer Rexford, Nick McKeown, and many other colleagues

## Slide 2: Announcements
Midterm grades and solutions to be released soon after lecture today
Distribution

## Slide 3: Announcements
We will accept re-grade requests up to noon, Oct 30
Regrade process if we made a clerical mistake:
  e.g., you selected answer iii, we graded as ii, etc.
  we’ll correct your score immediately
Regrade process if you disagree with our assessment
  we will re-grade your entire exam

## Slide 4
Last Lecture
  TCP Congestion control: the gory details
Today
  Wrap-up CC details (fast retransmit)
  Critically examining TCP
  Advanced techniques

## Slide 5: Recap: TCP congestion control
Congestion Window: CWND
  How many bytes can be sent without overflowing routers
  Computed by the sender using congestion control algorithm
Flow control window: AdvertisedWindow (RWND)
  How many bytes can be sent without overflowing receiver’s buffers
  Determined by the receiver and reported to the sender
Sender-side window = minimum{CWND, RWND}

## Slide 6: Recall: Three Issues
Discovering the available (bottleneck) bandwidth
  Slow Start
Adjusting to variations in bandwidth
  AIMD (Additive Increase Multiplicative Decrease)
Sharing bandwidth between flows
  AIMD vs. MIMD/AIAD…

## Slide 7: Recap: Implementation
State at sender
  CWND (initialized to a small constant)
  ssthresh (initialized to a large constant)
Events
  ACK (new data)
  dupACK (duplicate ACK for old data)
  Timeout

## Slide 8: Event: ACK (new data)
If CWND < ssthresh
  CWND += 1
CWND packets per RTT
Hence after one RTT with no drops: CWND = 2xCWND

## Slide 9: Event: ACK (new data)
If CWND < ssthresh
  CWND += 1
Else
  CWND = CWND + 1/CWND
Slow start phase
CWND packets per RTT
Hence after one RTT with no drops: CWND = CWND + 1
“Congestion Avoidance” phase (additive increase)

## Slide 10: Event: TimeOut
On Timeout
  ssthresh  CWND/2
  CWND  1

## Slide 11: Event: dupACK
dupACKcount ++
If dupACKcount = 3 /* fast retransmit */
  ssthresh = CWND/2
  CWND = CWND/2

## Slide 12: One Final Phase: Fast Recovery
The problem: congestion avoidance too slow in recovering from an isolated loss

## Slide 13: Example
Consider a TCP connection with:
  CWND=10 packets
  Last ACK had seq# 101
    i.e., receiver expecting next packet to have seq# 101
10 packets [101, 102, 103,…, 110] are in flight
  Packet 101 is dropped

## Slide 14: Timeline (at sender)
In flight: 101, 102, 103, 104, 105, 106, 107, 108, 109, 110
ACK 101 (due to 102) cwnd=10 dupACK#1 (no xmit)
ACK 101 (due to 103) cwnd=10 dupACK#2 (no xmit)
ACK 101 (due to 104) cwnd=10 dupACK#3 (no xmit)
RETRANSMIT 101 ssthresh=5 cwnd= 5
ACK 101 (due to 105) cwnd=5 + 1/5 (no xmit)
ACK 101 (due to 106) cwnd=5 + 2/5 (no xmit)
ACK 101 (due to 107) cwnd=5 + 3/5 (no xmit)
ACK 101 (due to 108) cwnd=5 + 4/5 (no xmit)
ACK 101 (due to 109) cwnd=5 + 5/5 (no xmit)
ACK 101 (due to 110) cwnd=6 + 1/5 (no xmit)
ACK 111 (due to 101)  only now can we transmit new packets
Plus no packets in flight so ACK “clocking” (to increase CWND) stalls for another RTT
✗
101

## Slide 15: Solution: Fast Recovery
Idea: Grant the sender temporary “credit” for each dupACK so as to keep packets in flight
If dupACKcount = 3
  ssthresh = cwnd/2
  cwnd = ssthresh + 3
While in fast recovery
  cwnd = cwnd + 1 for each additional duplicate ACK
Exit fast recovery after receiving new ACK
  set cwnd = ssthresh

## Slide 16: Timeline (at sender)
In flight: 101, 102, 103, 104, 105, 106, 107, 108, 109, 110
ACK 101 (due to 102) cwnd=10 dup#1
ACK 101 (due to 103) cwnd=10 dup#2
ACK 101 (due to 104) cwnd=10 dup#3
REXMIT 101 ssthresh=5 cwnd= 8 (5+3)
ACK 101 (due to 105) cwnd= 9 (no xmit)
ACK 101 (due to 106) cwnd=10 (no xmit)
ACK 101 (due to 107) cwnd=11 (xmit 111)
ACK 101 (due to 108) cwnd=12 (xmit 112)
ACK 101 (due to 109) cwnd=13 (xmit 113)
ACK 101 (due to 110) cwnd=14 (xmit 114)
ACK 111 (due to 101) cwnd = 5 (xmit 115)  exiting fast recovery
Packets 111-114 already in flight
ACK 112 (due to 111) cwnd = 5 + 1/5  back in congestion avoidance
✗

## Slide 17: TCP State Machine
slow start
congstn. avoid.
fast recovery
cwnd > ssthresh
timeout
dupACK=3
timeout
dupACK=3
new ACK
dupACK
new ACK
timeout
new ACK
dupACK
dupACK

## Slide 18: TCP State Machine
slow start
congstn. avoid.
fast recovery
cwnd > ssthresh
timeout
dupACK=3
timeout
dupACK=3
new ACK
dupACK
new ACK
timeout
new ACK
dupACK
dupACK

## Slide 19: TCP State Machine
slow start
congstn. avoid.
fast recovery
cwnd > ssthresh
timeout
dupACK=3
timeout
dupACK=3
new ACK
dupACK
new ACK
timeout
new ACK
dupACK
dupACK

## Slide 20: TCP State Machine
slow start
congstn. avoid.
fast recovery
cwnd > ssthresh
timeout
dupACK=3
timeout
dupACK=3
new ACK
dupACK
new ACK
timeout
new ACK
dupACK
dupACK

## Slide 21: TCP Flavors
TCP-Tahoe
  CWND =1 on triple dupACK
TCP-Reno
  CWND =1 on timeout
  CWND = CWND/2 on triple dupack
TCP-newReno
  TCP-Reno + improved fast recovery
TCP-SACK
  incorporates selective acknowledgements
Our default assumption

## Slide 22: Interoperability
How can all these algorithms coexist? Don’t we need a single, uniform standard?
What happens if I’m using Reno and you are using Tahoe, and we try to communicate?

## Slide 23
Last Lecture
  TCP Congestion control: the gory details
Today
  Wrap-up CC details (fast retransmit)
  Critically examining TCP
  Advanced techniques

## Slide 24: TCP Throughput Equation

## Slide 25: A Simple Model for TCP Throughput
A
Loss
time
cwnd
1
RTT
½ Wmax RTTs between drops
Avg. ¾ Wmax packets per RTTs

## Slide 26: A Simple Model for TCP Throughput
A
Loss
time
cwnd
½ Wmax RTTs between drops
Avg. ¾ Wmax packets per RTTs

## Slide 27: Implications (1): Different RTTs
Flows get throughput inversely proportional to RTT
TCP unfair in the face of heterogeneous RTTs!
A1
A2
B2
B1
bottleneck
link
100ms
200ms

## Slide 28: Implications (2): High Speed TCP
Assume RTT = 100ms, MSS=1500bytes, BW=100Gbps
What value of p is required to reach 100Gbps throughput?
  ~ 2 x 10-12
How long between drops?
  ~ 16.6 hours
How much data has been sent in this time?
  ~ 6 petabits
These are not practical numbers!

## Slide 29: Adapting TCP to High Speed
  Once past a threshold speed, increase CWND faster
  A proposed standard [Floyd’03]: once speed is past some threshold, change equation to p-.8 rather than p-.5
  Let the additive constant in AIMD depend on CWND
Other approaches?
  Multiple simultaneous connections (hack but works today)
  Router-assisted approaches (will see shortly)

## Slide 30: Implications (3): Rate-based CC
TCP throughput is “choppy”
  repeated swings between W/2 to W
Some apps would prefer sending at a steady rate
  e.g., streaming apps
A solution: “Equation-Based Congestion Control”
  ditch TCP’s increase/decrease rules and just follow the equation
  measure drop percentage p, and set rate accordingly
Following the TCP equation ensures we’re “TCP friendly”
  i.e., use no more than TCP does in similar setting

## Slide 31: Other Limitations of TCP Congestion Control

## Slide 32: (4) Loss not due to congestion?
TCP will confuse corruption with congestion
Flow will cut its rate
  Throughput ~ 1/sqrt(p) where p is loss prob.
  Applies even for non-congestion losses!
We’ll look at proposed solutions shortly…

## Slide 33: (5) How do short flows fare?
50% of flows have < 1500B to send; 80% < 100KB
Implication (1): short flows never leave slow start!
  short flows never attain their fair share
Implication (2): too few packets to trigger dupACKs
  Isolated loss may lead to timeouts
  At typical timeout values of ~500ms, might severely impact flow completion time

## Slide 34: (6) TCP fills up queues  long delays
A flow deliberately overshoots capacity, until it experiences a drop
Means that delays are large, and are large for everyone
  Consider a flow transferring a 10GB file sharing a bottleneck link with 10 flows transferring 100B

## Slide 35: (7) Cheating
Three easy ways to cheat
  Increasing CWND faster than +1 MSS per RTT

## Slide 36: Increasing CWND Faster
Limit rates:
x = 2y
C
x
y
x increases by 2 per RTT
y increases by 1 per RTT

## Slide 37: (7) Cheating
Three easy ways to cheat
  Increasing CWND faster than +1 MSS per RTT
  Opening many connections

## Slide 38: Open Many Connections
A
B
x
D
E
y
Assume
A starts 10 connections to B
D starts 1 connection to E
Each connection gets about the same throughput
Then A gets 10 times more throughput than D

## Slide 39: (7) Cheating
Three easy ways to cheat
  Increasing CWND faster than +1 MSS per RTT
  Opening many connections
  Using large initial CWND
Why hasn’t the Internet suffered a congestion collapse yet?

## Slide 40: (8) CC intertwined with reliability
Mechanisms for CC and reliability are tightly coupled
  CWND adjusted based on ACKs and timeouts
  Cumulative ACKs and fast retransmit/recovery rules
Complicates evolution
  Consider changing from cumulative to selective ACKs
  A failure of modularity, not layering
Sometimes we want CC but not reliability
  e.g., real-time applications
Sometimes we want reliability but not CC (?)

## Slide 41: Recap: TCP problems
Misled by non-congestion losses
Fills up queues leading to high delays
Short flows complete before discovering available capacity
AIMD impractical for high speed links
Sawtooth discovery too choppy for some apps
Unfair under heterogeneous RTTs
Tight coupling with reliability mechanisms
Endhosts can cheat
Could fix many of these with some help from routers!
Routers tell endpoints if they’re congested
Routers tell endpoints what rate to send at
Routers enforce fair sharing

## Slide 42: Router-Assisted Congestion Control
Three tasks for CC:
  Isolation/fairness
  Adjustment
  Detecting congestion

## Slide 43: How can routers ensure each flow gets its “fair share”?

## Slide 44: Fairness: General Approach
Routers classify packets into “flows”
  (For now) let’s assume flows are TCP connections
Each flow has its own FIFO queue in router
Router services flows in a fair fashion
  When line becomes free, take packet from next flow in a fair order
What does “fair” mean exactly?

## Slide 45: Max-Min Fairness
Given set of bandwidth demands ri and total bandwidth C, max-min bandwidth allocations are:
ai = min(f, ri)
where f is the unique value such that Sum(ai) = C
r1
r2
r3
?
?
?
C bits/s

## Slide 46: Example
C = 10; r1 = 8, r2 = 6, r3 = 2; N = 3
C/3 = 3.33 
  But r3’s need is only 2
  Can service all of r3
  Remove r3 from the accounting: C = C – r3 = 8; N = 2
C/2 = 4 
  Can’t service all of r1 or r2
  So hold them to the remaining fair share: f = 4
8
6
2
4
4
2
f = 4:
min(8, 4) = 4
min(6, 4) = 4
min(2, 4) = 2
10

## Slide 47: Max-Min Fairness
Given set of bandwidth demands ri and total bandwidth C, max-min bandwidth allocations are:
ai = min(f, ri)
where f is the unique value such that Sum(ai) = C
Property:
  If you don’t get full demand, no one gets more than you
This is what round-robin service gives if all packets are the same size

## Slide 48: How do we deal with packets of different sizes?
Mental model: Bit-by-bit round robin (“fluid flow”)
Can you do this in practice?
No, packets cannot be preempted
But we can approximate it
  This is what “fair queuing” routers do

## Slide 49: Fair Queuing (FQ)
For each packet, compute the time at which the last bit of a packet would have left the router if flows are served bit-by-bit
Then serve packets in the increasing order of their deadlines

## Slide 50: Example
1
2
3
4
5
1
2
3
4
1
2
3
1
2
4
3
4
5
5
6
1
2
1
3
2
3
4
4
5
6
5
5
6
Flow 1
(arrival traffic)
Flow 2
(arrival traffic)
Service
in fluid flow
system
FQ Packet
system
time
time
time
time

## Slide 51: Fair Queuing (FQ)
Think of it as an implementation of round-robin generalized to the case where not all packets are equal sized
Weighted fair queuing (WFQ): assign different flows different shares
Today, some form of WFQ implemented in almost all routers
  Not the case in the 1980-90s, when CC was being developed
  Mostly used to isolate traffic at larger granularities (e.g., per-prefix)

## Slide 52: FQ vs. FIFO
FQ advantages:
  Isolation: cheating flows don’t benefit
  Bandwidth share does not depend on RTT
  Flows can pick any rate adjustment scheme they want
Disadvantages:
  More complex than FIFO: per flow queue/state, additional per-packet book-keeping

## Slide 53: FQ in the big picture
FQ does not eliminate congestion  it just manages the congestion
1Gbps
100Mbps
1Gbps
5Gbps
1Gbps
Blue and Green get 0.5Gbps; any excess will be dropped
Will drop an additional 400Mbps from the green flow
If the green flow doesn’t drop its sending rate to 100Mbps, we’re wasting 400Mbps that could be usefully given to the blue flow

## Slide 54: FQ in the big picture
FQ does not eliminate congestion  it just manages the congestion
  robust to cheating, variations in RTT, details of delay, reordering, retransmission, etc.
But congestion (and packet drops) still occurs
And we still want end-hosts to discover/adapt to their fair share!
What would the end-to-end argument say w.r.t. congestion control?

## Slide 55: Fairness is a controversial goal
What if you have 8 flows, and I have 4?
  Why should you get twice the bandwidth
What if your flow goes over 4 congested hops, and mine only goes over 1?
  Why shouldn’t you be penalized for using more scarce bandwidth?
And what is a flow anyway?
  TCP connection
  Source-Destination pair?
  Source?

## Slide 56: Router-Assisted Congestion Control
CC has three different tasks:
  Isolation/fairness
  Rate adjustment
  Detecting congestion

## Slide 57: Why not just let routers tell endhosts what rate they should use?
Packets carry “rate field”
Routers insert “fair share” f in packet header
End-hosts set sending rate (or window size) to f
  hopefully (still need some policing of endhosts!)
This is the basic idea behind the “Rate Control Protocol” (RCP) from Dukkipati et al. ’07

## Slide 58: Flow Completion Time: TCP vs. RCP (Ignore XCP)
Flow Duration (secs) vs. Flow Size
RCP

## Slide 59: Why the improvement?

## Slide 60: Router-Assisted Congestion Control
CC has three different tasks:
  Isolation/fairness
  Rate adjustment
  Detecting congestion

## Slide 61: Explicit Congestion Notification (ECN)
Single bit in packet header; set by congested routers
  If data packet has bit set, then ACK has ECN bit set
Many options for when routers set the bit
  tradeoff between (link) utilization and (packet) delay
Congestion semantics can be exactly like that of drop
  I.e., endhost reacts as though it saw a drop
Advantages:
  Don’t confuse corruption with congestion; recovery w/ rate adjustment
  Can serve as an early indicator of congestion to avoid delays
  Easy (easier) to incrementally deploy
    Today: defined in RFC 3168 using ToS/DSCP bits in the IP header

## Slide 62: One final proposal: Charge people for congestion!
Use ECN as congestion markers
Whenever I get an ECN bit set, I have to pay $$
Now, there’s no debate over what a flow is, or what fair is…
Idea started by Frank Kelly at Cambridge
  “optimal” solution, backed by much math
  Great idea: simple, elegant, effective
  Unclear that it will impact practice

## Slide 63: Recap
TCP:
  somewhat hacky
  but practical/deployable
  good enough to have raised the bar for the deployment of new, more optimal, approaches
  though the needs of datacenters might change the status quo (future lecture)