## Slide 1: Project 3a is out!
Goal: implement a basic network firewall
  We give you the VM & framework.
  You implement the firewall logic.
Due: Nov 17 @ noon
Notes: The project 3a is out! (Ouch)
The goal of this project is to implement a basic network firewall. You will implement the firewall logic in the framework we give you.

## Slide 2: What Is Firewall?
Blocks malicious traffic
Blocks unauthorized traffic
Notes: A network firewall is the barrier between Internet and your computer. (n)
It blocks malicious inbound traffic, (n)
and unauthorized outbound traffic.

## Slide 3
ext
int
firewall
VM
Linux TCP/IP network stack
Notes: Here is a diagram of the VM framework.
We will provide you a VM. It has physical external interface ext, and a virtual internal interface int. (n)
The firewall program connects these two interfaces, and filters the traffic. You should implement the firewall logics here.

## Slide 4
ext
int
firewall
VM
Linux TCP/IP network stack
Decode the packet
Check the firewall rules
Pass or drop the packet
Notes: So here are the logic:
You parse the packet; Check the firewall rules and determine if the packet is matched; and then pass or drop the packet
We will go through these steps briefly.

## Slide 5: Packets on wire look like this…
and your firewall should decode this.
Notes: Packets on wire are in binary form, so the first step is to decode them.

## Slide 6: Firewall rules
Type 1: a combination of
  Protocol (TCP/UDP/ICMP)
  IP address or country (e.g., Canada)
  Port number
Type 2: domain names
  E.g., block DNS queries for *.facebook.com
Notes: The firewall is very basic, so we only need to implement two type of rules.
Rules can be a combination of protocol, ip address, and port number, or it can also be domain names for DNS queries.

## Slide 7
NO CHEATING
WE RUN COPY CHECKER
Notes: The final reminder: please do not copy codes from others, we will run copy checker for every submission.

## Slide 8: Questions?
General questions
  Ask your favorite GSI
Project-specific questions
  Chang Lan (main)
  Shoumik Palkar
  Sangjin Han
Start Early!
Notes: The project spec and code should be online by the end of today.
This project is led by Shoumik, Sangjin, and me.
If you have general questions such as protocols, packet formats, etc., feel free to ask your favorite GSI.
But if you have more specific questions, please ask one of us.

## Slide 9: Today
Router-assisted Congestion Control (wrap up)
Application layer: DNS

## Slide 10: Router-Assisted Congestion Control
Recall: Three tasks for CC:
  Fairness
  Rate adjustment
  Detecting congestion

## Slide 11: Router-Assisted Congestion Control
Recall: Three tasks for CC:
  Fairness  e.g., Fair Queuing
  Rate adjustment  e.g., Rate Control Protocol
  Detecting congestion  e.g., ECN

## Slide 12: Fairness: General Approach
Routers classify packets into “flows”
  Assume for now flows ~ TCP connections
Each flow has its own FIFO queue in router
Router services flows in a fair fashion

## Slide 13: Max-Min Fairness
Given set of bandwidth demands ri and total bandwidth C, max-min bandwidth allocations are:
ai = min(f, ri)
where f is the unique value such that Sum(ai) = C
This is what round-robin service gives if all packets are the same size
r1
r2
r3
?
?
?
C bits/s

## Slide 14: Fair Queuing is how we deal with packets of different sizes
Mental model: Bit-by-bit round robin
For each packet, compute its “deadline”
  deadline  the time at which the last bit of a packet would have left the router if flows are served bit-by-bit
Transmit packets in increasing order of deadlines

## Slide 15: Example
1
2
3
4
5
1
2
3
4
1
2
3
1
2
4
3
4
5
5
6
1
2
1
3
2
3
4
4
5
6
5
5
6
Flow 1
(arrival traffic)
Flow 2
(arrival traffic)
Bit-wise round-robin
FQ
time
time
time
time

## Slide 16: Exercise
A1
A2
A3
A4
C1
Flow A
(arrival traffic)
Flow B
(arrival traffic)
time
time
B1
Flow C
(arrival traffic)
time
B2
C2
What’s the packet order at the output for four scheduling disciplines?
  FIFO
  Round-Robin
  Fair Queuing
  Priority
Assume Flow A > B > C in priority and for breaking ties

## Slide 17: Router-Assisted Congestion Control
Recall: Three tasks for CC:
  Fairness  e.g., Fair Queuing
  Rate adjustment  e.g., Rate Control Protocol
  Detecting congestion  e.g., ECN

## Slide 18: Idea: Let routers tell endhosts what rate they should use
Packets carry “rate field”
Routers insert “fair share” f in packet header
End-hosts set sending rate (or window size) to f
  Note: still assumes end-hosts play by the rules
This is the basic idea behind the “Rate Control Protocol” (RCP) from Dukkipati&McKeown in 2007

## Slide 19: Flow Completion Time: TCP vs. RCP (Ignore XCP)
Flow Duration (secs) vs. Flow Size
RCP

## Slide 20: Why the improvement?

## Slide 21: Why is RCP important?
Congestion control had long focused on safety (primary) and fairness (secondary)
  TCP does a good enough job at both
RCP highlighted CC’s impact on performance
  performance matters a lot in today’s environment
RCP shows we can do better but is still fairly complex and not incrementally deployable

## Slide 22: RC3 – Mittal et al., 2014
RC3: Recursively Cautious Congestion Control
Senders transmit at max rate from the get-go
But packets are marked with priorities
  CWND packets are sent at priority#1
  The remaining at low priority
Routers implement priority scheduling (exists today)
  If no congestion, all packets get through (high performance)
  else, low priority packets dropped (safety and fairness)

## Slide 23: Router-Assisted Congestion Control
Recall: Three tasks for CC:
  Fairness  e.g., Fair Queuing
  Rate adjustment  e.g., Rate Control Protocol
  Detecting congestion  e.g., ECN

## Slide 24: Explicit Congestion Notification (ECN)
Single bit in packet header; set by congested routers
  Many options for when routers set the bit
  Tradeoff between (link) utilization and (packet) delay
Receiver relays ECN bit in its ACK to the sender
  Congestion semantics can be exactly like that of drop
  e.g., endhost reacts as though it saw a drop
Advantages:
  Don’t confuse corruption with congestion
  Serves as an early indicator of congestion to avoid delays
  Easy (easier) to incrementally deploy
  Today: defined in RFC 3168 using ToS/DSCP bits in the IP header

## Slide 25: A final proposal: Charge people for congestion!
Use ECN as congestion markers
Whenever I get an ECN bit set, I have to pay $$
Now, there’s no debate over what a flow is, or what fair is…
Idea started by Frank Kelly at Cambridge
  “optimal” solution, backed by much math
  Great idea: simple, elegant, effective
  Unclear that it will impact practice

## Slide 26: Recap!
TCP
  allows apps to assume reliable bytestream delivery
  with (mostly) fair and safe sharing of network resources
Congestion control
  avoid overloading the network to the point of collapse
  while sharing resources fairly
  and maximizing performance
  TCP does a good enough job at the first two but the last is more iffy

## Slide 27: Taking Stock
Course so far
  Concepts (links, delays, switches)
  Overall architecture (layers, protocols, principles)
  Network layer (how we interconnect hosts and networks)
  Transport layer (how we make best-effort usable to apps)
What’s left?
  Application layer (DNS, HTTP)  this week
  Lower layers (Ethernet, Wireless)  next
  Advanced topics (datacenters, SDN, IPv6) last ~2 weeks

## Slide 28: Some very special guest lectures
Nov 10: Yahel Ben-David (Wireless)
Nov 19: Stephen Strowes (IPv6)
Nov 24: Scott Shenker (SDN)
Dec 1: Panel: Careers in networking (tentative)

## Slide 29: Application Layer
Domain Name System (DNS)
  What’s behind (e.g.) instr.eecs.berkeley.edu?
HTTP and the Web
  What happens when you click on a link?

## Slide 30: Host Names & Addresses
Host addresses: e.g., 169.229.131.109
  a number used by protocols
  conforms to network structure (the “where”)
Host names: e.g., instr.eecs.berkeley.edu
  mnemonic name usable by humans
  conforms to organizational structure (the “who”)
The Domain Name System (DNS) is how we map from one to the other
  a directory service for hosts on the Internet

## Slide 31: Why bother?
Convenience
  Easier to remember www.google.com than 74.125.239.49
Provides a level of indirection!
  Decoupled names from addresses
  Many uses beyond just naming a specific host

## Slide 32: DNS: Early days
Mappings stored in a hosts.txt file (in /etc/hosts)
  maintained by the Stanford Research Institute (SRI)
  new versions periodically copied from SRI (via FTP)
As the Internet grew this system broke down
  SRI couldn’t handle the load
  conflicts in selecting names
  hosts had inaccurate copies of hosts.txt
The Domain Name System (DNS) was invented to fix this
  First name server implementation done by 4 UCB students!

## Slide 33: Goals?
Scalable
  many names
  many updates
  many users creating names
  many users looking up names
Highly available
Correct
  no naming conflicts (uniqueness)
  consistency
Lookups are fast

## Slide 34: How?
Partition the namespace
Distribute administration of each partition
  Autonomy to update my own (machines’) names
  Don’t have to track everybody’s updates
Distribute name resolution for each partition
How should we partition things?

## Slide 35: Key idea: hierarchical distribution
Three intertwined hierarchies
  Hierarchical namespace
    As opposed to original flat namespace
  Hierarchically administered
    As opposed to centralized administrator
  Hierarchy of servers
    As opposed to centralized storage

## Slide 36: Hierarchical Namespace
“Top Level Domains” are at the top
Domains are subtrees
  E.g: .edu, berkeley.edu, eecs.berkeley.edu
Name is leaf-to-root path
  instr.eecs.berkeley.edu
Name collisions trivially avoided!
  each domain’s responsibility
root
edu
com
gov
mil
org
net
uk
fr
berkeley
ucla
eecs
sims
instr
…
Notes: gTLDs and ccTLDs

## Slide 37: Hierarchical Administration
root
edu
com
gov
mil
org
net
uk
fr
berkeley
ucla
eecs
sims
instr
root
edu
com
gov
mil
org
net
uk
fr
berkeley
eecs
sims
A zone corresponds to an administrative authority responsible for a contiguous portion of the hierarchy
E.g.: UCB controls *.berkeley.edu and *.sims.berkeley.edu while EECS controls *.eecs.berkeley.edu
ICANN/IANA

## Slide 38: Server Hierarchy
Top of hierarchy: Root servers
  Location hardwired into other servers
Next Level: Top-level domain (TLD) servers
  .com, .edu, etc.
  Managed professionally
Bottom Level: Authoritative DNS servers
  Actually store the name-to-address mapping
  Maintained by the corresponding administrative authority

## Slide 39: Server Hierarchy
Every server knows the address of the root name server
  Root servers know the address of all TLD servers
  …
An authoritative DNS server stores name-to-address mappings (“resource records”) for all DNS names in the domain that it has authority for
 Each server stores a subset of the total DNS database
 Each server can discover the server(s) responsible for any portion of the hierarchy

## Slide 40: DNS Root
Located in Virginia, USA
Verisign, Dulles, VA

## Slide 41: DNS Root Servers
13 root servers (labeled A-M; see http://www.root-servers.org/)
B USC-ISI Marina del Rey, CA
L ICANN Los Angeles, CA
E NASA Mt View, CA
F Internet Software
Consortium
Palo Alto, CA
I Autonomica, Stockholm
K RIPE London
M WIDE Tokyo
A Verisign, Dulles, VA
C Cogent, Herndon, VA
D U Maryland College Park, MD
G US DoD Vienna, VA
H ARL Aberdeen, MD
J Verisign

## Slide 42: DNS Root Servers
B USC-ISI Marina del Rey, CA
L ICANN Los Angeles, CA
E NASA Mt View, CA
F Internet Software
Consortium,
Palo Alto, CA
(and 37 other locations)
I Autonomica, Stockholm (plus 29 other locations)
K RIPE London (plus 16 other locations)
M WIDE Tokyo
plus Seoul, Paris, San Francisco
A Verisign, Dulles, VA
C Cogent, Herndon, VA (also Los Angeles, NY, Chicago)
D U Maryland College Park, MD
G US DoD Vienna, VA
H ARL Aberdeen, MD
J Verisign (21 locations)
13 root servers (labeled A-M; see http://www.root-servers.org/)
Replicated via any-casting

## Slide 43: Anycast in a nutshell
Routing finds shortest paths to destination
What happens if multiple machines advertise the same address?
The network will deliver the packet to the closest machine with that address
This is called “anycast”
  Very robust
  Requires no modification to routing algorithms

## Slide 44: DNS Records
DNS servers store resource records (RRs)
  RR is (name, value, type, TTL)
Type = A: ( Address)
  name = hostname
  value = IP address
Type = NS: ( Name Server)
  name = domain
  value = name of dns server for domain

## Slide 45: DNS Records (cont’d)
Type = MX: ( Mail eXchanger)
  name = domain in email address
  value = name(s) of mail server(s)

## Slide 46: Inserting Resource Records into DNS
Example: you just created company “FooBar”
You get a block of IP addresses from your ISP
  say 212.44.9.128/25
Register foobar.com at registrar (e.g., Go Daddy)
  Provide registrar with names and IP addresses of your authoritative name server(s)
  Registrar inserts RR pairs into the .com TLD server:
    (foobar.com, dns1.foobar.com, NS)
    (dns1.foobar.com, 212.44.9.129, A)
Store resource records in your server dns1.foobar.com
  e.g., type A record for www.foobar.com
  e.g., type MX record for foobar.com

## Slide 47: Using DNS (Client/App View)
Two components
  Local DNS servers
  Resolver software on hosts
Local DNS server (“default name server”)
  Clients configured with the default server’s address or learn it via a host configuration protocol (e.g., DHCP – future lecture)
Client application
  Obtain DNS name (e.g., from URL)
  Triggers DNS request to its local DNS server

## Slide 48
DNS client (me.cs.berkeley.edu)
DNS server
root servers
local
(mydns.berkeley.edu)
.edu servers
nyu.edu servers

## Slide 49
DNS client (me.cs.berkeley.edu)
DNS server
root servers
.edu servers
nyu.edu servers
local
www.nyu.edu?
(mydns.berkeley.edu)

## Slide 50
root
DNS server
DNS client (me.cs.berkeley.edu)
DNS server
.edu servers
nyu.edu servers
(mydns.berkeley.edu)
www.nyu.edu?

## Slide 51
root
DNS server
DNS client (me.cs.berkeley.edu)
DNS server
.edu servers
nyu.edu servers
(mydns.berkeley.edu)
www.nyu.edu?

## Slide 52
root
DNS server
recursive DNS query
DNS client (me.cs.berkeley.edu)
DNS server
(mydns.berkeley.edu)
.edu servers
nyu.edu servers
www.nyu.edu?

## Slide 53
root
DNS server
DNS client (me.cs.berkeley.edu)
DNS server
(mydns.berkeley.edu)
.edu servers
nyu.edu servers

## Slide 54
root
DNS server
iterative DNS query
DNS client (me.cs.berkeley.edu)
DNS server
(mydns.berkeley.edu)
.edu servers
nyu.edu servers

## Slide 55: DNS Protocol
Query and Reply messages; both with the same message format
  see text/section for details
Client-Server interaction on UDP Port 53
  Spec supports TCP too, but not always implemented

## Slide 56: Goals – how are we doing?
Scalable
  many names
  many updates
  many users creating names
  many users looking up names
Highly available

## Slide 57: Per-domain availability
DNS servers are replicated
  Primary and secondary name servers required
  Name service available if at least one replica is up
  Queries can be load-balanced between replicas
Try alternate servers on timeout
  Exponential backoff when retrying same server

## Slide 58: Goals – how are we doing?
Scalable
  many names
  many updates
  many users creating names
  many users looking up names
Highly available
Correct
  no naming conflicts (uniqueness)
  consistency
Lookups are fast

## Slide 59
DNS client
DNS server
local
nyu.edu
DNS server
.edu TLD
DNS server
root
DNS server
Notes: How can we improve performance?

## Slide 60: Caching
Caching of DNS responses at all levels
Reduces load at all levels
Reduces delay experienced by DNS client

## Slide 61: DNS Caching
How DNS caching works
  DNS servers cache responses to queries
  Responses include a “time to live” (TTL) field
  Server deletes cached entry after TTL expires
Why caching is effective
  The top-level servers very rarely change
  Popular sites visited often  local DNS server often has the information cached

## Slide 62: Negative Caching
Remember things that don’t work
  Misspellings like www.cnn.comm and www.cnnn.com
  These can take a long time to fail the first time
  Good to remember that they don’t work
  … so the failure takes less time the next time around
Negative caching is optional

## Slide 63
How can one attack DNS?

## Slide 64
DNS client
DNS server
local
root
DNS server
.edu TLD
DNS server
nyu.edu
DNS server
Persa (the impersonator)
www.epfl.ch?
1.1.1.1

## Slide 65: How can one attack DNS?
Impersonate the local DNS server
  give the wrong IP address to the DNS client

## Slide 66
DNS client
DNS server
local
root
DNS server
.edu TLD
DNS server
epfl.ch
DNS server
Denis (the denial-of-service attacker)

## Slide 67: How can one attack DNS?
Impersonate the local DNS server
  give the wrong IP address to the DNS client
Denial-of-service the root or TLD servers
  make them unavailable to the rest of the world

## Slide 68
DNS client
DNS server
local
root
DNS server
.edu TLD
DNS server
nyu.edu
DNS server
Casha

## Slide 69: How can one attack DNS?
Impersonate the local DNS server
  give the wrong IP address to the DNS client
Denial-of-service the root or TLD servers
  make them unavailable to the rest of the world
Poison the cache of a DNS server
  increase the delay experienced by DNS clients

## Slide 70: Important Properties of DNS
Administrative delegation and hierarchy results in:
Easy unique naming
“Fate sharing” for network failures
Reasonable trust model
Caching lends scalability, performance

## Slide 71: DNS provides Indirection
Addresses can change underneath
  Move www.cnn.com to a new IP address
  Humans/apps are unaffected
Name could map to multiple IP addresses
  Enables load-balancing
Multiple names for the same address
  E.g., many services (mail, www, ftp) on same machine
Allowing “host” names to evolve into “service” names

## Slide 72: Next Lecture (Scott Shenker lecturing)
HTTP and the Web
(Broadcast) Ethernet