## Slide 1: Switched Ethernet

## Slide 2: Announcements
HW3 will be pushed out 2-3 days
  Both release and due dates
  Will post on piazza when we release
Get started on project#3!

## Slide 3: Last Time: Broadcast Ethernet
Ethernet as a shared medium
How hosts communicate using CSMA / CD
  Carrier sense: wait for link to be idle
  Collision detection: listen while transmitting
Today: “Switched” Ethernet

## Slide 4: Broadcast vs. Switched Ethernet
Ethernet was invented as a broadcast technology
  Each packet received by all attached hosts
  CSMA/CD for media access control
Current Ethernets are “switched”
  Point-to-point links between switches and to hosts
  No sharing, no CSMA/CD

## Slide 5: Why Switched Ethernet?
Ethernet switch
A
B
C
D
Enables concurrent communication
  Host A can talk to C, while B talks to D
  No collisions  no need for CSMA, CD
  No constraints on link lengths, etc.

## Slide 6: The evolution of Ethernet
From the shared media coax cables to dedicated links
From 3 Mbit/s experimental Ethernet to 100 Gbit/s
From electrical signaling to optical
Changed almost everything except the frame format
Lesson: the right interface can accommodate many changes
  Evolve the implementation while maintaining the interface (backward compatibility)

## Slide 7: Topics
Frames and framing
Addressing
Routing
Forwarding
Discovery: Bootstrapping end-to-end commn.

## Slide 8: Ethernet “Frames”
type
Encapsulates IP datagram
Preamble:
  7 bytes for clock synchronization
  1 byte to indicate start of frame
Addresses: 6 bytes
Type: 2 bytes, indicating higher-layer protocol (e.g., IP, Appletalk)
Data payload: max 1500 bytes, minimum 46 bytes
CRC: 4 bytes for error detection
Preamble
Dest. Address
Source Address
Data
CRC

## Slide 9: Framing frames
Physical layer puts bits on a link
But, two hosts connected on the same physical medium need to be able to exchange frames
  Service provided by the link layer
  Implemented by the network adaptor
Framing problem: how does the link layer determine where each frame begins and ends?

## Slide 10: Simple approach: count bytes
Sender includes number of bytes in header
Receiver extracts this number of bytes of body
But what if the Count field is corrupted?
  L2 will frame the wrong bytes  a framing error
  CRC tells you to discard this frame, but what about the next one?
53
Body
80
Body
53 bytes of data
21 bytes of data
61
Body
80
Body
61 bytes of data misdelivered
??? bytes of data misdelivered
???
Bogus count field

## Slide 11: Desynchronization
Once framing on a link is desynchronized, it can stay that way
Need a method to resynchronize

## Slide 12: Framing with sentinel bits
Delineate frame with special “sentinel” bit pattern
  e.g., 01111110  start, 01111111  end
Problem: what if sentinel occurs within frame?
Solution: bit stuffing
  Sender always inserts a 0 after five 1s in the frame contents
  Receiver always removes a 0 appearing after five 1s
01111110
01111111
Frame contents
Notes: 6 one’s  start
7 one’s  end

## Slide 13: When receiver sees five 1s…
If next bit 0, remove it, and begin counting again
  Because this must be a stuffed bit; we can’t be at beginning/end of frame (those had six or seven 1s)
If next bit 1 (i.e., we’ve seen six 1s) then:
  If following bit is 0, this is start of frame
    Because the receiver has seen 01111110
  If following bit is 1, this is end of frame
    Because the receiver has seen 01111111
01111110
01111111
Frame content

## Slide 14: Example: sentinel bits
Original data, including start/end of frame:
01111110011111101111101111100101111111
Sender rule: five 1s  insert a 0
  After bit stuffing at the sender:
01111110011111010111110011111000101111111
Receiver rule: five 1s and next bit 0  remove 0
01111110011111101111101111100101111111

## Slide 15: Outline
Frames and framing
Addressing
Routing
Forwarding
Discovery: Bootstrapping end-to-end commn.

## Slide 16: Medium Access Control Address
MAC address
  Numerical address associated with a network adapter
  Flat name space of 48 bits (e.g., 00-15-C5-49-04-A9 in HEX)
  Unique, hard-coded in the adapter when it is built
Hierarchical Allocation
  Blocks: assigned to vendors (e.g., Dell) by the IEEE
    First 24 bits (e.g., 00-15-C5-**-**-**)
  Adapter: assigned by the vendor from its block
    Last 24 bits

## Slide 17: MAC Address vs. IP Address
MAC addresses (used in link-layer)
  Hard-coded when adapter is built
  Flat name space of 48 bits (e.g., 00-0E-9B-6E-49-76)
  Like a social security number
  Portable, and can stay the same as the host moves
  Used to get packet between interfaces on same network
IP addresses
  Configured, or learned dynamically
  Hierarchical name space of 32 bits (e.g., 12.178.66.9)
  Like a postal mailing address
  Not portable, and depends on where the host is attached
  Used to get a packet to destination IP subnet

## Slide 18: Outline
Frames and framing
MAC addresses
Routing
Forwarding

## Slide 19: Routing with Switched Ethernet?
AMAC
BMAC
CMAC
DMAC
EMAC
FMAC

## Slide 20: Why does Ethernet not use LS/DV?
Concerns over scalability
  Flat MAC addresses cannot be aggregated like IP addresses
Legacy

## Slide 21: “Routing” with broadcast Ethernet
AMAC
BMAC
CMAC
DMAC
EMAC
FMAC
Sender transmits frame onto broadcast link
Frame contains destination MAC address
Each receiver’s link layer passes the frame to the network layer:
  If destination address matches the receiver’s MAC address
  Or if the destination addr. is the broadcast MAC address (ff:ff:ff:ff:ff:ff)

## Slide 22: “Routing” with broadcast Ethernet
AMAC
BMAC
CMAC
DMAC
EMAC
FMAC
Ethernet is `plug-n-play’
  A new host plugs into the Ethernet and is good to go
  No configuration by users or network operators
  Broadcast as a means of bootstraping communication

## Slide 23: Why does Ethernet not use LS/DV?
Concerns over scalability
  Flat MAC addresses cannot be aggregated like IP addresses
Legacy
  Backward compatibility with broadcast Ethernet
  Desire to maintain Ethernet’s plug-n-play behavior
  How broadcast Ethernet evolved

## Slide 24: Routing in “Extended LANs”
Local-Area Network (LAN)
Bridges relay broadcasts from one LAN to the other

## Slide 25: The “Broadcast Storm” Problem
Radia Perlman
Perlman’s idea: eliminate loops in the topology

## Slide 26: Easiest Way to Avoid Loops
Use a topology where loops are impossible!
Take arbitrary topology
Build spanning tree
  Sub-graph that includes all vertices but contains no cycles
  Links not in the spanning tree are not used to forward frames
Only one path to destinations on spanning trees
  So don’t have to worry about loops!

## Slide 27: Consider graph

## Slide 28: A Spanning Tree

## Slide 29: Another Spanning Tree

## Slide 30: Yet Another Spanning Tree

## Slide 31: Spanning Tree Protocol (Perlman‘85)
  Protocol by which bridges construct a spanning tree
  Nice properties
    Zero configuration (by operators or users)
    Self healing
  Still used today

## Slide 32: From Extended LANs to Switched Ethernet

## Slide 33: Switched Ethernet
Constraints (for backward compatibility)
  No changes to end-hosts
  Maintain plug-n-play aspect
Earlier Ethernet achieved plug-n-play by leveraging a broadcast medium
  Can we do the same in a switched topology?

## Slide 34: Flooding (still) leads to loops
1
2
4
3
B
A
C
D
Example: A wants to broadcast a message
A sends packet to 1
1 Floods to 2 and 4
2 Floods to B and 3
4 Floods to D and 3
3 Floods packet from 2 to C and 4
3 Floods packet from 4 to C and 2
4 Floods packet from 3 to D and 1
2 Floods packet from 3 to B and 1
1 Floods packet from 2 to A and 4
1 Floods packet from 4 to B and 2
….
A “broadcast storm” if the network contains a cycle of switches

## Slide 35: A Rejected Solution
1
2
4
3
B
A
C
D
Example: A wants to broadcast a message
A sends packet to 1
1 Floods to 2 and 4
2 Floods to B and 3
4 Floods to D and 3
3 Floods packet from 2 to C and 4
3 Floods packet from 4 to C and 2
done!
Can we have 3 remember that it has already received and flooded the message?

## Slide 36: Spanning Tree Approach
  Take arbitrary topology
  Pick subset of links that form a spanning tree

## Slide 37: You: Design a Spanning Tree Algorithm
Take 5 minutes, design with your neighbors, report back
Goals
  Distributed
  Self-configuring
  Must adapt when failures occur
    But don’t worry about that on first try…

## Slide 38: Algorithm Has Two Aspects
Pick a root:
  Destination to which shortest paths go
  Pick the one with the smallest identifier (MAC addr.)
Compute shortest paths to the root
  No shortest path can have a cycle
  Only keep the links on shortest-paths
  Break ties in some way (so we only keep one shortest path from each node)
Ethernet’s spanning tree construction does both with a single algorithm

## Slide 39: Breaking Ties
When there are multiple shortest paths to the root, choose the path that uses the neighbor switch with the lower ID.
One could use any tiebreaking system, but this is an easy one to remember and implement

## Slide 40: Constructing a Spanning Tree
Messages (Y, d, X)
  From node X
  Proposing Y as the root
  And advertising a distance d to Y
Switches elect the node with smallest identifier (MAC address) as root
  Y in the messages
Each switch determines if a link is on its shortest path to the root; excludes it from the tree if not
  d to Y in the message

## Slide 41: Steps in Spanning Tree Algorithm
Initially, each switch proposes itself as the root
  I.e., switch X announces (X, 0, X) to its neighbors
Switches update their view of the root
  Upon receiving message (Y, d, Z) from Z, check Y’s id
  If Y’s id < current root: set root = Y
Switches compute their distance from the root
  Add 1 to the shortest distance received from a neighbor
If root or shortest distance to it changed, send neighbors updated message (Y, d+1, X)

## Slide 42: Example (root, dist, from)
1
2
3
4
5
6
7
(1,0,1)
(2,0,2)
(3,0,3)
(4,0,4)
(5,0,5)
(6,0,6)
(7,0,7)
1
2
3
4
5
6
7
(1,0,1)
(2,0,2)
(1,1,3)
(2,1,4)
(1,1,5)
(1,1,6)
(2,1,7)
1
2
3
4
5
6
7
(1,0,1)
(1,2,2)
(1,1,3)
(2,1,4)
(1,1,5)
(1,1,6)
(2,1,7)
1
2
3
4
5
6
7
(1,0,1)
(1,2,3)
(1,1,3)
(1,3,4)
(1,1,5)
(1,1,6)
(1,3,7)
✗
✗
✗

## Slide 43: Example From Switch #4’s Viewpoint
Switch #4 thinks it is the root
  Sends (4, 0, 4) message to 2 and 7
Then, switch #4 hears from #2
  Receives (2, 0, 2) message from 2
  … and thinks that #2 is the root
  And realizes it is just one hop away
Then, switch #4 hears from #7
  Receives (2, 1, 7) from 7
  And realizes this is a longer path
  So, prefers its own one-hop path
  And removes 4-7 link from the tree
1
2
3
4
5
6
7

## Slide 44: Example From Switch #4’s Viewpoint
Switch #2 hears about switch #1
  Switch 2 hears (1, 1, 3) from 3
  Switch 2 starts treating 1 as root
  And sends (1, 2, 2) to neighbors
Switch #4 hears from switch #2
  Switch 4 starts treating 1 as root
  And sends (1, 3, 4) to neighbors
Switch #4 hears from switch #7
  Switch 4 receives (1, 3, 7) from 7
  And realizes this is a longer path
  So, prefers its own three-hop path
  And removes 4-7 Iink from the tree
1
2
3
4
5
6
7

## Slide 45: Links on spanning tree
3-1
5-1
6-1
2-3
4-2
7-2
1
2
3
4
5
6
7

## Slide 46: Now which ones are on the spanning tree?
2 is new root
3-2
6-2
4-2
7-2
5-6
2
3
4
5
6
7

## Slide 47: Robust Spanning Tree Algorithm
Algorithm must react to failures
  Failure of the root node
  Failure of other switches and links
Root switch sends periodic root announcement messages
  Other switches continue forwarding messages
Detecting failures through timeout (soft state)
  If no word from root, time out and claim to be the root!

## Slide 48: Outline
Frames and framing
MAC addresses
Routing
Forwarding
Discovery: Bootstrapping end-to-end commn.