## Slide 1: Missing pieces + Putting the pieces together
CS 168, Fall 2014
Sylvia Ratnasamy
Material thanks to Ion Stoica, Scott Shenker, Jennifer Rexford, Nick McKeown, and many other colleagues

## Slide 2: Today
Switched Ethernet (wrap-up)
  Frames and framing
  MAC addresses
  Routing
  Forwarding
Missing pieces and putting the pieces together

## Slide 3: Last Time
Switched Ethernet
  Frame formats
  MAC addresses
  Spanning Tree approach
    Take arbitrary topology
    Pick subset of links that form a spanning tree
Today: how do we forward over the spanning tree?

## Slide 4: Flooding on a Spanning Tree
Switches flood using the following rule:
  (Ignoring all ports not on spanning tree!)
  Originating switch sends packet out all ports
  When a packet arrives on one incoming port, send it out all ports other than the incoming port

## Slide 5: Flooding on Spanning Tree

## Slide 6: Flooding on Spanning Tree

## Slide 7: But isn’t flooding wasteful?
Yes, but we can use it to bootstrap more efficient forwarding
Idea: watch the packets going by, and learn from them
  If node A sees a packet from node B come in on a particular port, it knows what port to use to reach B!
  Works because there’s only one path to B

## Slide 8: Nodes can “learn” routes
Switch learns how to reach nodes by remembering where flooding packets came from
  If flood packet from Node A entered switch on port 4, then switch uses port 4 to send to Node A

## Slide 9: General Approach
Flood first packet to node you are trying to reach
All switches learn where you are
When destination responds, some switches learn where it is…
  Only some switches, because packet to you follows direct path, and is not flooded

## Slide 10: Learning from Flood Packets
Node A
Node A can be reached
through this port
Node A can be reached
through this port
Once a node has sent a flood message, all other switches know how to reach it….
Node B

## Slide 11: Node B Responds
Node A
Node B can be reached
through this port
When a node responds, some of the switches learn where it is
Node B
Node B can be reached
through this port
Node B can be reached
through this port
Node B can be reached
through this port

## Slide 12: Ethernet switches are “self learning”
When a packet arrives:
Inspect source MAC address, associate with incoming port
Store mapping in the switch table
Use time-to-live field to eventually forget mapping
A
B
C
D
Packet tells switch how to reach A.

## Slide 13: Self Learning: Handling Misses
When packet arrives with unfamiliar destination
Forward packet out all other ports
Response may teach switch about that destination
A
B
C
D

## Slide 14: Hence: Forwarding Rule
When switch receives a packet:
index the switch table using destination MAC
if entry found for destination {
if dest on port from which packet arrived then drop packet
else forward packet on port indicated
}
else flood
forward on all but the port
on which the frame arrived
Why do this?

## Slide 15: Summary of Learning Approach
Avoids loop by restricting to spanning tree
This makes flooding possible
Flooding allows packet to reach destination
And in the process switches learn how to reach source of flood
No route “computation”
Forwarding entries a consequence of traffic pattern

## Slide 16: Contrast
IP
  Packets forwarded on all links
  Aggregatable addresses
  Routing protocol computes loop-free paths
  Forwarding table computed by routing protocol
Ethernet
  Packets forwarded on subset of links (spanning tree)
  Flat addresses
  “Routing” protocol computes loop-free topology
  Forwarding table derived from data packets(+SPT for floods)

## Slide 17: Strengths of Ethernet’s Approach?
Plug-n-Play: zero-configuration / self-*
Simple
Cheap?

## Slide 18: Weaknesses of This Approach?
Much of the network bandwidth goes unused
  Forwarding is only over the spanning tree
Delay in reestablishing spanning tree
  Network is “down” until spanning tree rebuilt
  And rebuilt spanning tree may be quite different
Slow to react to host movement
  Entries must time out
Poor predictability
  Location of root and traffic pattern determines forwarding efficiency

## Slide 19: Today
Switched Ethernet (wrap-up)
  Frames and framing
  MAC addresses
  Routing
  Forwarding
Missing pieces and putting the pieces together

## Slide 20: Discovery
A host is “born” knowing only its MAC address
Must discover lots of information before it can communicate with a remote host B
  what is my IP address?
  what is B’s IP address? (remote)
  what is B’s MAC address? (if B is local)
  what is my first-hop router’s address? (if B is not local)
  …

## Slide 21: ARP and DHCP
Link layer discovery protocols
  ARP  Address Resolution Protocol
  DHCP  Dynamic Host Configuration Protocol
  confined to a single local-area network (LAN)
  rely on broadcast capability
Hosts
Router

## Slide 22: ARP and DHCP
Link layer discovery protocols
Serve two functions
  Discovery of local end-hosts
    for communication between hosts on the same LAN

## Slide 23: ARP and DHCP
Link layer discovery protocols
Serve two functions
  Discovery of local end-hosts
  Bootstrap communication with remote hosts
    what’s my IP address?
    who/where is my local DNS server?
    who/where is my first hop router?

## Slide 24: DHCP
“Dynamic Host Configuration Protocol”
  defined in RFC 2131
A host uses DHCP to discover
  its own IP address
  its netmask
  IP address(es) for its local DNS name server(s)
  IP address(es) for its first-hop “default” router(s)

## Slide 25: DHCP: operation
One or more local DHCP servers maintain required information
  IP address pool, netmask, DNS servers, etc.
  application that listens on UDP port 67

## Slide 26: DHCP: operation
One or more local DHCP servers maintain required information
Client broadcasts a DHCP discovery message
  L2 broadcast, to MAC address FF:FF:FF:FF:FF:FF

## Slide 27: DHCP: operation
One or more local DHCP servers maintain required information
Client broadcasts a DHCP discovery message
One or more DHCP servers responds with a DHCP “offer” message
  proposed IP address for client, lease time
  other parameters

## Slide 28: DHCP: operation
One or more local DHCP servers maintain required information
Client broadcasts a DHCP discovery message
One or more DHCP servers responds with a DHCP “offer” message
Client broadcasts a DHCP request message
  specifies which offer it wants
  echoes accepted parameters
  other DHCP servers learn they were not chosen

## Slide 29: DHCP: operation
One or more local DHCP servers maintain required information
Client broadcasts a DHCP discovery message
One or more DHCP servers responds with a DHCP “offer” message
Client broadcasts a DHCP request message
Selected DHCP server responds with an ACK

## Slide 30: DHCP: operation
One or more local DHCP servers maintain required information
Client broadcasts a DHCP discovery message
One or more DHCP servers responds with a DHCP “offer” message
Client broadcasts a DHCP request message
Selected DHCP server responds with an ACK
(DHCP “relay agents” used when the DHCP server isn’t on the same broadcast domain -- see text)

## Slide 31: DHCP uses “soft state”
  Soft state: if not refreshed, state is forgotten
  hard state: allocation is deliberately returned/withdrawn
  e.g., used to track address allocation in DHCP
Implementation:
  address allocations are associated with a lease period
  server: sets a timer associated with the record of allocation
  client: must request a refresh before lease period expires
  server: resets timer when a refresh arrives; sends ACK
  server: reclaims allocated address when timer expires
Simple, yet robust under failure
  state always fixes itself in (small constant of) lease time

## Slide 32: Soft state under failure
What happens when host XYZ fails?
  refreshes from XYZ stop
  server reclaims a.b.c.d after O(lease period)
Router
XYZ
DHCP Server
a.b.c.d is mine from (now’, now’+lease)
a.b.c.d is XYZ’s from (now, now+c.lease)

## Slide 33: Soft state under failure
What happens when server fails?
  ACKs from server stop
  XYZ releases address after O(lease period); send new request
  A new DHCP server can come up from a `cold start’ and we’re back on track in ~lease time
Router
XYZ
DHCP Server
a.b.c.d is mine from (now, now+lease)
a.b.c.d is XYZ’s from (now, now+c.lease)

## Slide 34: Soft state under failure
What happens if the network fails?
  refreshes and ACKs don’t get through
  XYZ release address; DHCP server reclaims it
Router
XYZ
DHCP Server
a.b.c.d is mine from (now, now+lease)
a.b.c.d is XYZ’s from (now, now+c.lease)

## Slide 35
Router
Host
Host
Host
Host
DHCP Server
Are we there yet?
DNS Server
What I learnt from DHCP
my IP: 1.2.3.48
netmask: 1.2.3.0/24 (255.255.255.0)
Local DNS: 1.2.3.156
router: 1.2.3.19

## Slide 36: Sending Packets Over Link-Layer
Link layer only understands MAC addresses
  Translate the destination IP address to MAC address
  Encapsulate the IP packet in a link-level (Ethernet) frame
Router
Host
Host
Host
Host
DNS
1.2.3.48
1.2.3.156
58-23-D7-FA-20-B0
90-E2-A1-09-66-1B
1.2.3.53
1.2.3.156
IP packet

## Slide 37: ARP: Address Resolution Protocol
Every host maintains an ARP table
  list of (IP address  MAC address) pairs
Consult the table when sending a packet
  Map destination IP address to destination MAC address
  Encapsulate the (IP) data packet with MAC header; transmit
But: what if IP address not in the table?
  Sender broadcasts: “Who has IP address 1.2.3.156?”
  Receiver responds: “MAC address 58-23-D7-FA-20-B0”
  Sender caches result in its ARP table

## Slide 38: What if the destination is remote?
Look up the MAC address of the first hop router
  1.2.3.48 uses ARP to find MAC address for first-hop router 1.2.3.19 rather than ultimate destination IP address
How does the red host know the destination is not local?
  Uses netmask (discovered via DHCP)
How does the red host know about 1.2.3.19?
  Also DHCP
host
host
DNS
...
host
host
host
...
router
router
1.2.3.0/24 (255.255.255.0)
5.6.7.0/24
1.2.3.156
1.2.3.48
1.2.3.19
router

## Slide 39: ARP header
Bit offset
=1 for Ethernet
=0x0800 for IPv4
1=request; 2=reply
=6 for Ethernet
=4 for IPv4

## Slide 40: Key Ideas in Both ARP and DHCP
Broadcasting: Can use broadcast to make contact
  Scalable because of limited size
Caching: remember the past for a while
  Store the information you learn to reduce overhead
Soft state: eventually forget the past
  Associate a time-to-live field with the information
  … and either refresh or discard the information
  Key for robustness in the face of unpredictable change

## Slide 41: Taking Stock: Naming
Layer | Examples | Structure | Configuration | Resolution Service
App. Layer | www.cs.berkeley.edu | organizational hierarchy | ~ manual | 
Network Layer | 123.45.6.78 | topological hierarchy | DHCP | 
Link layer | 45-CC-4E-12-F0-97 | vendor (flat) | hard-coded | 
DNS
ARP

## Slide 42: Discovery mechanisms
We’ve see two approaches
  Broadcast (ARP, DHCP)
    flooding doesn’t scale
    no centralized point of failure
    zero configuration
  Directory service (DNS)
    no flooding / scalable
    root of the directory is vulnerable (caching is key)
    needs configuration to bootstrap (local, root servers, etc.)
Open: can we get Internet-scale yet zero config?

## Slide 43: Steps in end-to-end communication
What do hosts need to know?
And how do they find out?

## Slide 44: Steps in reaching a destination
First look up destination’s IP address
  Need to know where my local DNS server is
    DHCP
  Also needs to know my own IP address
    DHCP

## Slide 45: Sending a Packet
On same subnet:
  Use MAC address of destination
  ARP
On some other subnet:
  Use MAC address of first-hop router
  DHCP + ARP
And how can a host tell whether destination is on same or other subnet?
  Use the netmask
  DHCP

## Slide 46: Example: A sending a packet to B
How does host A send an IP packet to host B?
A
R
B

## Slide 47: Example: A sending a packet to B
A
R
B
1. A sends packet to R. 2. R sends packet to B.

## Slide 48: A sends packet through router R
A
R
B
Host A constructs an IP packet to send to B
  Source 111.111.111.111, destination 222.222.222.222
Host A has a gateway router R
  Used to reach destinations outside of 111.111.111.0/24
  Address 111.111.111.110 for R learned via DHCP

## Slide 49: A sends packet through router R
Host A learns the MAC address of R’s interface
  ARP request: broadcast request for 111.111.111.110
  ARP response: R responds with E6-E9-00-17-BB-4B
Host A encapsulates the IP packet for B, and sends to R
A
R
B

## Slide 50: R Decides how to Forward Packet
Router R’s adapter receives the packet
  R extracts the IP packet from the Ethernet frame
  R sees the IP packet is destined to 222.222.222.222
Router R consults its forwarding table
  Packet matches 222.222.222.0/24 via other adapter (port)
A
R
B
Two points:
  IP routing table points to this port
  Destination address is within mask of port’s address (i.e., local)

## Slide 51: R sends packet to B
Router R’s learns the MAC address of host B
  ARP request: broadcast request for 222.222.222.222
  ARP response: B responds with 49-BD-D2-C7-56-2A
Router R encapsulates the packet and sends to B
A
R
B

## Slide 52
Are we there yet?
  Yes!

## Slide 53: Putting the pieces together
Assume: `cold start’ -- nothing cached anywhere
Assume: yourDNS on a different subnet from yourDHCP
Ignore intra- and interdomain routing protocols
Google’s datacenter
Dorm
You
yourDHCP
UCB
yourDNS
R
router
Count the number of protocols that come into play!
Walk through the steps required to download www.google.com/index.html from your laptop

## Slide 54: Step 1: Self discovery
You use DHCP to discover bootstrap parameters
  your IP addr (u.u.u.u)
  your DNS server’s IP (u.dns.ip.addr)
  R’s IP address (r.r.r.r)
  ..
Exchange between you and yourDHCP
Protocol count = 4
Dorm
You
yourDHCP
R
router
Ethernet
UDP
DHCP
IP

## Slide 55: Next…
You are ready to contact www.google.com
 need an IP address for www.google.com
 need to ask google’s DNS server
 need to ask my DNS server to ask google’s DNS…
 I know my DNS server’s IP addr is u.dns.ip.addr
 create a packet to send…
Ethernet
UDP
DNS
IP
destination MAC?
source: u.u.u..u
dst: u.dns.ip.addr

## Slide 56: Step 2: Getting out the door
You use ARP to discover the MAC address of R
Exchange between you and R
Protocol count = 5
Dorm
You
yourDHCP
R
router
Ethernet
ARP
dst MAC?

## Slide 57: Step 3: Send a DNS request
Exchange between you and yourDNS
Now ready to send that packet
Protocol count = 6
Ethernet
UDP
DNS
IP
source: u.u.u..u
dst: u.dns.ip.addr
R’s MAC
You
UCB
yourDNS
R
router

## Slide 58: Step 4: yourDNS does its thing
yourDNS resolves www.google.com
Protocol count = 6
yourDNS
root name server
top-level name server
google’s name server
www.google.com’s IP address is g.g.g.g
You

## Slide 59: Step 5: Getting the content (at last)
Google’s datacenter
You
UCB
R
Exchange between you and google’s server at g.g.g.g
Ethernet
TCP
HTTP
IP
source: u.u.u..u
dst: g.g.g.g
R’s MAC
Protocol count = 8

## Slide 60: Recap: Name discovery/resolution
MAC addresses?
  my own: hardcoded
  others: ARP (given IP address)
IP addresses?
  my own: DHCP
  others: DNS (given domain name)
    how do I bootstrap DNS communication? (DHCP)
Domain names?
  search engines