## Slide 1: Basic Concepts
CS168, Fall 2014 Sylvia Ratnasamy http://inst.eecs.berkeley.edu/~cs168/fa14/

## Slide 2: Administrivia
Discussion sections start Wednesday, Sep 10
Homework#1 out this week
  we will be using PandaGrader for submissions; stay tuned for details
Final exam scheduling conflicts

## Slide 3: Today
What is a network made of?
How is it shared?
How do we evaluate a network?

## Slide 4: Today
What is a network made of?
How is it shared?
How do we evaluate a network?

## Slide 5
end-system
switch
link
Internet Service Provider

## Slide 6
phone company

## Slide 7
phone company

## Slide 8
home PC
switch

## Slide 9
home PC
switch
DSL modem
DSLAM
central office
phone line
telephone
telephone network
...

## Slide 10: AT&T Central Offices in the Bay Area

## Slide 11: AT&T Central Office in Berkeley

## Slide 12: Digital Subscriber Line (DSL)
Twisted pair copper
3 separate channels
  downstream data channel
  upstream data channel
  2-way phone channel
up to 25 Mbps downstream
up to 2.5 Mbps upstream

## Slide 13: Why phone lines?

## Slide 14
cable company

## Slide 15
cable company

## Slide 16
home PC
switch

## Slide 17
home PC
switch
cable modem
CMTS
cable head end
copper
fiber
...

## Slide 18
switch
CMTS
cable head end
fiber

## Slide 19: Cable
Coaxial copper & fiber
up to 42.8 Mbps downstream
up to 30.7 Mbps upstream
shared broadcast medium

## Slide 20
university net

## Slide 21
university net

## Slide 22
workstation
“aggregate” switch
Ethernet cable
“local” switch
...

## Slide 23: Ethernet
Twisted pair copper
100 Mbps, 1 Gbps, 10 Gbps (each direction)

## Slide 24: & more
Cellular (smart phones)
Satellite (remote areas)
Fiber to the Home (home)
Optical carrier (Internet backbone)

## Slide 25
phone company
cable company
university net
WiFi
WiFi
WiFi

## Slide 26
What physical infrastructure is already available?

## Slide 27: Today
What is a network made of?
How is it shared?
How do we evaluate a network?

## Slide 28
shared link and switch resources

## Slide 29
O(n2) links
per-node capacity scales as 1/n
How do we scale a network to many end-systems?

## Slide 30
Switched networks enable efficient scaling!
How do we scale a network to many end-systems?

## Slide 31: Two approaches to sharing
Reservations
On demand

## Slide 32: Intuition: Three sources of “bursty” traffic
12Mbps
Time
Link capacity = 30Mbps
11Mbps
13Mbps

## Slide 33: Intuition: reservations
12Mbps
Time
11Mbps
13Mbps
Link capacity = 30Mbps
Each source gets 10Mbps
Frequent overloading

## Slide 34: Intuition: on demand
No overloading
Time
Link capacity = 30Mbps

## Slide 35
Switching on-demand exploits statistical multiplexing better than reservations
Sharing using the statistics of demand
Good for bursty traffic (average << peak demand)
Similar to insurance, with the same failure mode

## Slide 36: Intuition: on demand
What do we do under overload?
Time
Link capacity = 30Mbps

## Slide 37: Statistical multiplexing is a recurrent theme in computer science
Phone network rather than dedicated lines
  ancient history
Packet switching rather than circuits
  today’s lecture
Cloud computing
  shared vs. dedicated machines

## Slide 38: Two approaches to sharing
Reservations
On demand
How are these implemented?

## Slide 39: Two approaches to sharing
Reservations  circuit switching
On demand  packet switching
How are these implemented?

## Slide 40: Two approaches to sharing
Packet switching
  packets treated on demand
  admission control: per packet
Circuit switching
  resources reserved per active "connection"
  admission control: per connection
A hybrid: virtual circuits
  emulating circuit switching with packets (see text)

## Slide 41: Circuit Switching
src sends a reservation request to dst
(2) Switches “establish a circuit”
(3) src starts sending data
(4) src sends a “teardown circuit” message
dst
10Mb/s?
10Mb/s?
10Mb/s?
src
✔
✔
✔

## Slide 42: Circuit Switching
switch
src
dst
Reservation establishes a “circuit” within a switch

## Slide 43: Many kinds of “circuits”
Time division multiplexing
  divide time in time slots
  separate time slot per circuit
Frequency division multiplexing
  divide frequency spectrum in frequency bands
  separate frequency band per circuit
time
time
frequency

## Slide 44: Timing in Circuit Switching
time

## Slide 45: Timing in Circuit Switching
time

## Slide 46: Timing in Circuit Switching
time

## Slide 47: Timing in Circuit Switching
time

## Slide 48: Timing in Circuit Switching
time
Circuit establishment

## Slide 49: Timing in Circuit Switching
Data
time
Circuit establishment
Data transfer

## Slide 50: Timing in Circuit Switching
Data
time
Circuit establishment
Data transfer
Circuit teardown
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 51: Timing in Circuit Switching
time
Circuit establishment
Data transfer
Circuit teardown
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 52: Timing in Circuit Switching
Data
time
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 53: Timing in Circuit Switching
Information
time
Notes: Why the delays in the first pass of the establishment, but not in subsequent passes (or in teardown)?

## Slide 54: Circuit Switching
A
B
Circuit switching doesn’t “route around trouble”

## Slide 55: Circuit Switching
Pros
  predictable performance
  simple/fast switching (once circuit established)
Cons
  complexity of circuit setup/teardown
  inefficient when traffic is bursty
  circuit setup adds delay
  switch fails  its circuit(s) fails

## Slide 56: Packet switching
switch
dst
Each packet contains destination (dst)
Each packet treated independently

## Slide 57: Packet switching
With buffers to absorb transient overloads
switch
dst
Each packet contains destination (dst)
Each packet treated independently

## Slide 58: Packet Switching
Pros
  efficient use of network resources
  simpler to implement
  robust: can “route around trouble”
Cons
  unpredictable performance
  requires buffer management and congestion control

## Slide 59
On-demand or reserve?

## Slide 60: Today
What is a network made of?
How is it shared?
  will assume packet switching from here on
How do we evaluate a network?

## Slide 61: Today
What is a network made of?
How is it shared?
How do we evaluate a network?

## Slide 62: Performance Metrics
Delay
Loss
Throughput

## Slide 63: Delay
How long does it take to send a packet from its source to destination?

## Slide 64: Loss
What fraction of the packets sent to a destination are dropped?

## Slide 65: Throughput
At what rate is the destination receiving data from the source

## Slide 66: Delay
Consists of four components
  transmission delay
  propagation delay
  queuing delay
  processing delay
due to link properties
due to traffic mix and
switch internals

## Slide 67: A network link
Link bandwidth
  number of bits sent/received per unit time (bits/sec or bps)
Propagation delay
  time for one bit to move through the link (seconds)
Bandwidth-Delay Product (BDP)
  number of bits “in flight” at any time
  BDP = bandwidth × propagation delay
bandwidth
Propagation delay
delay x bandwidth

## Slide 68: Examples
Same city over a slow link:
  bandwidth: ~100Mbps
  propagation delay: ~0.1msec
  BDP: 10,000bits (1.25KBytes)
Cross-country over fast link:
  bandwidth: ~10Gbps
  propagation delay: ~10msec
  BDP: 108bits (12.5MBytes)

## Slide 69: 1. Transmission delay
How long does it take to push all the bits of a packet into a link?
Packet size / Transmission rate of the link
  e.g. 1000 bits / 100 Mbits per sec = 10 -5 sec

## Slide 70: 2. Propagation delay
How long does it take to move one bit from one end of a link to the other?
Link length / Propagation speed of link
  E.g. 30 kilometers / 3 108 meters per sec = 10-4 sec

## Slide 71: Packet Delay Sending 100B packets from A to B?
time=0
A
B
100Byte packet
Time
1Mbps, 1ms
Time to transmit one bit = 1/106s
Time to transmit 800 bits=800x1/106s
Time when that bit reaches B = 1/106+1/103s
The last bit reaches B at
(800x1/106)+1/103s
= 1.8ms

## Slide 72: Packet Delay Sending 100B packets from A to B?
A
B
100Byte packet
Time
1Mbps, 1ms
1Gbps, 1ms?
The last bit reaches B at
(800x1/106)+1/103s
= 1.8ms
1GB file in 100B packets
The last bit reaches B at
(800x1/109)+1/103s
= 1.0008ms
The last bit in the file reaches B at
(107x800x1/109)+1/103s
= 8001ms
107 x 100B packets

## Slide 73: Packet Delay: The “pipe” view Sending 100B packets from A to B?
A
B
100Byte packet
Time
1Mbps, 10ms
100Byte packet
100Byte packet
time 
BW 
pkt tx time

## Slide 74: Packet Delay: The “pipe” view Sending 100B packets from A to B?
1Mbps, 10ms (BDP=10,000)
time 
BW 
10Mbps, 1ms (BDP=10,000)
time 
BW 
1Mbps, 5ms (BDP=5,000)
time 
BW 

## Slide 75: Packet Delay: The “pipe” view Sending 100B packets from A to B?
1Mbps, 10ms (BDP=10,000)
time 
BW 
200B?
1Mbps, 10ms (BDP=10,000)
time 
BW 

## Slide 76: 3. Queuing delay
How long does a packet have to sit in a buffer before it is processed?

## Slide 77: Queuing delay: “pipe” view

## Slide 78: Queuing delay: “pipe” view
No overload!

## Slide 79: Queuing delay: “pipe” view
Transient Overload
Not a rare event!
Queue

## Slide 80: Queuing delay: “pipe” view
Queue
Transient Overload
Not a rare event!

## Slide 81: Queuing delay: “pipe” view
Queue
Transient Overload
Not a rare event!

## Slide 82: Queuing delay: “pipe” view
Queue
Transient Overload
Not a rare event!

## Slide 83: Queuing delay: “pipe” view
Queue
Transient Overload
Not a rare event!

## Slide 84: Queuing delay: “pipe” view
Queue
Transient Overload
Not a rare event!
Queues absorb transient bursts but introduce queuing delay

## Slide 85: Queuing delay: “pipe” view
What about persistent overload?
Will eventually drop packets (“loss”)

## Slide 86: Queuing Delay
How long does a packet have to sit in a buffer before it is processed?
Depends on traffic pattern
  arrival rate at the queue
  nature of arriving traffic (bursty or not?)
  transmission rate of outgoing link

## Slide 87: Queuing Delay
How long does a packet have to sit in a buffer before it is processed?
Characterized with statistical measures
  average queuing delay
  variance of queuing delay
  probability delay exceeds a threshold value

## Slide 88: Basic Queuing Theory Terminology
Arrival process: how packets arrive
  Average rate A
  Peak rate P
W: average time packets wait in the queue
  W for “waiting time”
L: average number of packets waiting in the queue
  L for “length of queue”

## Slide 89: Little’s Law (1961)
L = A x W
Compute L: count packets in queue every second
  How often does a single packet get counted? W times
Why do you care?
  Easy to compute L, harder to compute W
Notes: Row vs column

## Slide 90: 4. Processing Delay
How long does the switch take to process a packet?
typically assume this is negligible

## Slide 91: Recap
What is a network made of?
  What physical infrastructure exists?
How is it shared?
  On-demand or reserve?
How do we evaluate a network?
  Where is my delay coming from?
  To be contd…