## Slide 1: Basic Concepts (part 2): packet delays and layering
CS168, Fall 2014 Sylvia Ratnasamy http://inst.eecs.berkeley.edu/~cs168/fa14/

## Slide 2: Administrivia
Discussion sections start Monday, Sep 15
Homework#1 out tonight
  announce homework logistics

## Slide 3: Plan of attack
What is a network made of?
How is it shared?
How do we evaluate a network?
How is communication organized?

## Slide 4
end-system
switch
link
Internet Service Provider

## Slide 5
phone company

## Slide 6
home PC
switch
DSL modem
DSLAM
central office
phone line
telephone
telephone network
...

## Slide 7: Two approaches to sharing
Reservations  circuit switching
On demand  packet switching

## Slide 8: Circuit vs. Packets
Circuits
  predictable performance
  inefficient use of network resources
  complex (state in the network)
Packets
  unpredictable performance
  efficient use of network resources
  simple (no state in the network)

## Slide 9
What physical infrastructure is already available?
Reserve or on-demand?

## Slide 10: Today
What is a network made of?
How is it shared?
How do we evaluate a network?
How is communication organized?

## Slide 11: Performance Metrics
Delay
Loss
Throughput

## Slide 12: Delay
How long does it take to send a packet from its source to destination?

## Slide 13: Delay
Consists of four components
  transmission delay
  propagation delay
  queuing delay
  processing delay
due to link properties
due to traffic mix and
switch internals

## Slide 14: A network link
Link bandwidth
  number of bits sent/received per unit time (bits/sec or bps)
Propagation delay
  time for one bit to move through the link (seconds)
Bandwidth-Delay Product (BDP)
  number of bits “in flight” at any time
  BDP = bandwidth × propagation delay
bandwidth
Propagation delay
delay x bandwidth

## Slide 15: Examples
Same city over a slow link:
  bandwidth: ~100Mbps
  propagation delay: ~0.1msec
  BDP: 10,000bits (1.25KBytes)
Cross-country over fast link:
  bandwidth: ~10Gbps
  propagation delay: ~10msec
  BDP: 108bits (12.5MBytes)

## Slide 16: Packet Delay Sending 100B packets from A to B?
time=0
A
B
100Byte packet
Time
1Mbps, 1ms
Time to transmit one bit = 1/106s
Time to transmit 800 bits=800x1/106s
Time when that bit reaches B = 1/106+1/103s
The last bit reaches B at
(800x1/106)+1/103s
= 1.8ms

## Slide 17: Packet Delay Sending 100B packets from A to B?
A
B
100Byte packet
Time
1Mbps, 1ms
1Gbps, 1ms?
The last bit reaches B at
(800x1/106)+1/103s
= 1.8ms
1GB file in 100B packets
The last bit reaches B at
(800x1/109)+1/103s
= 1.0008ms
The last bit in the file reaches B at
(107x800x1/109)+1/103s
= 8001ms
107 x 100B packets

## Slide 18: Packet Delay: The “pipe” view Sending 100B packets from A to B?
A
B
100Byte packet
Time
1Mbps, 10ms
100Byte packet
100Byte packet
time 
BW 
pkt tx time

## Slide 19: Packet Delay: The “pipe” view Sending 100B packets from A to B?
1Mbps, 10ms (BDP=10,000)
time 
BW 
10Mbps, 1ms (BDP=10,000)
time 
BW 
1Mbps, 5ms (BDP=5,000)
time 
BW 

## Slide 20: Packet Delay: The “pipe” view Sending 100B packets from A to B?
1Mbps, 10ms (BDP=10,000)
time 
BW 
200B?
1Mbps, 10ms (BDP=10,000)
time 
BW 

## Slide 21: 1. Transmission delay
How long does it take to push all the bits of a packet into a link?
Packet size / Link bandwidth
  e.g. 1000 bits / 100 Mbits per sec = 10 -5 sec

## Slide 22: 2. Propagation delay
How long does it take to move one bit from one end of a link to the other?
Link length / Link propagation delay
  E.g. 30 kilometers / 3 108 meters per sec = 10-4 sec

## Slide 23: 3. Queuing delay
How long does a packet have to sit in a buffer before it is processed?

## Slide 24: Queuing delay: “pipe” view

## Slide 25: Queuing delay: “pipe” view
No queuing delay!

## Slide 26: Queuing delay: “pipe” view
Transient Overload
Not a rare event!
Queue

## Slide 27: Queuing delay: “pipe” view
Queue

## Slide 28: Queuing delay: “pipe” view
Queue

## Slide 29: Queuing delay: “pipe” view
Queue

## Slide 30: Queuing delay: “pipe” view
Queue

## Slide 31: Queuing delay: “pipe” view
Queue
Queues absorb transient bursts but introduce queuing delay

## Slide 32: Queuing delay: “pipe” view
What about persistent overload?
Will eventually drop packets (“loss”)

## Slide 33: Queuing delay
If arrival rate > departure rate
  approaches infinity (assuming an infinite buffer)

## Slide 34
arrival rate /departure rate
1
Average queuing delay
Notes: This plot shows the average queuing delay experienced by a packet arriving at a buffer,
as a function of this entity here, which is the arrival rate divided by the departure rate.
As this entity approaches 1 (the arrival rate approaches the departure rate),
the average delay goes to infinity.
The important thing to note about this curve is the shape.
When we approach close to this area here, the curve goes up very fast.
This means that small changes in arrival rate can have a dramatic impact on delay.
This is what happens when you are driving in a congested highway.
The smallest disturbance (like one car braking) can significantly increase your delay.
When you design a queuing system, you want it to operate far from that point.

## Slide 35: Queuing delay
If arrival rate > departure rate
  approaches infinity (assuming an infinite buffer)
  in practice, finite buffer  loss
If arrival rate < departure rate

## Slide 36
e.g., arrival rate < departure rate
Queue

## Slide 37: Queuing delay
If arrival rate > departure rate
  approaches infinity (assuming an infinite buffer)
  in practice, finite buffer  loss
If arrival rate < departure rate
  depends on burst size

## Slide 38: Queuing Delay
How long does a packet have to sit in a buffer before it is processed?
Depends on traffic pattern

## Slide 39: Queuing Delay
How long does a packet have to sit in a buffer before it is processed?
Depends on traffic pattern
Characterized with statistical measures
  average queuing delay
  average arrival rate
  average departure rate

## Slide 40: Basic Queuing Theory Terminology
Arrival process: how packets arrive
  Average rate A
W: average time packets wait in the queue
  W for “waiting time”
L: average number of packets waiting in the queue
  L for “length of queue”

## Slide 41: Little’s Law (1961)
L = A x W
Compute L: count packets in queue every second
  How often does a single packet get counted? W times
Why do you care?
  Easy to compute L, harder to compute W
Notes: Row vs column

## Slide 42: 4. Processing Delay
How long does the switch take to process a packet?
typically assume this is negligible

## Slide 43: Delay
Consists of four components
  transmission delay
  propagation delay
  queuing delay
  processing delay
due to link properties
due to traffic mix and
switch internals

## Slide 44
transmission
End-to-end delay
propagation
queuing
processing
transmission
propagation
queuing
processing
transmission
propagation

## Slide 45: Loss
What fraction of the packets sent to a destination are dropped?

## Slide 46: Throughput
At what rate is the destination receiving data from the source
  Data size / transfer time

## Slide 47
F/R + propagation delay
transmission rate R bits/sec
Average throughput =
Transfer time =
file of size F bits
R
packets of size L bits

## Slide 48
transmission rate R’ > R
transmission rate R
file of size F bits
packets of size L bits

## Slide 49
F/R + propagation delay +
L/R’
bottleneck link
min { R, R’ } = R
transmission rate R’ > R
transmission rate R
file of size F bits
Average throughput =
Transfer time =
packets of size L bits

## Slide 50
bottleneck link
min { R, R’ } = R
transmission rate R’ > R
transmission rate R
file of size F bits
Average throughput =
packets of size L bits

## Slide 51
bottleneck link
transmission rate R1
transmission rate R2

## Slide 52
transmission rate R1
transmission rate R2
bottleneck link

## Slide 53: Throughput
At what rate is the destination receiving data from the source?
Later in the semester
  TCP throughput, application-level throughput, etc.
  throughput vs. “goodput”

## Slide 54
What physical infrastructure is already available?
Reserve or on-demand?
Where’s my delay coming from?