## Slide 1: Plan of attack
What is a network made of?
How is it shared?
How do we evaluate a network?
How is communication organized?

## Slide 2: Three steps
Decompose the problem into tasks
Organize these tasks
Assign tasks to entities (who does what)

## Slide 3: Inspiration…
Dear John,
Your days are numbered.
--Pat
CEO A writes letter to CEO B
  Folds letter and hands it to administrative aide
Aide:
  Puts letter in envelope with CEO B’s full name
  Takes to FedEx
FedEx Office
  Puts letter in larger envelope
  Puts name and street address on FedEx envelope
  Puts package on FedEx delivery truck
FedEx delivers to other company

## Slide 4: The Path of the Letter
CEO
Aide
FedEx
CEO
Aide
FedEx
Location
Fedex Envelope (FE)
Letter
Envelope
Semantic Content
Identity
“Peers” in the same layer understand the same things
No one else needs to
Lowest level has most packaging

## Slide 5: In the Internet: decomposition
Applications
Reliable (or unreliable) transport
Best-effort global packet delivery
Best-effort local packet delivery
Physical transfer of bits

## Slide 6: In the Internet: organization
Applications
…built on…
…built on…
…built on…
…built on…
Reliable (or unreliable) transport
Best-effort global packet delivery
Best-effort local packet delivery
Physical transfer of bits
Application
Transport
Network
Data link
Physical
L1
L2
L3
L4
L7
nope, not a typo

## Slide 7: In the context of the Internet
Application
Presentation
Session
Transport
Network
Data link
Physical
1
2
3
4
5
6
7
The Open Systems Interconnect (OSI) model developed by the ISO included two additional layers that are often implemented as part of the application

## Slide 8: Layers
Layer = a part of a system with well-defined interfaces to other parts
One layer interacts only with layer above and layer below
Two layers interact only through the interface between them

## Slide 9: Protocols and Layers
Communication between peer layers on different systems is defined by protocols
Application
Transport
Network
Data link
Physical
L1
L2
L3
L4
L7
Application
Transport
Network
Data link
Physical
L1
L2
L3
L4
L7

## Slide 10: What is a Protocol?
Friendly greeting
Time?
2pm
Thank you
Friendly greeting

## Slide 11
CEO
Aide
FedEx
CEO
Aide
FedEx
Fedex Envelope (FE)

## Slide 12: What is a Protocol?
An agreement between parties on how to communicate
Defines the syntax of communication
  header  instructions for how to process the payload
  Each protocol defines the format of its packet headers
    e.g. “the first 32 bits carry the destination address”
01000111100010101001110100011001
Data
payload
header

## Slide 13: What is a Protocol?
An agreement between parties on how to communicate
Defines the syntax of communication
And semantics
  “first a hullo, then a request…”
  we’ll study many protocols later in the semester
Protocols exist at many levels, hardware and software
  defined by a variety of standards bodies (IETF, IEEE, ITU)

## Slide 14: Protocols at different layers
There is just one network-layer protocol!
Application
Transport
Network
Data link
Physical
L1
L2
L3
L4
L7
SMTP
HTTP
DNS
NTP
TCP
UDP
IP
Ethernet
FDDI
PPP
optical
copper
radio
PSTN

## Slide 15: Layer Encapsulation: Protocol Headers
TCP header
IP header
Ethernet header
HTTP request/response
User A
User B
Notes: Deepest level most header

## Slide 16: Three steps
Decomposition
Organization
Assignment

## Slide 17: The Path Through FedEx
Truck
Sorting
Office
Airport
FE
Sorting
Office
Airport
Truck
Sorting
Office
Airport
Crate
Crate
FE
New
Crate
Crate
FE
Higher “Stack”
at Ends
Partial “Stack”
During Transit
Deepest Packaging (Envelope+FE+Crate)
at the Lowest Level of Transport

## Slide 18: The Path Through FedEx
Truck
Sorting
Office
Airport
FE
Sorting
Office
Airport
Truck
Sorting
Office
Airport
Crate
Crate
FE
New
Crate
Crate
FE
Deepest Packaging (Envelope+FE+Crate)
at the Lowest Level of Transport

## Slide 19
What gets implemented where?
Application
Transport
Network
Data link
Physical
L1
L2
L3
L4
L7
Application
Transport
Network
Data link
Physical
L1
L2
L3
L4
L7

## Slide 20: What gets implemented at the end systems?
Bits arrive on wire, must make it up to application
Therefore, all layers must exist at host!

## Slide 21: What gets implemented in the network?
Bits arrive on wire  physical layer (L1)
Packets must be delivered across links and local networks  datalink layer (L2)
Packets must be delivered between networks for global delivery  network layer (L3)
The network does not support reliable delivery
  Transport layer (and above) not supported

## Slide 22: Simple Diagram
Lower three layers implemented everywhere
Top two layers implemented only at hosts
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
End system
End system
Switch
Notes: Why go up? Why not stay down in the lower levels?

## Slide 23: A closer look: end-system
  Application
    Web server, browser, mail, game
  Transport and network layer
    typically part of the operating system
  Datalink and physical layer
    hardware/firmware/drivers

## Slide 24: A closer look: network
switch
link
Internet Service Provider

## Slide 25: A closer look: network
switch
link
Internet Service Provider
routers

## Slide 26: What gets implemented in the network?
Bits arrive on wire  physical layer (L1)
Packets must be delivered across links and local networks  datalink layer (L2)
Packets must be delivered between networks for global delivery  network layer (L3)
Hence:
  switches: implement physical and datalink layers (L1, L2)
  routers: implement physical, datalink, network layers (L1, L2, L3)

## Slide 27: Switches vs. Routers
Switches do what routers do but don’t participate in global delivery, just local delivery
  switches only need to support L1, L2
  routers support L1-L3
Won’t focus on the router/switch distinction
  when I say switch, I almost always mean router
  almost all boxes support network layer these days

## Slide 28: Logical Communication
Layers interacts with peer’s corresponding layer
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
Host A
Host B
Router

## Slide 29: Physical Communication
Communication goes down to physical network
Then up to relevant layer
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
Host A
Host B
Router

## Slide 30: A Protocol-Centric Diagram
HTTP
TCP
IP
Ethernet
interface
HTTP
TCP
IP
Ethernet
interface
IP
IP
Ethernet
interface
Ethernet
interface
SONET
interface
SONET
interface
host
host
router
router
HTTP message
TCP segment
IP packet
IP packet
IP packet

## Slide 31: Why layers?
Reduce complexity
Improve flexibility

## Slide 32: Why not?
sub-optimal performance
cross-layer information often useful
  several “layer violations” in practice

## Slide 33
What physical infrastructure is already available?
Reserve or on-demand?
Where’s my delay coming from?
To layer or not? What layers? Where?

## Slide 34: Implications of Hourglass
Single network-layer protocol (IP)
Allows arbitrary networks to interoperate
  Any network that supports IP can exchange packets
Decouples applications from low-level networking technologies
  Applications function on all networks
Supports simultaneous innovations above and below IP
But changing IP itself is hard (e.g., IPv4  IPv6)

## Slide 35: Placing Network Functionality
Hugely influential paper: “End-to-End Arguments in System Design” by Saltzer, Reed, and Clark (‘84)
  articulated the “End-to-End Principle” (E2E)
Endless debate over what it means
Everyone cites it as supporting their position
Notes: Contrary to wisdom of the day!
Talmud

## Slide 36: Basic Observation
Some application requirements can only be correctly implemented end-to-end
  reliability, security, etc.
Implementing these in the network is hard
  every step along the way must be fail proof
Hosts
  Can satisfy the requirement without network’s help
  Will/must do so, since they can’t rely on the network
Notes: Contrary to wisdom of the day!
Talmud

## Slide 37: Example: Reliable File Transfer
Solution 1: make each step reliable, and string them together to make reliable end-to-end process
Solution 2: end-to-end check and retry
OS
Appl.
OS
Appl.
Host A
Host B
OK

## Slide 38: Discussion
Solution 1 is incomplete
  What happens if any network element misbehaves?
  Receiver has to do the check anyway!
Solution 2 is complete
  Full functionality can be entirely implemented at application layer with no need for reliability from lower layers
Is there any need to implement reliability at lower layers?
Notes: Contrary to wisdom of the day!
Talmud

## Slide 39: Summary of End-to-End Principle
Implementing functionality (e.g., reliability) in the network
  Doesn’t reduce host implementation complexity
  Does increase network complexity
  Probably increases delay and overhead on all applications even if they don’t need the functionality (e.g. VoIP)
However, implementing in the network can improve performance in some cases
  e.g., consider a very lossy link
Notes: Contrary to wisdom of the day!
Talmud

## Slide 40: Recap
Layering is a good way to organize networks
Unified Internet layer decouples apps from networks
E2E argument encourages us to keep IP simple