## Slide 1: BGP
CS168, Fall 2014
Sylvia Ratnasamy
http://inst.eecs.berkeley.edu/~cs168/fa14/

## Slide 2: Announcement
Canceling my office hours this week (09/25)
Instead, additional office hours
  Monday (09/29): 1-2pm
  Tuesday (09/30): 1-2pm

## Slide 3
“Interior Routers”
“Autonomous System (AS)” or “Domain” Region of a network under a single administrative entity
“Border Routers”

## Slide 4: Topology and routes shaped by the business relationships between ASes
Three basic relationships between two ASes
  A is a customer of B
  A is a provider of B
  A and B are peers
Business implications
  customer pays provider
  peers don’t pay each other
Notes: Ehy???

## Slide 5: Routing Follows the Money!
traffic allowed
traffic not allowed
A
B
C
D
E
F
Q
Pr
Cu
Peer
Peer

## Slide 6: Interdomain Routing: Setup
Destinations are IP prefixes (12.0.0.0/8)
Nodes are Autonomous Systems (ASes)
  Internals of each AS are hidden
Links represent both physical links and business relationships
BGP (Border Gateway Protocol) is the Interdomain routing protocol
  Implemented by AS border routers

## Slide 7: BGP: Basic Idea
Each AS selects the “best” route it hears advertised for a prefix
An AS advertises its best routes to one or more IP prefixes
You’ve heard this story before!
Notes: Arrows are routing message

## Slide 8: BGP inspired by Distance Vector
Per-destination route advertisements
No global sharing of network topology information
Iterative and distributed convergence on paths
With four crucial differences!

## Slide 9: Differences between BGP and DV (1) not picking shortest path routes
BGP selects the best route based on policy, not shortest distance (least cost)
How do we avoid loops?
2
3
1
Node 2 may prefer “2, 3, 1” over “2, 1”

## Slide 10: Differences between BGP and DV (2) path-vector routing
Key idea: advertise the entire path
  Distance vector: send distance metric per destination
  Path vector: send the entire path for each destination
C
B
A
d
“d: path (B,A)”
“d: path (A)”
data traffic
data traffic

## Slide 11: Differences between BGP and DV (2) path-vector routing
Key idea: advertise the entire path
  Distance vector: send distance metric per destination
  Path vector: send the entire path for each destination
Benefits
  loop avoidance is easy

## Slide 12: Differences between BGP and DV (3) Selective route advertisement
For policy reasons, an AS may choose not to advertise a route to a destination
Hence, reachability is not guaranteed even if graph is connected
AS 2
AS 3
AS 1
Example: AS#2 does not want to carry traffic between AS#1 and AS#3

## Slide 13: Differences between BGP and DV (4) BGP may aggregate routes
For scalability, BGP may aggregate routes for different prefixes
AT&T a.0.0.0/8
LBL a.b.0.0/16
UCB a.c.0.0/16
a.*.*.* is this way
foo.com a.d.0.0/16
a.b.*.* is this way
a.c.*.* is this way
a.d.*.* is this way

## Slide 14: BGP: Outline
BGP policy
  typical policies, how they’re implemented
BGP protocol details
Issues with BGP

## Slide 15: Policy imposed in how routes are selected and exported
Selection: Which path to use?
  controls whether/how traffic leaves the network
Export: Which path to advertise?
  controls whether/how traffic enters the network
Can reach 128.3/16
blah blah
Route selection
A
P
C
B
Q
Route export
Notes: Arrows: routing messages!

## Slide 16: Typical Selection Policy
In decreasing order of priority
  make/save money (send to customer > peer > provider)
  maximize performance (smallest AS path length)
  minimize use of my network bandwidth (“hot potato”)
  …
  …

## Slide 17: Typical Export Policy
Destination prefix advertised by… | Export route to…
Customer | Everyone (providers, peers, other customers)
Peer | Customers
Provider | Customers
We’ll refer to these as the “Gao-Rexford” rules
(capture common -- but not required! -- practice!)

## Slide 18: Gao-Rexford
peers
providers
customers
With Gao-Rexford, the AS policy graph is a DAG (directed acyclic graph) and routes are “valley free”

## Slide 19: BGP: Today
BGP policy
  typical policies, how they’re implemented
BGP protocol details
  stay awake as long as you can…
BGP issues

## Slide 20: Who speaks BGP?
Border router
Internal router
Border routers at an Autonomous System
Notes: Say “There are four parts to internet routing” (don’t say in route selection)

## Slide 21: What does “speak BGP” mean?
Implement the BGP protocol standard
  read more here: http://tools.ietf.org/html/rfc4271
Specifies what messages to exchange with other BGP “speakers”
  message types (e.g., route advertisements, updates)
  message syntax
And how to process these messages
  e.g., “when you receive a BGP update, do…. “
  follows BGP state machine in the protocol spec + policy decisions, etc.

## Slide 22: BGP “sessions”
A border router speaks BGP with border routers in other ASes
“eBGP session”
Notes: Say “There are four parts to internet routing” (don’t say in route selection)

## Slide 23: BGP “sessions”
A border router speaks BGP with other (interior and border) routers in its own AS
“iBGP session”
Notes: Say “There are four parts to internet routing” (don’t say in route selection)

## Slide 24: eBGP, iBGP, IGP
eBGP: BGP sessions between border routers in different ASes
  Learn routes to external destinations
iBGP: BGP sessions between border routers and other routers within the same AS
  distribute externally learned routes internally
IGP: “Interior Gateway Protocol” = Intradomain routing protocol
  provide internal reachability
  e.g., OSPF, RIP

## Slide 25: Some Border Routers Don’t Need BGP
Customer that connects to a single upstream ISP
  The ISP can advertise prefixes into BGP on behalf of customer
  … and the customer can simply default-route to the ISP
Provider
Customer
Install default routes pointing to Provider
Install routes 130.132.0.0/16 pointing to Customer
130.132.0.0/16

## Slide 26: Putting the pieces together
Provide internal reachability (IGP)
Learn routes to external destinations (eBGP)
Distribute externally learned routes internally (iBGP)
Travel shortest path to egress (IGP)
6
2
4
9
2
1
3
3

## Slide 27: Basic Messages in BGP
Open
  Establishes BGP session
  BGP uses TCP [will make sense in 1-2weeks]
Notification
  Report unusual conditions
Update
  Inform neighbor of new routes
  Inform neighbor of old routes that become inactive
Keepalive
  Inform neighbor that connection is still viable

## Slide 28: Route Updates
Format <IP prefix: route attributes>
  attributes describe properties of the route
Two kinds of updates
  announcements: new routes or changes to existing routes
  withdrawal: remove routes that no longer exist

## Slide 29: Route Attributes
Routes are described using attributes
  Used in route selection/export decisions
Some attributes are local
  i.e., private within an AS, not included in announcements
Some attributes are propagated with eBGP route announcements
There are many standardized attributes in BGP
  We will discuss a few

## Slide 30: Attributes (1): ASPATH
Carried in route announcements
Vector that lists all the ASes a route advertisement has traversed (in reverse order)
AS 7018
AT&T
AS 12654
128.112.0.0/16
AS path = 7018 88
AS 88
Princeton, 128.112/16
IP prefix = 128.112.0.0/16
AS path = 88

## Slide 31: Attributes (2): LOCAL PREF
“Local Preference”
Used to choose between different AS paths
The higher the value the more preferred
Local to an AS; carried only in iBGP messages
AS4
AS2
AS3
AS1
140.20.1.0/24
BGP table at AS4:
Notes: Because communicated to all IBGP routers within AS, all routers have a common view of how to exit the AS.
This differs from MED in 2 ways: (1) the destination prefix can be anywhere in the internet, not just in the next AS (as in the case for MED). (2) the AS that sets Local_Pref, is also the one that uses it. This allows one node to tell everyone locally what the best way out is.
MED can’t be used in this example because there is exactly one connection between any pair of AS’s.

## Slide 32: Example: iBGP and LOCAL PREF
Both routers prefer the path through AS 2 on the left
I-BGP
AS 4
AS 3
Local Pref = 100
Local Pref = 90
AS 2
AS1

## Slide 33: Attributes (3) : MED
“Multi-Exit Discriminator”
Used when ASes are interconnected via 2 or more links to specify how close a prefix is to the link it is announced on
Lower is better
AS announcing prefix sets MED
AS receiving prefix (optionally!) uses MED to select link
Link B
Link A
MED=10
MED=50
AS1
AS2
AS3
destination prefix

## Slide 34: Attributes (4): IGP cost
Used for hot-potato routing
  Each router selects the closest egress point based on the path cost in intra-domain protocol
hot potato
A
B
C
D
G
E
F
4
5
3
9
3
4
10
8
8
A
B
dst

## Slide 35: IGP may conflict with MED
Dsf
A
B
MED=100
MED=500

## Slide 36: Typical Selection Policy
In decreasing order of priority
  make/save money (send to customer > peer > provider)
  maximize performance (smallest AS path length)
  minimize use of my network bandwidth (“hot potato”)
  …
  …

## Slide 37: Using Attributes
Rules for route selection in priority order
Priority | Rule | Remarks
1 | LOCAL PREF | Pick highest LOCAL PREF
2 | ASPATH | Pick shortest ASPATH length
3 | MED | Lowest MED preferred
4 | eBGP > iBGP | Did AS learn route via eBGP (preferred) or iBGP?
5 | iBGP path | Lowest IGP cost to next hop (egress router)
6 | Router ID | Smallest next-hop router’s IP address as tie-breaker

## Slide 38: BGP UPDATE Processing
Best Route
Selection
Apply Import
Policies
Best Route
Table
Apply Export
Policies
forwarding
Entries
BGP
Updates
BGP
Updates
IP Forwarding Table
Open ended programming.
Constrained only by vendor configuration language
Data plane
Control plane
Data packets
Data packets

## Slide 39: BGP: Today
BGP policy
  typical policies, how they’re implemented
BGP protocol details
BGP issues

## Slide 40: Issues with BGP
Reachability
Security
Convergence
Performance
Anomalies

## Slide 41: Reachability
In normal routing, if graph is connected then reachability is assured
With policy routing, this does not always hold
AS 2
AS 3
AS 1
Provider
Provider
Customer

## Slide 42: Security
An AS can claim to serve a prefix that they actually don’t have a route to (blackholing traffic)
  Problem not specific to policy or path vector
  Important because of AS autonomy
  Fixable: make ASes “prove” they have a path
Note: AS may forward packets along a route different from what is advertised
  Tell customers about fictitious short path…
  Much harder to fix!

## Slide 43: Convergence
Result: If all AS policies follow “Gao-Rexford” rules, BGP is guaranteed to converge (safety)
For arbitrary policies, BGP may fail to converge!

## Slide 44: Example of Policy Oscillation
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
“1” prefers “1 3 0”
over “1 0” to reach “0”

## Slide 45: Step-by-Step of Policy Oscillation
Initially: nodes 1, 2, 3 know only shortest path to 0
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0

## Slide 46
1 advertises its path 1 0 to 2
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
advertise: 1 0
Step-by-Step of Policy Oscillation

## Slide 47
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
Step-by-Step of Policy Oscillation

## Slide 48
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
advertise: 3 0
3 advertises its path 3 0 to 1
Step-by-Step of Policy Oscillation

## Slide 49
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
Step-by-Step of Policy Oscillation

## Slide 50
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
withdraw: 1 0
1 withdraws its path 1 0 from 2
Step-by-Step of Policy Oscillation

## Slide 51
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
Step-by-Step of Policy Oscillation

## Slide 52
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
advertise: 2 0
2 advertises its path 2 0 to 3
Step-by-Step of Policy Oscillation

## Slide 53
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
Step-by-Step of Policy Oscillation

## Slide 54
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
withdraw: 3 0
3 withdraws its path 3 0 from 1
Step-by-Step of Policy Oscillation

## Slide 55
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
Step-by-Step of Policy Oscillation

## Slide 56
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
1 advertises its path 1 0 to 2
Step-by-Step of Policy Oscillation
advertise: 1 0

## Slide 57
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
Step-by-Step of Policy Oscillation

## Slide 58
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
withdraw: 2 0
2 withdraws its path 2 0 from 3
Step-by-Step of Policy Oscillation

## Slide 59
1
2
3
1 3 0
1 0
3 2 0
3 0
2 1 0
2 0
0
We are back to where we started!
Step-by-Step of Policy Oscillation

## Slide 60: Convergence
Result: If all AS policies follow “Gao-Rexford” rules, BGP is guaranteed to converge (safety)
For arbitrary policies, BGP may fail to converge!
Why should this trouble us?

## Slide 61: Performance Nonissues
Internal routing (non)
  Domains typically use “hot potato” routing
  Not always optimal, but economically expedient
Policy not about performance (non)
  So policy-chosen paths aren’t shortest
AS path length can be misleading (non)
  20% of paths inflated by at least 5 router hops
Notes: Lesson: not being optimal: who cares
Not being connected: we all care!!

## Slide 62: Performance (example)
AS path length can be misleading
  An AS may have many router-level hops
AS 4
AS 3
AS 2
AS 1
BGP says that
path 4 1 is better
than path 3 2 1

## Slide 63: Real Performance Issue: Slow convergence
BGP outages are biggest source of Internet problems
Labovitz et al. SIGCOMM’97
    10% of routes available less than 95% of time
    Less than 35% of routes available 99.99% of the time
Labovitz et al. SIGCOMM 2000
    40% of path outages take 30+ minutes to repair
But most popular paths are very stable
Notes: Lesson: not being optimal: who cares
Not being connected: we all care!!

## Slide 64: BGP Misconfigurations
BGP protocol is both bloated and underspecified
  lots of attributes
  lots of leeway in how to set and interpret attributes
  necessary to allow autonomy, diverse policies
  but also gives operators plenty of rope
Much of this configuration is manual and ad hoc
And the core abstraction is fundamentally flawed
  disjoint per-router configuration to effect AS-wide policy
  now strong industry interest in changing this! [later: SDN]
Notes: Lesson: not being optimal: who cares
Not being connected: we all care!!

## Slide 65: BGP: How did we get here?
BGP was designed for a different time
  before commercial ISPs and their needs
  before address aggregation
  before multi-homing
We don’t get a second chance: `clean slate’ designs virtually impossible to deploy
Thought experiment: how would you design a policy-driven interdomain routing solution? How would you deploy it?
1989 : BGP-1 [RFC 1105]
  Replacement for EGP (1984, RFC 904)
1990 : BGP-2 [RFC 1163]
1991 : BGP-3 [RFC 1267]
1995 : BGP-4 [RFC 1771]
  Support for Classless Interdomain Routing (CIDR)
Notes: Lesson: not being optimal: who cares
Not being connected: we all care!!

## Slide 66: Next Time.
Wrap up the network layer!
  the IPv4 header
  IP routers