## Slide 1: The IP Data Plane
CS168, Fall 2014
Sylvia Ratnasamy
http://inst.eecs.berkeley.edu/~cs168/fa14/

## Slide 2: The IP layer
So far: focused mostly on routing protocols
  how routers discover and select end-to-end paths
  part of a network’s control plane
Today: the data plane
  what data packets look like at the IP layer
  how routers forward these IP packets

## Slide 3: Recall: Layer Encapsulation
transport
network
network
link
app
Alice
Bob
network
Router
Notes: Deepest level most header

## Slide 4: Recall: IP packet
IP packet contains a header and payload
  payload is opaque to the network
  header is what we care about
  first end-to-end layer (going bottom-up)
IP header
IP payload
IP packet

## Slide 5: Designing the IP header
Think of the IP header as an interface
  between the source and destination end-systems
  between the source and network (routers)
Designing an interface
  what task(s) are we trying to accomplish?
  what information is needed to do it?
Header reflects information needed for basic tasks

## Slide 6: What are these tasks? (in network)
Parse packet
Carry packet to the destination
Deal with problems along the way
  loops
  corruption
  packet too large
Accommodate evolution
Specify any special handling

## Slide 7: What information do we need?
Parse packet
Carry packet to the destination
Deal with problems along the way
  loops
  corruption
  packet too large
Accommodate evolution
Specify any special handling

## Slide 8: What information do we need?
Parse packet
  IP version number (4 bits), packet length (16 bits)
Carry packet to the destination
  Destination’s IP address (32 bits)
Deal with problems along the way
  loops:
  corruption:
  packet too large:

## Slide 9: What information do we need?
Parse packet
  IP version number (4 bits), packet length (16 bits)
Carry packet to the destination
  Destination’s IP address (32 bits)
Deal with problems along the way
  loops: TTL (8 bits)
  corruption: checksum (16 bits)
  packet too large: fragmentation fields (32 bits)

## Slide 10: Preventing Loops (TTL)
Forwarding loops cause packets to cycle for a looong time
  left unchecked would accumulate to consume all capacity
Time-to-Live (TTL) Field (8 bits)
  decremented at each hop, packet discarded if reaches 0
  …and “time exceeded” message is sent to the source

## Slide 11: Header Corruption (Checksum)
Checksum (16 bits)
  Particular form of checksum over packet header
If not correct, router discards packets
  So it doesn’t act on bogus information
Checksum recalculated at every router
  Why?
  Why only header?

## Slide 12: Fragmentation
Every link has a “Maximum Transmission Unit” (MTU)
  largest number of bits it can carry as one unit
A router can split a packet into multiple “fragments” if the packet size exceeds the link’s MTU
Must reassemble to recover original packet
Will return to fragmentation shortly…

## Slide 13: What information do we need?
Parse packet
  IP version number (4 bits), packet length (16 bits)
Carry packet to the destination
  Destination’s IP address (32 bits)
Deal with problems along the way
  TTL (8 bits), checksum (16 bits), fragmentation (32 bits)
Accommodate evolution
  version number (4 bits) (+ fields for special handling)
Specify any special handling

## Slide 14: Special handling
“Type of Service” (8 bits)
  allow packets to be treated differently based on needs
    e.g., indicate priority, congestion notification
  has been redefined several times
  now called “Differentiated Services Code Point (DSCP)”

## Slide 15: Options
Optional directives to the network
  not used very often
  16 bits of metadata + option-specific data
Examples of options
  Record Route
  Strict Source Route
  Loose Source Route
  Timestamp
  …..

## Slide 16: What information do we need?
Parse packet
  IP version number (4 bits), packet length (16 bits)
Carry packet to the destination
  Destination’s IP address (32 bits)
Deal with problems along the way
  TTL (8 bits), checksum (16 bits), fragmentation (32 bits)
Accommodate evolution
  version number (4 bits) (+ fields for special handling)
Specify any special handling
  ToS (8 bits), Options (variable length)

## Slide 17: IP Packet Structure
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload
32 bits

## Slide 18: Parse packet
Header length (4 bits)
  Number of 32-bit words in the header
  Typically “5” (for a 20-byte IPv4 header)
  Can be more when IP options are used

## Slide 19: IP Packet Structure
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload
For fragmentation
32 bits

## Slide 20: What are these tasks? (at the destination end-system)
Tell destination what to do with the received packet
Get responses to the packet back to the source

## Slide 21: Telling End-Host How to Handle Packet
Protocol (8 bits)
  Identifies the higher-level protocol
  Important for de-multiplexing at receiving host
Application
Transport
Network
Data link
Physical
SMTP
HTTP
DNS
NTP
TCP
UDP
IP
Ethernet
FDDI
PPP
optical
copper
radio
PSTN

## Slide 22: Telling End-Host How to Handle Packet
Protocol (8 bits)
  Identifies the higher-level protocol
  Important for de-multiplexing at receiving host
Most common examples
  E.g., “6” for the Transmission Control Protocol (TCP)
  E.g., “17” for the User Datagram Protocol (UDP)
IP header
IP header
TCP header
UDP header
protocol=6
protocol=17

## Slide 23: What are these tasks? (at the destination end-system)
Tell destination what to do with the received packet
  Transport layer protocol (8 bits)
Get responses to the packet back to the source
  Source IP address (32 bits)

## Slide 24: IP Packet Structure
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload
32 bits

## Slide 25: A closer look at fragmentation
Every link has a “Maximum Transmission Unit” (MTU)
  largest number of bits it can carry as one unit
A router can split a packet into multiple “fragments” if the packet size exceeds the link’s MTU
Must reassemble to recover original packet

## Slide 26: Example of fragmentation
A 4000 byte packet crosses a link w/ MTU=1500B
4000B
1500B
…

## Slide 27: Example of fragmentation
20
4000
3980
20
1480
1500
20
1200
1220
20
1300
1320
A 4000 byte packet crosses a link w/ MTU=1500B
IP header

## Slide 28: DIY exercise in header engineering
Take 5 minutes to design fragmentation scheme
  Work with your neighbors
At the end of 5 minutes, be ready to tell me:
  How many fields you need?
  What are they and why?
Don’t look for the answer elsewhere, the goal is to think about the problem!

## Slide 29: Why reassemble?
20
4000
3980
20
1480
1500
20
1200
1220
20
1300
1320
IP header
20
TCP
TCP
TCP
HTTP
HTTP
HTTP
Must reassemble before sending the packet to the higher layers!

## Slide 30: A few considerations
Where to reassemble?
Fragments can get lost
Fragments can follow different paths
Fragments can get fragmented again

## Slide 31: Where should reassembly occur?
Classic case of E2E principle
At next-hop router imposes burden on network
  complicated reassembly algorithm
  must hold onto fragments/state
Any other router may not work
  Fragments may take different paths
Little benefit, large cost for network reassembly
Hence, reassembly is done at the destination

## Slide 32: Reassembly: what fields?
Need a way to identify fragments of the packet
 introduce an identifier
Fragments get lost?
   need some form of sequence number or offset?
Sequence numbers / offset
  How do I know when I have them all? (need max seq# / flag)
  What if a fragment gets re-fragmented?

## Slide 33: IPv4’s fragmentation fields
Identifier: which fragments belong together
Flags:
  Reserved: ignore
  DF: don’t fragment
    may trigger error message back to sender
  MF: more fragments coming
Offset: portion of original payload this fragment contains
  in 8-byte units

## Slide 34: IP Packet Structure
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload
32 bits

## Slide 35: Why This Works
Fragment without MF set (last fragment)
  Tells host which are the last bits in original payload
All other fragments fill in holes
Can tell when holes are filled, regardless of order
  Use offset field
Q: why use a byte-offset for fragments rather than numbering each fragment?
  Allows further fragmentation of fragments

## Slide 36: Example of fragmentation (contd.)
20
4000
3980
20
1480
1500
20
1200
1220
20
1300
1320
Packet split into 3 pieces
Example:

## Slide 37: Example of fragmentation, contd.
4000 byte packet from host 1.2.3.4 to 3.4.5.6 …
… traverses a link with MTU 1,500 bytes
Version
4
Header
Length
5
Type of Service
0
Total Length: 4000
Identification: 56273
R/D/M
0/0/0
Fragment Offset: 0
TTL
127
Protocol
6
Checksum: 44019
Source Address: 1.2.3.4
Destination Address: 3.4.5.6
(3980 more bytes of payload here)

## Slide 38: Example of fragmentation, contd.
Datagram split into 3 pieces. Possible first piece:
Version
4
Header
Length
5
Type of Service
0
Total Length: 1500
Identification: 56273
R/D/M
0/0/1
Fragment Offset: 0
TTL
127
Protocol
6
Checksum: xxx
Source Address: 1.2.3.4
Destination Address: 3.4.5.6

## Slide 39: Example of fragmentation, contd.
Possible second piece: Frag#1 covered 1480bytes
Version
4
Header
Length
5
Type of Service
0
Total Length: 1220
Identification: 56273
R/D/M
0/0/1
Fragment Offset: 185
(185 * 8 = 1480)
TTL
127
Protocol
6
Checksum: yyy
Source Address: 1.2.3.4
Destination Address: 3.4.5.6

## Slide 40: Example of fragmentation, contd.
Possible third piece: 1480+1200 = 2680
Version
4
Header
Length
5
Type of Service
0
Total Length: 1320
Identification: 56273
R/D/M
0/0/0
Fragment Offset: 335
(335 * 8 = 2680)
TTL
127
Protocol
6
Checksum: zzz
Source Address: 1.2.3.4
Destination Address: 3.4.5.6

## Slide 41: IP Packet Structure
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 42: Quick Security Analysis of IP Header

## Slide 43: Focus on Sender Attacks
  Vulnerabilities sender can exploit
Ignore (for now) attacks by others:
  Traffic analysis
  Snooping payload
  Denial of service

## Slide 44: IP Packet Structure
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 45: IP Address Integrity
Source address should be the sending host
  But, who’s checking?
  You could send packets with any source you want
  Why is checking hard?
Notes: No notion of identity that has any cryptographic binding to address (or any kind of binding that is visible to network).

## Slide 46: Implications of IP Address Integrity
Why would someone use a bogus source address?
Launch a denial-of-service attack
  Send excessive packets to the destination
  … to overload the node, or the links leading to the node
  But: victim can identify/filter you by the source address
Evade detection by “spoofing”
  Put someone else’s source address in the packets
    Or: use many different ones so can’t be filtered
Or: as a way to bother the spoofed host
  Spoofed host is wrongly blamed
  Spoofed host may receive return traffic from the receiver

## Slide 47: More Security Implications
IP options
  Misuse: e.g., Source Route lets sender control path taken through network - say, sidestep security monitoring
  IP options often processed in router’s slow path  attacker can try to overload routers
  Firewalls often configured to drop packets with options.

## Slide 48: Security Implications of TOS? (8 bits)
Attacker sets TOS priority for their traffic?
  If regular traffic does not set TOS, then network prefers the attack traffic, greatly increasing damage
What if network charges for TOS traffic …
  … and attacker spoofs the victim’s source address?
Today, network TOS generally does not work
  TOS now redefined for differentiated service
  Mostly set/used by network operators, not end-systems

## Slide 49: Security Implications of Fragmentation?
Allows evasion of network monitoring/enforcement
E.g., split an attack across multiple fragments
  Packet inspection won’t match a “signature”
Monitor must remember previous fragments
  But that costs state, which is another vector of attack
Nasty-at
Offset=0
tack-bytes
Offset=8

## Slide 50: More Fragmentation Attacks
What if 2 overlapping fragments are inconsistent?
How does network monitor know whether receiver sees USERNAME NICE or USERNAME EVIL?
USERNAME
Offset=0
NICE
Offset=8
EVIL
Offset=8

## Slide 51: Even More Fragmentation Attacks
What happens if attacker doesn’t send all of the fragments in a packet?
Receiver (or firewall) winds up holding the ones they receive for a long time
  State-holding attack

## Slide 52: Security Implications of TTL? (8 bits)
Allows discovery of topology (a la traceroute)
Can provide a hint that a packet is spoofed
  It arrives at a router w/ a TTL different than packets from that address usually have
    Because path from attacker to router has different # hops
  Though this is brittle in the presence of routing changes
Initial value is somewhat distinctive to sender’s operating system. This plus other such initializations allow OS fingerprinting …
  Which allow attacker to infer its likely vulnerabilities

## Slide 53: Other Security Implications?
No apparent problems with protocol field (8 bits)
  It’s just a de-muxing handle
  If set incorrectly, next layer will find packet ill-formed
Bad IP checksum field (16 bits) will cause packet to be discarded by the network
  Not an effective attack…

## Slide 54: Let’s take a quick look at the IPv6 header…

## Slide 55: IPv6
Motivated (prematurely) by address exhaustion
  Addresses four times as big
Steve Deering focused on simplifying IP
  got rid of all fields that were not absolutely necessary
  “spring cleaning” for IP
Result is an elegant, if unambitious, protocol

## Slide 56: What “clean up” would you do?
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 57: Summary of Changes
Eliminated fragmentation (why?)
Eliminated checksum (why?)
New options mechanism (next header) (why?)
Eliminated header length (why?)
Expanded addresses
Added Flow Label

## Slide 58: IPv4 and IPv6 Header Comparison
Version | IHL | Type of Service | Total Length |  | 
Identification |  |  | Flags | Fragment Offset | 
Time to Live |  | Protocol | Header Checksum |  | 
Source Address |  |  |  |  | 
Destination Address |  |  |  |  | 
Options |  |  |  |  | Padding
Version | Traffic Class | Flow Label |  | 
Payload Length |  |  | Next Header | Hop Limit
Source Address |  |  |  | 
Destination Address |  |  |  | 
IPv4
IPv6
Field name kept from IPv4 to IPv6
Fields not kept in IPv6
Name & position changed in IPv6
New field in IPv6

## Slide 59: Philosophy of Changes
Don’t deal with problems: leave to ends
  Eliminated fragmentation
  Eliminated checksum
  Why retain TTL?
Simplify handling:
  New options mechanism (uses next header approach)
  Eliminated header length
    Why couldn’t IPv4 do this?
Provide general flow label for packet
  Not tied to semantics
  Provides great flexibility

## Slide 60: IP header design
More nuanced than it first seems!
Must juggle multiple goals
  Robustness
  Efficiency
  Security
  Completeness
Plus feature interactions
  E.g., what happens to IP options when we fragment?
And future evolution