## Slide 1: IP Routers
CS 168, Fall 2014
Kay Ousterhout (standing in for Sylvia Ratnasamy)
http://inst.eecs.berkeley.edu/~cs168/
Material thanks to Ion Stoica, Scott Shenker, Jennifer Rexford, Nick McKeown, and many other colleagues

## Slide 2: Context
Control plane
  How to route traffic to each possible destination
  Jointly computed using BGP
Data plane
  Necessary fields in IP header of each packet
Today: How IP routers forward packets
  Focus on data plane
Today (maybe): Transport layer
Notes: Routing protocols: last week, this week in section
IP packets: discussed what’s needed in the header to get packets across the network (simple: address, slightly more nuanced: TTL to avoid loops)

## Slide 3: IP Routers
Core building block of the Internet infrastructure
$120B+ industry
Vendors: Cisco, Huawei, Juniper, Alcatel-Lucent (account for >90%)

## Slide 4: Lecture #4: Routers Forward Packets
to MIT
to UW
UCB
to NYU
Destination | Next Hop
UCB | 4
UW | 5
MIT | 2
NYU | 3
Forwarding Table
111010010
MIT
switch#2
switch#5
switch#3
switch#4
Notes: Recall from lecture 4: job of router is to forward packet. See packet header with destination address, determine what link to send that packet on next

## Slide 5: Router definitions
1
2
3
4
5
…
N-1
N
N = number of external router “ports”
R = speed (“line rate”) of a port
Router capacity = N x R
R bits/sec

## Slide 6: Networks and routers
AT&T
BBN
NYU
UCB
core
core
edge (ISP)
edge (enterprise)
home, small business
Notes: Bunch of different kinds of routers: small for homes, routers that connect different ISPs or ISPs to enterprises (edge)

## Slide 7: Examples of routers (core)
72 racks, >1MW
Cisco CRS
  R=10/40/100 Gbps
  NR = 922 Tbps
  Netflix: 0.7GB per hour (1.5Mb/s)
  ~600 million concurrent Netflix users

## Slide 8: Examples of routers (edge)
Cisco ASR
  R=1/10/40 Gbps
  NR = 120 Gbps

## Slide 9: Examples of routers (small business)
Cisco 3945E
  R = 10/100/1000 Mbps
  NR < 10 Gbps

## Slide 10: What’s inside a router?
1
2
N
1
2
N
Linecards (input)
Interconnect (Switching)
Fabric
Route/Control Processor
Linecards (output)
Processes packets on their way in
Processes packets before they leave
Transfers packets from input to output ports
Input and Output for the same port are on one physical linecard

## Slide 11: What’s inside a router?
1
2
N
1
2
N
Linecards (input)
Interconnect (Switching)
Fabric
Route/Control Processor
Linecards (output)
(1) Implement IGP and BGP protocols; compute routing tables
(2) Push forwarding tables to the line cards

## Slide 12: What’s inside a router?
1
2
N
1
2
N
Linecards (input)
Interconnect Fabric
Route/Control Processor
Linecards (output)
Constitutes the data plane
Constitutes the control plane
Notes: Control plane: software. Makes decisions over long time horizons.
Data plane: mostly hardware. A decision for each packet.

## Slide 13: Input Linecards
Tasks
  Receive incoming packets (physical layer stuff)
  Update the IP header
Version
Header
Length
Type of Service
(TOS)
Total Length (Bytes)
16-bit Identification
Flags
Fragment Offset
Time to
Live (TTL)
Protocol
Header Checksum
Source IP Address
Destination IP Address
Options (if any)
Payload
Notes: Receiving incoming packets: signal on a wire to bits
What are the header fields that need to be updated?

## Slide 14: Input Linecards
Tasks
  Receive incoming packets (physical layer stuff)
  Update the IP header
    TTL, Checksum, Options (maybe), Fragment (maybe)
  Lookup the output port for the destination IP address
  Queue the packet at the switch fabric
Challenge: speed!
  100B packets @ 40Gbps  new packet every 20 nano secs!
Typically implemented with specialized hardware
  ASICs, specialized “network processors”
  “exception” processing often done at control processor
Notes: Next: one particular part of the functionality: how to determine the output port for the destination IP address

## Slide 15: Looking up the output port
One entry for each address  4 billion entries!
For scalability, addresses are aggregated
Notes: How does a router determine which output port for the packet!

## Slide 16
AT&T a.0.0.0/8
France Telecom
LBL a.b.0.0/16
UCB a.c.0.0/16
a.c.*.* is this way
a.b.*.* is this way
Notes: Example from lecture 6. Remember / notation: needs to match first 8 bits

## Slide 17
AT&T a.0.0.0/8
France Telecom
LBL a.b.0.0/16
UCB a.c.0.0/16
a.*.*.* is this way
Notes: Example from lecture 6: two customers of AT&T can be aggregated; do not need to be individually advertised.

## Slide 18: But aggregation is imperfect…
AT&T a.0.0.0/8
France Telecom
LBL a.b.0.0/16
UCB a.c.0.0/16
a.*.*.* is this way
ESNet
a.*.*.* is this way
BUT a.c.*.* is this way
ESNet must maintain routing entries for both a.*.*.* and a.c.*.*
Notes: Now there’s this exception: a.c.*.* is different

## Slide 19: Find the longest prefix that matches
AT&T a.0.0.0/8
France Telecom
LBL a.b.0.0/16
UCB a.c.0.0/16
a.*.*.* is this way
ESNet
a.*.*.* is this way
BUT a.c.*.* is this way
Destination | Next Hop
a.*.*.* | at&t
a.c.*.* | ucb
… | …
ESNet’s Forwarding Table
Notes: Now there’s this exception: a.c.*.* is different

## Slide 20: Longest Prefix Match Lookup
Packet with destination address 12.82.100.101 is sent to interface 2, as 12.82.100.xxx is the longest prefix matching packet’s destination address
1
2
128.16.120.111
12.82.100.101
…
…
3
12.82.xxx.xxx
1
128.16.120.xxx
12.82.100.xxx
2

## Slide 21: Example #1: 4 Prefixes, 4 Ports
Prefix | Port
201.143.0.0/22 | Port 1
201.143.4.0.0/24 | Port 2
201.143.5.0.0/24 | Port 3
201.143.6.0/23 | Port 4
201.143.0.0/22
201.143.4.0/24
201.143.5.0/24
201.143.6.0/23
ISP Router
Port 1
Port 2
Port 3
Port 4

## Slide 22: Finding a match
Incoming packet destination: 201.143.7.0
Prefix | Port
201.143.0.0/22 | Port 1
201.143.4.0.0/24 | Port 2
201.143.5.0.0/24 | Port 3
201.143.6.0/23 | Port 4

## Slide 23: Finding a match: convert to binary
Incoming packet destination: 201.143.7.210
11001001
10001111
00000111
11010010
11001001
10001111
000000−−
−−−−−−−
11001001
10001111
00000100
−−−−−−−
11001001
10001111
00000101
−−−−−−−
11001001
10001111
0000011−
−−−−−−−
201.143.0.0/22
201.143.4.0/24
201.143.5.0/24
201.143.6.0/23
Routing table

## Slide 24: Finding a match: convert to binary
Incoming packet destination: 201.143.7.210
11001001
10001111
00000111
11010010
11001001
10001111
000000−−
−−−−−−−
11001001
10001111
00000100
−−−−−−−
11001001
10001111
00000101
−−−−−−−
11001001
10001111
0000011−
−−−−−−−
201.143.0.0/22
201.143.4.0/24
201.143.5.0/24
201.143.6.0/23
Routing table

## Slide 25: Finding a match: convert to binary
Incoming packet destination: 201.143.7.210
11001001
10001111
00000111
11010010
11001001
10001111
000000−−
−−−−−−−
11001001
10001111
00000100
−−−−−−−
11001001
10001111
00000101
−−−−−−−
11001001
10001111
0000011−
−−−−−−−
201.143.0.0/22
201.143.4.0/24
201.143.5.0/24
201.143.6.0/23
Routing table

## Slide 26: Finding a match: convert to binary
Incoming packet destination: 201.143.7.210
11001001
10001111
00000111
11010010
11001001
10001111
000000−−
−−−−−−−
11001001
10001111
00000100
−−−−−−−
11001001
10001111
00000101
−−−−−−−
11001001
10001111
0000011−
−−−−−−−
201.143.0.0/22
201.143.4.0/24
201.143.5.0/24
201.143.6.0/23
Routing table

## Slide 27: Longest prefix matching
Incoming packet destination: 201.143.7.210
11001001
10001111
00000111
11010010
11001001
10001111
000000−−
−−−−−−−
11001001
10001111
00000100
−−−−−−−
11001001
10001111
00000111
0−−−−−−
11001001
10001111
0000011−
−−−−−−−
201.143.0.0/22
201.143.4.0/24
201.143.7.0/25
201.143.6.0/23
Routing table
NOT Check an address against all destination prefixes and select the prefix it matches with on the most bits

## Slide 28: Finding Match Efficiently
Testing each entry to find a match scales poorly
  On average: O(number of entries)
Leverage tree structure of binary strings
  Set up tree-like data structure
Return to example:
Prefix | Port
1100100110001111000000********** | 1
110010011000111100000100******** | 2
110010011000111100000101******** | 3
11001001100011110000011********* | 4
Prefix | Port
1100100110001111000000********** | 1
110010011000111100000100******** | 2
110010011000111100000101******** | 3
11001001100011110000011********* | 4

## Slide 29: Consider four three-bit prefixes
Just focusing on the bits where all the action is….
0**  Port 1
100  Port 2
101  Port 3
11*  Port 4

## Slide 30: Tree Structure
00*
000
001
0
1
01*
010
011
0
1
11*
110
111
0
1
10*
100
101
0
1
0**
0
1
1**
0
1
***
0
1
0**  Port 1
100  Port 2
101  Port 3
11*  Port 4
Notes: Idea: build tree to help with match. When a new packet comes in, walk the tree to determine the correct port.
Each level in the tree: one bit. Root: all wild cards

## Slide 31: Walk Tree: Stop at Prefix Entries
00*
000
001
0
1
01*
010
011
0
1
11*
110
111
0
1
10*
100
101
0
1
0**
0
1
1**
0
1
***
0
1
0**  Port 1
100  Port 2
101  Port 3
11*  Port 4
Notes: Many more advanced techniques for this….

## Slide 32: Walk Tree: Stop at Prefix Entries
00*
000
001
0
1
01*
010
011
0
1
11*
110
111
0
1
10*
100
101
0
1
0**
0
1
1**
0
1
***
0
1
P1
P2
P3
P4
0**  Port 1
100  Port 2
101  Port 3
11*  Port 4
Notes: Many more advanced techniques for this….

## Slide 33: Slightly Different Example
Several of the unique prefixes go to same port
0**  Port 1
100  Port 2
101  Port 1
11*  Port 1

## Slide 34: Prefix Tree
00*
000
001
0
1
01*
010
011
0
1
11*
110
111
0
1
10*
100
101
0
1
0**
0
1
1**
0
1
***
0
1
P1
P2
P1
P1
0**  Port 1
100  Port 2
101  Port 1
11*  Port 1
Notes: In this simple example, we can simplify the tree: most entries go to a single port.

## Slide 35: More Compact Representation
00*
000
001
0
1
01*
010
011
0
1
11*
110
111
0
1
10*
100
101
0
1
0**
0
1
1**
0
1
***
0
1
P1
P2
P1
P1
Notes: In this simple example, we can simplify the tree: most entries go to a single port.

## Slide 36: More Compact Representation
10*
100
0
1**
0
***
1
P2
P1
Record port associated with latest match, and only over-ride when it matches another prefix during walk down tree
If you ever leave path, you are done, last matched prefix is answer
Notes: Many more advanced techniques for this….

## Slide 37: LPM in real routers
Real routers use far more advanced/complex solutions than the approaches I just described
  but what we discussed is their starting point
With many heuristics and optimizations that leverage real-world patterns
  Some destinations more popular than others
  Some ports lead to more destinations
  Typical prefix granularities

## Slide 38: Recap: Input linecards
Main challenge is processing speeds
Tasks involved:
  Update packet header (easy)
  LPM lookup on destination address (harder)
Mostly implemented with specialized hardware

## Slide 39: Output Linecard
Packet classification: map each packet to a “flow”
  Flow (for now): set of packets between two particular endpoints
Buffer management: decide when and which packet to drop
Scheduler: decide when and which packet to transmit
1
2
Scheduler
flow 1
flow 2
flow n
Classifier
Buffer management

## Slide 40: Output Linecard
Packet classification: map each packet to a “flow”
  Flow (for now): set of packets between two particular endpoints
Buffer management: decide when and which packet to drop
Scheduler: decide when and which packet to transmit
Used to implement various forms of policy
  Deny all e-mail traffic from ISP-X to Y (access control)
  Route IP telephony traffic from X to Y via PHY_CIRCUIT (policy)
  Ensure that no more than 50 Mbps are injected from ISP-X (QoS)

## Slide 41: Simplest: FIFO Router
No classification
Drop-tail buffer management: when buffer is full drop the incoming packet
First-In-First-Out (FIFO) Scheduling: schedule packets in the same order they arrive
1
2
Scheduler
Buffer

## Slide 42: Packet Classification
Classify an IP packet based on a number of fields in the packet header, e.g.,
  source/destination IP address (32 bits)
  source/destination TCP port number (16 bits)
  Type of service (TOS) byte (8 bits)
  Type of protocol (8 bits)
In general fields are specified by range
  classification requires a multi-dimensional range search!
1
2
Scheduler
flow 1
flow 2
flow n
Classifier
Buffer management

## Slide 43: Scheduler
One queue per “flow”
Scheduler decides when and from which queue to send a packet
Goals of a scheduling algorithm:
  Fast!
  Depends on the policy being implemented (fairness, priority, etc.)
1
2
Scheduler
flow 1
flow 2
flow n
Classifier
Buffer management

## Slide 44: Example: Priority Scheduler
Priority
Scheduler
Priority scheduler: packets in the highest priority queue are always served before the packets in lower priority queues
High priority
Medium priority
Low priority

## Slide 45: Example: Round Robin Scheduler
Round robin: packets are served from each queue in turn
Fair Scheduler
High priority
Medium priority
Low priority

## Slide 46: Connecting input to output: Switch fabric
1
2
N
1
2
N
Linecards (input)
Interconnect Fabric
Route/Control Processor
Linecards (output)

## Slide 47: Today’s Switch Fabrics: Mini-Network!
1
2
N
1
2
N
Linecards (input)
Route/Control Processor
Linecards (output)

## Slide 48: Point-to-Point Switch (3rd Generation)
Line
Card
MAC
Local
Buffer
Memory
CPU
Card
Line
Card
MAC
Local
Buffer
Memory
Switched Backplane
Line Interface
CPU
Memory
Fwding
Table
Routing
Table
Fwding
Table
(*Slide by Nick McKeown)

## Slide 49: What’s hard about the switch fabric?
to MIT
to UW
UCB
to NYU
111010010
MIT
switch#2
switch#5
switch#3
switch#4
Queuing!
111010010
MIT
?
Notes: Possible that two packets arrive at the same time, for the same destination. Which one gets sent first?

## Slide 50: Queuing
1
2
N
1
2
N
Linecards (input)
Route/Control Processor
Linecards (output)
1
1

## Slide 51: Output queuing
1
2
N
1
2
N
Linecards (input)
Route/Control Processor
Linecards (output)
1
1

## Slide 52: Output queuing
1
2
N
1
2
N
Linecards (input)
Route/Control Processor
Linecards (output)
1
1

## Slide 53: Input queuing
1
2
N
1
2
N
Linecards (input)
Route/Control Processor
Linecards (output)
1
1

## Slide 54: Input Queuing: Challenges
1
2
N
1
2
N
Linecards (input)
Route/Control Processor
Linecards (output)
1
1
Fabric Scheduler
(1) Need a (FAST) internal fabric scheduler!
Notes: Fabric scheduler needed to decide which packets go first

## Slide 55: Challenge 2: Head of line blocking
1
2
N
1
2
N
Linecards (input)
Route/Control Processor
Linecards (output)
1
1
Head of line blocking
2
Fabric Scheduler
Limits throughput to approximately 58% of capacity

## Slide 56: Fixing head of line blocking: Virtual Output Queues
1
2
N
Linecards (input)
1
1
2
N
2
1
N
N
1
2
N
Linecards (output)

## Slide 57: Shared Memory (1st Generation)
Route
Table
CPU
Buffer
Memory
Line
Interface
MAC
Line
Interface
MAC
Line
Interface
MAC
Limited by rate of shared memory
Shared Backplane
Line card
CPU
Memory
(* Slide by Nick McKeown, Stanford Univ.)

## Slide 58: Shared Bus (2nd Generation)
Route
Table
CPU
Line
Card
Buffer
Memory
Line
Card
MAC
Buffer
Memory
Line
Card
MAC
Buffer
Memory
Fwding
Cache
Fwding
Cache
Fwding
Cache
MAC
Buffer
Memory
Limited by shared bus
(* Slide by Nick McKeown)

## Slide 59: 3rd Gen. Router: Switched Interconnects
NxR
This is called an “output queued” switch

## Slide 60
Fabric Scheduler
3rd Gen. Router: Switched Interconnects
This is called an “input queued” switch

## Slide 61
1 x R
Fabric Scheduler
3rd Gen. Router: Switched Interconnects

## Slide 62: Reality is more complicated
Commercial (high-speed) routers use
  combination of input and output queuing
  complex multi-stage switching topologies (Clos, Benes)
  distributed, multi-stage schedulers (for scalability)
We’ll consider one simpler context
  de-facto architecture for a long time and still used in lower-speed routers

## Slide 63: Context
Crossbar fabric
Centralized scheduler
Input ports
Output ports

## Slide 64: Scheduling
Goal: run links at full capacity, fairness across inputs
Scheduling formulated as finding a matching on a bipartite graph
Practical solutions look for a good maximal matching (fast)
Input ports
Output ports

## Slide 65: IP Routers Recap
Core building block of Internet
Scalable addressing  Longest Prefix Matching
Need fast implementations for:
  Longest prefix matching
  Switch fabric scheduling

## Slide 66: Transport Layer
Layer at end-hosts, between the application and network layer
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
Host A
Host B
Router

## Slide 67: Why do we need a transport layer?

## Slide 68: Why a transport layer?
Demultiplex packets between many applications
Additional services on top of IP

## Slide 69: Why a transport layer: Demultiplexing
IP packets are addressed to a host but end-to-end communication is between application processes at hosts
  Need a way to decide which packets go to which applications (multiplexing/demultiplexing)

## Slide 70: Why a transport layer: Demultiplexing
Transport
Network
Datalink
Physical
Application
Host A
Host B
Datalink
Physical
browser
telnet
mmedia
ftp
browser
IP
many application processes
Drivers +NIC
Operating System

## Slide 71: Why a transport layer: Demultiplexing
Host A
Host B
Datalink
Physical
browser
telnet
mmedia
ftp
browser
IP
many application processes
Datalink
Physical
telnet
ftp
IP
HTTP server
Transport
Transport
Communication between hosts
(128.4.5.6 162.99.7.56)
Communication between processes
at hosts

## Slide 72: Why a transport layer: Improved service model
IP provides a weak service model (best-effort)
  Packets can be corrupted, delayed, dropped, reordered, duplicated
  No guidance on how much traffic to send and when
  Dealing with this is tedious for application developers

## Slide 73: Role of the Transport Layer
Communication between application processes
  Mux and demux from/to application processes
  Implemented using ports

## Slide 74: Role of the Transport Layer
Communication between application processes
Provide common end-to-end services for app layer [optional]
  Reliable, in-order data delivery
  Well-paced data delivery
    too fast may overwhelm the network
    too slow is not efficient

## Slide 75: Role of the Transport Layer
Communication between processes
Provide common end-to-end services for app layer [optional]
TCP and UDP are the common transport protocols
  also SCTP, MTCP, SST, RDP, DCCP, …

## Slide 76: Role of the Transport Layer
Communication between processes
Provide common end-to-end services for app layer [optional]
TCP and UDP are the common transport protocols
UDP is a minimalist, no-frills transport protocol
  only provides mux/demux capabilities

## Slide 77: Role of the Transport Layer
Communication between processes
Provide common end-to-end services for app layer [optional]
TCP and UDP are the common transport protocols
UDP is a minimalist, no-frills transport protocol
TCP is the whole-hog protocol
  offers apps a reliable, in-order, bytestream abstraction
  with congestion control
  but no performance guarantees (delay, bw, etc.)

## Slide 78: Summary
IP Routers
  $$$
  Line cards receive packets, change headers
  LPM for scalable addressing
  Fast hardware needed for LPM, fabric scheduling
Transport Layer
  Demultiplexes between applications on same host
  2 protocols:
    UDP: minimal protocol
    TCP: reliable, in order byte stream (more next week!)