University of California at Berkeley

College of Engineering

Department of Electrical Engineering and Computer Science

EECS 150									R. H. Katz

Fall 2000

Problem Set # 8/9 (Assigned 2 November, Due 17 November)

- Recall the sequence detector FSM described in lecture: the machine outputs a 1 whenever the input sequence …010… has been detected, as long as the string 100 has not been encountered. Implement this state machine with a trickier datapath: a shift register for the state register and a comparator to detect the critical sequences.

- Design a datapath down to the block diagram level of its functional units to support this state machine. Define your register transfer operations, control signals, bus architecture, and timing behavior.

EQ

EQ

One input bit per clk cycle and a shift each clk cycle.

- Design the state machine that implements the behavior of the specification above in terms of how it orchestrates the execution of the datapath you designed in part (a).

- Design an Arithmetic Logic Unit to the following specification. The ALU has 4 control inputs: M, S2, S1, S0, a carry-in and carry-out, and bit slice data inputs Ai and Bi (for each bit of the ALU).  When M=1, the ALU is in arithmetic mode and when M=0, it is in logic mode. Develop a gate level implementation for a single bit of the ALU.

# Text boxes

Logic

S0

S1

S2

S[2:0]

010

MUX

Bi

CLK

Stop

Comparator

Comparator

Output

Stop

100

S[2:0]

1

Bi

Bi

Shift Register

S[2:0]

CLK

CLK

IN

Input

1 || 0

100

010

10

01

[0]

[0]

1

1

1

1

0

0

0

0

[1]

[0]

[0]

0

0

[0]

1

1

0

1

Start

Bi

Bi

Ai

Ai

Ai

Ai

Ai

0

MUX

Arith

S0

S1

Co

1

1

Ai

Co

Ci

Bi

Ai

Co

Ci

1

Ai

Co

1

Bi’

Ai

F

M

Logic

Arith