University of California at Berkeley

College of Engineering

Department of Electrical Engineering and Computer Science

EECS 150									R. H. Katz

Fall 2000

Solutions Set # 2

- Simplify the following expressions using the laws and theorems of Boolean Algebra:

- S(A,B,C) = A’ B’ C + A’ B C’ + A B’ C’ + A B C

= A’ (B’C + BC’) + A (B’C’ + BC)

= A’ (B XOR C) + A ((B XOR C)’ )

= A XOR B XOR C

- F(A,B,C) = A’ B’ C’ + A’ B’ C + A B’ C’ + A B’ C + A B C’ + A B C

= A’B’ (C’ + C) + AB’ (C’ + C) + AB (C’ + C)

= A’B’ + AB’ + AB

= A’B’ + AB’ + AB’ +AB

= B’ (A’ + A) + A (B’ + B)

= B’ + A

- G(A,B,C,D) = A’ B’ C’ D’ + A’ B’ C D’ + A B’ C’ D’ + A B’ C D + A B C’ D’ + A B C D

= A’B’D’ (C’ + C) + AC’D’ (B’ +B) + ACD (B’ +B)

= A’B’D’ + AC’D’ +ACD

= A’B’D’ + A ((C XOR D)’ )

- Use K-maps on the expressions of Problem 1. Show your work in K-map form. For 1(a)-(c):

- Find the minimized sum of products form.

1a)

| C \AB | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- |
| 0 | 0 | 1 | 0 | 1 |
| 1 | 1 | 0 | 1 | 0 |

S = A’B’C + A’BC’ ABC + AB’C’

1b)

| C \AB | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- |
| 0 | 1 | 0 | 1 | 1 |
| 1 | 1 | 0 | 1 | 1 |

F = B’ + A

1c)

| CD\AB | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- |
| 00 | 1 | 0 | 1 | 1 |
| 01 | 0 | 0 | 0 | 0 |
| 11 | 0 | 0 | 1 | 1 |
| 10 | 1 | 0 | 0 | 0 |

G = AC’D’ + ACD + A’B’D’

- Find the minimized product of sums form.

1a)

| C \AB | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- |
| 0 | 0 | 1 | 0 | 1 |
| 1 | 1 | 0 | 1 | 0 |

S’ = A’B’C’ + A’BC + ABC’ + AB’C

= (A’B’C’)’ (A’BC)’ ( ABC’)’ (AB’C)’

= (A + B + C) (A + B’ + C’) (A’ + B’ + C) (A’ + B + C’)

1b)

| C \AB | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- |
| 0 | 1 | 0 | 1 | 1 |
| 1 | 1 | 0 | 1 | 1 |

F’ = BA’

=  A + B’

1c)

| CD\AB | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- |
| 00 | 1 | 0 | 1 | 1 |
| 01 | 0 | 0 | 0 | 0 |
| 11 | 0 | 0 | 1 | 1 |
| 10 | 1 | 0 | 0 | 0 |

G’ = C’D + A’B + A’D + ACD’

= (C’D)’ (A’B)’ (A’D)’ (ACD’)’

= (C + D’) (A + B’) (A + D’) (A’ + C’ + D)

- Find the minimized sum of products form of the function’s complement.

k-maps are the same from part b

1a)  S’ = A’B’C’ + A’BC + ABC’ + AB’C

1b)  F’ = A’B

1c)  G’ = A’D + A’B + C’D + ACD’

- Find the minimized product of sums form of the function’s complement.

K-maps are the same from part a

1a)  F  = A’B’C + A’BC’ +ABC + AB’C’

F’ = (A + B + C’) (A + B’ + C) ( A’ + B’ + C’) (A’ + B + C)

1b)  F =  A + B’

F’ = A’B

1c)  G = AC’D’ + ACD + A’B’D’

G’ =  (A’ + C + D) ( A’ + C’ + D’) (A + B + D)

3i)

- One possible solution:  F(A,B,C,D) = (A + (B C)) (C’ + D) = ( (A’ (B C) ’) ’) (C D’)’ )’

- One possible solution: F(A,B,C,D) = (A + (B C)) (C’ + D) = ( (A + (B’+C’)’)’ + (C’ + D)’)’

c)  F = AC’ + AD + BCD

d) F = (A+B)(A+C)(C’+D)

e) The simplest implementation is the NOR gate implementation. It uses the least gates of all the above implementations.

3ii)

- One possible solution: G(A,B,C,D) =((A+B’)D) + (A+(BC)) = ( (A’B’)D)’ ( (A’(BC)’)’)’ )’

- One possible solution: G(A,B,C,D) = ((A+B’)D) + (A+(BC))

= (((A+B’)’ + D’)’ + ((B’ + C’)’ + A)’’)’’

- G = A + BC + B’D

- G = (A+B’+C)(A+B+D)

e) The sum of products implementation is the simplest to implement in this case. It uses the least gates of the four implementations.

4a)

4b)            W = AC’                                                     X = BC’ + AB + AD’

Y = AB’CD                                                 Z = BD’ + A’BC

4c)  W = A+C’         X = (A+C’)(B+D’)    Y = AB’CD   Z = BC(B’+D’)

5a)

5b)           By2 = D’                                        By3 = A’B’C’D’ + A’B’CD + AC’D + BCD’

By6 = A’B’C’D’ + BCD’

5c)  By2 cannot be simplified any further.

By3 can be rewritten as A’B’(C’D’ + CD) + AC’D + BCD’ or A’B’(’C’D’ XOR CD) + AC’D + BCD’

By6 can be rewritten as D’(A’B’C’+BC) but is not that much simpler than the original other than the fact that the four input AND gate can be replaced by a three input AND gate.