EECS150 Homework #4 Solutions:

1)

a)

b)

c)

2)

a)

| Initial State | reset | in | out | Next State |
| --- | --- | --- | --- | --- |
| S0 | 0 | 0 | 0 | S0 |
| S0 | 0 | 1 | 0 | S1 |
| S0 | 1 | 0 | 0 | S0 |
| S0 | 1 | 1 | 0 | S1 |
| S1 | 0 | 0 | 1 | S1 |
| S1 | 0 | 1 | 1 | S2 |
| S1 | 1 | 0 | 1 | S0 |
| S1 | 1 | 1 | 1 | S1 |
| S2 | 0 | 0 | 0 | S1 |
| S2 | 0 | 1 | 0 | S2 |
| S2 | 1 | 0 | 0 | S0 |
| S2 | 1 | 1 | 0 | S1 |

| IS1 | IS0 | reset | in | out | NS1 | NS0 |
| --- | --- | --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| 0 | 0 | 0 | 1 | 0 | 0 | 1 |
| 0 | 0 | 1 | 0 | 0 | 0 | 0 |
| 0 | 0 | 1 | 1 | 0 | 0 | 1 |
| 0 | 1 | 0 | 0 | 1 | 0 | 1 |
| 0 | 1 | 0 | 1 | 1 | 1 | 1 |
| 0 | 1 | 1 | 0 | 1 | 0 | 0 |
| 0 | 1 | 1 | 1 | 1 | 0 | 1 |
| 1 | 1 | 0 | 0 | 0 | 0 | 1 |
| 1 | 1 | 0 | 1 | 0 | 1 | 1 |
| 1 | 1 | 1 | 0 | 0 | 0 | 0 |
| 1 | 1 | 1 | 1 | 0 | 1 | 0 |

b)

3)

5-16)

4)

| Initial State | Input | X0 | X1 | X2 | X3 | Next State |
| --- | --- | --- | --- | --- | --- | --- |
| Start | 0 | 0 | 0 | 0 | 0 | Start |
| Start | 1 | 0 | 0 | 0 | 0 | S1 |
| S1 | 0 | 0 | 0 | 0 | 0 | S7 |
| S1 | 1 | 0 | 0 | 0 | 0 | S2 |
| S2 | 0 | 0 | 0 | 0 | 0 | S5 |
| S2 | 1 | 0 | 0 | 0 | 0 | S3 |
| S3 | 0 | 0 | 0 | 0 | 0 | Start |
| S3 | 1 | 0 | 0 | 0 | 0 | S4 |
| S4 | 0 | 1 | 0 | 0 | 0 | Start |
| S4 | 1 | 1 | 0 | 0 | 0 | S1 |
| S5 | 0 | 0 | 0 | 0 | 0 | Start |
| S5 | 1 | 0 | 0 | 0 | 0 | S6 |
| S6 | 0 | 0 | 1 | 0 | 0 | Start |
| S6 | 1 | 0 | 1 | 0 | 0 | S1 |
| S7 | 0 | 0 | 0 | 0 | 0 | S10 |
| S7 | 1 | 0 | 0 | 0 | 0 | S8 |
| S8 | 0 | 0 | 0 | 0 | 0 | Start |
| S8 | 1 | 0 | 0 | 0 | 0 | S9 |
| S9 | 0 | 0 | 0 | 1 | 0 | Start |
| S9 | 1 | 0 | 0 | 1 | 0 | S1 |
| S10 | 0 | 0 | 0 | 0 | 0 | Start |
| S10 | 1 | 0 | 0 | 0 | 0 | S11 |
| S11 | 0 | 0 | 0 | 0 | 1 | Start |
| S11 | 1 | 0 | 0 | 0 | 1 | S1 |

3-34)

module Prob334 (A,B,C,D,x,y,z);

input A,B,C,D;

output x,y,z;

assign x = A & ((C & D) | B) | (B & ~C);

assign y = ((A & ~B) | (~A & B) & (C | ~D));

assign z = ~((A | B) & (~C | (~D & B)));

endmodule

3-35)

- line 1: Dash not allowed, use underscore and needs semicolon at the end

- line 2: keyword should be input, not inputs and last comma should be a semicolon

- line 3: keyword should be output not Output

- line 4: A cannot be used as an output

- line 5: no instance name, too many items in portlist

- line 6: module type should be or not OR, no instance name

3-36)

3-37)

module Prob337 (A,B,C,x);

input A,B,C;

output x;

assign x = (A & B) | (A & C) | (B & C);

endmodule

4-38)

module Prob438 (A,B,S,x);

input [3:0] A,B;

input S;

output [3:0] x;

wire s0, w0,w1,w2,w3,w4,w5,w6,w7;

not n0(S, s0);

and a0(A[3],s0,w0),

a1(A[2],s0,w1),

a2(A[1],s0,w2),

a3(A[0],s0,w3),

a4(B[3],S,w4),

a5(B[2],S,w5),

a6(B[1],S,w6),

a7(B[0],S,w7);

or o0(w0,w4,x[3]),

o1(w1,w5,x[2]),

o2(w2,w6,x[1]),

o3(w3,w7,x[0]);

endmodule

The function acts like a multiplexor with a tristate buffer on the output.  If E is 0, then the output is disconnected.  Other wise, if S is 1 then the output is A and if S is 0, the output is B.

4-44)

module Prob444 (A,B,S,x);

input [3:0] A,B;

input [1:0] S;

output [3:0] x;

always @ (A or B or S)

case (S)

2’b00: x = A + B;

2’b01: x = A – B;

2’b10: x = A & B;

2’b11: x = A | B;

endcase

endmodule

5-21)

Initial statements are only executed once.  Always statements are executed every time or every time a specified set of conditions are satisfied.

5-22)

5-25)

module Prob525 (D1,D2,S,Q, clk);

input D1,D2,S, clk;

output Q;

reg Q;

always @ (posedge clk)

Q = S ? D2 : D1;

endmodule

5-30)

Using blocking assignments would take the output from the AND gate and feed it directly to the OR gate, instead of having to go through the flip-flop.

6)

http://www.vextools.com

- A collection of various Verilog utilities

http://daggit.pagecreator.com/ver/vertex.html

- A Verilog parser

http://www.openverification.org/

- A collection of Verilog modules

http://www.geocities.com/SiliconValley/Campus/3216/GTKWave/gtkwave-win32.html

- A free windows based waveform viewer

http://mufasa.informatik.uni-mannheim.de/lsra/projects/fsmdes/

- A java-based finite state machine designer

http://www.geda.seul.org/tools/icarus/

- An open source Verilog compiler

http://www.mpce.mq.edu.au/~spon/verilog/

- A Verilog pre processor

http://www.verilog.com/verilog-mode.html

- Verilog mode for emacs

http://chipvault.sourceforge.net/

- VHDL/Verilog chip design organization tool

http://www.burbleland.com/v2html/v2html.html

- Converts Verilog to html