# EECS150: Components and Design Techniques for Digital Systems

University of California 
Dept. of Electrical Engineering and Computer Sciences

| Mid Term 2 | Fall 2007 |
| --- | --- |

Last name: ____Solutions___________ 	First name_______________________

Student ID: _________________________	Login: ____________________

Lab meeting time: ________________ 	TA's name: ____________________

You may use a single 8.5x11 sheet of notes..  No calculators!  This booklet contains 7 numbered pages, including room to show your work. Please, no extra stray pieces of paper.  Put your name on every page. The exam contains 7substantive questions and 100 points, so just over 1 point per minute.  Browse through the questions before you start. You have 1.5 hours, so relax, work thoughtfully and give clear answers.  Good luck!

I certify that my answers to this exam are my own work.  If I am taking this exam early, I certify that I shall not discuss the exam questions, the exam answers, or the content of the exam with anyone until after the scheduled exam time.  If I am taking this exam in scheduled time, I certify that I have not discussed the exam with anyone who took it early.

Signature: ______________________________________

|  | Score | Count |
| --- | --- | --- |
| Problem 1 [10] |  |  |
| Problem 2 [10] |  |  |
| Problem 3 [15] |  |  |
| Problem 4 [15] |  |  |
| Problem 5 [15] |  |  |
| Problem 6 [15] |  |  |
| Problem 7 [20] |  |  |
| Total [100] |  |  |

Problem 1. (10)  Number Representation

For each of the following, what is the value represented by the 8-bit binary pattern 11111000?  Also, give the binary representation for its negative.

| Number System | Decimal Value of 11111000 | Bit representation of its negative |
| --- | --- | --- |
| Two’s complement | -8 | 00001000 |
| Unsigned | 248 | None |
| One’s complement | -7 | 00000111 |
| Excess 127 | 121 | 00000110 |
| Two’s complement fixed point with the binary point in the middle of the 8 bits | -0.5 | 00001000 |

Problem 2. (10)  Floating Point

Draw a line matching each occurrence in the left column to the conditions in the right column that best describes when it can occur.

| Occurrence |  | Conditions |
| --- | --- | --- |
| addition of two normalized floating point numbers results in a DENORM? |  | Two numbers |
| multiplication of two normalized floating point numbers results in a DENORM |  | Two numbers of small magnitude |
| addition of two normalized floating point numbers result in an overflow |  | Two numbers of large magnitude |
| multiplication of two normalized floating point numbers result in an overflow |  | Two numbers of small magnitude and opposite sign |
|  |  | Two numbers of large magnitude and opposite sign |
|  |  | Two numbers of opposite sign and a difference of small magnitude |
|  |  | Two numbers of opposite sign and a difference of large magnitude |

Problem 3. (15) Logic

- Prove (by drawing a simple diagram) that any logic function can be implemented using full adder cells.

A	B	0

AB

0	    1

NAND(A,B)

- How would you build an 8-bit parity circuit using a small number of FAs?

In[0]	In[1]	In[2]	In[3]	In[4]	In[5]	   In[6]	    In[7]	       0

.

Problem 4 (15). Circuit Delays

Determine the maximum clock rate for the circuit shown below.  Assume the following:

- The primitive inverter delay is 100 ps.  All wire delays are 0.

- The primitive delay of each gate is the number specified inside the gate.  It is in units of primitive inverter delays.

- The actual delay of a gate in the circuit is a linear function of its primitive gate delay and its fanout:  Actual delay = primitive delay + 0.25 * (# of fanouts more than 1)

  - Any logic gate, flip-flop or output port counts as one fanout of a gate. For example, the XOR gate in the circuit below has a fanout of 2.

  - Flip-flop outputs incur fanout-related delays, just like gates.

- Flip-flop setup time and clock-to-Q time are each  2 inverter delays.

- The maximum skew between any two clock inputs is 100 ps.

State clearly any other assumptions you make. Show your work.

The critical path is shown on the diagram above

Min Period 	= (Clk-to-Q + (FF-fanout + (XOR + (NAND + (NOR + (Setup + (max-skew =

= 200ps + 25ps + (3 + 0.25(2-1))*100ps +

(2 + 0.25(2-1))*100ps + 2*100ps + 200ps + 100ps

= 225ps + 325ps + 225ps + 200ps + 200ps +100ps = 1275ps

max frequency = 1/min period = 784 MHz

Problem 5 (15). Often in hardware design it is possible to produce optimized circuits for special cases that are faster or more compact than that for the general case.

- Construct a compact, low delay circuit for a 16-bit “times 14” using adders and/or carry-save adders.

- Show how to improve your circuit by using one or more subtractor.

- Result = A*8 + A*4 + A*2 = A||000 + A||00 + A||0

- Result = A*16 – A*2 = A||0000 – sx(3)||A||0

Problem 6. (15). Memory

Describe each of the steps involved in a DRAM write operation. (We are looking for a single brief sentence or two for each major step.)

- Prior to the write, OE_l and WE_l are disasserted (OE_l = 1, WE_l = 1) and the DRAM chip is essentially inactive.

- Drive Row Address; then assert RAS

- Drive Data; then asset WE_L

- Drive Col address; then assert CAS  (for late, reverse these)

- Deassert WE_L, CAS, RAS

Problem 7 (20). Debugging verilog

Find and correct 6 errors in the verilog modules below.  Additional errors count for 1 point of extra credit each.  The exact function of the FSM  is not important – the errors are basic and common.

module ShiftRegister(Clock, Reset, SIn, POut);

input		Clock, SIn, Reset;

output reg	[7:0]	POut;

always @ ( posedge Clock )

if (Reset)

POut <= 8’b0;

POut <=	{POut[6:0], SIn};

endmodule

module FSM(In, Out, OutValid, Clock, Reset);

input			In, Clock, Reset;

output reg	[7:0]	Out;

output		OutValid;

reg			CurrentState, NextState;

reg			ShiftReset, OutValid;

ShiftRegister	Shifter(Clock, ShiftReset, Out, In,);

parameter	STATE_Idle =			1'b0,

STATE_A =				1'b1,

always @ ( posedge Clock ) begin

if (Reset) 	CurrentState <=		STATE_Idle;

else 		CurrentState <=		NextState;

end

always @ ( CurrentState, Sin, Out ) begin

case ( CurrentState )

STATE_Idle: begin

if ( In ) begin

NextState =		STATE_A;

ShiftReset =	1'b1;

end

else begin

NextState = 	CurrentState;

ShiftReset = 	1’b0;

end

OutValid =		1’b0;

end

STATE_A: begin

if ( ~Out[7]) begin

NextState =		STATE_A;

OutValid =		1'b1;

end

else begin

NextState =		STATE_Idle;

OutValid =		1'b0;

End

ShiftReset =	1'b0;

end

endcase

end

endmodule

# Text boxes

A	B	Cin

S	Cout

A	B	Cin

S	Cout

Parity

Parity is just the XOR of all input bits which can be obtained by using the Sum outputs from the FA’s

Since all combinational logic can be made out of NAND gates, showing a NAND constructed of FAs is sufficient.  Answers that constructed all 3 primitives AND, OR and NOT were also acceptable.

A	B	Cin

S	Cout

A	B	Cin

S	Cout

A	B	Cin

S	Cout

A	B	Cin

S	Cout