CS150

Covers: 								Week 1, Lecture 2

- Summary of 2-input logic functions

- Input and output of logic functions

- Boolean logic and notation using gates

- DeMorgan’s theorem and bubble pushing

- Bigger logic circuits

- Addition & Half and Full adder

- Introduction to Timing

- Summary of 2-input logic functions

Some 2-input gate symbols:

_                                                       __

X                     X                               X                  OR, when used with a gate:

A

AB                    B                                AB

A

A+B                   B                                  A+B

_                    A                                        _

A+B                   B                                   A+B

___                    A                                  __

AB                    B                                  AB     ( NAND )

____

____                   A                                 A+B      ( NOR )

A+B                   B

2)	Input and output of logic functions

(  Combinatorial circuits ( No memory/state )

How many combinations of outputs ( in other words, how many functions ) are possible for a 1-input, 1-output combinational circuit?

There are 4 possible functions.

For 0-input, 1-output circuits: 2 possible functions

For 1-input, 1-output circuits: 4 possible functions

For 2-input, 1-output circuits: 16 possible functions

If the circuit has n inputs and one output, then there are 2n possible output combinations or representable functions.

Examples: 8 inputs ( 256 output combinations. 256 inputs ( ( # of atoms in universe.

(  Sequential  Circuits ( No memory/state )

How many combinations of outputs ( in other words, how many functions ) are possible for a 1-input, 1-output sequential circuit?

For clocked synchronous circuits:

Input Xi is X at time i. The value of F at time i is F(Xi, Xi-1, Xi-2, Xi-3…).

# of functions undeterminable…

For asynchronous circuits:

Fi = F( Xt   (t  ( I )

3)	Boolean logic and notation using gates

Other important theorems of Boolean logic:

X+0 = X		X(1 = X

X+1 = 1		X(0 = 0

X+X = X	X(X = X

X = X

X+X = 1		X(X = 0

4)	DeMorgan’s theorem and bubble pushing

DeMorgan’s theorem: Get the complement of an expression by:

- Replace all literals with complements

- 1 ( 0, 0 ( 1

- Replace ORs with ANDs and ANDs with ORs.

Example:	_     _   _

F = AB  then	F = A+B

_     _ _

F = A+B then 	F = AB

Bubble pushing is just DeMorgan’s theorem using symbols:

Example:	       _   _

F = AB  then	F = A+B

_   _

F = AB  then	F = A+B

_ _

F = A+B then 	F = AB

_ _

F = A+B then 	F = AB

5)	Bigger logic circuits

Lab XOR circuit analysis using DeMorgan’s…

Simplifying circuit using bubble pushing…

(

6)	Addition & half and full adder

Remember how you add in base 10:

1 1 1

- 789

+456                     456

579	             1245

No carry              Carry

3-inputs per digit: Ai, Bi, Carry ini-1

2-Outputs per digit: Sumi, Carryi

Binary addition is same thing.

Half adder ( No carry in ):

Step 1: Identify inputs and outputs.              	Step 2: Truth table		Step 3: Equation

S = A(B	C = AB

Step 4: Circuit

Full adder ( With Carry in ):

Example of binary addition:

1 	              There are only carries of “1” in binary.

01010

01101

10111

Step 1: Identify inputs and outputs.		Step 2: Truth table.	Step 3: Equations

_ _      _ _ __     _

S = ABCI+ABCI+ABCI+ABCI

= A(B(C

C = BCI + ACI + AB

Step 4: Circuit

OR ( among others ):

7)	Introduction to Timing

# Text boxes

CI

B

CO

S

Half

Adder

A

A  B  CI     S    CO

0   0   0      0     0

0   0   1      1     0

0   1   0      1     0

0   1   1      0     1

1   0   0      1     0

1   0   1      0     1

1   1   0      0     1

1   1   1      1     1

One bit addition:

CO    	     CI

A

+ B

S

C

S

B

A

A  B        S    C

0   0        0     0

0   1        1     0

1   0        1     0

1   1        0     1

Si

CO

Ai

Bi

CIi-1

S  ( Sum )

CO ( Carry Out )

A

B

B

A

(

B

A

B

A

A

F(A,B,C)

A

B

C

B

(

___

AB

B

A

___    ___        _    _        _   _         _     _

AAB BAB  = AAB+BAB = A(A+B)+B(A+B) = AB + AB

= A(B

_

NOTE:     BAB = B+AB

___

BAB

___

AAB

A

B

F		OUT

INPUTS  	Possible outputs ( For a particular F the outputs are described by a single column. )

A    B		OUT0  OUT1 OUT2 OUT3 OUT4  OUT5 OUT6 OUT7 OUT8  OUT9 OUT10 OUT11 OUT12  OUT13 OUT14 OUT15

- 0		 0        0      0       0       0        0       0       0       1        1       1        1         1         1        1         1

- 1		 0        0      0       0       1        1       1       1       0        0       0        0         1         1        1         1

- 0		 0        0      1       1       0        0       1       1       0        0       1        1         0         0        1         1

1     1		 0        1      0       1       0        1       0       1       0        1       0        1         0         1        0         1

Explanation: When F is an AND gate the output of F is represented by the values in column OUT1.

Outputs and their functions:			Some more complicated functions:

OUT0 ( The 0 function

OUT1 ( AND  ( AB )

OUT3 ( A

OUT5 ( B

OUT6 ( XOR  ( A(B )

OUT7 ( OR    ( A+B )

OUT8 ( NOR    ( A+B )

OUT9 ( XNOR   ( A(B )

OUT10 ( NOT B   ( B )

OUT12 ( NOT A   ( A )

OUT14 ( NAND   ( AB )

OUT15 ( The 1 function

OUT2 ( AB

OUT4 ( AB

OUT13 ( A+B

F(X)

X

X     F0    F1    F2    F3

0      0      0      1      1

1      0      1      0      1

XOR

A    B		A(B

- 0		0

- 1		1

- 0		1

1     1		0

_           _

A(B = AB + AB

INPUTS  		_   _ 		_ _

A    B		A+B	A+B	AB	AB

- 0		0	1	0	1

- 1		1	1	0	0

- 0		1	1	0	0

1     1		1	0	1	0

_ _                          =

A+B = AB

_   _                          =

AB = A+B

____    _ _

A+B = AB

___    _   _

AB = A+B

F(Xi, Xi-1, Xi-2, Xi-3…    )

The result of F(X) is influenced by past events.

X

Commutative:	X+Y = Y+X		XY = YX

Associative:	X+(Y+Z) = (X+Y)+Z	X(YZ) = (XY)Z

Distributive:	X(Y+Z) = XY+XZ	X+(YZ) = (X+Y)(X+Z)

_

AB

_

AB

A(B

A

B

A

B

Half

Adder

CI

S

CO

B

A

A    1

0

B    1

0

CO 1

0

S     1

0

Time