CS150

Week 8, lecture 1

Covers:

- Number systems

- Computer datapaths

- Addition

- Hardware

- Number systems

S/M ( (Sign)(Magnitude)		0, 1, 2, 3 , 0, -1, -2,-3      What to do about decimal?

1’s complement ( X = 2n – 1 – X	0, 1, 2, 3, -3, -2, -1, 0      2 zeros			Addition simple. Easy to ??

2’s complement ( X* = 2n – X	0, 1, 2, 3, -4, -3, -2, -1     Harder to connect (a little)	Addition easy

2)	Computer datapaths

Fig. 11.4, 11.13

Also in book…STT:

3)	Addition

Overflow/Underflow

Representation of negative numbers

Hardware

How do you add (say you only have 4 bits.):

5			5			-5			-5

7			-7			7			-7

--------      	                          ------                                    -------                                --------

12			-2			2			-12

Overflow.	                           OK		        Same as		     Underflow

Can’t represent 12	   Subtract smaller 	      7 – 5 = 2		Can’t represent -12

with 4 bits	           from larger and negate			                     with 4 bits

Addition sign rules for A + B = C:

A & B same sign: 	Add and C’s sign is the same as A & B’s.

A & B different signs: 	Subtract smaller number from larger number.

Use sign of the bigger of  |A| & |B|

## Sign/Magnitude        Represents –(2n-1-1) to +(2n-1-1)

n-Bit number.

n = 4 : 	-7 to 7

n = 8 : 	-127 to 127

n = 32 : 	-2 billion to 2 billion

1st bit is sign bit. 1 ( negative			# of bits        1         n-1

0 ( positive

X = Xn-1Xn-2Xn-3…X1X0		0100 = 4

___

- X = Xn-1Xn-2Xn-3…X1X0		1100 = -4

Problem: 2 zeros. 0000 & 1000

## 1’s complement 		Represents –(2n-1-1) to +(2n-1-1)

X = Xn-1Xn-2Xn-3…X1X0		0100 = 4

__   __  __      __  __

- X = Xn-1Xn-2Xn-3…X1  X0		1011 = -4

Problem: Still 2 zeros. 0000 & 1111

Note symmetry.  0000 (( 1111,   0100 (( 1011…

## 2’s complement 		Represents –2n-1 to +(2n-1-1)

X = Xn-1Xn-2Xn-3…X1X0		0100 = 4

__   __  __      __  __

- X = Xn-1Xn-2Xn-3…X1  X0  + 1	1100 = -4

No 2 zero problem!

3 = 0011		-3 = 1100 + 1 = 1101

0 = 0000		-0 = 1111 + 1 = 0000

-6 = 1010	--6 = 0101 + 1 = 0110

-8 = 1000	--8 = 0111 + 1 = 1000 = -8!!!!! ERROR!!!   Why?

000  	001 	010  	011  	100  	101  	110  	111

Sign/Mag            	0	1	2	3	-0	-1	-2	-3

1’s Comp	0	1	2	3	-3	-2	-1	-0  Note symmetry  2 (( -2

010 (( 101

2’s Comp	0	1	2	3	-4	-3	-2	-1 Note 1xxx = -(2n-1 – xxx)

Most

negative

Addition revisited:

Sign/Mag: Same as decimal

001	                  110    (-2)		    111  (-3)

+ 011		+ 011    (+3)		+  010  (+2)

000	                  001    (+1)	    	    101   (-1)

Overflow

1’s Complement: Positive numbers ( No problem

-2	   1101	 (-2)		    1110  (-1)

+1	+ 0001	 (+1)		+  0010  (+2)

-1              1110	 (-1)	    	    0000   (0)

?????????????  Why? End around carry

1’s complement is painful to implement in hardware:

If we just shifted the negative number right we’d get rid of the end-around-carry problem.

But shifting the negative number right just gives us 2’s complement!!!!

-2	1110		1111	-1

1	0001	 	0010	 2

-1	1111		0001	 1

Which are the correct results…

Overflow in 2’s complement:	Cin n-1 = Coutn-1

Why?:

0	1	2	3	-4	-3	-2	-1

Overflow (

(Add to make number bigger than 3. Carry-in makes it negative. Can’t be carry out.)

( Underflow

(Add to make number smaller than –4. No carry makes it positive. Carry-out is guaranteed )

Either one of these gives a top bit that tells you whether there’s been overflow.

Note:

Positive numbers are the same in all systems.

Sign/Mag and 1’s complement have 2 zeros (bad).

Sign/Mag is hard to make adders (bad).

2’s complement is a little harder to negate (bad).

4)	Hardware

half-adder:

Full adder

Adder/subtracter

A + B

_

A + ( B + 1 )

Delays: Say all gates have a delay of 5ns.

Then:

tAS = 25

tAC = 35

tCS =

This disagrees with Katz: Is carry-in (C0) zero?

Note: Why would not want to make a 64 bit adder this way? (Hint: How does the delay increase per bit?)

# Text boxes

Si

Ci+1

Ai

Bi

# Ci

Overflow/Underflow

An-1

B n-1

A

B

--

A

B

I

R

P

C

S3

A3   B3

Full

Adder

S2

A2   B2

Full

Adder

S1

A1   B1

Full

Adder

Cout

Cin

S0

A0   B0

Cin

__

Add/sub

4

4

4

Full

Adder

OV (overflow?)

NEG (Negative?)

CO (Cout)

Sum

A

B

_

B

+

Si

Ci+1

Ai

Bi

# Ci

S

C

A

B

M

U

X

An-1

B n-1

nth bit

n-1

M

U

X

M

A

R

# RAM

A

B

+

A>B

M

B

R

ACC

ALU

Not

taken

SAME

SAME

Branch

Store

Load

Jump

Add

Increment

PC

Fetch

# RAM

MAR

IR

PC

M

B

R

ACC

ALU

000 	001 	010 	011 	100 	101 	110 	111 	000 	001 …

X > 0			1’s Comp:     2n-1-X			2n

2’s Comp:     2n-X	2n-1