# Professor Fearing								             Fall 1998

CS 150 Problem Set 11

Solutions by Nadeem (nma@cory.eecs)

1. K-Maps

Here is the truth table for the function:

| A3A2A1A0 | log2 | BC.DE |
| --- | --- | --- |
| 0000 | x | xx.xx |
| 0001 | 0 | 00.00 |
| 0010 | 1 | 01.00 |
| 0011 | 1.58 | 01.10 |
| 0100 | 2 | 10.00 |
| 0101 | 2.32 | 10.01 |
| 0110 | 2.59 | 10.10 |
| 0111 | 2.81 | 10.11 |
| 1000 | 3 | 11.00 |
| 1001 | 3.17 | 11.01 |
| 1010 | 3.32 | 11.01 |
| 1011 | 3.46 | 11.10 |
| 1100 | 3.58 | 11.10 |
| 1101 | 3.70 | 11.11 |
| 1110 | 3.81 | 11.11 |
| 1111 | 3.91 | 11.11 |

B is 1 when the input is 4, 5, 6, 7, 8, 9, 10, 11, 12, 13, 14, and 15, while 0 is a don’t care value.   This is written as:

B = (4, 5, 6, 7, 8, 9, 10, 11, 12, 13, 14, 15) + D(0)

Now fill in the K-Map table with 0, 1, and X and circle all of the entries where B is 1.

|  | A1A0 |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| A3A2 |  | 00 | 10 | 11 | 10 |
|  | 00 | x | 0 | 0 | 0 |
|  | 01 | 1 | 1 | 1 | 1 |
|  | 11 | 1 | 1 | 1 | 1 |
|  | 10 | 1 | 1 | 1 | 1 |

Next you can figure out the boolean equation by looking at which values are circled. There will be one sum term for each circle.  In this case, one circle corresponds to when A2 is 1 and the other to when A3 is 1.  So, the equation is:

B = A2 + A3

C = (2, 3, 8, 9, 10, 11, 12, 13, 14, 15) + D(0)

|  | A1A0 |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| A3A2 |  | 00 | 10 | 11 | 10 |
|  | 00 | x | 0 | 1 | 1 |
|  | 01 | 0 | 0 | 0 | 0 |
|  | 11 | 1 | 1 | 1 | 1 |
|  | 10 | 1 | 1 | 1 | 1 |

C = A3 + A1A2

D = (3, 6, 7, 11, 12, 13, 14, 15) + D(0)

|  | A1A0 |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| A3A2 |  | 00 | 10 | 11 | 10 |
|  | 00 | x | 0 | 1 | 0 |
|  | 01 | 0 | 0 | 1 | 1 |
|  | 11 | 1 | 1 | 1 | 1 |
|  | 10 | 0 | 0 | 1 | 0 |

D = A1A0 + A3A2 + A2A0

E = (5, 7, 11, 12, 13, 14, 15) + D(0)

|  | A1A0 |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| A3A2 |  | 00 | 10 | 11 | 10 |
|  | 00 | x | 0 | 0 | 0 |
|  | 01 | 0 | 1 | 1 | 0 |
|  | 11 | 0 | 1 | 1 | 1 |
|  | 10 | 0 | 1 | 0 | 1 |

E = A0A2 + A3A1A0 + A3A1A0

B = A2 + A3

C = A3 + A1A2

D = A1A0 + A3A2 + A2A0

E = A0A2 + A3A1A0 + A3A1A0

To find Product of Sums form, cirlce the 0s and invert the equation.

B = (1, 2, 3) + D(0)

|  | A1A0 |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| A3A2 |  | 00 | 10 | 11 | 10 |
|  | 00 | x | 0 | 0 | 0 |
|  | 01 | 1 | 1 | 1 | 1 |
|  | 11 | 1 | 1 | 1 | 1 |
|  | 10 | 1 | 1 | 1 | 1 |

B = A3A2

B = A3A2

B = A2 + A3

C = (4, 5, 6, 7) + D(0)

|  | A1A0 |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| A3A2 |  | 00 | 10 | 11 | 10 |
|  | 00 | x | 0 | 1 | 1 |
|  | 01 | 0 | 0 | 0 | 0 |
|  | 11 | 1 | 1 | 1 | 1 |
|  | 10 | 1 | 1 | 1 | 1 |

C = (A3 + A1)(A3 + A1)

D = (1, 2, 4, 5, 8, 9, 10) + D(0)

|  | A1A0 |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| A3A2 |  | 00 | 10 | 11 | 10 |
|  | 00 | x | 0 | 1 | 0 |
|  | 01 | 0 | 0 | 1 | 1 |
|  | 11 | 1 | 1 | 1 | 1 |
|  | 10 | 0 | 0 | 1 | 0 |

D = (A3 + A1)(A2 + A1)(A0 + A2)

E = (1, 2, 3, 4, 6, 8, 11, 12) + D(0)

|  | A1A0 |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| A3A2 |  | 00 | 10 | 11 | 10 |
|  | 00 | x | 0 | 0 | 0 |
|  | 01 | 0 | 1 | 1 | 0 |
|  | 11 | 0 | 1 | 1 | 1 |
|  | 10 | 0 | 1 | 0 | 1 |

E = (A3 + A2)(A1 + A0)(A0 + A3)(A2 + A1 + A0)

B = A2 + A3

C = (A3 + A1)(A3 + A1)

D = (A3 + A1)(A2 + A1)(A0 + A2)

E = (A3 + A2)(A1 + A0)(A0 + A3)(A2 + A1 + A0)

2. State Minimization

| Present State | Next State | Output |
| --- | --- | --- |
|  | IN = 0 | IN = 1 |  |
| A | A | C | 0 |
| B | D | B | 1 |
| C | D | B | 0 |
| D | B | C | 0 |
| E | E | F | 0 |
| F | G | B | 0 |
| G | B | F | 0 |

Fill out every entry in the state table with the next states for each input.  The following is the first entry for states A and B:

| SA | SB |  |
| --- | --- | --- |
| A | D | IN = 0 |
| C | B | IN = 1 |

After filling out the table, first cross out the pairs that have different outputs.  In this case, state B is the only state that outputs a 1, so cross out the states paired with state B.

| SB | A | D |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | C | B |  |  |  |  |  |  |  |  |  |  |
| SC | A | E | D | D |  |  |  |  |  |  |  |  |
|  | C | B | B | B |  |  |  |  |  |  |  |  |
| SD | A | B | D | B | D | B |  |  |  |  |  |  |
|  | C | C | B | C | B | C |  |  |  |  |  |  |
| SE | A | E | D | E | D | E | B | E |  |  |  |  |
|  | C | F | B | F | B | F | C | F |  |  |  |  |
| SF | A | G | D | G | D | G | B | G | E | G |  |  |
|  | C | B | B | B | B | B | C | B | F | B |  |  |
| SG | A | B | D | B | D | B | B | B | E | B | G | B |
|  | C | F | B | F | B | F | C | F | F | F | B | F |
|  | SA | SB | SC | SD | SE | SF |

Next, look for the state pairs within each cell that have already been crossed out.  This means the states are not equivalent, so cross it out.  In this case, any state paired up state B as the next state should be crossed out.

| SB |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| SC | A | E |  |  |  |  |  |  |  |  |  |  |
|  | C | B |  |  |  |  |  |  |  |  |  |  |
| SD | A | B |  |  | D | B |  |  |  |  |  |  |
|  | C | C |  |  | B | C |  |  |  |  |  |  |
| SE | A | E |  |  | D | E | B | E |  |  |  |  |
|  | C | F |  |  | B | F | C | F |  |  |  |  |
| SF | A | G |  |  | D | G | B | G | E | G |  |  |
|  | C | B |  |  | B | B | C | B | F | B |  |  |
| SG | A | B |  |  | D | B | B | B | E | B | G | B |
|  | C | F |  |  | B | F | C | F | F | F | B | F |
|  | SA | SB | SC | SD | SE | SF |

Check again if there any more state pairs that have next states that are not equivalent.

| SB |  |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| SC |  |  |  |  |  |  |  |  |  |  |  |  |
| SD |  |  |  |  |  |  |  |  |  |  |  |  |
| SE | A | E |  |  |  |  |  |  |  |  |  |  |
|  | C | F |  |  |  |  |  |  |  |  |  |  |
| SF |  |  |  |  | D | G |  |  |  |  |  |  |
|  |  |  |  |  | B | B |  |  |  |  |  |  |
| SG |  |  |  |  |  |  | B | B |  |  |  |  |
|  |  |  |  |  |  |  | C | F |  |  |  |  |
|  | SA | SB | SC | SD | SE | SF |

Equivalent states: E = A, C = F, D = G.

# Text boxes

A2

A3

D/G

[ 0]

C/F

[ 0]

A/E

[ 0]

B

[ 1]

1

1

1

1

0

0

0

0