9/20 & 9/22

CS150

Section week 4

- Loadable counters:  Discussed in section…

- D, T, & JK Flip-Flops

D Flip-Flop truth table	    T Flip-Flop truth table	    JK Flip-Flop truth table

D   Q				 T    Q				J   K      Q

0				0				0   0

1				1				0   1

1   0

Implement the following counter's NS logic:				1   1

Using JK flip-flops:

Using D flip-flops:	    Using Toggle flip-flops:

Logic:			     Logic:

- Timing ( Statistics for Xilinx chip: 4-97 )

3a) Setup & hold time ( no clock skew ).

For both D flip flops:

5ns < Tcko < 10ns

What’s the maximum setup time possible?

What’s the equation to find the maximum possible setup time?

What’s the maximum hold time possible?

What’s the equation to find the maximum possible hold time?

3b) Setup and Hold times ( no clock skew – same circuit )

For both flip flops:

Tsetup = 15ns

Thold = 20ns

What’s the possible range for Tcko?

What’s the equation to find the minimum Tcko?

What’s the equation to find the maximum Tcko?

3c) Setup and Hold times when there is clock skew

For both flip flops:

Tsetup = 15ns

Thold = 20ns

Delay = 10ns

What’s the minimum Tcko possible?

What’s the equation to find the minimum Tcko?

What’s the maximum Tcko?

What’s the equation for the maximum Tcko?

3d)  Setup and Hold times when there is feedback

For both flip flops:

Tsetup = 5ns	       5ns < Tcko < 15ns  	  What’s the fastest clock where

Thold = 10ns	       8ns < Tp < 12ns   	  this circuit will still work?

# Text boxes

Delay

D1          Q1

C

0

1

PS1  PS0   NS1 NS0

0      0	      1       0

0      1	      0       0

1      0	      1       1

1      1	      0       1

D0         Q0

C

CLK

0ns			   25ns			    50ns			     75ns		       	     100ns

CLK

D0

CLK2

Q0/D1

D1          Q1

C

D0         Q0

C

PS1  PS0   T1   NS1  T0  NS0

0      0	              1             0

0      1	              0             0

1      0	              1             1

1      1	              0             1

CLK

0ns		tsetup	   25ns	  thold		    50ns		    tsetup	     75ns	       thold	       	     100ns

CLK

D0

Q0/D1

0ns			   25ns			    50ns			     75ns		       	     100ns

Possible  Final:

PS1  PS0   J1 K1   J1 K1 NS1 J0 K0  NS0

0      0	                            1                 0

0      1	                            0                 0

1      0	                            1                 1

1      1	                            0                 1

3

1

2

0

JK flip-flops: For PS1=0 and PS0 = 0, NS1 = 1. To get the  JK flip-flop that has PS1’s value in it to change from 0 to 1, J1-K1 can equal 1-0, or 1-1. In other words, as long as J1 = 1, PS1 will change from 0 to a NS of 1. It doesn’t matter what K1 equals. Therefore the second column: 1 X.    (X=Don’t care)

0 X

X 1

1 X

X 0

CLK

D0

Q0

Q1

1 0      1 X

1 1

0 0      0 X

0 1

0 0      X 0

1 0

0 1      X 1

1 1

0

1

1

0

D             Q

C

CLK

Answers in RED

D1          Q1

C

CLK

D

Q

D0         Q0

C

1

0

0

1

Q

0

1

Q

CLK

Q

Q

40ns

Tsumax = Period – Tckomax

5ns

Tholdmax = Tckomin

Can change in this range

D0 can’t change in the                  area...   45ns < Tcko < 60ns

Tckomin = Thold

Tckomax = Period - Tsetup

D0 can’t change in the                area.

Q0/D1 can’t change in the                area

Tckomin > 30ns

Tckomin > Thold + Delay

Tckomax  < 45ns

Tckomax < Period – Tsetup + Delay

Tsetup		Thold

Tsetup		Thold

Tckomin

Tckomax

Tpmin

Tpmax

When looking for the fastest clock, you look for the shortest period using all the max delays of the components you go thru. In this case, the path goes thru the flip-flop (use Tckomax), and the inverter (use Tpmax). And this signal needs to get to the flip-flop Tsumax before the next clock. Therefore:

Period = Tckomax + Tpmax + Tsetup = 15ns + 12ns + 5ns = 32ns    Clock = 1/Period

D1  Q1

D0  Q0

___

PS0

PS1

T0  Q0

T1  Q1

________

PS1(PS0

PS1(PS0

___

PS0

PS0

PS1

PS1

J0  Q0

K0

J1  Q1

K1