# University of California at Berkeley

## College of Engineering

Department of Electrical Engineering and Computer Sciences

### EECS150								J. Wawrzynek

# Spring 2000								E. Caspi

#### Homework #8 – Solution

The following solutions are reproduced from the Katz textbook’s solutions manual.

5.12	Remainder function:  R1R0 = D2D1D0 mod C1C0.

- We begin by writing the truth table, noting the following simplifications:

- (anything) mod 0 = X  (don’t care)

- (anything) mod 1 = 0

- 0 mod (anything) = 0

| D2 | D1 | D0 | C1 | C0 | R1 | R0 |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 0 | 0 | X | X |  | 0mod0 = X |
| 0 | 0 | 0 | 0 | 1 | 0 | 0 |  | 0mod1 = 0 |
| 0 | 0 | 0 | 1 | 0 | 0 | 0 |  | 0mod2 = 0 |
| 0 | 0 | 0 | 1 | 1 | 0 | 0 |  | 0mod3 = 0 |
| 0 | 0 | 1 | 0 | 0 | X | X |  | 1mod0 = X |
| 0 | 0 | 1 | 0 | 1 | 0 | 0 |  | 1mod1 = 0 |
| 0 | 0 | 1 | 1 | 0 | 0 | 1 |  | 1mod2 = 1 |
| 0 | 0 | 1 | 1 | 1 | 0 | 1 |  | 1mod3 = 1 |
| 0 | 1 | 0 | 0 | 0 | X | X |  | 2mod0 = X |
| 0 | 1 | 0 | 0 | 1 | 0 | 0 |  | 2mod1 = 0 |
| 0 | 1 | 0 | 1 | 0 | 0 | 0 |  | 2mod2 = 0 |
| 0 | 1 | 0 | 1 | 1 | 1 | 0 |  | 2mod3 = 2 |
| 0 | 1 | 1 | 0 | 0 | X | X |  | 3mod0 = X |
| 0 | 1 | 1 | 0 | 1 | 0 | 0 |  | 3mod1 = 0 |
| 0 | 1 | 1 | 1 | 0 | 0 | 1 |  | 3mod2 = 1 |
| 0 | 1 | 1 | 1 | 1 | 0 | 0 |  | 3mod3 = 0 |
| 1 | 0 | 0 | 0 | 0 | X | X |  | 4mod0 = X |
| 1 | 0 | 0 | 0 | 1 | 0 | 0 |  | 4mod1 = 0 |
| 1 | 0 | 0 | 1 | 0 | 0 | 0 |  | 4mod2 = 0 |
| 1 | 0 | 0 | 1 | 1 | 0 | 1 |  | 4mod3 = 1 |
| 1 | 0 | 1 | 0 | 0 | X | X |  | 5mod0 = X |
| 1 | 0 | 1 | 0 | 1 | 0 | 0 |  | 5mod1 = 0 |
| 1 | 0 | 1 | 1 | 0 | 0 | 1 |  | 5mod2 = 1 |
| 1 | 0 | 1 | 1 | 1 | 1 | 0 |  | 5mod3 = 2 |
| 1 | 1 | 0 | 0 | 0 | X | X |  | 6mod0 = X |
| 1 | 1 | 0 | 0 | 1 | 0 | 0 |  | 6mod1 = 0 |
| 1 | 1 | 0 | 1 | 0 | 0 | 0 |  | 6mod2 = 0 |
| 1 | 1 | 0 | 1 | 1 | 0 | 0 |  | 6mod3 = 0 |
| 1 | 1 | 1 | 0 | 0 | X | X |  | 7mod0 = X |
| 1 | 1 | 1 | 0 | 1 | 0 | 0 |  | 7mod1 = 0 |
| 1 | 1 | 1 | 1 | 0 | 0 | 1 |  | 7mod2 = 1 |
| 1 | 1 | 1 | 1 | 1 | 0 | 1 |  | 7mod3 = 1 |

- 5-Variable Karnaugh maps for R1 and R0:

| C1C0 | R1 (D2=0) |  | C1C0 | R1 (D2=1) |
| --- | --- | --- | --- | --- |
| D1D0 | 00 | 01 | 11 | 10 |  | D1D0 | 00 | 01 | 11 | 10 |
| 00 | X | 0 | 0 | 0 |  | 00 | X | 0 | 0 | 0 |
| 01 | X | 0 | 0 | 0 |  | 01 | X | 0 | 1 | 0 |
| 11 | X | 0 | 0 | 0 |  | 11 | X | 0 | 0 | 0 |
| 10 | X | 0 | 1 | 0 |  | 10 | X | 0 | 0 | 0 |
| C1C0 | R0 (D2=0) |  | C1C0 | R0 (D2=1) |
| D1D0 | 00 | 01 | 11 | 10 |  | D1D0 | 00 | 01 | 11 | 10 |
| 00 | X | 0 | 0 | 0 |  | 00 | X | 0 | 1 | 0 |
| 01 | X | 0 | 1 | 1 |  | 01 | X | 0 | 0 | 1 |
| 11 | X | 0 | 0 | 1 |  | 11 | X | 0 | 1 | 1 |
| 10 | X | 0 | 0 | 0 |  | 10 | X | 0 | 0 | 0 |

Simplified expressions:

R1 = D2’D1D0’C1C0 + D2D1’D0C1C0

R0 = D0C0’ + D2’D1’D0C1 + D2D1D0C1

- Converting the AND-OR network to NAND-NAND:

# Text boxes

D2’

D1’

D0

C1

D2

D1

D0

C1

D2’

D1

D0’

C1

C0

R0

R1

D2

D1’

D0

C1

C0

D0

C0’