# University of California at Berkeley

## College of Engineering

Department of Electrical Engineering and Computer Sciences

### EECS150								J. Wawrzynek

# Spring 2000								E. Caspi

#### Quiz #3 – Solution

There are many possible solutions – we present 3 plausible ones.  There are two preliminary points which are important in all solutions:

- s=1.  Since this is a combinational circuit, not a sequential one, we do not need the flip flop.  In all cases, the output multiplexor should  pass on the signal which bypasses the flip flop (i.e. s=1).

- Decompose the 8-input OR.  A single CLB cannot possibly implement the 8-input OR which generates y.  You must decompose that OR gate.  This is easy, since OR is associative:  a+b+c = (a+b)+c = a+(b+c).  That means a wide OR can be implemented by a sequence of smaller ORs as well as by a tree (as in Homework #2, problem 2, which did the same for a wide XOR).  To minimize total CLB usage, the particular OR decomposition you choose should depend on the partitioning of the rest of the circuit.

# Recall that this is our CLB:

The easiest way to use the CLB is as a 4-LUT.  We compose the 4-LUT from the pair of 3-LUTs by feeding the same 3 inputs into {b,c,d} as into {e,f,g} and by using a for the fourth input.  The first 3-LUT implements the 4-LUT function assuming a=0 while the second assumes a=1.  This technique is demonstrated in Homework #3, problem 3.

# A very simple partitioning can be done using 11 4-LUTs.  Each of the 8 AND-AND terms uses one CLB, and the OR is partitioned into a tree of 3 CLBs.

| a | b | c | d | e | f | g | s | h |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| x3 | x0 | x1 | x2 | x0 | x1 | x2 | 1 | t9 |
| x4 | x0 | x1 | x2 | x0 | x1 | x2 | 1 | t10 |
| x5 | x0 | x1 | x2 | x0 | x1 | x2 | 1 | t11 |
| x6 | x0 | x1 | x2 | x0 | x1 | x2 | 1 | t12 |
| x7 | x0 | x1 | x2 | x0 | x1 | x2 | 1 | t13 |
| x8 | x0 | x1 | x2 | x0 | x1 | x2 | 1 | t14 |
| x9 | x0 | x1 | x2 | x0 | x1 | x2 | 1 | t15 |
| x10 | x0 | x1 | x2 | x0 | x1 | x2 | 1 | t16 |
| t12 | t9 | t10 | t11 | t9 | t10 | t11 | 1 | w0 |
| t16 | t13 | t14 | t15 | t13 | t14 | t15 | 1 | w1 |
| 0 | w0 | w1 | - | - | - | - | 1 | y |

Implementation in 11 CLBs

(4-LUT configuration).

The following partition in 5 CLBs is due to Drew Pertula.  The 8 AND-AND terms can be grouped into 4 pairs, where the difference between each pair is the inversion of the x2 input.  This guarantees that, in any such pair, one AND-AND term is forced to zero.  Since the AND-AND terms are subsequently OR-ed, the value of x2 effectively selects which among each pair of AND-AND terms will pass to the output.  Now we can pack each pair of OR-ed AND-AND terms into a single CLB – each AND-AND (now without x2 as an input) gets a 3-LUT, and x2 controls the multiplexer to select one of them.  This requires 4 CLBs (2 AND-ANDs in each), and one additional CLB to OR their outputs (using a 4-LUT configuration).  Total: 5 CLBs.

| a | b | c | d | e | f | g | s | h |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| x2 | x0 | x1 | x3 | x0 | x1 | x4 | 1 | w0 |
| x2 | x0 | x1 | x5 | x0 | x1 | x6 | 1 | w1 |
| x2 | x0 | x1 | x7 | x0 | x1 | x8 | 1 | w2 |
| x2 | x0 | x1 | x9 | x0 | x1 | x10 | 1 | w3 |
| w3 | w0 | w1 | w2 | w0 | w1 | w2 | 1 | y |

Implementation in 5 CLBs.

We can do one better – 3 CLBs.  You must first realize that the circuit is an 8-to-1 multiplexor.  It chooses one of {x3,…,x10} according to the select bus {x2,x1,x0}.  The first column of ANDs implements a decoder, converting the binary number {x2,x1,x0} into a one-hot representation {t1,…,t8} – only one of {t1,…,t8} will be 1, the rest 0.  The second column masks out the unselected inputs from {x3,…,x10} by AND-ing them with 0 – only one of {t9,…,t16} will actually copy an x input, the rest will be 0.  The final OR simply passes-on whichever result was selected.

An 8-to-1 multiplexor can be implemented by a tree of 2-to-1 multiplexors.  A 2-to-1 multiplexor fits in a 3-LUT.  A CLB combines 2 2-to-1 muxes into a 4-to-1 mux.  A pair of such CLBs fed through a 2-to-1 multiplexor in a third CLB forms an 8-to-1 mux.

| a | b | c | d | e | f | g | s | h |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| x1 | x3 | x4 | x2 | x5 | x6 | x2 | 1 | t4 |
| x1 | x7 | x8 | x2 | x9 | x10 | x2 | 1 | t5 |
| 0 | t4 | t5 | x0 | - | - | - | 1 | y |

Implementation in 3 CLBs.

# Text boxes

x

0

x

1

x

2

x

3

x

4

x

5

x

6

x

7

x

8

x

9

x

1

0

y

t

1

t

2

t

3

t

4

t

5

t

6

t

7

t

8

t

9

t

1

0

t

1

1

t

1

2

t

1

3

t

1

4

t

1

5

t

1

6

w0

w1

x

0

x

1

x

2

x

3

x

4

x

5

x

6

x

7

x

8

x

9

x

1

0

y

t

1

t

2

t

3

t

4

t

5

t

6

t

7

t

8

t

9

t

1

0

t

1

1

t

1

2

t

1

3

t

1

4

t

1

5

t

1

6

w0

w1

w2

w3

t5

t4

t3

t2

t1

t0

y

x0

x1

x2

x10

x9

x8

x7

x6

x5

x4

x3