# University of California at Berkeley

## College of Engineering

Department of Electrical Engineering and Computer Sciences

### EECS150								J. Wawrzynek

# Spring 2000								E. Caspi

#### Quiz #7 – Solution

Using two memory ports, the following design simultaneously accesses both components of each linked-list element.  The pointer component (address NEXT) is accessed via port b, while the value component (address NEXT+1) is accessed via port a.

Available components:

- 8 and 16-bit registers with synchronous clear (CL)

- 16-bit adder

- 8-bit zero-comparator

# Text boxes

NEXT

SUM

1

(only need lower 8 bits of this
16-bit adder)

+

START

=0 ?

+

DONE

SUM

CL

CL

16

16  (zero-padded from 8)

16

8

8

8

16

8