CS 150 Problem Set# 10/11 Solutions					Wen Hui Guan

- Processor Datapath

Additional assumptions:

  - It’s a single-cycle processor implementation

  - Each instruction fetch requires burst reading 3 sequential words from the instruction ROM based on the current PC

  - Register decoding is done by the controller from the first or second words read,

depending on the decoded instruction.

d.	The machine starts once the Go button is pressed

2.

# Controller Output Signals

| Control Signals | RegWr | RegDest | Src_sel | Op <3:0> | Load | WrData <1:0> | Brz | WE | CS | Xfer |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| I n s t r u c t i o n s | ADD | 1 | 0 | R[x1x0] | 00xx | x | 01 | 0 | 0 | 0 | 0 |
|  | NAND | 1 | 0 | R[x1x0] | 01xx | x | 01 | 0 | 0 | 0 | 0 |
|  | LSR | 1 | 0 | 0 | 1000 | 1 | 10 | 0 | 0 | 0 | 0 |
|  | LSL | 1 | 0 | 0 | 1001 | 1 | 10 | 0 | 0 | 0 | 0 |
|  | ASR | 1 | 0 | 0 | 1010 | 1 | 10 | 0 | 0 | 0 | 0 |
|  | RSL | 1 | 0 | 0 | 1011 | 1 | 10 | 0 | 0 | 0 | 0 |
|  | Xfer | 1 | R[y3y2] | R[y1y0] | 1100 | x | x | 0 | 0 | 0 | 1 |
|  | LOAD | 1 | 0 | x | 1101 | x | 0 | 0 | 0 | 1 | 0 |
|  | STOR | 0 | x | x | 1110 | x | x | 0 | 1 | 1 | x |
|  | BRZ | 0 | x | 0 | 1111 | x | x | 1 | 0 | 0 | x |

# Register Transfer Operations

| Transfer Operations | Control Signals |
| --- | --- |
| R[0] ( R[0] | RegDest = 00, Src_sel = 00, xfer=1 |
| R[0] ( R[1] | RegDest = 00, Src_sel = 01, xfer=1 |
| R[0] ( R[2] | RegDest = 00, Src_sel = 10, xfer=1 |
| R[0] ( R[3] | RegDest = 00, Src_sel = 11, xfer=1 |
| R[1] ( R[0] | RegDest = 01, Src_sel = 00, xfer=1 |
| R[1] ( R[1] | RegDest = 01, Src_sel = 01, xfer=1 |
| R[1] ( R[2] | RegDest = 01, Src_sel = 10, xfer=1 |
| R[1] ( R[3] | RegDest = 01, Src_sel = 11, xfer=1 |
| R[2] ( R[0] | RegDest = 10, Src_sel = 00, xfer=1 |
| R[2] ( R[1] | RegDest = 10, Src_sel = 01, xfer=1 |
| R[2] ( R[2] | RegDest = 10, Src_sel = 10, xfer=1 |
| R[2] ( R[3] | RegDest = 10, Src_sel = 11, xfer=1 |
| R[3] ( R[0] | RegDest = 11, Src_sel = 00, xfer=1 |
| R[3] ( R[1] | RegDest = 11, Src_sel = 01, xfer=1 |
| R[3] ( R[2] | RegDest = 11, Src_sel = 10, xfer=1 |
| R[3] ( R[3] | RegDest = 11, Src_sel = 11, xfer=1 |

- Controller (Moore Machine implementation)

Outputs are control signals to the datapath.