University of California at Berkeley

College of Engineering

Department of Electrical Engineering and Computer Science

EECS 150									R. H. Katz

Spring 2001

Homework Quiz # 0 (19 January)

Diagnostic Quiz—This Will NOT Be Graded!

## Name: __________________________________________      SID:________________

Consider the following schematic:

- Write down the Boolean equation for output C as a function of inputs A and B, expressed in terms of AND, OR, and NOT operations:

- Draw the Truth Table that describes the function C:

A     B       C

0      0

0      1

1      0

1      1

- Write down the simplest Boolean equation that describes the function C. (If you know the K-map method, you may use it). By “simplest” we mean the equation with the fewest AND, OR, and NOT operations:

- This circuit implements a well known and famous Boolean function. What is its name?