University of California at Berkeley

College of Engineering

Department of Electrical Engineering and Computer Science

EECS 150									R. H. Katz

Spring 2001

Homework Quiz # 6 (9 March)

## Name: __________________________________________      SID:________________

Consider a 3-bit counter that behaves as follows. The counter has a mode input M. When M is true, the counter counts in the sequence 0, 2, 4, 6, 1, 3, 5, 7, 0 and repeat. When M is false, the counter counts in the sequence 0, 1, 6, 7, 2, 3, 4, 5, 0 and repeat. The M input can change at anytime to cause the counter to change into either mode.

- Complete the Encoded STATE TRANSITION TABLE for this counter.

- Use the K-maps below to find the minimized two-level implementation of the counter’s next state functions.

Q2 =

Q1 =

Q0 =

# Text boxes

Q2    Q1    Q0

M

0

1

0

1

0

1

0

1

D0

0

0

1

1

0

0

1

1

D1

0

0

0

0

1

1

1

1

D2

0

0

0

0

0

0

0

0

D0

D2

Q2

Q2    Q1    Q0

M

0

1

0

1

0

1

0

1

D0

0

0

1

1

0

0

1

1

D0

D2

M

D2

1

1

1

1

1

1

1

1

Q1

D1

Q0

D1

M

D0

D2

D1

M

D1

0

0

0

0

1

1

1

1