University of California at Berkeley

College of Engineering

Department of Electrical Engineering and Computer Science

EECS 150									R. H. Katz

Spring 2007

Problem Set # 8 (Assigned 20 March, Due 6 April)

- Derive a table to show the coverage of various stuck-at-0 and stuck-at-1 faults by the eight possible input combinations. What is the minimum test set for this circuit?

| Test w1 w2 w3 | Fault Detection |
| --- | --- |
|  | a/0 | a/1 | b/0 | b/1 | c/0 | c/1 | d/0 | d/1 | f/0 | f/1 |
| 000 |  | x |  | x |  |  | x |  |  | x |
| 001 |  |  |  |  |  |  |  |  |  | x |
| 010 |  |  | x |  |  | x |  | x | x |  |
| 011 |  |  |  |  | x |  |  |  |  | x |
| 100 | x |  |  |  |  | x |  | x | x |  |
| 101 |  |  |  |  | x |  |  |  |  | x |
| 110 |  |  |  |  |  | x |  | x | x |  |
| 111 |  |  |  |  |  |  |  |  |  | x |

2.	In the following circuit, are all single stuck-at-0 and stuck-at-1 faults in the circuit detectable? If not, explain why?

No, for example on input [W1,W2,W3] = 001 F2 will be 0 if d is 0 or 1 so you cannot detect that error. This is just one example of how stuck at 0 and stuck at 1 faults can be undetectable.

3.  Given the following MEALY MACHINE State Transition Table, use the Implication Chart method to minimize the number of states. Draw the resulting minimized state diagram.

- Given your minimized state diagram for Problem 3, perform three alternative state assignments:

- Assign your states sequentially (e.g., A=0, B=1, C=2, …);

A = 00, B = 01, C/E = 10, D/F = 11

- Assign your states using a 1 Hot Encoding (e.g., A=001, B=010, C=100);

A = 0001, B = 0010, C/E = 0100, D/F = 1000

- Assign states using the heuristics presented in lecture.

A = 01, B = 10, C/E = 11, D/F = 00

- Implement your three assignments using K-maps. Which yields the best implementation and why?

Part (a) implementation:

Part (b) implementation:

Part (c) implementation:

Part (c) yields the simplest implementation

# Text boxes

d

c

b

a

f

d

c

a

b