## Slide 1: CS 152 Computer Architecture and Engineering Lecture 3 - From CISC to RISC
Krste Asanovic
Electrical Engineering and Computer Sciences
University of California at Berkeley
http://www.eecs.berkeley.edu/~krste
http://inst.eecs.berkeley.edu/~cs152

## Slide 2: Last Time in Lecture 2
ISA is the hardware/software interface
  Defines set of programmer visible state
  Defines instruction format (bit encoding) and instruction semantics
  Examples: IBM 360, MIPS, RISC-V, x86, JVM
Many possible implementations of one ISA
  360 implementations: model 30 (c. 1964), z12 (c. 2012)
  x86 implementations: 8086 (c. 1978), 80186, 286, 386, 486, Pentium, Pentium Pro, Pentium-4 (c. 2000), Core 2 Duo, Nehalem, Sandy Bridge, Ivy Bridge, Atom, AMD Athlon, Transmeta Crusoe, SoftPC
  MIPS implementations: R2000, R4000, R10000, R18K, …
  JVM: HotSpot, PicoJava, ARM Jazelle, …
Microcoding: straightforward methodical way to implement machines with low logic gate count and complex instructions

## Slide 3: “Iron Law” of Processor Performance
Instructions per program depends on source code, compiler technology, and ISA
Cycles per instructions (CPI) depends on ISA and µarchitecture
Time per cycle depends upon the µarchitecture and base technology
Time = Instructions Cycles Time
Program Program * Instruction * Cycle

## Slide 4: CPI for Microcoded Machine
Inst 3
7 cycles
Inst 1
Inst 2
5 cycles
10 cycles
Total clock cycles = 7+5+10 = 22
Total instructions = 3
CPI = 22/3 = 7.33
CPI is always an average over a large number of instructions.
Time

## Slide 5: Technology Influence
When microcode appeared in 50s, different technologies for:
  Logic: Vacuum Tubes
  Main Memory: Magnetic cores
  Read-Only Memory: Diode matrix, punched metal cards,…
Logic very expensive compared to ROM or RAM
ROM cheaper than RAM
ROM much faster than RAM
But seventies brought advances in integrated circuit technology and semiconductor memory…

## Slide 6: First Microprocessor Intel 4004, 1971
4-bit accumulator architecture
8µm pMOS
2,300 transistors
3 x 4 mm2
750kHz clock
8-16 cycles/inst.
Made possible by new integrated circuit technology

## Slide 7: Microprocessors in the Seventies
Initial target was embedded control
  First micro, 4-bit 4004 from Intel, designed for a desktop printing calculator
  Constrained by what could fit on single chip
  Accumulator architectures, similar to earliest computers
  Hardwired state machine control
8-bit micros (8085, 6800, 6502) used in hobbyist personal computers
  Micral, Altair, TRS-80, Apple-II
  Usually had 16-bit address space (up to 64KB directly addressable)
  Often came with simple BASIC language interpreter built into ROM or loaded from cassette tape.
7

## Slide 8: VisiCalc – the first “killer” app for micros
Microprocessors had little impact on conventional computer market until VisiCalc spreadsheet for Apple-II
Apple-II used Mostek 6502 microprocessor running at 1MHz
[ Personal Computing Ad, 1979 ]
Floppy disks were originally invented by IBM as a way of shipping IBM 360 microcode patches to customers!

## Slide 9: DRAM in the Seventies
Dramatic progress in semiconductor memory technology
1970, Intel introduces first DRAM, 1Kbit 1103
1979, Fujitsu introduces 64Kbit DRAM
=> By mid-Seventies, obvious that PCs would soon have >64KBytes physical memory
9

## Slide 10: Microprocessor Evolution
Rapid progress in 70s, fueled by advances in MOSFET technology and expanding markets
Intel i432
  Most ambitious seventies’ micro; started in 1975 - released 1981
  32-bit capability-based object-oriented architecture
  Instructions variable number of bits long
  Severe performance, complexity, and usability problems
Motorola 68000 (1979, 8MHz, 68,000 transistors)
  Heavily microcoded (and nanocoded)
  32-bit general-purpose register architecture (24 address pins)
  8 address registers, 8 data registers
Intel 8086 (1978, 8MHz, 29,000 transistors)
  “Stopgap” 16-bit processor, architected in 10 weeks
  Extended accumulator architecture, assembly-compatible with 8080
  20-bit addressing through segmented addressing scheme
10

## Slide 11: IBM PC, 1981
Hardware
  Team from IBM building PC prototypes in 1979
  Motorola 68000 chosen initially, but 68000 was late
  IBM builds “stopgap” prototypes using 8088 boards from Display Writer word processor
  8088 is 8-bit bus version of 8086 => allows cheaper system
  Estimated sales of 250,000
  100,000,000s sold
Software
  Microsoft negotiates to provide OS for IBM. Later buys and modifies QDOS from Seattle Computer Products.
Open System
  Standard processor, Intel 8088
  Standard interfaces
  Standard OS, MS-DOS
  IBM permits cloning and third-party software

## Slide 12
[ Personal Computing Ad, 11/81]

## Slide 13: Microprogramming: early Eighties
Evolution bred more complex micro-machines
  Complex instruction sets led to need for subroutine and call stacks in µcode
  Need for fixing bugs in control programs was in conflict with read-only nature of µROM
  Writable Control Store (WCS) (B1700, QMachine, Intel i432, …)
With the advent of VLSI technology assumptions about ROM & RAM speed became invalid more complexity
Better compilers made complex instructions less important.
Use of numerous micro-architectural innovations, e.g., pipelining, caches and buffers, made multiple-cycle execution of reg-reg instructions unattractive

## Slide 14: Analyzing Microcoded Machines
John Cocke and group at IBM
  Working on a simple pipelined processor, 801, and advanced compilers inside IBM
  Ported experimental PL.8 compiler to IBM 370, and only used simple register-register and load/store instructions similar to 801
  Code ran faster than other existing compilers that used all 370 instructions! (up to 6MIPS whereas 2MIPS considered good before)
Emer, Clark, at DEC
  Measured VAX-11/780 using external hardware
  Found it was actually a 0.5MIPS machine, although usually assumed to be a 1MIPS machine
  Found 20% of VAX instructions responsible for 60% of microcode, but only account for 0.2% of execution time!
VAX8800
  Control Store: 16K*147b RAM, Unified Cache: 64K*8b RAM
  4.5x more microstore RAM than cache RAM!

## Slide 15: IC Technology Changes Tradeoffs
Logic, RAM, ROM all implemented using MOS transistors
Semiconductor RAM ~ same speed as ROM

## Slide 16: Nanocoding
MC68000 had 17-bit µcode containing either 10-bit µjump or 9-bit nanoinstruction pointer
  Nanoinstructions were 68 bits wide, decoded to give 196 control signals
µcode ROM
nanoaddress
µcode
next-state
µaddress
PC (state)
nanoinstruction ROM
data
Exploits recurring control signal patterns in µcode, e.g.,
ALU0 A  Reg[rs1]
...
ALUi0 A  Reg[rs1]
...
User PC
Inst. Cache
Hardwired Decode
RISC

## Slide 17: From CISC to RISC
Use fast RAM to build fast instruction cache of user-visible instructions, not fixed hardware microroutines
  Contents of fast instruction memory change to fit what application needs right now
Use simple ISA to enable hardwired pipelined implementation
  Most compiled code only used a few of the available CISC instructions
  Simpler encoding allowed pipelined implementations
Further benefit with integration
  In early ‘80s, could finally fit 32-bit datapath + small caches on a single chip
  No chip crossings in common case allows faster operation

## Slide 18: Berkeley RISC Chips
RISC-I (1982) Contains 44,420 transistors, fabbed in 5 µm NMOS, with a die area of 77 mm2, ran at 1 MHz. This chip is probably the first VLSI RISC.
RISC-II (1983) contains 40,760 transistors, was fabbed in 3 µm NMOS, ran at 3 MHz, and the size is 60 mm2.
Stanford built some too…

## Slide 19: CS152 Administrivia
PS1 and Lab 1 available on website
  Due Thursday February 14 at start of class
Quiz 1 on Tuesday February 19 in class
Class moving to ETCHEVERRY 3108 starting Thursday!

## Slide 20: “Iron Law” of Processor Performance
Instructions per program depends on source code, compiler technology, and ISA
Cycles per instructions (CPI) depends on ISA and µarchitecture
Time per cycle depends upon the µarchitecture and base technology
Time = Instructions Cycles Time
Program Program * Instruction * Cycle
Microarchitecture | CPI | cycle time
Microcoded | >1 | short
Single-cycle unpipelined | 1 | long
Pipelined | 1 | short
This lecture

## Slide 21: Hardware Elements
Combinational circuits
  Mux, Decoder, ALU, ...
Synchronous state elements
  Flipflop, Register, Register file, SRAM, DRAM
Edge-triggered: Data is sampled at the rising edge
Clk
D
Q
En
ff
Q
D
Clk
En
OpSelect
- Add, Sub, ...
- And, Or, Xor, Not, ...
- GT, LT, EQ, Zero, ...
Result
Comp?
A
B
ALU
Sel
O
A0
A1
An-1
Mux
.
.
.
lg(n)
A
Decoder
.
.
.
O0
O1
On-1
lg(n)

## Slide 22: Register Files
Reads are combinational
ReadData1
ReadSel1
ReadSel2
WriteSel
Register
file
2R+1W
ReadData2
WriteData
WE
Clock
rd1
rs1
rs2
ws
wd
rd2
we
ff
Q0
D0
Clk
En
ff
Q1
D1
ff
Q2
D2
ff
Qn-1
Dn-1
...
...
...
register

## Slide 23: Register File Implementation
RISC-V integer instructions have at most 2 register source operands
reg 31
rd
clk
reg 1
wdata
we
rs1
rdata1
rdata2
reg 0
…
32
…
5
32
32
…
rs2
5
5

## Slide 24: A Simple Memory Model
MAGIC
RAM
ReadData
WriteData
Address
WriteEnable
Clock
Reads and writes are always completed in one cycle
  a Read can be done any time (i.e. combinational)
  a Write is performed at the rising clock edge
  if it is enabled
   the write address and data
  must be stable at the clock edge
Later in the course we will present a more realistic model of memory

## Slide 25: Implementing RISC-V
Single-cycle per instruction datapath & control logic (Should be review of CS61C)

## Slide 26: Instruction Execution
Execution of an instruction involves
Instruction fetch
Decode and register fetch
ALU operation
Memory operation (optional)
Write back (optional)
and compute address of next instruction

## Slide 27: Datapath: Reg-Reg ALU Instructions
RegWrite Timing?
5 5 5 10 7
rd rs1 rs2 func opcode rd  (rs1) func (rs2)
31 27 26 22 21 17 16 7 6 0
0x4
Add
clk
addr
inst
Inst.
Memory
PC
Inst<26:22>
Inst<21:17>
Inst<31:27>
Inst<16:0>
OpCode
ALU
ALU
Control
RegWriteEn
clk
rd1
GPRs
rs1
rs2
wa
wd
rd2
we

## Slide 28: Datapath: Reg-Imm ALU Instructions
5 5 12 3 7
rd rs1 immediate12 func opcode rd  (rs1) op immediate
31 27 26 22 21 10 9 7 6 0
Imm
Select
ImmSel
inst<21:10>
OpCode
0x4
Add
clk
addr
inst
Inst.
Memory
PC
ALU
RegWriteEn
clk
rd1
GPRs
rs1
rs2
wa
wd
rd2
we
inst<26:22>
inst<31:27>
inst<9:0>
ALU
Control

## Slide 29: Conflicts in Merging Datapath
Imm
Select
ImmSel
OpCode
0x4
Add
clk
addr
inst
Inst.
Memory
PC
ALU
RegWrite
clk
rd1
GPRs
rs1
rs2
wa
wd
rd2
we
inst<26:22>
Inst<31:27>
Inst<21:10>
Inst<16:0>
ALU
Control
Inst<9:0>
Introduce
muxes
rd rs1 immediate12 func3 opcode rd  (rs1) op immediate
5 5 5 10 7
rd rs1 rs2 func10 opcode rd  (rs1) func (rs2)
Inst<21:17>

## Slide 30: Datapath for ALU Instructions
<16:0>
rd rs1 immediate12 func3 opcode rd  (rs1) op immediate
5 5 5 10 7
rd rs1 rs2 func10 opcode rd  (rs1) func (rs2)
Op2Sel
Reg / Imm
Imm
Select
ImmSel
OpCode
0x4
Add
clk
addr
inst
Inst.
Memory
PC
ALU
RegWriteEn
clk
rd1
GPRs
rs1
rs2
wa
wd
rd2
we
<26:22>
<21:17>
FuncSel
ALU
Control
<31:27>
<6:0>

## Slide 31: Load/Store Instructions
WBSel
ALU / Mem
rs1 is the base register
rd is the destination of a Load, rs2 is the data source for a Store
Op2Sel
“base”
disp
ImmSel
OpCode
FuncSel
ALU
Control
ALU
0x4
Add
clk
addr
inst
Inst.
Memory
PC
RegWriteEn
clk
rd1
GPRs
rs1
rs2
wa
wd
rd2
we
Imm
Select
clk
MemWrite
addr
wdata
rdata
Data
Memory
we
rd rs1 immediate12 func3 opcode Load
5 5 5 7 3 7 Addressing Mode
imm rs1 rs2 imm func3 opcode Store (rs) + displacement

## Slide 32: RISC-V Conditional Branches
Compare two integer registers for equality (BEQ/BNE) or signed magnitude (BLT/BGE) or unsigned magnitude (BLTU/BGEU)
12-bit immediate encodes branch target address as a signed offset from PC, in units of 16-bits (i.e., shift left by 1 then add to PC).
7
6
0
opcode
3
9
7
func3
7
16
10
imm[6:0]
5
21
17
rs2
5
26
22
rs1
5
31
27
imm[11:7]
BEQ/BNE
BLT/BGE
BLTU/BGEU

## Slide 33: Conditional Branches (BEQ/BNE/BLT/BGE/BLTU/BGEU)
0x4
Add
PCSel
clk
WBSel
MemWrite
addr
wdata
rdata
Data
Memory
we
Op2Sel
ImmSel
OpCode
Bcomp?
FuncSel
clk
clk
addr
inst
Inst.
Memory
PC
rd1
GPRs
rs1
rs2
wa
wd
rd2
we
Imm
Select
ALU
ALU
Control
Add
br
pc+4
RegWrEn
Br Logic

## Slide 34: RISC-V Unconditional Jumps
25-bit immediate encodes jump target address as a signed offset from PC, in units of 16-bits (i.e., shift left by 1 then add to PC). (+/- 16MB)
JAL is a subroutine call that also saves return address (PC+4) in register x1
J
JAL
7
6
0
opcode
25
31
7
Jump Offset[24:0]

## Slide 35: RISC-V Register Indirect Jumps
Jumps to target address given by adding 12-bit offset (not shifted by 1 bit) to register rs1
The return address (PC+4) is written to rd (can be x0 if value not needed)
The RDNPC instruction simply writes return address to register rd without jumping (used for dynamic linking)
7
6
0
opcode
3
9
7
func3
12
21
10
Imm[11:0]
5
26
22
rs1
JALR
RDNPC
5
31
27
rd

## Slide 36: Full RISCV1Stage Datapath (Lab1)

## Slide 37: Hardwired Control is pure Combinational Logic
combinational
logic
op code
Equal?
ImmSel
Op2Sel
FuncSel
MemWrite
WBSel
WASel
RegWriteEn
PCSel

## Slide 38: ALU Control & Immediate Extension
Inst<6:0> (Opcode)
Decode Map
Inst<16:7> (Func)
ALUop
0?
+
FuncSel
( Func, Op, +, 0? )
ImmSel
( IType12, BsType12,
BrType12)

## Slide 39: Hardwired Control Table
Opcode | ImmSel | Op2Sel | FuncSel | MemWr | RFWen | WBSel | WASel | PCSel
ALU |  |  |  |  |  |  |  | 
ALUi |  |  |  |  |  |  |  | 
LW |  |  |  |  |  |  |  | 
SW |  |  |  |  |  |  |  | 
BEQtrue |  |  |  |  |  |  |  | 
BEQfalse |  |  |  |  |  |  |  | 
J |  |  |  |  |  |  |  | 
JAL |  |  |  |  |  |  |  | 
JALR |  |  |  |  |  |  |  | 
Op2Sel= Reg / Imm WBSel = ALU / Mem / PC
WASel = rd / X1 PCSel = pc+4 / br / rind / jabs
*
*
*
no
yes
rind
PC
rd
jabs
*
*
*
no
yes
PC
X1
jabs
*
*
*
no
no
*
*
pc+4
BrType12
*
*
no
no
*
*
br
BrType12
*
*
no
no
*
*
pc+4
BsType12
Imm
+
yes
no
*
*
pc+4
*
Reg
Func
no
yes
ALU
rd
IType12
Imm
Op
pc+4
no
yes
ALU
rd
pc+4
IType12
Imm
+
no
yes
Mem
rd

## Slide 40: Single-Cycle Hardwired Control
We will assume clock period is sufficiently long for all of the following steps to be “completed”:
Instruction fetch
Decode and register fetch
ALU operation
Data fetch if required
Register write-back setup time
 tC > tIFetch + tRFetch + tALU+ tDMem+ tRWB
At the rising edge of the following clock, the PC, register file and memory are updated

## Slide 41: Summary
Microcoding became less attractive as gap between RAM and ROM speeds reduced, and logic implemented in same technology as memory
Complex instruction sets difficult to pipeline, so difficult to increase performance as gate count grew
Iron Law explains architecture design space
  Trade instruction/program, cycles/instruction, and time/cycle
Load-Store RISC ISAs designed for efficient pipelined implementations
  Very similar to vertical microcode
  Inspired by earlier Cray machines (CDC 6600/7600)
RISC-V ISA will be used in lectures, problems, and labs
  Berkeley RISC chips: RISC-I, RISC-II, SOAR (RISC-III), SPUR (RISC-IV)

## Slide 42: Acknowledgements
These slides contain material developed and copyright by:
  Arvind (MIT)
  Krste Asanovic (MIT/UCB)
  Joel Emer (Intel/MIT)
  James Hoe (CMU)
  John Kubiatowicz (UCB)
  David Patterson (UCB)
MIT material derived from course 6.823
UCB material derived from course CS252