## Slide 1: CS 152 Computer Architecture and Engineering Lecture 5 - Pipelining II (Branches, Exceptions)
Krste Asanovic
Electrical Engineering and Computer Sciences
University of California at Berkeley
http://www.eecs.berkeley.edu/~krste
http://inst.eecs.berkeley.edu/~cs152

## Slide 2: Last time in Lecture 4
Pipelining increases clock frequency, while growing CPI more slowly, hence giving greater performance
Pipelining of instructions is complicated by HAZARDS:
  Structural hazards (two instructions want same hardware resource)
  Data hazards (earlier instruction produces value needed by later instruction)
  Control hazards (instruction changes control flow, e.g., branches or exceptions)
Techniques to handle hazards:
  Interlock (hold newer instruction until older instructions drain out of pipeline and write back results)
  Bypass (transfer value from older instruction to newer instruction as soon as available somewhere in machine)
  Speculate (guess effect of earlier instruction)
Time = Instructions Cycles Time
Program Program * Instruction * Cycle
Reduces because fewer logic gates on critical paths between flip-flops
Increases because of pipeline bubbles

## Slide 3: Control Hazards
What do we need to calculate next PC?
For Jumps
  Opcode, PC and offset
For Jump Register
  Opcode, Register value, and PC
For Conditional Branches
  Opcode, Register (for condition), PC and offset
For all other instructions
  Opcode and PC ( and have to know it’s not one of above )

## Slide 4: PC Calculation Bubbles
      time
      t0 t1 t2 t3 t4 t5 t6 t7 . . . .
(I1) x1 x0 + 10 IF1 ID1 EX1 MA1 WB1
(I2) x3 x2 + 17 IF2 IF2 ID2 EX2 MA2 WB2
(I3) IF3 IF3 ID3 EX3 MA3 WB3
(I4) IF4 IF4 ID4 EX4 MA4 WB4
  time
  t0 t1 t2 t3 t4 t5 t6 t7 . . . .
IF I1 - I2 - I3 - I4
ID I1 - I2 - I3 - I4
EX I1 - I2 - I3 - I4
MA I1 - I2 - I3 - I4
WB I1 - I2 - I3 - I4
Resource
Usage
-  pipeline bubble

## Slide 5: Speculate next address is PC+4
I1 096 ADD
I2 100 J 304
I3 104 ADD
I4 304 ADD
kill
A jump instruction kills (not stalls)
the following instruction
stall
How?
I2
I1
104
IR
IR
PC
addr
inst
Inst
Memory
0x4
Add
bubble
IR
E
M
Add
Jump?
PCSrc (pc+4 / jabs / rind/ br)
PC

## Slide 6: Pipelining Jumps
I1 096 ADD
I2 100 J 304
I3 104 ADD
I4 304 ADD
kill
I2
I1
104
stall
IR
IR
PC
addr
inst
Inst
Memory
0x4
Add
bubble
IR
E
M
Add
Jump?
PCSrc (pc+4 / jabs / rind/ br)
IRSrcD = Case opcodeD
  J, JAL bubble
  ... IM
To kill a fetched instruction -- Insert a mux before IR
Any interaction between stall and jump?
bubble
IRSrcD
I2
I1
304
bubble
PC
Notes: Kill takes precedence over stall.

## Slide 7: Jump Pipeline Diagrams
  time
  t0 t1 t2 t3 t4 t5 t6 t7 . . . .
IF I1 I2 I3 I4 I5
ID I1 I2 - I4 I5
EX I1 I2 - I4 I5
MA I1 I2 - I4 I5
WB I1 I2 - I4 I5
      time
      t0 t1 t2 t3 t4 t5 t6 t7 . . . .
(I1) 096: ADD IF1 ID1 EX1 MA1 WB1
(I2) 100: J 304 IF2 ID2 EX2 MA2 WB2
(I3) 104: ADD IF3 - - - -
(I4) 304: ADD IF4 ID4 EX4 MA4 WB4
Resource
Usage
-  pipeline bubble

## Slide 8: Pipelining Conditional Branches
I1 096 ADD
I2 100 BEQ x1,x2 +200
I3 104 ADD
I4 300 ADD
BEQ?
I2
I1
104
stall
IR
IR
PC
addr
inst
Inst
Memory
0x4
Add
bubble
IR
E
M
PCSrc (pc+4 / jabs / rind / br)
bubble
IRSrcD
Branch condition is not known until the execute stage
  what action should be taken in the
  decode stage ?
A
Y
ALU
Taken?

## Slide 9: Pipelining Conditional Branches
I1 096 ADD
I2 100 BEQ x1,x2 +200
I3 104 ADD
I4 300 ADD
stall
IR
IR
PC
addr
inst
Inst
Memory
0x4
Add
bubble
IR
E
M
PCSrc (pc+4 / jabs / rind / br)
bubble
IRSrcD
A
Y
ALU
Taken?
If the branch is taken
  - kill the two following instructions
  - the instruction at the decode stage is not valid  stall signal is not valid
I2
I1
108
I3
Bcond?
?

## Slide 10: Pipelining Conditional Branches
I1: 096 ADD
I2: 100 BEQ x1,x2 +200
I3: 104 ADD
I4: 300 ADD
stall
IR
IR
PC
addr
inst
Inst
Memory
0x4
Add
bubble
IR
E
M
PCSrc (pc+4/jabs/rind/br)
bubble
A
Y
ALU
Taken?
I2
I1
108
I3
Bcond?
Jump?
IRSrcD
IRSrcE
If the branch is taken
  - kill the two following instructions
  - the instruction at the decode stage is not valid  stall signal is not valid
Add
PC
PC

## Slide 11: Branch Pipeline Diagrams (resolved in execute stage)
  time
  t0 t1 t2 t3 t4 t5 t6 t7 . . . .
IF I1 I2 I3 I4 I5
ID I1 I2 I3 - I5
EX I1 I2 - - I5
MA I1 I2 - - I5
WB I1 I2 - - I5
      time
      t0 t1 t2 t3 t4 t5 t6 t7 . . . .
(I1) 096: ADD IF1 ID1 EX1 MA1 WB1
(I2) 100: BEQ +200 IF2 ID2 EX2 MA2 WB2
(I3) 104: ADD IF3 ID3 - - -
(I4) 108: IF4 - - - -
(I5) 300: ADD IF5 ID5 EX5 MA5 WB5
Resource
Usage
-  pipeline bubble

## Slide 12: Use simpler branches (e.g., only compare one reg against zero) with compare in decode stage
  time
  t0 t1 t2 t3 t4 t5 t6 t7 . . . .
IF I1 I2 I3 I4 I5
ID I1 I2 - I4 I5
EX I1 I2 - I4 I5
MA I1 I2 - I4 I5
WB I1 I2 - I4 I5
      time
      t0 t1 t2 t3 t4 t5 t6 t7 . . . .
(I1) 096: ADD IF1 ID1 EX1 MA1 WB1
(I2) 100: BEQZ +200 IF2 ID2 EX2 MA2 WB2
(I3) 104: ADD IF3 - - - -
(I4) 300: ADD IF4 ID4 EX4 MA4 WB4
Resource
Usage
-  pipeline bubble

## Slide 13: Branch Delay Slots (expose control hazard to software)
Change the ISA semantics so that the instruction that follows a jump or branch is always executed
  gives compiler the flexibility to put in a useful instruction where normally a pipeline bubble would have resulted.
I1 096 ADD
I2 100 BEQZ r1, +200
I3 104 ADD
I4 300 ADD
Delay slot instruction executed regardless of branch outcome

## Slide 14: Branch Pipeline Diagrams (branch delay slot)
  time
  t0 t1 t2 t3 t4 t5 t6 t7 . . . .
IF I1 I2 I3 I4
ID I1 I2 I3 I4
EX I1 I2 I3 I4
MA I1 I2 I3 I4
WB I1 I2 I3 I4
      time
      t0 t1 t2 t3 t4 t5 t6 t7 . . . .
(I1) 096: ADD IF1 ID1 EX1 MA1 WB1
(I2) 100: BEQZ +200 IF2 ID2 EX2 MA2 WB2
(I3) 104: ADD IF3 ID3 EX3 MA3 WB3
(I4) 300: ADD IF4 ID4 EX4 MA4 WB4
Resource
Usage

## Slide 15: Post-1990 RISC ISAs don’t have delay slots
Encodes microarchitectural detail into ISA
  C.f. IBM 650 drum layout
Performance issues
  E.g., I-cache miss on delay slot causes machine to wait, even if delay slot is a NOP
Complicates more advanced microarchitectures
  30-stage pipeline with four-instruction-per-cycle issue
Better branch prediction reduced need

## Slide 16: Why an Instruction may not be dispatched every cycle (CPI>1)
Full bypassing may be too expensive to implement
  typically all frequently used paths are provided
  some infrequently used bypass paths may increase cycle time and counteract the benefit of reducing CPI
Loads have two-cycle latency
  Instruction after load cannot use load result
  MIPS-I ISA defined load delay slots, a software-visible pipeline hazard (compiler schedules independent instruction or inserts NOP to avoid hazard). Removed in MIPS-II (pipeline interlocks added in hardware)
    MIPS:“Microprocessor without Interlocked Pipeline Stages”
Conditional branches may cause bubbles
  kill following instruction(s) if no delay slots
Machines with software-visible delay slots may execute significant number of NOP instructions inserted by the compiler. NOPs increase instructions/program!

## Slide 17: RISC-V Branches and Jumps
Instruction Taken known? Target known?
J
JR
B<cond.>
Each instruction fetch depends on one or two pieces of information from the preceding instruction:
1) Is the preceding instruction a taken branch?
2) If so, what is the target address?
After Inst. Decode
After Inst. Decode
After Inst. Decode
After Inst. Decode
After Reg. Fetch
After Execute

## Slide 18: Branch Penalties in Modern Pipelines
A
PC Generation/Mux
P
Instruction Fetch Stage 1
F
Instruction Fetch Stage 2
B
Branch Address Calc/Begin Decode
I
Complete Decode
J
Steer Instructions to Functional units
R
Register File Read
E
Integer Execute
Remainder of execute pipeline
(+ another 6 stages)
UltraSPARC-III instruction fetch pipeline stages
(in-order issue, 4-way superscalar, 750MHz, 2000)
Branch Target Address Known
Branch Direction &
Jump Register Target Known

## Slide 19: Reducing Control Flow Penalty
Software solutions
  Eliminate branches - loop unrolling
    Increases the run length
  Reduce resolution time - instruction scheduling
    Compute the branch condition as early as possible (of limited value because branches often in critical path through code)
Hardware solutions
  Find something else to do - delay slots
    Replaces pipeline bubbles with useful work (requires software cooperation)
  Speculate - branch prediction
    Speculative execution of instructions beyond the branch
Notes: Like using compiler to avoid WAW hazards, one can use compiler to reduce control flow penalty.

## Slide 20: Branch Prediction
Motivation:
  Branch penalties limit performance of deeply pipelined processors
  Modern branch predictors have high accuracy
  (>95%) and can reduce branch penalties significantly
Required hardware support:
  Prediction structures:
    Branch history tables, branch target buffers, etc.
  Mispredict recovery mechanisms:
    Keep result computation separate from commit
    Kill instructions following branch in pipeline
    Restore state to that following branch

## Slide 21: Static Branch Prediction
Overall probability a branch is taken is ~60-70% but:
ISA can attach preferred direction semantics to branches, e.g., Motorola MC88110
  bne0 (preferred taken) beq0 (not taken)
ISA can allow arbitrary choice of statically predicted direction, e.g., HP PA-RISC, Intel IA-64 typically reported as ~80% accurate
backward
90%
forward
50%

## Slide 22: Dynamic Branch Prediction learning based on past behavior
Temporal correlation
  The way a branch resolves may be a good predictor of the way it will resolve at the next execution
Spatial correlation
  Several branches may resolve in a highly correlated manner (a preferred path of execution)

## Slide 23: Branch Prediction Bits
Assume 2 BP bits per instruction
Change the prediction after two consecutive mistakes!
¬take
wrong
taken
¬ taken
taken
taken
taken
¬take
right
take
right
take
wrong
¬ taken
¬ taken
¬ taken
BP state:
(predict take/¬take) x (last prediction right/wrong)

## Slide 24: Branch History Table
4K-entry BHT, 2 bits/entry, ~80-90% correct predictions
0
0
Fetch PC
Branch?
Target PC
+
I-Cache
Opcode
offset
Instruction
k
BHT Index
2k-entry
BHT,
2 bits/entry
Taken/¬Taken?

## Slide 25: Exploiting Spatial Correlation Yeh and Patt, 1992
History register, H, records the direction of the last N branches executed by the processor
if (x[i] < 7) then
y += 1;
if (x[i] < 5) then
c -= 4;
If first condition false, second condition also false

## Slide 26: Two-Level Branch Predictor
Pentium Pro uses the result from the last two branches
to select one of the four sets of BHT bits (~95% correct)
0
0
k
Fetch PC
Shift in Taken/¬Taken results of each branch
2-bit global branch history shift register
Taken/¬Taken?

## Slide 27: Speculating Both Directions
An alternative to branch prediction is to execute both directions of a branch speculatively
  resource requirement is proportional to the number of concurrent speculative executions
  only half the resources engage in useful work when both directions of a branch are executed speculatively
  branch prediction takes less resources than speculative execution of both paths
With accurate branch prediction, it is more cost effective to dedicate all resources to the predicted direction!

## Slide 28: Limitations of BHTs
Only predicts branch direction. Therefore, cannot redirect fetch stream until after branch target is determined.
UltraSPARC-III fetch pipeline
Correctly predicted
taken branch penalty
Jump Register penalty
A
PC Generation/Mux
P
Instruction Fetch Stage 1
F
Instruction Fetch Stage 2
B
Branch Address Calc/Begin Decode
I
Complete Decode
J
Steer Instructions to Functional units
R
Register File Read
E
Integer Execute
Remainder of execute pipeline
(+ another 6 stages)

## Slide 29: CS152 Administrivia
Quiz 1 on Feb 19 will cover PS1, Lab1, lectures 1-5, and associated readings.

## Slide 30: Branch Target Buffer
BP bits are stored with the predicted target address.
IF stage: If (BP=taken) then nPC=target else nPC=PC+4
Later: check prediction, if wrong then kill the instruction and update BTB & BPb else update BPb
IMEM
PC
Branch
Target
Buffer
(2k entries)
k
BPb
predicted
target
BP
target

## Slide 31: Address Collisions
What will be fetched after the instruction at 1028?
BTB prediction =
Correct target =

Assume a
128-entry
BTB
BPb
target
take
236
1028 Add .....
132 Jump +104
Instruction
Memory
236
1032
kill PC=236 and fetch PC=1032
Is this a common occurrence?
Can we avoid these bubbles?

## Slide 32: BTB is only for Control Instructions
BTB contains useful information for branch and jump instructions only
 Do not update it for other instructions
For all other instructions the next PC is PC+4 !
How to achieve this effect without decoding the instruction?

## Slide 33: Branch Target Buffer (BTB)
Keep both the branch PC and target PC in the BTB
PC+4 is fetched if match fails
Only taken branches and jumps held in BTB
Next PC determined before branch fetched and decoded
2k-entry direct-mapped BTB
(can also be associative)
I-Cache
PC
k
Valid
valid
Entry PC
=
match
predicted
target
target PC

## Slide 34: Combining BTB and BHT
BTB entries are considerably more expensive than BHT, but can redirect fetches at earlier stage in pipeline and can accelerate indirect branches (JR)
BHT can hold many more entries and is more accurate
A
PC Generation/Mux
P
Instruction Fetch Stage 1
F
Instruction Fetch Stage 2
B
Branch Address Calc/Begin Decode
I
Complete Decode
J
Steer Instructions to Functional units
R
Register File Read
E
Integer Execute
BTB
BHT
BHT in later pipeline stage corrects when BTB misses a predicted taken branch
BTB/BHT only updated after branch resolves in E stage

## Slide 35: Uses of Jump Register (JR)
Switch statements (jump to address of matching case)
Dynamic function call (jump to run-time function address)
Subroutine returns (jump to return address)
How well does BTB work for each of these cases?
BTB works well if same case used repeatedly
BTB works well if same function usually called, (e.g., in C++ programming, when objects have same type in virtual function call)
BTB works well if usually return to the same place
 Often one function called from many distinct call sites!

## Slide 36: Subroutine Return Stack
Small structure to accelerate JR for subroutine returns, typically much more accurate than BTBs.
&fb()
&fc()
Push call address when function call executed
Pop return address when subroutine return decoded
fa() { fb(); }
fb() { fc(); }
fc() { fd(); }
&fd()
k entries
(typically k=8-16)

## Slide 37: Interrupts: altering the normal flow of control
Ii-1
HI1
HI2
HIn
Ii
Ii+1
program
interrupt
handler
An external or internal event that needs to be processed by another (system) program. The event is usually unexpected or rare from program’s point of view.

## Slide 38: Causes of Interrupts
Asynchronous: an external event
  input/output device service-request
  timer expiration
  power disruptions, hardware failure
Synchronous: an internal event (a.k.a. traps or exceptions)
  undefined opcode, privileged instruction
  arithmetic overflow, FPU exception
  misaligned memory access
  virtual memory exceptions: page faults, TLB misses, protection violations
  system calls, e.g., jumps into kernel
Interrupt: an event that requests the attention of the processor

## Slide 39: History of Exception Handling
First system with exceptions was Univac-I, 1951
  Arithmetic overflow would either
    1. trigger the execution a two-instruction fix-up routine at address 0, or
    2. at the programmer's option, cause the computer to stop
  Later Univac 1103, 1955, modified to add external interrupts
    Used to gather real-time wind tunnel data
First system with I/O interrupts was DYSEAC, 1954
  Had two program counters, and I/O signal caused switch between two PCs
  Also, first system with DMA (direct memory access by I/O device)
[Courtesy Mark Smotherman]

## Slide 40: DYSEAC, first mobile computer!
Carried in two tractor trailers, 12 tons + 8 tons
Built for US Army Signal Corps
[Courtesy Mark Smotherman]

## Slide 41: Asynchronous Interrupts: invoking the interrupt handler
An I/O device requests attention by asserting one of the prioritized interrupt request lines
When the processor decides to process the interrupt
  It stops the current program at instruction Ii, completing all the instructions up to Ii-1 (precise interrupt)
  It saves the PC of instruction Ii in a special register (EPC)
  It disables interrupts and transfers control to a designated interrupt handler running in the kernel mode

## Slide 42: Interrupt Handler
Saves EPC before enabling interrupts to allow nested interrupts 
  need an instruction to move EPC into GPRs
  need a way to mask further interrupts at least until EPC can be saved
Needs to read a status register that indicates the cause of the interrupt
Uses a special indirect jump instruction RFE (return-from-exception) which
  enables interrupts
  restores the processor to the user mode
  restores hardware status and control state

## Slide 43: Synchronous Interrupts
A synchronous interrupt (exception) is caused by a particular instruction
In general, the instruction cannot be completed and needs to be restarted after the exception has been handled
  requires undoing the effect of one or more partially executed instructions
In the case of a system call trap, the instruction is considered to have been completed
  a special jump instruction involving a change to privileged kernel mode

## Slide 44: Exception Handling 5-Stage Pipeline
How to handle multiple simultaneous exceptions in different pipeline stages?
How and where to handle external asynchronous interrupts?
PC
Inst. Mem
D
Decode
E
M
Data Mem
W
+
Illegal Opcode
Overflow
Data address Exceptions
PC address Exception
Asynchronous Interrupts

## Slide 45: Exception Handling 5-Stage Pipeline
PC
Inst. Mem
D
Decode
E
M
Data Mem
W
+
Illegal Opcode
Overflow
Data address Exceptions
PC address Exception
Asynchronous
Interrupts
Exc
D
PC
D
Exc
E
PC
E
Exc
M
PC
M
Cause
EPC
Kill D Stage
Kill F Stage
Kill E Stage
Select Handler PC
Kill Writeback
Commit Point

## Slide 46: Exception Handling 5-Stage Pipeline
Hold exception flags in pipeline until commit point (M stage)
Exceptions in earlier pipe stages override later exceptions for a given instruction
Inject external interrupts at commit point (override others)
If exception at commit: update Cause and EPC registers, kill all stages, inject handler PC into fetch stage

## Slide 47: Speculating on Exceptions
Prediction mechanism
  Exceptions are rare, so simply predicting no exceptions is very accurate!
Check prediction mechanism
  Exceptions detected at end of instruction execution pipeline, special hardware for various exception types
Recovery mechanism
  Only write architectural state at commit point, so can throw away partially executed instructions after exception
  Launch exception handler after flushing pipeline
Bypassing allows use of uncommitted instruction results by following instructions

## Slide 48: Exception Pipeline Diagram
  time
  t0 t1 t2 t3 t4 t5 t6 t7 . . . .
IF I1 I2 I3 I4 I5
ID I1 I2 I3 - I5
EX I1 I2 - - I5
MA I1 - - - I5
WB - - - - I5
      time
      t0 t1 t2 t3 t4 t5 t6 t7 . . . .
(I1) 096: ADD IF1 ID1 EX1 MA1 - overflow!
(I2) 100: XOR IF2 ID2 EX2 - -
(I3) 104: SUB IF3 ID3 - - -
(I4) 108: ADD IF4 - - - -
(I5) Exc. Handler code IF5 ID5 EX5 MA5 WB5
Resource
Usage

## Slide 49: Acknowledgements
These slides contain material developed and copyright by:
  Arvind (MIT)
  Krste Asanovic (MIT/UCB)
  Joel Emer (Intel/MIT)
  James Hoe (CMU)
  John Kubiatowicz (UCB)
  David Patterson (UCB)
MIT material derived from course 6.823
UCB material derived from course CS252