## Slide 1: CS 152 Computer Architecture and Engineering Lecture 19: Directory-Based Cache Protocols
Krste Asanovic
Electrical Engineering and Computer Sciences
University of California, Berkeley
http://www.eecs.berkeley.edu/~krste
http://inst.cs.berkeley.edu/~cs152

## Slide 2: Recap: Snoopy Cache Protocols
Use snoopy mechanism to keep all processors’ view of memory coherent
M1
M2
M3
Snoopy
Cache
DMA
Physical
Memory
Memory
Bus
Snoopy
Cache
Snoopy
Cache
DISKS

## Slide 3: Recap: MESI: An Enhanced MSI protocol increased performance for private data
M
E
S
I
M: Modified Exclusive
E: Exclusive but unmodified
S: Shared
I: Invalid
Each cache line has a tag
Address tag
state
bits
Write miss
Other processor
intent to write
Read miss,
shared
Other processor
intent to write
P1 write
Read by any
processor
Other processor reads
P1 writes back
P1 read
P1 write
or read
Cache state in processor P1
P1 intent to write
Read miss, not shared
Other processor
reads
Other processor intent to write, P1 writes back

## Slide 4: Performance of Symmetric Shared-Memory Multiprocessors
Cache performance is combination of:
Uniprocessor cache miss traffic
Traffic caused by communication
  Results in invalidations and subsequent cache misses
Coherence misses
  Sometimes called a Communication miss
  4th C of cache misses along with Compulsory, Capacity, & Conflict.

## Slide 5: Coherency Misses
True sharing misses arise from the communication of data through the cache coherence mechanism
  Invalidates due to 1st write to shared line
  Reads by another CPU of modified line in different cache
  Miss would still occur if line size were 1 word
False sharing misses when a line is invalidated because some word in the line, other than the one being read, is written into
  Invalidation does not cause a new value to be communicated, but only causes an extra cache miss
  Line is shared, but no word in line is actually shared  miss would not occur if line size were 1 word

## Slide 6: Example: True v. False Sharing v. Hit?
Time | P1 | P2 | True, False, Hit? Why?
1 | Write x1 |  | 
2 |  | Read x2 | 
3 | Write x1 |  | 
4 |  | Write x2 | 
5 | Read x2 |  | 
Assume x1 and x2 in same cache line. P1 and P2 both read x1 and x2 before.
True miss; invalidate x1 in P2
False miss; x1 irrelevant to P2
False miss; x1 irrelevant to P2
True miss; x2 not writeable
True miss; invalidate x2 in P1

## Slide 7: MP Performance 4 Processor Commercial Workload: OLTP, Decision Support (Database), Search Engine
Uniprocessor cache misses improve with cache size increase (Instruction, Capacity/Conflict, Compulsory)
True sharing and false sharing unchanged going from 1 MB to 8 MB (L3 cache)

## Slide 8: MP Performance 2MB Cache Commercial Workload: OLTP, Decision Support (Database), Search Engine
True sharing, false sharing increase going from 1 to 8 CPUs

## Slide 9: Scaling Snoopy/Broadcast Coherence
When any processor gets a miss, must probe every other cache
Scaling up to more processors limited by:
  Communication bandwidth over bus
  Snoop bandwidth into tags
Can improve bandwidth by using multiple interleaved buses with interleaved tag banks
  E.g, two bits of address pick which of four buses and four tag banks to use – (e.g., bits 7:6 of address pick bus/tag bank, bits 5:0 pick byte in 64-byte line)
Buses don’t scale to large number of connections, so can use point-to-point network for larger number of nodes, but then limited by tag bandwidth when broadcasting snoop requests.
Insight: Most snoops fail to find a match!

## Slide 10: Scalable Approach: Directories
Every memory line has associated directory information
  keeps track of copies of cached lines and their states
  on a miss, find directory entry, look it up, and communicate only with the nodes that have copies if necessary
  in scalable networks, communication with directory and copies is through network transactions
Many alternatives for organizing directory information

## Slide 11: Directory Cache Protocol (Lab 5 Handout)
Assumptions: Reliable network, FIFO message delivery between any given source-destination pair
CPU
Cache
Interconnection Network
Directory Controller
DRAM Bank
Directory Controller
DRAM Bank
CPU
Cache
CPU
Cache
CPU
Cache
CPU
Cache
CPU
Cache
Directory Controller
DRAM Bank
Directory Controller
DRAM Bank
Data
Tag
Stat.
Each line in cache has state field plus tag
Data
Stat.
Directry
Each line in memory has state field plus bit vector directory with one bit per processor
Notes: Delay is a fact of life
Serialization by directory, no longer the bus
SC not guarantied

## Slide 12: Cache States
For each cache line, there are 4 possible states:
  C-invalid (= Nothing): The accessed data is not resident in the cache.
  C-shared (= Sh): The accessed data is resident in the cache, and possibly also cached at other sites. The data in memory is valid.
  C-modified (= Ex): The accessed data is exclusively resident in this cache, and has been modified. Memory does not have the most up-to-date data.
  C-transient (= Pending): The accessed data is in a transient state (for example, the site has just issued a protocol request, but has not received the corresponding protocol reply).
Notes: - common cases
- read miss to private (victim clean or dirty)
- write miss to private
- read miss to shared
- write miss to shared

## Slide 13: Home directory states
For each memory line, there are 4 possible states:
  R(dir): The memory line is shared by the sites specified in dir (dir is a set of sites). The data in memory is valid in this state. If dir is empty (i.e., dir = ε), the memory line is not cached by any site.
  W(id): The memory line is exclusively cached at site id, and has been modified at that site. Memory does not have the most up-to-date data.
  TR(dir): The memory line is in a transient state waiting for the acknowledgements to the invalidation requests that the home site has issued.
  TW(id): The memory line is in a transient state waiting for a line exclusively cached at site id (i.e., in C-modified state) to make the memory line at the home site up-to-date.

## Slide 14: Read miss, to uncached or shared line
Directory Controller
DRAM Bank
CPU
Cache
1
Load request at head of CPU->Cache queue.
2
Load misses in cache.
3
Send ShReq message to directory.
4
Message received at directory controller.
5
Access state and directory for line. Line’s state is R, with zero or more sharers.
6
Update directory by setting bit for new processor sharer.
7
Send ShRep message with contents of cache line.
8
ShRep arrives at cache.
9
Update cache tag and data and return load data to CPU.
Interconnection Network
Notes: Delay is a fact of life
Serialization by directory, no longer the bus
SC not guarantied

## Slide 15: Write miss, to read shared line
Directory Controller
DRAM Bank
CPU
Cache
1
Store request at head of CPU->Cache queue.
2
Store misses in cache.
3
Send ExReq message to directory.
4
ExReq message received at directory controller.
5
Access state and directory for line. Line’s state is R, with some set of sharers.
6
Send one InvReq message to each sharer.
11
ExRep arrives at cache
12
Update cache tag and data, then store data from CPU
Interconnection Network
CPU
Cache
7
InvReq arrives at cache.
8
Invalidate cache line. Send InvRep to directory.
9
InvRep received. Clear down sharer bit.
10
When no more sharers, send ExRep to cache.
Multiple sharers
CPU
Cache
CPU
Cache
Notes: Delay is a fact of life
Serialization by directory, no longer the bus
SC not guarantied

## Slide 16: Concurrency Management
Protocol would be easy to design if only one transaction in flight across entire system
But, want greater throughput and don’t want to have to coordinate across entire system
Great complexity in managing multiple outstanding concurrent transactions to cache lines
  Can have multiple requests in flight to same cache line!

## Slide 17: CS152 Administrivia
Final quiz, Thursday May 2
  Multiprocessors, Memory models, Cache coherence
  Lectures 17-19, PS 5, Lab 5

## Slide 18: Protocol Messages
There are 10 different protocol messages:
Category | Messages
Cache to Memory Requests | ShReq, ExReq
Memory to Cache Requests | WbReq, InvReq, FlushReq
Cache to Memory Responses | WbRep(v), InvRep, FlushRep(v)
Memory to Cache Responses | ShRep(v), ExRep(v)
Notes: LL-SC

## Slide 19: Cache State Transitions (from invalid state)

## Slide 20: Cache State Transitions (from shared state)

## Slide 21: Cache State Transitions (from exclusive state)

## Slide 22: Cache Transitions (from pending)

## Slide 23: Home Directory State Transitions
Messages sent from site id

## Slide 24: Home Directory State Transitions
Messages sent from site id

## Slide 25: Home Directory State Transitions
Messages sent from site id

## Slide 26: Home Directory State Transitions
Messages sent from site id

## Slide 27: Acknowledgements
These slides contain material developed and copyright by:
  Arvind (MIT)
  Krste Asanovic (MIT/UCB)
  Joel Emer (Intel/MIT)
  James Hoe (CMU)
  John Kubiatowicz (UCB)
  David Patterson (UCB)
MIT material derived from course 6.823
UCB material derived from course CS252