## Slide 1: CS 152 Computer Architecture and Engineering CS252 Graduate Computer Architecture Lecture 16 GPUs (Graphics Processing Units)
Krste Asanovic
Electrical Engineering and Computer Sciences
University of California at Berkeley
http://www.eecs.berkeley.edu/~krste
http://inst.eecs.berkeley.edu/~cs152

## Slide 2: Last Time in Lecture 15
Vector supercomputers
Vector register versus vector memory
Scaling performance with lanes
Stripmining
Chaining
Masking
Scatter/Gather

## Slide 3: Types of Parallelism
Instruction-Level Parallelism (ILP)
  Execute independent instructions from one instruction stream in parallel (pipelining, superscalar, VLIW)
Thread-Level Parallelism (TLP)
  Execute independent instruction streams in parallel (multithreading, multiple cores)
Data-Level Parallelism (DLP)
  Execute multiple operations of the same type in parallel (vector/SIMD execution)
Which is easiest to program?
Which is most flexible form of parallelism?
  i.e., can be used in more situations
Which is most efficient?
  i.e., greatest tasks/second/area, lowest energy/task

## Slide 4: Resurgence of DLP
Convergence of application demands and technology constraints drives architecture choice
New applications, such as graphics, machine vision, speech recognition, machine learning, etc. all require large numerical computations that are often trivially data parallel
SIMD-based architectures (vector-SIMD, subword-SIMD, SIMT/GPUs) are most efficient way to execute these algorithms

## Slide 5: Packed SIMD Extensions
Short vectors added to existing microprocessors ISAs, for multimedia
Use existing 64-bit registers split into 2x32b or 4x16b or 8x8b
  Lincoln Labs TX-2 from 1957 had 36b datapath split into 2x18b or 4x9b
  Newer designs have wider registers
    128b for PowerPC Altivec, Intel SSE2/3/4
    256b for Intel AVX
Single instruction operates on all elements within register
16b
16b
16b
16b
32b
32b
64b
8b
8b
8b
8b
8b
8b
8b
8b
16b
16b
16b
16b
16b
16b
16b
16b
16b
16b
16b
16b
+
+
+
+
4x16b adds

## Slide 6: Multimedia Extensions versus Vectors
Limited instruction set
  no vector length control
  no strided load/store or scatter/gather
  unit-stride loads must be naturally aligned to whole register width (e.g., 64 or 128-bit)
Limited vector register length
  requires superscalar issue to keep multiply/add/load units busy
  loop unrolling to hide latencies increases register pressure
Trend towards fuller vector support in microprocessors
  Better support for misaligned memory accesses
  Support of double-precision (64-bit floating-point)
  New Intel AVX spec (announced April 2008), 256b vector registers (expandable up to 1024b) , adding scatter/gather
  New ARM SVE/MVE vector ISA closer to traditional vector designs

## Slide 7: DLP important for conventional CPUs
Prediction for x86 processors, from Hennessy & Patterson, 5th edition
  Note: Educated guess, not Intel product plans!
TLP: 2+ cores / 2 years
DLP: 2x width / 4 years
DLP will account for more mainstream parallelism growth than TLP in next decade.
  SIMD –single-instruction multiple-data (DLP)
  MIMD- multiple-instruction multiple-data (TLP)

## Slide 8: Graphics Processing Units (GPUs)
Original GPUs were dedicated fixed-function devices for generating 3D graphics (mid-late 1990s) including high-performance floating-point units
  Provide workstation-like graphics for PCs
  User could configure graphics pipeline, but not really program it
Over time, more programmability added (2001-2005)
  E.g., New language Cg for writing small programs run on each vertex or each pixel, also Windows DirectX variants
  Massively parallel (millions of vertices or pixels per frame) but very constrained programming model
Some users noticed they could do general-purpose computation by mapping input and output data to images, and computation to vertex and pixel shading computations
  Incredibly difficult programming model as had to use graphics pipeline model for general computation

## Slide 9: General-Purpose GPUs (GP-GPUs)
In 2006, Nvidia introduced GeForce 8800 GPU, which supported a new programming language CUDA (in 2007)
  “Compute Unified Device Architecture”
  Subsequently, broader industry pushing for OpenCL, a vendor-neutral version of same ideas.
Idea: Take advantage of GPU computational performance and memory bandwidth to accelerate some kernels for general-purpose computing
Attached processor model: Host CPU issues data-parallel kernels to GP-GPU for execution
This lecture has a simplified version of Nvidia CUDA-style model and only considers GPU execution for computational kernels, not graphics
  Would need whole other course to describe graphics processing

## Slide 10: Simplified CUDA Programming Model
Computation performed by a very large number of independent small scalar threads (CUDA threads or microthreads) grouped into thread blocks.
// C version of DAXPY loop.
void daxpy(int n, double a, double*x, double*y)
{ for (int i=0; i<n; i++)
y[i] = a*x[i] + y[i]; }
// CUDA version.
__host__ // Piece run on host processor.
int nblocks = (n+255)/256; //256 CUDA threads/block
daxpy<<<nblocks,256>>>(n,2.0,x,y);
__device__ // Piece run on GP-GPU.
void daxpy(int n, double a, double*x, double*y)
{ int i = blockIdx.x*blockDim.x + threadId.x;
if (i<n) y[i]=a*x[i]+y[i]; }

## Slide 11: Programmer’s View of Execution
blockIdx 0
threadId 0
threadId 1
threadId 255
blockIdx 1
threadId 0
threadId 1
threadId 255
blockIdx
(n+255/256)
threadId 0
threadId 1
threadId 255
Create enough blocks to cover input vector
(NVIDIA calls this ensemble of blocks a Grid, can be 2-dimensional)
Conditional (i<n) turns off unused threads in last block
blockDim = 256 (programmer can choose)

## Slide 12: Hardware Execution Model
GPU
GPU is built from multiple parallel cores, each core contains a multithreaded SIMD processor with multiple lanes but with no scalar processor
  some adding “scalar coprocessors” now
CPU sends whole “grid” over to GPU, which distributes thread blocks among cores (each thread block executes on one core)
  Programmer unaware of number of cores
Core 0
Lane 0
Lane 1
Lane 15
Core 1
Lane 0
Lane 1
Lane 15
Core 15
Lane 0
Lane 1
Lane 15
GPU Memory
CPU
CPU Memory

## Slide 13: Historical Retrospective, Cray-2 (1985)
243MHz ECL logic
2GB DRAM main memory (128 banks of 16MB each)
  Bank busy time 57 clocks!
Local memory of 128KB/core
1 foreground + 4 background vector processors
Foreground CPU
Shared Memory
Core 0
Lane
Local Memory
Core 0
Lane
Local Memory
Core 0
Lane
Local Memory
Core 0
Lane
Local Memory

## Slide 14: “Single Instruction, Multiple Thread” (SIMT)
GPUs use a SIMT model, where individual scalar instruction streams for each CUDA thread are grouped together for SIMD execution on hardware (NVIDIA groups 32 CUDA threads into a warp)
µT0
µT1
µT2
µT3
µT4
µT5
µT6
µT7
ld x, (z)
mul a
ld y, (w)
add
st y, (w)
Scalar instruction stream
SIMD execution across warp

## Slide 15: Implications of SIMT Model
All “vector” loads and stores are scatter-gather, as individual µthreads perform scalar loads and stores
  GPU adds hardware to dynamically coalesce individual µthread loads and stores to mimic vector loads and stores
Every µthread has to perform stripmining calculations redundantly (“am I active?”) as there is no scalar processor equivalent

## Slide 16: CS152 Administrivia
PS 4 and Lab 3 due Monday April 5
Lab 4 out on Wednesday March 31
Special Announcement, Project Prizes!
  Apple donating specially engraved Airpod Pro as prizes
  Awarded to top two teams in open-ended portions of labs 3,4,5

## Slide 17: CS252 Administrivia
This week’s readings: Branch Prediction
Project prize, sponsored by Apple
  Top team receives engraved Airpod Pros

## Slide 18: Conditionals in SIMT model
Simple if-then-else are compiled into predicated execution, equivalent to vector masking
More complex control flow compiled into branches
How to execute a vector of branches? Vector function calls?
µT0
µT1
µT2
µT3
µT4
µT5
µT6
µT7
tid=threadid
If (tid >= n) skip
Call func1
add
st y
Scalar instruction stream
SIMD execution across warp
skip:

## Slide 19: Branch Divergence
Hardware tracks which µthreads take or don’t take branch
If all go the same way, then keep going in SIMD fashion
If not, create mask vector indicating taken/not-taken
Keep executing not-taken path under mask, push taken branch PC+mask onto a hardware stack and execute later
When can execution of µthreads in warp reconverge?

## Slide 20: NVIDIA Instruction Set Arch.
ISA is an abstraction of the hardware instruction set
  “Parallel Thread Execution (PTX)”
    opcode.type d,a,b,c;
  Uses virtual registers
  Translation to machine code is performed in software
  Example:
  shl.s32 R8, blockIdx, 9 ; Thread Block ID * Block size (512 or 29)
  add.s32 R8, R8, threadIdx ; R8 = i = my CUDA thread ID
  ld.global.f64 RD0, [X+R8] ; RD0 = X[i]
  ld.global.f64 RD2, [Y+R8] ; RD2 = Y[i]
  mul.f64 R0D, RD0, RD4 ; Product in RD0 = RD0 * RD4 (scalar a)
  add.f64 R0D, RD0, RD2 ; Sum in RD0 = RD0 + RD2 (Y[i])
  st.global.f64 [Y+R8], RD0 ; Y[i] = sum (X[i]*a + Y[i])
Graphical Processing Units

## Slide 21: Conditional Branching
Like vector architectures, GPU branch hardware uses internal masks
Also uses
  Branch synchronization stack
    Entries consist of masks for each SIMD lane
    I.e. which threads commit their results (all threads execute)
  Instruction markers to manage when a branch diverges into multiple execution paths
    Push on divergent branch
  …and when paths converge
    Act as barriers
    Pops stack
Per-thread-lane 1-bit predicate register, specified by programmer
Graphical Processing Units

## Slide 22: Example
if (X[i] != 0)
X[i] = X[i] – Y[i];
else X[i] = Z[i];
ld.global.f64 RD0, [X+R8] ; RD0 = X[i]
setp.neq.s32 P1, RD0, #0 ; P1 is predicate register 1
@!P1, bra ELSE1, *Push ; Push old mask, set new mask bits
; if P1 false, go to ELSE1
ld.global.f64 RD2, [Y+R8] ; RD2 = Y[i]
sub.f64 RD0, RD0, RD2 ; Difference in RD0
st.global.f64 [X+R8], RD0 ; X[i] = RD0
@P1, bra ENDIF1, *Comp ; complement mask bits
; if P1 true, go to ENDIF1
ELSE1: ld.global.f64 RD0, [Z+R8] ; RD0 = Z[i]
st.global.f64 [X+R8], RD0 ; X[i] = RD0
ENDIF1: <next instruction>, *Pop ; pop to restore old mask
Graphical Processing Units

## Slide 23: Warps are multithreaded on core
One warp of 32 µthreads is a single thread in the hardware
Multiple warp threads are interleaved in execution on a single core to hide latencies (memory and functional unit)
A single thread block can contain multiple warps (up to 512 µT max in CUDA), all mapped to single core
Can have multiple blocks executing on one core
[Nvidia, 2010]

## Slide 24: GPU Memory Hierarchy
[ Nvidia, 2010]

## Slide 25: SIMT
Illusion of many independent threads
But for efficiency, programmer must try and keep µthreads aligned in a SIMD fashion
  Try and do unit-stride loads and store so memory coalescing kicks in
  Avoid branch divergence so most instruction slots execute useful work and are not masked off

## Slide 26: Nvidia Fermi GF100 GPU
[Nvidia, 2010]

## Slide 27: Fermi “Streaming Multiprocessor” Core

## Slide 28: NVIDIA Pascal Multithreaded GPU Core

## Slide 29: Fermi Dual-Issue Warp Scheduler

## Slide 30: Important of Machine Learning for GPUs
NVIDIA stock price 40x in 9 years (since deep learning became important)

## Slide 31: Apple A12 Processor (2018)
83.27mm2
7nm technology
[Source: Tech Insights, AnandTech]