## Slide 1: CS 152 Computer Architecture and Engineering Lecture 22: Virtual Machines
Krste Asanovic
Electrical Engineering and Computer Sciences
University of California, Berkeley
http://www.eecs.berkeley.edu/~krste
http://inst.eecs.berkeley.edu/~cs152

## Slide 2: Last Time in Lecture 20
Implementing Mutual Exclusion synchronization is possible using regular loads and stores, but is complicated and inefficient
Most architectures add atomic read-modify-write synchronization primitives to support mutual-exclusion
Lock-based synchronization is susceptible to lock-owning thread being descheduled while holding lock
Non-blocking synchronization tries to provide mutual exclusion without holding a lock
  Compare-and-swap, makes forward progress but complex instruction and susceptible to ABA problem
  Double-wide compare-and-swap prevents ABA problem but is now even more complex instruction
Load-Reserved/Store-Conditional pair reduces instruction complexity
  Protects based on address not values, so not susceptible to ABA
  Can livelock, unless add forward progress guarantee
Transactional Memory is slowly entering commercial use
  Complex portability/compatibility story

## Slide 3: Software Applications
How is a software application encoded?
  What are you getting when you buy a software application?
  What machines will it work on?
  Who do you blame if it doesn’t work, i.e., what contract(s) were violated?
Usually, applications encoded using an application binary interface (ABI)
  Binary encoding of instructions, initial data, and system (or environment) calls
  Distinct from an application programming interface (API), which is at source code level

## Slide 4: Types of Virtual Machine (VM)
User Virtual Machines run a single application according to some standard ABI
  Example user ABIs include Win32 for windows and Java Virtual Machine (JVM)
“(Operating) System Virtual Machines” provide a complete system environment at binary ISA level
  E.g., IBM VM/370, VMware ESX Server, and Xen
  Single computer runs multiple VMs, and can support a multiple, different OSes
    On conventional platform, single OS “owns” all HW resources
    With a VM, multiple OSes all share HW resources
Underlying HW platform is called the host, where its resources used to run guest VMs (user and/or system)

## Slide 5: User Virtual Machine = ISA + Environment
ISA alone not sufficient to write useful programs, need I/O too!
Direct access to memory mapped I/O via load/store instructions problematic
  time-shared systems
  portability
Operating system usually responsible for I/O
  sharing devices and managing security
  hiding different types of hardware (e.g., EIDE vs. SCSI disks)
ISA communicates with operating system through some standard mechanism, i.e., ecall instructions on RISC-V
  example RISC-V Linux system call convention:
  addi a7, x0, <syscall-num> # syscall number in a7
  addi a0, x0, argval # a0-a6 hold arguments
  ecall # cause trap into OS
  # On return from ecall, a0 holds return value

## Slide 6: Application Binary Interface (ABI)
Programs are usually distributed in a binary format that encodes the program text (instructions) and initial values of some data segments
Virtual machine specifications include
  what state is available at process creation
  which instructions are available (the ISA)
  what system calls are possible (I/O, or the environment)
The ABI is a specification of the binary format used to encode programs for a virtual machine
Operating system implements the virtual machine
  at process startup, OS reads the binary program, creates an environment for it, then begins to execute the code, handling traps for I/O calls, emulation, etc.

## Slide 7: OS Can Support Multiple User VMs
Virtual machine features change over time with new versions of operating system
  new ISA instructions added
  new types of I/O are added (e.g., asynchronous file I/O)
Common to provide backwards compatibility so old binaries run on new OS
  SunOS 5 (System V Release 4 Unix, Solaris) can run binaries compiled for SunOS4 (BSD-style Unix)
  Windows 98 runs MS-DOS programs
If ABI needs instructions not supported by native hardware, OS can provide in software

## Slide 8: ISA Implementations Partly in Software
Often good idea to implement part of ISA in software:
Expensive but rarely used instructions can cause trap to OS emulation routine:
  e.g., decimal arithmetic in MicroVax implementation of VAX ISA
Infrequent but difficult operand values can cause trap
  e.g., IEEE floating-point subnormals cause traps in many floating-point unit implementations
Old machine can trap unused opcodes, allows binaries for new ISA to run on old hardware
  e.g., Sun SPARC v8 added integer multiply instructions, older v7 CPUs trap and emulate

## Slide 9: Supporting Non-Native ISAs
Run programs for one ISA on hardware with different ISA
Software Interpreter (OS software interprets instructions at run-time)
  E.g., OS 9 for PowerPC Macs had interpreter for 68000 code
Binary Translation (convert at install and/or load time)
  IBM AS/400 to modified PowerPC cores
  DEC tools for VAX->MIPS->Alpha
Dynamic Translation (non-native ISA to native ISA at run time)
  Sun’s HotSpot Java JIT (just-in-time) compiler
  Transmeta Crusoe, x86->VLIW code morphing
  OS X for Intel Macs had dynamic binary translator for PowerPC (Rosetta)
  New ARM M1 Macs have dynamic translation from x86 to ARM
Run-time Hardware Emulation
  IBM 360 had optional IBM 1401 emulator in microcode
  First Intel Itanium converted x86 to native VLIW (two software-visible ISAs)
  ARM cores supported 32-bit ARM, 16-bit Thumb, and JVM (three software-visible ISAs!) – newer cores support AArch32 32-bit and AArch64 64-bit ISAs

## Slide 10: Software Interpreter
Fetch and decode one instruction at a time in software
Memory image of guest VM lives in host interpreter data memory
Interpreter Data
Interpreter Code
Interpreter Stack
while(!stop)
{
inst = Code[PC];
PC += 4;
execute(inst);
}
fetch-decode loop
Guest ISA Code
Guest ISA Data
Executable on Disk
Guest ISA Code
Guest ISA Data
Guest Stack
Load into interpreter process memory

## Slide 11: Software Interpreter
Easy to code, small code footprint
Slow, approximately 50-100x slower than native execution for RISC ISA hosted on RISC ISA
Problem is time taken to decode instructions
  fetch instruction from memory
  switch tables to decode opcodes
  extract register specifiers using bit shifts
  access register file data structure
  execute operation
  return to main fetch loop

## Slide 12: Binary Translation
Each guest ISA instruction translates into some set of host (or native) ISA instructions
Instead of dynamically fetching and decoding instructions at run-time, translate entire binary program and save result as new native ISA executable
Removes interpretive fetch-decode overhead
Can do compiler optimizations on translated code to improve performance
  register allocation for values flowing between guest ISA instructions
  native instruction scheduling to improve performance
  remove unreachable code
  inline assembly procedures

## Slide 13: Binary Translation, Take 1
Guest ISA Code
Guest ISA Data
Executable on Disk
Native ISA Code
Guest ISA Data
Executable on Disk
Native Data
Translate to native ISA code
Data unchanged
Native translation might need extra data workspace

## Slide 14: Binary Translation Problems
Branch and Jump targets
  guest code:
  j L1
  ...
  L1: lw r1, (r4)
  jr (r1)
  native code
j
translation
lw
translation
jr
translation
native jump at end of block jumps to native translation of lw
Where should the jump register go?

## Slide 15: PC Mapping Table
Table gives translated PC for each guest PC
Indirect jumps translated into code that looks in table to find where to jump to
  can optimize well-behaved guest code for subroutine call/return by using native PC in return links
If can branch to any guest PC, then need one table entry for every instruction in hosted program  big table
If can branch to any PC, then either
  limit inter-instruction optimizations
  large code explosion to hold optimizations for each possible entry into sequential code sequence
Only minority of guest instructions are indirect jump targets, want to find these
  design a highly structured VM design
  use run-time feedback of target locations

## Slide 16: Binary Translation Problems
Self-modifying code!
  sw r1, (r2) # r2 points into code space
Rare in most code, but has to be handled if allowed by guest ISA
Usually handled by including interpreter and marking modified code pages as “interpret only”
Have to invalidate all native branches into modified code pages

## Slide 17: Binary Translation, Take 2
Guest ISA Code
Guest ISA Data
Executable on Disk
Native ISA Code
Executable on Disk
PC Mapping Table
Guest ISA Code
Guest ISA Data
Native Interpreter
Translate to native ISA code
Keep copy of code and data in native data segment
Interpreter used for run-time modified code, checks for jumps back into native code using PC mapping table
Translation has to check for modified code pages then jump to interpeter
Mapping table used for indirect jumps and to jump from interpreter back into native translations

## Slide 18: IBM System/38 and AS/400
System/38 announced 1978
  AS/400 is follow-on line, now called “System I” or “iSeries”
High-level instruction set interface designed for binary translation
Memory-memory instruction set, never directly executed by hardware
Hardware Machine
Horizontal Microcode
Vertical Microcode
High-Level Architecture Interface
Languages, Database, Utilities
Control Program Facility
User Applications
Replaced by modified PowerPC cores in newer iSeries machines
Used 48-bit CISC engine in earlier machines

## Slide 19: Dynamic Translation
Translate code sequences as needed at run-time, but cache results
Can optimize code sequences based on dynamic information (e.g., branch targets encountered)
Tradeoff between optimizer run-time and time saved by optimizations in translated code
Technique used in Java JIT (Just-In-Time) compilers, Javascript engines, and Virtual Machine Monitors (for system VMs)
Also, Transmeta Crusoe and Apple M1 Macs for x86 emulation

## Slide 20: Dynamic Binary Translation Example:
Data RAM
Disk
x86
Binary
Runtime -- Execution
x86
Binary
Code Cache
Code Cache
Tags
Translator
x86 Parser &
High Level
Translator
High Level
Optimization
Low Level
Code Generation
Low Level
Optimization and
Scheduling
Starting Address

## Slide 21: Chaining
Runtime -- Execution
Code Cache
Code Cache
Tags
Before chaining:
add %r5, %r6, %r7
li %next_addr_reg, next_addr #load address
#of next block
j dispatch loop
After chaining:
add %r5, %r6, %r7
j physical location of translated
code for next_block

## Slide 22: CS152 Administrivia
PS5 due Monday April 26th
Lab 5 due on May 3rd
Midterm grades
  Will have one week for regrade requests

## Slide 23: CS152 Midterm-2 Grade Distribution

## Slide 24: CS252 Administrivia
Thursday April 29th Project Checkpoint
  Schedule 8-minute Zoom calls during discussion period
  Please have status slides, what’s completed, what’s left to do

## Slide 25: Transmeta Crusoe (2000)
Converts x86 ISA into internal native VLIW format using software at run-time  “Code Morphing”
Optimizes across x86 instruction boundaries to improve performance
Translations cached to avoid translator overhead on repeated execution
Completely invisible to operating system – looks like x86 hardware processor
[ Following slides contain examples taken from “The Technology Behind Crusoe Processors”, Transmeta Corporation, 2000 ]

## Slide 26: Transmeta VLIW Engine
Two VLIW formats, 64-bit and 128-bit, contains 2 or 4 RISC-like operations
VLIW engine optimized for x86 code emulation
  evaluates condition codes the same way as x86
  has 80-bit floating-point unit
  partial register writes (update 8 bits in 32 bit register)
Support for fast instruction writes
  run-time code generation important
Initially, two different VLIW implementations, low-end TM3120, high-end TM5400
  native ISA differences invisible to user, hidden by translation system
  new eight-issue VLIW core planned (TM6000 series)

## Slide 27: Crusoe System
VLIW Processor
Inst. Cache
Data Cache
Crusoe CPU
x86 DRAM
Code Morph DRAM
x86 BIOS Flash
Code Morph Compiler Code (VLIW)
Translation Cache (VLIW)
Workspace
Portion of system DRAM is used by Code Morph software and is invisible to x86 machine
Crusoe Boot Flash ROM
Compressed compiler held in boot ROM
System DRAM

## Slide 28: Transmeta Translation
addl %eax, (%esp) # load data from stack, add to eax
addl %ebx, (%esp) # load data from stack, add to ebx
movl %esi, (%ebp) # load esi from memory
subl %ecx, 5 # sub 5 from ecx
x86 code:
ld %r30, [%esp] # load from stack into temp
add.c %eax, %eax, %r30 # add to %eax,set cond.codes
ld %r31, [%esp]
add.c %ebx, %ebx, %r31
ld %esi, [%ebp]
sub.c %ecx, %ecx, 5
first step, translate into RISC ops:

## Slide 29: Compiler Optimizations
ld %r30, [%esp] # load from stack into temp
add.c %eax, %eax, %r30 # add to %eax,set cond.codes
ld %r31, [%esp]
add.c %ebx, %ebx, %r31
ld %esi, [%ebp]
sub.c %ecx, %ecx, 5
RISC ops:
ld %r30, [%esp] # load from stack only once
add %eax, %eax, %r30
add %ebx, %ebx, %r30 # reuse data loaded earlier
ld %esi, [%ebp]
sub.c %ecx, %ecx, 5 # only this cond. code needed
Optimize:

## Slide 30: Scheduling
ld %r30, [%esp] # load from stack only once
add %eax, %eax, %r30
add %ebx, %ebx, %r30 # reuse data loaded earlier
ld %esi, [%ebp]
sub.c %ecx, %ecx, 5 # only this cond. code needed
Optimized RISC ops:
ld %r30, [%esp]; sub.c %ecx, %ecx, 5
ld %esi, [%ebp]; add %eax, %eax, %r30; add %ebx, %ebx, %r30
Schedule into VLIW code:

## Slide 31: Translation Overhead
Highly optimizing compiler takes considerable time to run, adds run-time overhead
Only worth doing for frequently executed code
Translation adds instrumentation into translations that counts how often code executed, and which way branches usually go
As count for a block increases, higher optimization levels are invoked on that code

## Slide 32: Exceptions
ld %r30, [%esp]; sub.c %ecx, %ecx, 5
ld %esi, [%ebp]; add %eax, %eax, %r30; add %ebx, %ebx, %r30
Scheduled VLIW code:
addl %eax, (%esp) # load data from stack, add to eax
addl %ebx, (%esp) # load data from stack, add to ebx
movl %esi, (%ebp) # load esi from memory
subl %ecx, 5 # sub 5 from ecx
Original x86 code:
x86 instructions executed out-of-order with respect to original program flow
Need to restore state for precise traps

## Slide 33: Shadow Registers and Store Buffer
All registers have working copy and shadow copy
Stores held in software controlled store buffer, loads can snoop
At end of translation block, commit changes by copying values from working regs to shadow regs, and by releasing stores in store buffer
On exception, re-execute x86 code using interpreter

## Slide 34: Handling Self-Modifying Code
When a translation is made, mark the associated x86 code page as being translated in page table
Store to translated code page causes trap, and associated translations are invalidated

## Slide 35: System VMs: Supporting Multiple OSs on Same Hardware
Can virtualize the environment that an operating system sees, an OS-level VM, or system VM
Hypervisor layer implements sharing of real hardware resources by multiple OS VMs that each think they have a complete copy of the machine
  Popular in early days to allow mainframe to be shared by multiple groups developing OS code
  Used in modern mainframes to allow multiple versions of OS to be running simultaneously  OS upgrades with no downtime!
  Example for PCs: VMware allows Windows OS to run on top of Linux (or vice-versa)
Requires trap on access to privileged hardware state
  easier if OS interface to hardware well defined

## Slide 36: Introduction to System Virtual Machines
VMs developed in late 1960s
  Remained important in mainframe computing over the years
  Largely ignored in single-user computers of 1980s and 1990s
Recently regained popularity due to
  increasing importance of isolation and security in modern systems,
  failures in security and reliability of standard operating systems,
  sharing of a single computer among many unrelated users,
  and the dramatic increases in raw speed of processors, which makes the overhead of VMs more acceptable

## Slide 37: Virtual Machine Monitors (VMMs)
Virtual machine monitor (VMM) or hypervisor is software that supports VMs
VMM determines how to map virtual resources to physical resources
Physical resource may be time-shared, partitioned, or emulated in software
VMM is much smaller than a traditional OS;
  isolation portion of a VMM is  10,000 lines of code

## Slide 38: VMM Overhead?
Depends on the workload
User-level processor-bound programs (e.g., SPEC benchmarks) have zero-virtualization overhead
  Runs at native speeds since OS rarely invoked
I/O-intensive workloads that are OS-intensive execute many system calls and privileged instructions, can result in high virtualization overhead
  For System VMs, goal of architecture and VMM is to run almost all instructions directly on native hardware
If I/O-intensive workload is also I/O-bound, low processor utilization since waiting for I/O
  processor virtualization can be hidden, so low virtualization overhead

## Slide 39: Other Uses of VMs
Managing Software
  VMs provide an abstraction that can run the complete SW stack, even including old OSes like DOS
  Typical deployment: some VMs running legacy OSes, many running current stable OS release, few testing next OS release
Managing Hardware
  VMs allow separate SW stacks to run independently yet share HW, thereby consolidating number of servers
    Some run each application with compatible version of OS on separate computers, as separation helps dependability
  Migrate running VM to a different computer
    Either to balance load or to evacuate from failing HW

## Slide 40: Requirements of a Virtual Machine Monitor
A VM Monitor
  Presents a SW interface to guest software,
  Isolates state of guests from each other, and
  Protects itself from guest software (including guest OSes)
Guest software should behave on a VM exactly as if running on the native HW
  Except for performance-related behavior or limitations of fixed resources shared by multiple VMs
Guest software should not be able to change allocation of real system resources directly
Hence, VMM must control  everything even though guest VM and OS currently running is temporarily using them
  Access to privileged state, Address translation, I/O, Exceptions and Interrupts, …

## Slide 41: Requirements of a Virtual Machine Monitor
VMM must be at higher privilege level than guest VM, which generally run in user mode
  Execution of privileged instructions handled by VMM
E.g., Timer interrupt: VMM suspends currently running guest VM, saves its state, handles interrupt, determine which guest VM to run next, and then load its state
  Guest VMs that rely on timer interrupt provided with virtual timer and an emulated timer interrupt by VMM
Requirements of system virtual machines are same as paged-virtual memory:
At least 2 processor modes, system and user
Privileged subset of instructions available only in system mode, trap if executed in user mode
  All system resources controllable only via these instructions

## Slide 42: ISA Support for Virtual Machines
If VMs are planned for during design of ISA, easy to reduce instructions that must be executed by a VMM and how long it takes to emulate them
  Since VMs have been considered for desktop/PC server apps only recently, most ISAs were created without virtualization in mind, including 80x86 and most RISC architectures
VMM must ensure that guest system only interacts with virtual resources  conventional guest OS runs as user mode program on top of VMM
  If guest OS attempts to access or modify information related to HW resources via a privileged instruction--for example, reading or writing the page table pointer--it will trap to the VMM
If not, VMM must intercept instruction and support a virtual version of the sensitive information as the guest OS expects (examples soon)

## Slide 43: Impact of VMs on Virtual Memory
Virtualization of virtual memory if each guest OS in every VM manages its own set of page tables?
VMM separates real and physical memory
  Makes real memory a separate, intermediate level between virtual memory and physical memory
  Some use the terms virtual memory, physical memory, and machine memory to name the 3 levels
  Guest OS maps virtual memory to real memory via its page tables, and VMM page tables map real memory to physical memory
VMM maintains a shadow page table that maps directly from the guest virtual address space to the physical address space of HW
  Rather than pay extra level of indirection on every memory access
  VMM must trap any attempt by guest OS to change its page table or to access the page table pointer

## Slide 44: ISA Support for VMs & Virtual Memory
IBM 370 architecture added additional level of indirection that is managed by the VMM
  Guest OS keeps its page tables as before, so the shadow pages are unnecessary
To virtualize software TLB, VMM manages the real TLB and has a copy of the contents of the TLB of each guest VM
  Any instruction that accesses the TLB must trap
  TLBs with Process ID tags support a mix of entries from different VMs and the VMM, thereby avoiding flushing of the TLB on a VM switch
Recent processor designs have added similar mechanisms to accelerate VMMs

## Slide 45: Recursive Virtualization
Previous discussion had VMM separate from guest OS
Can have an OS provide recursive support for own guest OS (e..g, KVM in Linux)
  Aka known as “type-2” hypervisor in contrast to “type-1” VMM-style hypervisor
Made easier with correct hardware support
  RISC-V hypervisor extension supports type-1 and type-2 hypervisors

## Slide 46: Impact of Virtualization on I/O
Most difficult part of virtualization
  Increasing number of I/O devices attached to the computer
  Increasing diversity of I/O device types
  Sharing of a real device among multiple VMs,
  Supporting the myriad of device drivers that are required, especially if different guest OSes are supported on the same VM system
Give each VM generic versions of each type of I/O device driver, and let VMM handle real I/O
Method for mapping virtual to physical I/O device depends on the type of device:
  Disks partitioned by VMM to create virtual disks for guest VMs
  Network interfaces shared between VMs in short time slices, and VMM tracks messages for virtual network addresses to ensure that guest VMs only receive their messages

## Slide 47: Acknowledgements
These slides contain material developed and copyright by:
  Arvind (MIT)
  Krste Asanovic (MIT/UCB)
  Joel Emer (Intel/MIT)
  James Hoe (CMU)
  John Kubiatowicz (UCB)
  David Patterson (UCB)
MIT material derived from course 6.823
UCB material derived from course CS252