## Slide 1: CS162 Operating Systems and Systems Programming Lecture 14 Caching (Finished), Demand Paging
October 19th, 2015
Prof. John Kubiatowicz
http://cs162.eecs.Berkeley.edu

## Slide 2: Recall: In Machine Structures (eg. 61C) …
Caching is the key to memory system performance
Average Access time = (Hit Rate x HitTime) + (Miss Rate x MissTime)
HitRate + MissRate = 1
HitRate = 90% => Average Access Time = 19 ns
HitRate = 99% => Average Access Time = 10.9ns
Processor
Main
Memory
(DRAM)
100ns
10ns
Second
Level
Cache
(SRAM)
Processor
Main
Memory
(DRAM)
100ns
Access time = 100ns

## Slide 3: Why Does Caching Help? Locality!
Temporal Locality (Locality in Time):
  Keep recently accessed data items closer to processor
Spatial Locality (Locality in Space):
  Move contiguous blocks to the upper levels
Address Space
0
2n - 1
Probability
of reference
Lower Level
Memory
Upper Level
Memory
To Processor
From Processor
Blk X
Blk Y
Notes: How does the memory hierarchy work? Well it is rather simple, at least in principle.
In order to take advantage of the temporal locality, that is the locality in time, the memory hierarchy will keep those more recently accessed data items closer to the processor because chances are (points to the principle), the processor will access them again soon.
In order to take advantage of the spatial locality, not ONLY do we move the item that has just been accessed to the upper level, but we ALSO move the data items that are adjacent to it.
+1 = 15 min. (X:55)

## Slide 4: Memory Hierarchy
Take advantage of the principle of locality to:
  Present as much memory as in the cheapest technology
  Provide access at speed offered by the fastest technology
L3 Cache (shared)
Registers
Core
Core
Secondary Storage (Disk)
Processor
Main
Memory
(DRAM)
1
10,000,000
(10 ms)
Speed (ns):
10-30
100
100Bs
Size (bytes):
MBs
GBs
TBs
Registers
L1 Cache
L1 Cache
L2 Cache
L2 Cache
0.3
3
10kBs
100kBs
Secondary Storage (SSD)
100,000 (0.1 ms)
100GBs
Notes: The design goal is to present the user with as much memory as is available in the cheapest technology (points to the disk).
While by taking advantage of the principle of locality, we like to provide the user an average access speed that is very close to the speed that is offered by the fastest technology.
(We will go over this slide in details in the next lecture on caches).
+1 = 16 min. (X:56)

## Slide 5: A Summary on Sources of Cache Misses
Compulsory (cold start or process migration, first reference): first access to a block
  “Cold” fact of life: not a whole lot you can do about it
  Note: If you are going to run “billions” of instruction, Compulsory Misses are insignificant
Capacity:
  Cache cannot contain all blocks access by the program
  Solution: increase cache size
Conflict (collision):
  Multiple memory locations mapped to the same cache location
  Solution 1: increase cache size
  Solution 2: increase associativity
Coherence (Invalidation): other process (e.g., I/O) updates memory
Notes: (Capacity miss) That is the cache misses are due to the fact that the cache is simply not large enough to contain all the blocks that are accessed by the program.
The solution to reduce the Capacity miss rate is simple: increase the cache size.
Here is a summary of other types of cache miss we talked about.
First is the Compulsory misses. These are the misses that we cannot avoid. They are caused when we first start the program.
Then we talked about the conflict misses. They are the misses that caused by multiple memory locations being mapped to the same cache location.
There are two solutions to reduce conflict misses. The first one is, once again, increase the cache size. The second one is to increase the associativity.
For example, say using a 2-way set associative cache instead of directed mapped cache.
But keep in mind that cache miss rate is only one part of the equation. You also have to worry about cache access time and miss penalty. Do NOT optimize miss rate alone.
Finally, there is another source of cache miss we will not cover today. Those are referred to as invalidation misses caused by another process, such as IO , update the main memory so you have to flush the cache to avoid inconsistency between memory and cache.
+2 = 43 min. (Y:23)

## Slide 6: Review: How is a Block found in a Cache?
Index Used to Lookup Candidates in Cache
  Index identifies the set
Tag used to identify actual copy
  If no candidates match, then declare cache miss
Block is minimum quantum of caching
  Data select field used to select data within block
  Many caching applications don’t have data select field
Block
offset
Block Address
Tag
Index
Set Select
Data Select

## Slide 7: Review: Direct Mapped Cache
:
0x50
Valid Bit
:
Cache Tag
Byte 32
0
1
2
3
:
Cache Data
Byte 0
Byte 1
Byte 31
:
Byte 33
Byte 63
:
Byte 992
Byte 1023
:
31
Direct Mapped 2N byte cache:
  The uppermost (32 - N) bits are always the Cache Tag
  The lowest M bits are the Byte Select (Block Size = 2M)
Example: 1 KB Direct Mapped Cache with 32 B Blocks
  Index chooses potential block
  Tag checked to verify block
  Byte select chooses byte within block
Ex: 0x50
Ex: 0x00
Cache Index
0
4
31
Cache Tag
Byte Select
9
Ex: 0x01
Notes: Let’s use a specific example with realistic numbers: assume we have a 1 KB direct mapped cache with block size equals to 32 bytes.
In other words, each block associated with the cache tag will have 32 bytes in it (Row 1).
With Block Size equals to 32 bytes, the 5 least significant bits of the address will be used as byte select within the cache block.
Since the cache size is 1K byte, the upper 32 minus 10 bits, or 22 bits of the address will be stored as cache tag.
The rest of the address bits in the middle, that is bit 5 through 9, will be used as Cache Index to select the proper cache entry.
+2 = 30 min. (Y:10)

## Slide 8: Review: Set Associative Cache
Cache Index
0
4
31
Cache Tag
Byte Select
8
Cache Data
Cache Block 0
Cache Tag
Valid
:
:
:
Cache Data
Cache Block 0
Cache Tag
Valid
:
:
:
Mux
0
1
Sel1
Sel0
OR
Hit
N-way set associative: N entries per Cache Index
  N direct mapped caches operates in parallel
Example: Two-way set associative cache
  Cache Index selects a “set” from the cache
  Two tags in the set are compared to input in parallel
  Data is selected based on the tag result
Compare
Compare
Cache Block
Notes: This is called a 2-way set associative cache because there are two cache entries for each cache index. Essentially, you have two direct mapped cache works in parallel.
This is how it works: the cache index selects a set from the cache. The two tags in the set are compared in parallel with the upper bits of the memory address.
If neither tag matches the incoming address tag, we have a cache miss.
Otherwise, we have a cache hit and we will select the data on the side where the tag matches occur.
This is simple enough. What is its disadvantages?
+1 = 36 min. (Y:16)

## Slide 9: Review: Fully Associative Cache
Fully Associative: Every block can hold any line
  Address does not include a cache index
  Compare Cache Tags of all Cache Entries in Parallel
Example: Block Size=32B blocks
  We need N 27-bit comparators
  Still have byte select to choose from within block
:
Cache Data
Byte 0
Byte 1
Byte 31
:
Byte 32
Byte 33
Byte 63
:
Valid Bit
:
:
Cache Tag
0
4
Cache Tag (27 bits long)
Byte Select
31
=
=
=
=
=
Ex: 0x01
Notes: While the direct mapped cache is on the simple end of the cache design spectrum, the fully associative cache is on the most complex end.
It is the N-way set associative cache carried to the extreme where N in this case is set to the number of cache entries in the cache.
In other words, we don’t even bother to use any address bits as the cache index.
We just store all the upper bits of the address (except Byte select) that is associated with the cache block as the cache tag and have one comparator for every entry.
The address is sent to all entries at once and compared in parallel and only the one that matches are sent to the output. This is called an associative lookup.
Needless to say, it is very hardware intensive. Usually, fully associative cache is limited to 64 or less entries.
Since we are not doing any mapping with the cache index, we will never push any other item out of the cache because multiple memory locations map to the same cache location.
Therefore, by definition, conflict miss is zero for a fully associative cache. This, however, does not mean the overall miss rate will be zero.
Assume we have 64 entries here. The first 64 items we accessed can fit in.
But when we try to bring in the 65th item, we will need to throw one of them out to make room for the new item. This bring us to the third type of cache misses: Capacity Miss.
+3 = 41 min. (Y:21)

## Slide 10: Where does a Block Get Placed in a Cache?
Example: Block 12 placed in 8 block cache
0 1 2 3 4 5 6 7
Block
no.
Direct mapped:
block 12 can go only into block 4 (12 mod 8)
Set associative:
block 12 can go anywhere in set 0 (12 mod 4)
0 1 2 3 4 5 6 7
Block
no.
Set
0
Set
1
Set
2
Set
3
Fully associative:
block 12 can go anywhere
0 1 2 3 4 5 6 7
Block
no.
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
32-Block Address Space:
1 1 1 1 1 1 1 1 1 1 2 2 2 2 2 2 2 2 2 2 3 3
Block
no.

## Slide 11: Review: Which block should be replaced on a miss?
Easy for Direct Mapped: Only one possibility
Set Associative or Fully Associative:
  Random
  LRU (Least Recently Used)
2-way 4-way 8-way Size LRU Random LRU Random LRU Random
16 KB 5.2% 5.7% 4.7% 5.3% 4.4% 5.0%
64 KB 1.9% 2.0% 1.5% 1.7% 1.4% 1.5%
256 KB 1.15% 1.17% 1.13% 1.13% 1.12% 1.12%

## Slide 12: Review: What happens on a write?
Write through: The information is written to both the block in the cache and to the block in the lower-level memory
Write back: The information is written only to the block in the cache.
  Modified cache block is written to main memory only when it is replaced
  Question is block clean or dirty?
Pros and Cons of each?
  WT:
    PRO: read misses cannot result in writes
    CON: Processor held up on writes unless writes buffered
  WB:
    PRO: repeated writes not sent to DRAM processor not held up on writes
    CON: More complex Read miss may require writeback of dirty data

## Slide 13: Administrivia
Still working on the grading of exams
  No deadline yet, will let you know
Solutions are done!
  Will post them on the website tomorrow

## Slide 14: Caching Applied to Address Translation
Question is one of page locality: does it exist?
  Instruction accesses spend a lot of time on the same page (since accesses sequential)
  Stack accesses have definite locality of reference
  Data accesses have less page locality, but still some…
Can we have a TLB hierarchy?
  Sure: multiple levels at different sizes/speeds
Data Read or Write
(untranslated)
CPU
Physical
Memory
TLB
Translate
(MMU)
No
Virtual
Address
Physical
Address
Yes
Cached?
Save
Result

## Slide 15: What Actually Happens on a TLB Miss?
Hardware traversed page tables:
  On TLB miss, hardware in MMU looks at current page table to fill TLB (may walk multiple levels)
    If PTE valid, hardware fills TLB and processor never knows
    If PTE marked as invalid, causes Page Fault, after which kernel decides what to do afterwards
Software traversed Page tables (like MIPS)
  On TLB miss, processor receives TLB fault
  Kernel traverses page table to find PTE
    If PTE valid, fills TLB and returns from fault
    If PTE marked as invalid, internally calls Page Fault handler
Most chip sets provide hardware traversal
  Modern operating systems tend to have more TLB faults since they use translation for many things
  Examples:
    shared segments
    user-level portions of an operating system

## Slide 16: Transparent Exceptions: TLB/Page fault
How to transparently restart faulting instructions?
  (Consider load or store that gets TLB or Page fault)
  Could we just skip faulting instruction?
    No: need to perform load or store after reconnecting physical page
Hardware must help out by saving:
  Faulting instruction and partial state
    Need to know which instruction caused fault
    Is single PC sufficient to identify faulting position????
  Processor State: sufficient to restart user thread
    Save/restore registers, stack, etc
What if an instruction has side-effects?
Software
Load TLB
Faulting
Inst 1
Faulting
Inst 1
Faulting
Inst 2
Faulting
Inst 2
Fetch page/
Load TLB
User
OS
TLB Faults

## Slide 17: Consider weird things that can happen
What if an instruction has side effects?
  Options:
    Unwind side-effects (easy to restart)
    Finish off side-effects (messy!)
  Example 1: mov (sp)+,10
    What if page fault occurs when write to stack pointer?
    Did sp get incremented before or after the page fault?
  Example 2: strcpy (r1), (r2)
    Source and destination overlap: can’t unwind in principle!
    IBM S/370 and VAX solution: execute twice – once read-only
What about “RISC” processors?
  For instance delayed branches?
    Example: bne somewhere ld r1,(sp)
    Precise exception state consists of two PCs: PC and nPC
  Delayed exceptions:
    Example: div r1, r2, r3 ld r1, (sp)
    What if takes many cycles to discover divide by zero, but load has already caused page fault?
Notes: Nachos and other systems: hardware saves state, to help you. Role of nextPC, LoadReg, etc.
Other examples: 68000 was non-virtualizable. Couldn’t restart after a fault
So Apollo Computers put 2 68000 in every workstation:
Executes user code (hangs on fault)
Handles fault (no overlapped I/O)
Intel i860 (came out same time as 486): doesn’t provide failing virtual address. Have to go back and disassemble instruction to figure out what failed…
Moral: have to know lots of stuff to do hardware design: hardware/compilers/OS

## Slide 18: Precise Exceptions
Precise  state of the machine is preserved as if program executed up to the offending instruction
  All previous instructions completed
  Offending instruction and all following instructions act as if they have not even started
  Same system code will work on different implementations
  Difficult in the presence of pipelining, out-of-order execution, ...
  MIPS takes this position
Imprecise  system software has to figure out what is where and put it all back together
Performance goals often lead designers to forsake precise interrupts
  system software developers, user, markets etc. usually wish they had not done this
Modern techniques for out-of-order execution and branch prediction help implement precise interrupts

## Slide 19: What happens on a Context Switch?
Need to do something, since TLBs map virtual addresses to physical addresses
  Address Space just changed, so TLB entries no longer valid!
Options?
  Invalidate TLB: simple but might be expensive
    What if switching frequently between processes?
  Include ProcessID in TLB
    This is an architectural solution: needs hardware
What if translation tables change?
  For example, to move page from memory to disk or vice versa…
  Must invalidate TLB entry!
    Otherwise, might think that page is still in memory!
  Called “TLB Consistency”

## Slide 20: What TLB organization makes sense?
Needs to be really fast
  Critical path of memory access
    In simplest view: before the cache
    Thus, this adds to access time (reducing cache speed)
  Seems to argue for Direct Mapped or Low Associativity
However, needs to have very few conflicts!
  With TLB, the Miss Time extremely high!
  This argues that cost of Conflict (Miss Time) is much higher than slightly increased cost of access (Hit Time)
Thrashing: continuous conflicts between accesses
  What if use low order bits of page as index into TLB?
    First page of code, data, stack may map to same entry
    Need 3-way associativity at least?
  What if use high order bits as index?
    TLB mostly unused for small programs
CPU
TLB
Cache
Memory

## Slide 21: TLB organization: include protection
How big does TLB actually have to be?
  Usually small: 128-512 entries
  Not very big, can support higher associativity
TLB usually organized as fully-associative cache
  Lookup is by Virtual Address
  Returns Physical Address + other info
What happens when fully-associative is too slow?
  Put a small (4-16 entry) direct-mapped cache in front
  Called a “TLB Slice”
Example for MIPS R3000:
0xFA00 0x0003 Y N Y R/W 34 0x0040 0x0010 N Y Y R 0 0x0041 0x0011 N Y Y R 0
Virtual Address Physical Address Dirty Ref Valid Access ASID

## Slide 22: Example: R3000 pipeline includes TLB “stages”
Inst Fetch
Dcd/ Reg
ALU / E.A
Memory
Write Reg
TLB I-Cache RF Operation WB
E.A. TLB D-Cache
MIPS R3000 Pipeline
ASID
V. Page Number
Offset
12
20
6
0xx User segment (caching based on PT/TLB entry)
100 Kernel physical space, cached
101 Kernel physical space, uncached
11x Kernel virtual space
Allows context switching among
64 user processes without TLB flush
Virtual Address Space
TLB
  64 entry, on-chip, fully associative, software TLB fault handler

## Slide 23: Reducing translation time further
As described, TLB lookup is in serial with cache lookup:
Machines with TLBs go one step further: they overlap TLB lookup with cache access.
  Works because offset available early
Virtual Address
TLB Lookup
V
Access
Rights
PA
V page no.
offset
10
P page no.
offset
10
Physical Address

## Slide 24: Overlapping TLB & Cache Access (1/2)
Main idea:
  Offset in virtual address exactly covers the “cache index” and “byte select”
  Thus can select the cached byte(s) in parallel to perform address translation
Offset
Virtual Page #
index
tag / page #
byte
virtual address
physical address

## Slide 25: Overlapping TLB & Cache Access
Here is how this might work with a 4K cache:
What if cache size is increased to 8KB?
  Overlap not complete
  Need to do something else. See CS152/252
Another option: Virtual Caches
  Tags in cache are virtual addresses
  Translation only happens on cache misses
TLB
4K Cache
10
2
00
4 bytes
index
1 K
page #
disp
20
assoc
lookup
32
Hit/
Miss
FN
Data
Hit/
Miss
=
FN

## Slide 26: Putting Everything Together: Address Translation
Physical Address:
Offset
Physical
Page #
Virtual Address:
Offset
Virtual
P2 index
Virtual
P1 index
PageTablePtr
Page Table
(1st level)
Page Table
(2nd level)
Physical
Memory:

## Slide 27: Putting Everything Together: TLB
Page Table
(2nd level)
PageTablePtr
Page Table
(1st level)
Offset
Physical
Page #
Virtual Address:
Offset
Virtual
P2 index
Virtual
P1 index
Physical
Memory:
Physical Address:
…
TLB:

## Slide 28: Putting Everything Together: Cache
Page Table
(2nd level)
PageTablePtr
Page Table
(1st level)
Virtual Address:
Offset
Virtual
P2 index
Virtual
P1 index
…
TLB:
Offset
Physical
Memory:
Physical Address:
Physical
Page #
…
tag:
block:
cache:
index
byte
tag

## Slide 29: Next Up: What happens when …
virtual address
MMU
PT
instruction
physical address
page#
frame#
offset
page fault
Operating System
exception
Page Fault Handler
load page from disk
update PT entry
Process
scheduler
retry
frame#
offset

## Slide 30: Where are all places that caching arises in Operating Systems?
Direct use of caching techniques
  paged virtual memory (mem as cache for disk)
  TLB (cache of PTEs)
  file systems (cache disk blocks in memory)
  DNS (cache hostname => IP address translations)
  Web proxies (cache recently accessed pages)
Which pages to keep in memory?
  All-important “Policy” aspect of virtual memory
  Will spend a bit more time on this in a moment

## Slide 31: Impact of caches on Operating Systems
Indirect - dealing with cache effects
Process scheduling
  which and how many processes are active ?
  large memory footprints versus small ones ?
  priorities ?
  Shared pages mapped into VAS of multiple processes ?
Impact of thread scheduling on cache performance
  rapid interleaving of threads (small quantum) may degrade cache performance
    increase average memory access time (AMAT) !!!
Designing operating system data structures for cache performance
Maintaining the correctness of various caches
  TLB consistency:
    With PT across context switches ?
    Across updates to the PT ?

## Slide 32: Working Set Model
As a program executes it transitions through a sequence of “working sets” consisting of varying sized subsets of the address space
Time
Address

## Slide 33: Cache Behavior under WS model
Amortized by fraction of time the WS is active
Transitions from one WS to the next
Capacity, Conflict, Compulsory misses
Applicable to memory caches and pages. Others ?
Hit Rate
Cache Size
new working set fits
0
1

## Slide 34: Another model of Locality: Zipf
Likelihood of accessing item of rank r is α1/ra
Although rare to access items below the top few, there are so many that it yields a “heavy tailed” distribution.
Substantial value from even a tiny cache
Substantial misses from even a very large one
Chart: P access(rank) = 1/rank
pop a=1 | 0.19278 | 0.096388 | 0.064259 | 0.048194 | 0.038555 | 0.032129 | 0.027539 | 0.024097 | 0.02142 | 0.019278 | 0.017525 | 0.016065 | 0.014829 | 0.01377 | 0.012852 | 0.012048 | 0.01134 | 0.01071 | 0.010146 | 0.0096388 | 0.0091798 | 0.0087625 | 0.0083815 | 0.0080323 | 0.007711 | 0.0074144 | 0.0071398 | 0.0068848 | 0.0066474 | 0.0064259 | 0.0062186 | 0.0060242 | 0.0058417 | 0.0056699 | 0.0055079 | 0.0053549 | 0.0052102 | 0.005073 | 0.004943 | 0.0048194 | 0.0047018 | 0.0045899 | 0.0044832 | 0.0043813 | 0.0042839 | 0.0041908 | 0.0041016 | 0.0040162 | 0.0039342 | 0.0038555
Hit Rate(cache) | 0.19278 | 0.28916 | 0.35342 | 0.40162 | 0.44017 | 0.4723 | 0.49984 | 0.52394 | 0.54536 | 0.56463 | 0.58216 | 0.59822 | 0.61305 | 0.62682 | 0.63967 | 0.65172 | 0.66306 | 0.67377 | 0.68392 | 0.69356 | 0.70274 | 0.7115 | 0.71988 | 0.72791 | 0.73562 | 0.74304 | 0.75018 | 0.75706 | 0.76371 | 0.77014 | 0.77635 | 0.78238 | 0.78822 | 0.79389 | 0.7994 | 0.80475 | 0.80996 | 0.81504 | 0.81998 | 0.8248 | 0.8295 | 0.83409 | 0.83857 | 0.84296 | 0.84724 | 0.85143 | 0.85553 | 0.85955 | 0.86348 | 0.86734

## Slide 35: Demand Paging
Modern programs require a lot of physical memory
  Memory per system growing faster than 25%-30%/year
But they don’t use all their memory all of the time
  90-10 rule: programs spend 90% of their time in 10% of their code
  Wasteful to require all of user’s code to be in memory
Solution: use main memory as cache for disk
On-Chip
Cache
Control
Datapath
Secondary
Storage
(Disk)
Processor
Main
Memory
(DRAM)
Second
Level
Cache
(SRAM)
Tertiary
Storage
(Tape)
Caching

## Slide 36: Illusion of Infinite Memory
Page
Table
TLB
Disk is larger than physical memory 
  In-use virtual memory can be bigger than physical memory
  Combined memory of running processes much larger than physical memory
    More programs fit into memory, allowing more concurrency
Principle: Transparent Level of Indirection (page table)
  Supports flexible placement of physical data
    Data could be on disk or somewhere across network
  Variable location of data transparent to user program
    Performance issue, not correctness issue
Physical
Memory
512 MB
Disk
500GB

Virtual
Memory
4 GB

## Slide 37: Demand Paging is Caching
Since Demand Paging is Caching, must ask:
  What is block size?
    1 page
  What is organization of this cache (i.e. direct-mapped, set-associative, fully-associative)?
    Fully associative: arbitrary virtualphysical mapping
  How do we find a page in the cache when look for it?
    First check TLB, then page-table traversal
  What is page replacement policy? (i.e. LRU, Random…)
    This requires more explanation… (kinda LRU)
  What happens on a miss?
    Go to lower level to fill miss (i.e. disk)
  What happens on a write? (write-through, write back)
    Definitely write-back. Need dirty bit!

## Slide 38: Review: What is in a PTE?
What is in a Page Table Entry (or PTE)?
  Pointer to next-level page table or to actual page
  Permission bits: valid, read-only, read-write, write-only
Example: Intel x86 architecture PTE:
  Address same format previous slide (10, 10, 12-bit offset)
  Intermediate page tables called “Directories”
  P: Present (same as “valid” bit in other architectures)
  W: Writeable
  U: User accessible
  PWT: Page write transparent: external cache write-through
  PCD: Page cache disabled (page cannot be cached)
  A: Accessed: page has been accessed recently
  D: Dirty (PTE only): page has been modified recently
  L: L=14MB page (directory only). Bottom 22 bits of virtual address serve as offset
Page Frame Number
(Physical Page Number)
Free
(OS)
0
L
D
A
PCD
PWT
U
W
P
0
1
2
3
4
5
6
7
8
11-9
31-12

## Slide 39: Demand Paging Mechanisms
Cache
PTE helps us implement demand paging
  Valid  Page in memory, PTE points at physical page
  Not Valid  Page not in memory; use info in PTE to find it on disk when necessary
Suppose user references page with invalid PTE?
  Memory Management Unit (MMU) traps to OS
    Resulting trap is a “Page Fault”
  What does OS do on a Page Fault?:
    Choose an old page to replace
    If old page modified (“D=1”), write contents back to disk
    Change its PTE and any cached TLB to be invalid
    Load new page into memory from disk
    Update page table entry, invalidate TLB for new entry
    Continue thread from original faulting location
  TLB for new page will be loaded when thread continued!
  While pulling pages off disk for one process, OS runs another process from ready queue
    Suspended process sits on wait queue

## Slide 40: Loading an executable into memory
.exe
  lives on disk in the file system
  contains contents of code & data segments, relocation entries and symbols
  OS loads it into memory, initializes registers (and initial stack pointer)
  program sets up stack and heap upon initialization: CRT0
disk (huge)
memory
code
data
info
exe

## Slide 41: Create Virtual Address Space of the Process
Utilized pages in the VAS are backed by a page block on disk
  called the backing store
  typically in an optimized block store, but can think of it like a file
disk (huge)
memory
code
data
heap
stack
kernel
process VAS
sbrk
kernel code & data
user page
frames
user pagetable

## Slide 42: Create Virtual Address Space of the Process
User Page table maps entire VAS
All the utilized regions are backed on disk
  swapped into and out of memory as needed
For every process
disk (huge, TB)
memory
code
data
heap
stack
kernel
process VAS (GBs)
kernel code & data
user page
frames
user pagetable
code
data
heap
stack

## Slide 43: Create Virtual Address Space of the Process
User Page table maps entire VAS
  resident pages to the frame in memory they occupy
  the portion of it that the HW needs to access must be resident in memory
disk (huge, TB)
memory
code
data
heap
stack
kernel
VAS – per process
kernel code & data
user page
frames
user pagetable
code
data
heap
stack
PT

## Slide 44: Provide Backing Store for VAS
User Page table maps entire VAS
Resident pages mapped to memory frames
For all other pages, OS must record where to find them on disk
disk (huge, TB)
memory
code
data
heap
stack
kernel
kernel code & data
user page
frames
user pagetable
code
data
heap
stack
VAS – per process

## Slide 45: What data structure is required to map non-resident pages to disk?
FindBlock(PID, page#) => disk_block
  Some OSs utilize spare space in PTE for paged blocks
  Like the PT, but purely software
Where to store it?
  In memory – can be compact representation if swap storage is contiguous on disk
  Could use hash table (like Inverted PT)
Usually want backing store for resident pages too.
May map code segment directly to on-disk image
  Saves a copy of code to swap file
May share code segment with multiple instances of the program

## Slide 46: Provide Backing Store for VAS
disk (huge, TB)
memory
kernel code & data
user page
frames
user pagetable
code
data
heap
stack
code
data
heap
stack
kernel
VAS 1
PT 1
code
data
heap
stack
kernel
VAS 2
PT 2
heap
stack
data

## Slide 47: On page Fault …
disk (huge, TB)
memory
kernel code & data
user page
frames
user pagetable
code
data
heap
stack
code
data
heap
stack
kernel
VAS 1
PT 1
code
data
heap
stack
kernel
VAS 2
PT 2
heap
stack
data
active process & PT

## Slide 48: On page Fault … find & start load
disk (huge, TB)
memory
kernel code & data
user page
frames
user pagetable
code
data
heap
stack
code
data
heap
stack
kernel
VAS 1
PT 1
code
data
heap
stack
kernel
VAS 2
PT 2
heap
stack
data
active process & PT

## Slide 49: On page Fault … schedule other P or T
disk (huge, TB)
memory
kernel code & data
user page
frames
user pagetable
code
data
heap
stack
code
data
heap
stack
kernel
VAS 1
PT 1
code
data
heap
stack
kernel
VAS 2
PT 2
heap
stack
data
active process & PT

## Slide 50: On page Fault … update PTE
disk (huge, TB)
memory
kernel code & data
user page
frames
user pagetable
code
data
heap
stack
code
data
heap
stack
kernel
VAS 1
PT 1
code
data
heap
stack
kernel
VAS 2
PT 2
heap
stack
data
active process & PT

## Slide 51: Eventually reschedule faulting thread
disk (huge, TB)
memory
kernel code & data
user page
frames
user pagetable
code
data
heap
stack
code
data
heap
stack
kernel
VAS 1
PT 1
code
data
heap
stack
kernel
VAS 2
PT 2
heap
stack
data
active process & PT

## Slide 52: Summary: Steps in Handling a Page Fault

## Slide 53: Demand Paging (more details)
Does software-loaded TLB need use bit? Two Options:
  Hardware sets use bit in TLB; when TLB entry is replaced, software copies use bit back to page table
  Software manages TLB entries as FIFO list; everything not in TLB is Second-Chance list, managed as strict LRU
Core Map
  Page tables map virtual page  physical page
  Do we need a reverse mapping (i.e. physical page  virtual page)?
    Yes. Clock algorithm runs through page frames. If sharing, then multiple virtual-pages per physical page
    Can’t push page out to disk without invalidating all PTEs

## Slide 54: Summary (1/2)
The Principle of Locality:
  Program likely to access a relatively small portion of the address space at any instant of time.
    Temporal Locality: Locality in Time
    Spatial Locality: Locality in Space
Three (+1) Major Categories of Cache Misses:
  Compulsory Misses: sad facts of life. Example: cold start misses.
  Conflict Misses: increase cache size and/or associativity
  Capacity Misses: increase cache size
  Coherence Misses: Caused by external processors or I/O devices
Cache Organizations:
  Direct Mapped: single block per set
  Set associative: more than one block per set
  Fully associative: all entries equivalent
Notes: Let’s summarize today’s lecture. I know you have heard this many times and many ways but it is still worth repeating.
Memory hierarchy works because of the Principle of Locality which says a program will access a relatively small portion of the address space at any instant of time.
There are two types of locality: temporal locality, or locality in time and spatial locality, or locality in space.
So far, we have covered three major categories of cache misses.
Compulsory misses are cache misses due to cold start. You cannot avoid them but if you are going to run billions of instructions anyway, compulsory misses usually don’t bother you.
Conflict misses are misses caused by multiple memory location being mapped to the same cache location.
The nightmare scenario is the ping pong effect when a block is read into the cache but before we have a chance to use it, it was immediately forced out by another conflict miss.
You can reduce Conflict misses by either increase the cache size or increase the associativity, or both.
Finally, Capacity misses occurs when the cache is not big enough to contains all the cache blocks required by the program. You can reduce this miss rate by making the cache larger.
There are two write policy as far as cache write is concerned. Write through requires a write buffer and a nightmare scenario is when the store occurs so frequent that you saturates your write buffer.
The second write polity is write back. In this case, you only write to the cache and only when the cache block is being replaced do you write the cache block back to memory.
+3 = 77 min. (Y:57)

## Slide 55: Summary (2/2)
A cache of translations called a “Translation Lookaside Buffer” (TLB)
  Relatively small number of entries (< 512)
  Fully Associative (Since conflict misses expensive)
  TLB entries contain PTE and optional process ID
On TLB miss, page table must be traversed
  If located PTE is invalid, cause Page Fault
On context switch/change in page table
  TLB entries must be invalidated somehow
TLB is logically in front of cache
  Thus, needs to be overlapped with cache access to be really fast
Precise Exception specifies a single instruction for which:
  All previous instructions have completed (committed state)
  No following instructions nor actual instruction have started
Notes: No fancy replacement policy is needed for the direct mapped cache.
As a matter of fact, that is what cause direct mapped trouble to begin with: only one place to go in the cache--causes conflict misses.
No fancy replacement policy is needed for the direct mapped cache.
As a matter of fact, that is what cause direct mapped trouble to begin with: only one place to go in the cache--causes conflict misses.
Besides working at Sun, I also teach people how to fly whenever I have time.
Statistic have shown that if a pilot crashed after an engine failure, he or she is more likely to get killed in a multi-engine light airplane than a single engine airplane.
The joke among us flight instructors is that: sure, when the engine quit in a single engine stops, you have one option: sooner or later, you land. Probably sooner.
But in a multi-engine airplane with one engine stops, you have a lot of options. It is the need to make a decision that kills those people.