## Slide 1: CS162 Operating Systems and Systems Programming Lecture 18 Queuing Theory, File Systems
November 2nd, 2015
Prof. John Kubiatowicz
http://cs162.eecs.Berkeley.edu

## Slide 2: Recall: I/O Performance
Response Time = Queue + I/O device service time
User
Thread
Queue
[OS Paths]
Controller
I/O
device
Performance of I/O subsystem
  Metrics: Response Time, Throughput
  Effective BW per op = transfer size / response time
    EffBW(n) = n / (S + n/B) = B / (1 + SB/n )
  Contributing factors to latency:
    Software paths (can be loosely modeled by a queue)
    Hardware controller
    I/O device service time
Queuing behavior:
  Can lead to big increases of latency as utilization increases
  Solutions?
100%
Response
Time (ms)
Throughput (Utilization)
(% total BW)
0
100
200
300
0%

## Slide 3: A Simple Deterministic World
Assume requests arrive at regular intervals, take a fixed time to process, with plenty of time between …
Service rate (μ = 1/TS) - operations per sec
Arrival rate: (λ = 1/TA) - requests per second
Utilization: U = λ/μ , where λ < μ
Average rate is the complete story
Queue
Server
arrivals
departures
TQ
TS
TA
TA
TA

## Slide 4: A Ideal Linear World
What does the queue wait time look like?
  Grows unbounded at a rate ~ (Ts/TA) till request rate subsides
Offered Load (TS/TA)
Delivered Throughput
0
1
1
time
Queue delay
time
Queue delay
Delivered Throughput
0
1
1
Offered Load (TS/TA)
Empty Queue
Saturation
Unbounded

## Slide 5: A Bursty World
Requests arrive in a burst, must queue up till served
Same average arrival time, but almost all of the requests experience large queue delays
Even though average utilization is low
Queue
Server
arrivals
departures
T Q
T S
Q depth
Server
Arrivals

## Slide 6: So how do we model the burstiness of arrival?
Chart: 
| 1E-3 | 0.01 | 0.02 | 0.04 | 0.08 | 0.16 | 0.32 | 0.64 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 10
f(x) | 0.999 | 0.99005 | 0.9802 | 0.96079 | 0.92312 | 0.85214 | 0.72615 | 0.52729 | 0.36788 | 0.13534 | 0.049787 | 0.018316 | 0.0067379 | 0.0024788 | 0.00091188 | 0.00033546 | 4.54e-05
Likelihood of an event occuring is independent of how long we’ve been waiting
Elegant mathematical framework if you start with exponential distribution
  Probability density function of a continuous random variable with a mean of 1/λ
  f(x) = λe-λx
  “Memoryless”
Lots of short arrival intervals (i.e., high instantaneous rate)
Few long gaps (i.e., low instantaneous rate)
x (λ)
mean arrival interval (1/λ)

## Slide 7: Background: General Use of random distributions
Server spends variable time with customers
  Mean (Average) m1 = p(T)T
  Variance 2 = p(T)(T-m1)2 = p(T)T2-m12
  Squared coefficient of variance: C = 2/m12 Aggregate description of the distribution.
Important values of C:
  No variance or deterministic  C=0
  “memoryless” or exponential  C=1
    Past tells nothing about future
    Many complex systems (or aggregates) well described as memoryless
  Disk response times C  1.5 (majority seeks < avg)
Mean
(m1)
mean
Memoryless
Distribution
of service times


## Slide 8: Introduction to Queuing Theory
Departures
Arrivals
Queuing System
What about queuing time??
  Let’s apply some queuing theory
  Queuing Theory applies to long term, steady state behavior  Arrival rate = Departure rate
Arrivals characterized by some probabilistic distribution
Departures characterized by some probabilistic distribution
Queue
Controller
Disk
Notes: Old and New Testament by Kleirock
Regret skipping as grad student

## Slide 9: Little’s Law
In any stable system
  Average arrival rate = Average departure rate
the average number of tasks in the system (N) is equal to the throughput (B) times the response time (L)
N (ops) = B (ops/s) x L (s)
Regardless of structure, bursts of requests, variation in service
  instantaneous variations, but it washes out in the average
  Overall requests match departures
arrivals
departures
N
B
L

## Slide 10: A Little Queuing Theory: Some Results
Assumptions:
  System in equilibrium; No limit to the queue
  Time between successive arrivals is random and memoryless
Parameters that describe our system:
  : mean number of arriving customers/second
  Tser: mean time to service a customer (“m1”)
  C: squared coefficient of variance = 2/m12
  μ: service rate = 1/Tser
  u: server utilization (0u1): u = /μ =   Tser
Parameters we wish to compute:
  Tq: Time spent in queue
  Lq: Length of queue =   Tq (by Little’s law)
Results:
  Memoryless service distribution (C = 1):
    Called M/M/1 queue: Tq = Tser x u/(1 – u)
  General service distribution (no restrictions), 1 server:
    Called M/G/1 queue: Tq = Tser x ½(1+C) x u/(1 – u))
Arrival Rate

Queue
Server
Service Rate
μ=1/Tser

## Slide 11: A Little Queuing Theory: An Example
Example Usage Statistics:
  User requests 10 x 8KB disk I/Os per second
  Requests & service exponentially distributed (C=1.0)
  Avg. service = 20 ms (From controller+seek+rot+trans)
Questions:
  How utilized is the disk?
    Ans: server utilization, u = Tser
  What is the average time spent in the queue?
    Ans: Tq
  What is the number of requests in the queue?
    Ans: Lq
  What is the avg response time for disk request?
    Ans: Tsys = Tq + Tser
Computation:
 (avg # arriving customers/s) = 10/s
Tser (avg time to service customer) = 20 ms (0.02s)
u (server utilization) =  x Tser= 10/s x .02s = 0.2
Tq (avg time/customer in queue) = Tser x u/(1 – u) = 20 x 0.2/(1-0.2) = 20 x 0.25 = 5 ms (0 .005s)
Lq (avg length of queue) =  x Tq=10/s x .005s = 0.05
Tsys (avg time/customer in system) =Tq + Tser= 25 ms

## Slide 12: Queuing Theory Resources
Handouts page contains Queueing Theory Resources:
  Scanned pages from Patterson and Hennesey book that gives further discussion and simple proof for general eq.
  A complete website full of resources
Midterms with queueing theory questions:
  Midterm IIs from previous years that I’ve taught
Assume that Queueing theory is fair game for Midterm II and/or the final!

## Slide 13: Administrivia
HW3 – Moved deadline to Wednesday (11/04)
  Sorry about fact that server was down!
Project 2 code due this Friday!
Midterm I Regrade requests: Due this Wednesday
Midterm II: Coming up in 3 weeks! (11/23)
  7-10PM, “here” (2040, 2050, 2060 VLSB)
  Topics up to and including previous Wednesday
  2 pages of hand-written notes, both sides

## Slide 14: Quick Aside: Big Projects
What is a big project?
  Time/work estimation is hard
  Programmers are eternal optimistics (it will only take two days)!
    This is why we bug you about starting the project early
    Had a grad student who used to say he just needed “10 minutes” to fix something. Two hours later…
Can a project be efficiently partitioned?
  Partitionable task decreases in time as you add people
  But, if you require communication:
    Time reaches a minimum bound
    With complex interactions, time increases!
  Mythical person-month problem:
    You estimate how long a project will take
    Starts to fall behind, so you add more people
    Project takes even more time!

## Slide 15: Techniques for Partitioning Tasks
Functional
  Person A implements threads, Person B implements semaphores, Person C implements locks…
  Problem: Lots of communication across APIs
    If B changes the API, A may need to make changes
    Story: Large airline company spent $200 million on a new scheduling and booking system. Two teams “working together.” After two years, went to merge software. Failed! Interfaces had changed (documented, but no one noticed). Result: would cost another $200 million to fix.
Task
  Person A designs, Person B writes code, Person C tests
  May be difficult to find right balance, but can focus on each person’s strengths (Theory vs systems hacker)
  Since Debugging is hard, Microsoft has two testers for each programmer
Most CS162 project teams are functional, but people have had success with task-based divisions

## Slide 16: Communication
More people mean more communication
  Changes have to be propagated to more people
  Think about person writing code for most fundamental component of system: everyone depends on them!
  You should be meeting in person at least twice/week!
Miscommunication is common
  “Index starts at 0? I thought you said 1!”
Who makes decisions?
  Individual decisions are fast but trouble
  Group decisions take time
  Centralized decisions require a big picture view (someone who can be the “system architect”)
Often designating someone as the system architect can be a good thing
  Better not be clueless
  Better have good people skills
  Better let other people do work

## Slide 17: Coordination
More people  no one can make all meetings!
  They miss decisions and associated discussion
  Example from earlier class: one person missed meetings and did something group had rejected
People have different work styles
  Some people work in the morning, some at night
  How do you decide when to meet or work together?
What about project slippage?
  It will happen, guaranteed!
  Example: phase 4 of one project, everyone busy but not talking. One person way behind. No one knew until very end – too late!
Hard to add people to existing group
  Members have already figured out how to work together

## Slide 18: Optimize I/O Performance
Howto improve performance?
  Make everything faster 
  More Decoupled (Parallelism) systems
    multiple independent buses or controllers
  Optimize the bottleneck to increase service rate
    Use the queue to optimize the service
  Do other useful work while waiting
Queues absorb bursts and smooth the flow
Admissions control (finite queues)
  Limits delays, but may introduce unfairness and livelock
Response Time = Queue + I/O device service time
User
Thread
Queue
[OS Paths]
Controller
I/O
device
100%
Response
Time (ms)
Throughput (Utilization)
(% total BW)
0
100
200
300
0%

## Slide 19: When is the disk performance highest?
When there are big sequential reads, or
When there is so much work to do that they can be piggy backed (reordering queues—one moment)
OK, to be inefficient when things are mostly idle
Bursts are both a threat and an opportunity
<your idea for optimization goes here>
  Waste space for speed?
Other techniques:
  Reduce overhead through user level drivers
  Reduce the impact of I/O delays by doing other useful work in the meantime

## Slide 20: Disk Scheduling
Disk can do only one request at a time; What order do you choose to do queued requests?
FIFO Order
  Fair among requesters, but order of arrival may be to random spots on the disk  Very long seeks
SSTF: Shortest seek time first
  Pick the request that’s closest on the disk
  Although called SSTF, today must include rotational delay in calculation, since rotation can be as long as seek
  Con: SSTF good at reducing seeks, but may lead to starvation
SCAN: Implements an Elevator Algorithm: take the closest request in the direction of travel
  No starvation, but retains flavor of SSTF
C-SCAN: Circular-Scan: only goes in one direction
  Skips any requests on the way back
  Fairer than SCAN, not biased towards pages in middle
2,3
2,1
3,10
7,2
5,2
2,2
Head
User
Requests
1
4
2
Disk Head
3

## Slide 21: Review: Device Drivers
Device Driver: Device-specific code in the kernel that interacts directly with the device hardware
  Supports a standard, internal interface
  Same kernel I/O system can interact easily with different device drivers
  Special device-specific configuration supported with the ioctl() system call
Device Drivers typically divided into two pieces:
  Top half: accessed in call path from system calls
    implements a set of standard, cross-device calls like open(), close(), read(), write(), ioctl(), strategy()
    This is the kernel’s interface to the device driver
    Top half will start I/O to device, may put thread to sleep until finished
  Bottom half: run as interrupt routine
    Gets input or transfers next block of output
    May wake sleeping threads if I/O now complete

## Slide 22: Kernel vs User-level I/O
Both are popular/practical for different reasons:
  Kernel-level drivers for critical devices that must keep running, e.g. display drivers.
    Programming is a major effort, correct operation of the rest of the kernel depends on correct driver operation.
  User-level drivers for devices that are non-threatening, e.g USB devices in Linux (libusb).
    Provide higher-level primitives to the programmer, avoid every driver doing low-level I/O register tweaking.
    The multitude of USB devices can be supported by Less-Than-Wizard programmers.
    New drivers don’t have to be compiled for each version of the OS, and loaded into the kernel.

## Slide 23: Kernel vs User-level Programming Styles
Kernel-level drivers
  Have a much more limited set of resources available:
    Only a fraction of libc routines typically available.
    Memory allocation (e.g. Linux kmalloc) much more limited in capacity and required to be physically contiguous.
    Should avoid blocking calls.
    Can use asynchrony with other kernel functions but tricky with user code.
User-level drivers
  Similar to other application programs but:
    Will be called often – should do its work fast, or postpone it – or do it in the background.
    Can use threads, blocking operations (usually much simpler) or non-blocking or asynchronous.

## Slide 24: Performance: multiple outstanding requests
Suppose each read takes 10 ms to service.
If a process works for 100 ms after each read, what is the utilization of the disk?
  U = 10 ms / 110ms = 9%
What it there are two such processes?
  U = (10 ms + 10 ms) / 110ms = 18%
What if each of those processes have two such threads?
Queue
Server

## Slide 25: Recall: How do we hide I/O latency?
Blocking Interface: “Wait”
  When request data (e.g., read() system call), put process to sleep until data is ready
  When write data (e.g., write() system call), put process to sleep until device is ready for data
Non-blocking Interface: “Don’t Wait”
  Returns quickly from read or write request with count of bytes successfully transferred to kernel
  Read may return nothing, write may write nothing
Asynchronous Interface: “Tell Me Later”
  When requesting data, take pointer to user’s buffer, return immediately; later kernel fills buffer and notifies user
  When sending data, take pointer to user’s buffer, return immediately; later kernel takes data and notifies user

## Slide 26: I/O & Storage Layers
High Level I/O
Low Level I/O
Syscall
File System
I/O Driver
Application / Service
streams
handles
registers
descriptors
Commands and Data Transfers
Disks, Flash, Controllers, DMA
Operations, Entities and Interface
file_open, file_read, … on struct file * & void *
we are here …

## Slide 27: Recall: C Low level I/O
Operations on File Descriptors – as OS object representing the state of a file
  User has a “handle” on the descriptor
#include <fcntl.h>
#include <unistd.h>
#include <sys/types.h>
int open (const char *filename, int flags [, mode_t mode])
int creat (const char *filename, mode_t mode)
int close (int filedes)
Bit vector of:
Access modes (Rd, Wr, …)
Open Flags (Create, …)
Operating modes (Appends, …)
Bit vector of Permission Bits:
User|Group|Other X R|W|X
http://www.gnu.org/software/libc/manual/html_node/Opening-and-Closing-Files.html

## Slide 28: Recall: C Low Level Operations
When write returns, data is on its way to disk and can be read, but it may not actually be permanent!
ssize_t read (int filedes, void *buffer, size_t maxsize)
- returns bytes read, 0 => EOF, -1 => error
ssize_t write (int filedes, const void *buffer, size_t size)
- returns bytes written
off_t lseek (int filedes, off_t offset, int whence)
int fsync (int fildes) – wait for i/o to finish
void sync (void) – wait for ALL to finish

## Slide 29: Building a File System
File System: Layer of OS that transforms block interface of disks (or other block devices) into Files, Directories, etc.
File System Components
  Disk Management: collecting disk blocks into files
  Naming: Interface to find files by name, not by blocks
  Protection: Layers to keep data secure
  Reliability/Durability: Keeping of files durable despite crashes, media failures, attacks, etc
User vs. System View of a File
  User’s view:
    Durable Data Structures
  System’s view (system call interface):
    Collection of Bytes (UNIX)
    Doesn’t matter to system what kind of data structures you want to store on disk!
  System’s view (inside OS):
    Collection of blocks (a block is a logical transfer unit, while a sector is the physical transfer unit)
    Block size  sector size; in UNIX, block size is 4KB

## Slide 30: Translating from User to System View
What happens if user says: give me bytes 2—12?
  Fetch block corresponding to those bytes
  Return just the correct portion of the block
What about: write bytes 2—12?
  Fetch block
  Modify portion
  Write out Block
Everything inside File System is in whole size blocks
  For example, getc(), putc()  buffers something like 4096 bytes, even if interface is one byte at a time
From now on, file is a collection of blocks
File
System

## Slide 31: So you are going to design a file system …
What factors are critical to the design choices?
Durable data store => it’s all on disk
Disks Performance !!!
  Maximize sequential access, minimize seeks
Open before Read/Write
  Can perform protection checks and look up where the actual file resource are, in advance
Size is determined as they are used !!!
  Can write (or read zeros) to expand the file
  Start small and grow, need to make room
Organized into directories
  What data structure (on disk) for that?
Need to allocate / free blocks
  Such that access remains efficient

## Slide 32: Disk Management Policies
Basic entities on a disk:
  File: user-visible group of blocks arranged sequentially in logical space
  Directory: user-visible index mapping names to files (next lecture)
Access disk as linear array of sectors. Two Options:
  Identify sectors as vectors [cylinder, surface, sector]. Sort in cylinder-major order. Not used much anymore.
  Logical Block Addressing (LBA). Every sector has integer address from zero up to max number of sectors.
  Controller translates from address  physical position
    First case: OS/BIOS must deal with bad sectors
    Second case: hardware shields OS from structure of disk
Need way to track free disk blocks
  Link free blocks together  too slow today
  Use bitmap to represent free space on disk
Need way to structure files: File Header
  Track which blocks belong at which offsets within the logical file structure
  Optimize placement of files’ disk blocks to match access and usage patterns

## Slide 33: Components of a File System
Directory
Structure
File path
File Index
Structure
File number
…
Data blocks

## Slide 34: Components of a file system
Open performs name resolution
  Translates pathname into a “file number”
    Used as an “index” to locate the blocks
  Creates a file descriptor in PCB within kernel
  Returns a “handle” (another int) to user process
Read, Write, Seek, and Sync operate on handle
  Mapped to descriptor and to blocks
file name
offset
directory
file number
offset
index structure
Storage block

## Slide 35: Directories

## Slide 36: Directory
Basically a hierarchical structure
Each directory entry is a collection of
  Files
  Directories
    A link to another entries
Each has a name and attributes
  Files have data
Links (hard links) make it a DAG, not just a tree
  Softlinks (aliases) are another name for an entry

## Slide 37: I/O & Storage Layers
High Level I/O
Low Level I/O
Syscall
File System
I/O Driver
Application / Service
streams
handles
registers
descriptors
Commands and Data Transfers
Disks, Flash, Controllers, DMA
…
Data blocks
#4 - handle
Directory Structure

## Slide 38: File
Named permanent storage
Contains
  Data
    Blocks on disk somewhere
  Metadata (Attributes)
    Owner, size, last opened, …
    Access rights
      R, W, X
      Owner, Group, Other (in Unix systems)
      Access control list in Windows system
…
Data blocks
File descriptor
Fileobject (inode)
Position
File handle

## Slide 39: Summary
Queuing Latency:
  M/M/1 and M/G/1 queues: simplest to analyze
  As utilization approaches 100%, latency  
  Tq = Tser x ½(1+C) x u/(1 – u))
File System:
  Transforms blocks into Files and Directories
  Optimize for access and usage patterns
  Maximize sequential access, allow efficient random access
File (and directory) defined by header, called “inode”
Multilevel Indexed Scheme
  Inode contains file info, direct pointers to blocks,
  indirect blocks, doubly indirect, etc..
4.2 BSD Multilevel index files
  Inode contains pointers to actual blocks, indirect blocks, double indirect blocks, etc.
  Optimizations for sequential access: start new files in open ranges of free blocks, rotational Optimization