## Slide 1: CS 162: Operating Systems and Systems Programming
November 26, 2019
Instructor: David E. Culler
https://cs162.eecs.berkeley.edu
Lecture 25: End-to-End Architecture and TCP

## Slide 2: Recall: Two-Phase Commit
Consensus Goal: Everyone agrees on the state of the distributed system
  Doesn’t depend who you ask. Doesn’t matter if nodes go down
Distributed Transactions
  Atomic, can’t revert once agreement is reached
Voting protocol requires unanimity
Transaction committed if and only if: all workers and coordinator vote to commit
  Nodes never take back their vote
  Nodes work in lock step (for an item)
    Don’t perform new transactions until old one is resolved
    Stall until transaction is resolved
Majority-based protocols make progress despite failed nodes
  Add considerable complexity

## Slide 3: Bottom line: in a network . . .
All distributed systems boil down to message passing
  Across a network, the internet
  Spread across the world
Things fail
  Nodes die, software crashes, routers too, messages get corrupted in flight, …
  Dealing with reliability / failure is inherent
  Many techniques to utilize
Limited knowledge of what happened is fundamental
Question is what steps are taken at what level ?
  What is the “contract” with the infrastructure?
  What can we reason from and what can we not?

## Slide 4: The E2E Concept
Traditional Engineering Goal: design the infrastructure to meet application requirements
  Optimizing for Cost, Reliability, Performance, …
Challenge: infrastructure is most costly & difficult to create and evolves most slowly
  Applications evolve rapidly, as does technology
End-to-end Design Concept
  Utilize intelligence at the point of application
  Infrastructure need not meet all application requirements directly
  Only what the end-points cannot reasonably do themselves
    Avoid redundancy, semantic mismatch, …
  Enable applications and incorporate technological advance
Design for Change! - and specialization
  Layers & protocols

## Slide 5: Recall: Sockets over TCP/IP
socket
Request Connection
Server
Client
Special kind of socket: server socket
  Has file descriptor
  Can’t read or write
Two operations:
  listen(): Start allowing clients to connect
  accept(): Create a new socket for a particular client connection
Server
Socket
connection
new
socket
Connection
socket
connection

## Slide 6: Socket Setup over TCP/IP
5-Tuple identifies each connection:
  Source IP Address
  Destination IP Address
  Source Port Number
  Destination Port Number
  Protocol (TCP here)
  Often, Client Port “randomly” assigned
    Done by OS during client socket setup
  Server Port often “well known”
    80 (web), 443 (secure web), 25 (sendmail), etc
    Well-known ports from 0—1023
socket
Request Connection
Server
Client
Server
Socket
connection
new
socket
Connection
socket
connection

## Slide 7: Recall: Sockets in Schematic
Client
Server
read response
Close Client Socket
Create Client Socket
Connect it to server (host:port)
Create Server Socket
Bind it to an Address
(host:port)
Listen for Connection
Close Connection Socket
Close Server Socket
write request
write response
Accept syscall()
Connection Socket
Connection Socket
read request

## Slide 8: Linux Network Architecture

## Slide 9: Networking Challenge
Many different applications
  Email, Web, Online Games, etc.
Many different network types and technologies
  Wireless, Wired, Optical, etc.
Inherently distributed, parts can fail, no overall management authority, …
How do we manage this complexity?
Such that the whole is more “reliable” than its parts
  Available, despite underlying unreliability

## Slide 10: Networking Challenge
Re-implement every application for every technology?
No
Skype
SSH
NFS
Packet
Radio
Coaxial
cable
Fiber
optic
Application
Transmission
Media
HTTP

## Slide 11: Networking Challenge
Re-implement sockets for every technology?
No
Skype
SSH
NFS
Coaxial
cable
Fiber
optic
Application
Transmission
Media
HTTP
Sockets
UDP/IPv4
UDP/IPv6
TCP/IPv4
TCP/IPv6

## Slide 12: Layering
Complex services from simpler ones
  Physical and Link Layers (Wi-Fi, Ethernet, …)
    Unreliable, local exchange of limited-size frames
  Network (IP) – routing between local networks
    Unreliable, global exchange of limited-size packets
  Transport (e.g., TCP or UDP) – Glue
    Reliable (with retries), ordering, stream of bytes
    Not-neccesarily reliable datagrams (UDP)
  Application – Everything on top of sockets

## Slide 13: The Internet Hourglass
Data Link
Physical
Applications
The Hourglass Model
Waist
SMTP
HTTP
NTP
DNS
TCP
UDP
IP
Ethernet
SONET
802.11
Transport
Fiber
Copper
Radio
Sockets – the OS “Hourglass”

## Slide 14: Internet Protocol (IP)
Internet Protocol: Internet’s network layer
Service it provides: “Best-Effort” Packet Delivery
  Tries it’s “best” to deliver packet to its destination
  Packets may be lost
  Packets may be corrupted
  Packets may be delivered out of order
source
destination
IP network
Transport
Network
Datalink
Physical
Session
Present.
Application

## Slide 15: Internet: Network of Networks
subnet1
subnet2
Router
Other
subnets
Router
Router
Transcontinental
Link
subnet3
Other
subnets
Hierarchy of Networks: Scales to billions of hosts

## Slide 16: Internet Protocol Features
Routing – an IP packet goes anywhere
  Just need the destination IP address
Fragmentation – split big messages into smaller pieces
  Think about downloading a file
  Maximum size 64K
  Reassemble at destination
  Hides differences in link/physical layers
Multiple protocols running on top
  ICMP, TCP, UDP, …

## Slide 17: Internet Protocol "Non-Features"
Unreliable Delivery ("Best Effort")
  IP packet delivery not guaranteed
  May be lost by underlying physical layer (e.g., radio noise)
  May be dropped in transit
Out-of-order/duplicate delivery
  Tolerance of physical layer retrying transmission
  Tolerance of multiple paths

## Slide 18: Internet Architecture: The Five Layers
Lower three layers implemented everywhere
Top two layers implemented only at hosts
Logically, layers interacts with peer’s corresponding layer
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
Host A
Host B
Router
sockets
sockets

## Slide 19: Physical Communication
Communication goes down to physical network
Then from network peer to peer
Then up to relevant layer
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
Host A
Host B
Router

## Slide 20: Implications of Hourglass
There is only one Network-Layer Protocol: IP
Allows networks to interoperate
Above IP: Applications function on all networks
Below IP: Change network’s construction without disturbing applications
One drawback: Changing IP itself (e.g. transitioning to IPv6) very involved

## Slide 21: End-to-End Principal
Seen as a guiding principle of the Internet
Some types of network functionality can only be correctly implemented end-to-end
  Reliability, security, etc.
Implementing complex functionality in the network:
  Doesn’t necessarily reduce complexity on end hosts
  Does increase network complexity
  Imposes a cost on all applications, even if they don’t need the functionality

## Slide 22: Example: Reliable File Transfer
Solution 1: make each step reliable, and then concatenate them
Solution 2: end-to-end check and try again if necessary
OS
Appl.
OS
Appl.
Host A
Host B
OK

## Slide 23: Summary: Network Layers
Link Layer (local network)
  Send frames addressed to neighboring machines
  Ethernet, Wi-Fi
Network layer (connecting local networks)
  Forwarding between local networks
  Send packets addressed to machines anywhere
  IP
Transport Layer (making streams)
  Turn sequence of packets into reliable byte stream
  TCP
OS: Sockets abstraction : Application
  File Handle, Read/Write like files
  But setup/teardown very different from open/close

## Slide 24: Layering: Packets in Envelopes
101010100110101110
Physical Layer
Physical Layer
101010100110101110
Datalink Layer
Trans.
Hdr.
Net.
Hdr.
Frame
Hdr.
Datalink Layer
Trans.
Hdr.
Net.
Hdr.
Frame
Hdr.
Data
Data
Network Layer
Trans.
Hdr.
Net.
Hdr.
Network Layer
Trans.
Hdr.
Net.
Hdr.
Data
Data
Transport Layer
Trans.
Hdr.
Transport Layer
Trans.
Hdr.
Data
Data
Data
Application Layer
Application Layer
Data

## Slide 25: Ordered Messages: Problem
Want to divide a message into packets / frames
Think about downloading a file over IP
  64K max packet size
IP might reorder these packets
  Imagine receiving the end of a file before the beginning!

## Slide 26: Ordered Messages: Solution
Simulate ordered messages on top of unordered messages
Assign each packet a sequence number: 0, 1, 2, 3, …
  If packets arrive out of order, hold on to them
  Deliver them in order to user (through socket interface)
Example: Hold on to #3 until #2 arrives, etc.

## Slide 27: Reliable Message Delivery: Problem
All physical networks can garble or drop packets
  Physical hardware problems (bad wire, bad signal)
Therefore, IP can garble or drop packets
  It doesn't repair this itself (end-to-end principle!)
Building reliable message delivery
  Confirm that packets aren't garbled
  Confirm that packets arrive exactly once

## Slide 28: Using Acknowledgements
Checksum: Detect garbled packets
Receiver sends a packet to acknowledge when a packet received and ungarbled
  No acknowledgement? Resend after timeout
What if acknowledgement dropped?
  Packet is resent (wasteful), second chance to acknowledge
B
A
Packet
ack
B
A
Packet
ack
Packet
Timeout

## Slide 29: What about duplicates?
Add a Sequence Number
Wait for its Ack before sending the next
  “stop and wait”
Latency limits bandwidth
  Remember Little’s Law
  N = L*B
With sequence #s can detect duplicates and maintain order
B
A
Pkt #0
Ack #0
Pkt #1
Ack #1
Pkt #2
Ack #2

## Slide 30: Window-Based Acknowledgements
Windowing protocol (not quite TCP)
Send up to N packets without ack
  Allows pipelining of packets
  N limits queue size
Both source and destination need to store N packets (why?)
Each packet has sequence number
  ACK says "Received all packets up to number X"
  Advances window
B
A
N=5
Queue
ack#0
ack#4
pkt#0
pkt#4

## Slide 31: Transport Layer (4)
Service:
  Provide end-to-end communication between processes
  Demultiplexing of communication between hosts
  Possible other services:
    Reliability in the presence of errors
    Timing properties
    Rate adaption (flow-control, congestion control)
Interface: send message to “specific process” at given destination; local process receives messages sent to it
  How are they named?
Protocol: port numbers, perhaps implement reliability, flow control, packetization of large messages, framing
Prime Examples: TCP and UDP
Transport
Network
Datalink
Physical
Session
Present.
Application

## Slide 32: Internet Transport Protocols
Datagram service (UDP)
  No-frills extension of “best-effort” IP
  Multiplexing/Demultiplexing among processes
Reliable, in-order delivery (TCP)
  Connection set-up & tear-down
  Discarding corrupted packets (segments)
  Retransmission of lost packets (segments)
  Flow control
  Congestion control
Services not available
  Delay and/or bandwidth guarantees
  Sessions that survive change-of-IP-address
Transport
Network
Datalink
Physical
Session
Present.
Application

## Slide 33: Application Layer (7 - not 5!)
Service: any service provided to the end user
Interface: depends on the application
Protocol: depends on the application
Examples: Skype, SMTP (email), HTTP (Web), Halo, BitTorrent …
What happened to layers 5 & 6?
  “Session” and “Presentation” layers
  Part of OSI architecture, but not Internet architecture
  Their functionality is provided by application layer
Transport
Network
Datalink
Physical
Session
Present.
Application

## Slide 34: Socket API
Base level Network programming interface
Socket
API
TCP
UDP
IP
Application
Transport
Network

## Slide 35: BSD Socket API
Created at UC Berkeley (1980s)
Most popular network API
Ported to various OSes, various languages
  Windows Winsock, BSD, OS X, Linux, Solaris, …
  Socket modules in Java, Python, Perl, …
Similar to Unix file I/O API
  In the form of file descriptor (sort of handle).
  Can share same read()/write()/close() system calls

## Slide 36: TCP: Transport Control Protocol
Reliable, in-order, and at most once delivery
Stream oriented: messages can be of arbitrary length
Provides multiplexing/demultiplexing to IP
Provides congestion and flow control
Application examples: file transfer, chat, http

## Slide 37: TCP Service
Open connection: 3-way handshaking
Reliable byte stream transfer from (IPa, TCP_Port1) to (IPb, TCP_Port2)
  Indication if connection fails: Reset
Close (tear-down) connection

## Slide 38: Recall: Socket creation and connection
File systems provide a collection of permanent objects in structured name space
  Processes open, read/write/close them
  Files exist independent of the processes
Sockets provide a means for processes to communicate (transfer data) to other processes.
Creation and connection is more complex
Form 2-way pipes between processes
  Possibly worlds away

## Slide 39: Recall: Client Protocol
char *hostname;
int sockfd, portno;
struct sockaddr_in serv_addr;
struct hostent *server;
server = buildServerAddr(&serv_addr, hostname, portno);
/* Create a TCP socket */
sockfd = socket(AF_INET, SOCK_STREAM, 0)
/* Connect to server on port */
connect(sockfd, (struct sockaddr *) &serv_addr, sizeof(serv_addr)
printf("Connected to %s:%d\n",server->h_name, portno);
/* Carry out Client-Server protocol */
client(sockfd);
/* Clean up on termination */
close(sockfd);
Notes: Addressing Family, vs Protocol Family. Still see PF_INET in the man page. But AF_INET is what is used everywhere

## Slide 40: Recall: Sockets in Schematic
Client
Server
read response
Close Client Socket
Create Client Socket
Connect it to server (host:port)
Create Server Socket
Bind it to an Address
(host:port)
Listen for Connection
Close Connection Socket
Close Server Socket
write request
write response
Accept syscall()
Connection Socket
Connection Socket
read request

## Slide 41: Open Connection: 3-Way Handshaking
Goal: agree on a set of parameters, i.e., the start sequence number for each side
  Starting sequence number: sequence of first byte in stream
  Starting sequence numbers are random

## Slide 42: Open Connection: 3-Way Handshaking
Server waits for new connection calling listen()
Sender call connect() passing socket which contains server’s IP address and port number
  OS sends a special packet (SYN) containing a proposal for first sequence number, x
Client (initiator)
Server
SYN, SeqNum = x
Active Open
Passive Open
connect()
listen()
time

## Slide 43: Open Connection: 3-Way Handshaking
If it has enough resources, server calls accept() to accept connection, and sends back a SYN ACK packet containing
  Client’s sequence number incremented by one, (x + 1)
    Why is this needed?
  A sequence number proposal, y, for first byte server will send
Client (initiator)
Server
SYN, SeqNum = x
SYN and ACK, SeqNum = y and Ack = x + 1
ACK, Ack = y + 1
Active Open
Passive Open
connect()
listen()
accept()
allocate buffer space
time

## Slide 44: 3-Way Handshaking (cont’d)
Three-way handshake adds 1 RTT delay
Why?
  Congestion control: SYN (40 byte) acts as cheap probe
  Protects against delayed packets from other connection (would confuse receiver)

## Slide 45: Close Connection
Goal: both sides agree to close the connection
4-way connection tear down
FIN
FIN ACK
FIN
FIN ACK
Host 1
Host 2
Can retransmit FIN ACK if it is lost
timeout
closed
close
close
closed
data

## Slide 46: Recall: Sockets in Schematic
Client
Server
read response
Close Client Socket
Create Client Socket
Connect it to server (host:port)
Create Server Socket
Bind it to an Address
(host:port)
Listen for Connection
Close Connection Socket
Close Server Socket
write request
write response
Accept syscall()
Connection Socket
Connection Socket
read request

## Slide 47: The Transfer Part - Reliability

## Slide 48: TCP Sliding Window
Window represents packets:
  That might need to be re-sent (dropped, garbled)
  That receiver needs to buffer (in-order delivery to user)
0 1 2 3 4 5 6 7
0 1 2 3 4 5 6 7
ACK 0

## Slide 49: Transmission Control Protocol (TCP)
Reliable byte stream between two processes on different machines, over the Internet
Bi-directional: two streams for every connection
Segments byte streams into “packets”, hands those to IP
  IP may “fragment” into link frames
Window-based acknowledgement protocol
Automatically retransmits lost packets
Adjusts rate of transmission to avoid congestion
  How? Window Size
Router
Router
Stream in:
Stream out:
zyxwvuts
gfedcba

## Slide 50: Reliable Transfer
Retransmit missing packets
  Numbering of packets and ACKs
Do this efficiently
  Keep transmitting whenever possible
  Detect missing packets and retransmit quickly
Two schemes
  Stop & Wait
  Sliding Window (Go-back-n and Selective Repeat)

## Slide 51: Window-Based Acknowledgement
Packet lost?
  Resent after timeout (no ACK received)
Acknowledgement lost?
  Packet resent, causing ACK to be resent, too
Discard out-of-order packets?
  If no, need some way to indicate holes in window

## Slide 52: Detecting Packet Loss?
Timeouts
  Sender timeouts on not receiving ACK
Missing ACKs
  Receiver ACKs each packet
  Sender detects a missing packet when seeing a gap in the sequence of ACKs
  Need to be careful! Packets and ACKs might be reordered
NACK: Negative ACK
  Receiver sends a NACK specifying a packet it is missing

## Slide 53: Stop & Wait w/o Errors
Send; wait for ack; repeat
RTT: Round Trip Time (RTT): time it takes a packet to travel from sender to receiver and back
  One-way latency (d): one way delay from sender and receiver
ACK 1
Time
Sender
Receiver
1
2
ACK 2
3
RTT
RTT
RTT = 2*d
(if latency is
symmetric)
d

## Slide 54: Stop & Wait w/o Errors
How many packets can you send?
1 packet / RTT
Throughput: number of bits delivered to receiver per sec
ACK 1
Time
Sender
Receiver
1
2
ACK 2
3
RTT
RTT

## Slide 55: Stop & Wait w/o Errors
Say, RTT = 100ms
1 packet = 1500 bytes
Throughput = 1500*8bits/0.1s = 120 Kbps
ACK 1
Time
Sender
Receiver
1
2
ACK 2
3
RTT
RTT

## Slide 56: Stop & Wait w/o Errors
Can be very inefficient for high capacity links
Throughput doesn’t depend on the network capacity  even if capacity is 1Gbps, we can only send 120 Kbps!
ACK 1
Time
Sender
Receiver
1
2
ACK 2
3
RTT
RTT

## Slide 57: Stop & Wait with Errors
If a loss wait for a retransmission timeout and retransmit
How do you pick the timeout?
ACK 1
Time
Sender
Receiver
1
RTT
timeout
1

## Slide 58: Sliding Window
window = set of adjacent sequence numbers
The size of the set is the window size
Assume window size is n
Let A be the last ACK’d packet of sender without gap; then window of sender = {A+1, A+2, …, A+n}
Sender can send packets in its window
Let B be the last received packet without gap by receiver, then window of receiver = {B+1,…, B+n}
Receiver can accept out of sequence, if in window

## Slide 59: Sliding Window w/o Errors
Throughput = W*packet_size/RTT
Time
Window size (W) = 3 packets
Sender
Receiver
1
{1}
2
{1, 2}
3
{1, 2, 3}
4
{2, 3, 4}
5
{3, 4, 5}
Unacked packets
in sender’s window
Out-o-seq packets
in receiver’s window
{}
6
{4, 5, 6}
.
.
.
.
.
.
{}
{}

## Slide 60: Example: Sliding Window w/o Errors
Assume
  Link capacity, C = 1Gbps
  Latency between end-hosts, RTT = 80ms
  packet_length = 1000 bytes
What is the window size W to match link’s capacity, C?
Solution
  We want Throughput = C
  Throughput = W*packet_size/RTT
  C = W*packet_size/RTT
  W = C*RTT/packet_size = 109bps*80*10-3s/(8000b) = 104 packets
Window size ~ Bandwidth (Capacity), delay (RTT/2)

## Slide 61: Sliding Window with Errors
Two approaches
  Go-Back-n (GBN)
  Selective Repeat (SR)
In the absence of errors they behave identically
Go-Back-n (GBN)
  Transmit up to n unacknowledged packets
  If timeout for ACK(k), retransmit k, k+1, …
  Typically uses NACKs instead of ACKs
    Recall, NACK specifies first in-sequence packet missed by receiver

## Slide 62: GBN Example with Errors
Window size (W) = 3 packets
Sender
Receiver
1
2
3
4
5
{}
{}
{}
6
{5}
{5,6}
4 is
missing
Timeout
Packet 4
4
5
6
{}
Why doesn’t sender retransmit packet 4 here?
Assume packet 4 lost!
Out-o-seq packets
in receiver’s window
NACK 4
NACK 4

## Slide 63: Selective Repeat (SR)
Sender: transmit up to n unacknowledged packets
Assume packet k is lost
Receiver: indicate packet k is missing (use ACKs)
Sender: retransmit packet k

## Slide 64: SR Example with Errors
Time
Sender
Receiver
1
2
3
4
5
6
4
7
Window size (W) = 3 packets
{1}
{1, 2}
{1, 2, 3}
{2, 3, 4}
{3, 4, 5}
{4, 5, 6}
{4,5,6}
{7}
Unacked packets
in sender’s window
ACK 5
ACK 6

## Slide 65: TCP Windows and Seq. Numbers
Sender has three regions:
  Sent and acknowledged
  Sent and not acknowledged
  Not yet sent
Sequence Numbers
Sent
not acked
Sent
acked
Not yet
sent
Sender
Not yet
received
Received
Given to app
Received
Buffered
Receiver

## Slide 66: TCP Windows and Seq. Numbers
Receiver has three regions:
  Received and acknowledged
  Received and buffered
  Not yet received
Sequence Numbers
Sent
not acked
Sent
acked
Not yet
sent
Sender
Not yet
received
Received
Given to app
Received
Buffered
Receiver

## Slide 67: Window-Based Acknowledgements
Seq:190
Size:40
Seq:230
A:190/210
Seq:260
A:190/210
Seq:300
A:190/210
Seq:190
A:340/60
Seq:340
A:380/20
Seq:380
A:400/0
A:100/300
Seq:100
A:140/260
Seq:140
A:190/210
100
Seq:100
Size:40
140
Seq:140
Size:50
190
Seq:230
Size:30
230
260
Seq:260
Size:40
300
Seq:300
Size:40
340
Seq:340
Size:40
380
Seq:380
Size:20
400
Retransmit!

## Slide 68: Congestion
Too much data trying to flow through some part of the network
IP's solution: Drop packets
What happens to TCP connection?
  Lots of retransmission – wasted work
  Lots of waiting for timeouts – underutilized connection

## Slide 69: Congestion Avoidance
Solution: Adjust Window Size
AIMD: Additive Increase, Multiplicative Decrease
  When packet dropped (missed ack), cut window size in half
  If no timeouts, increase window size by C for each acknowledgement received
    Until half the old window then slower

## Slide 70: Congestion Avoidance: Changing Window

## Slide 71: Congestion Avoidance
Congestion
  How long should timeout be for re-sending messages?
    Too long  wastes time if message lost
    Too short  retransmit even though ACK will arrive shortly
  Stability problem: more congestion  ACK is delayed  unnecessary timeout  more traffic  more congestion
    Closely related to window size at sender: too big means putting too much data into network
How does the sender’s window size get chosen?
  Must be less than receiver’s advertised buffer size
  Try to match the rate of sending packets with the rate that the slowest link can accommodate
  Sender uses an adaptive algorithm to decide size of N
    Goal: fill network between sender and receiver
    Basic technique: slowly increase size of window until acknowledgements start being delayed/lost
TCP solution: “slow start” (start sending slowly)
  If no timeout, slowly increase window size (throughput) by 1 for each ACK received
  Timeout  congestion, so cut window size in half
  “Additive Increase, Multiplicative Decrease”
Notes: 2nd thing we use window-based acknowledgment protocol for:
Avoid overwhelming network

## Slide 72: Summary: Network Layers
Link Layer (local network)
  Send frames addressed to neighboring machines
  Ethernet, Wi-Fi
Network layer (connecting local networks)
  Forwarding between local networks
  Send packets addressed to machines anywhere
  IP
Transport Layer (making streams)
  Turn sequence of packets into reliable byte stream
  TCP

## Slide 73: Glue: Adding Functionality
Physical Reality: Frames | Abstraction: Stream
Limited Size | Arbitrary Size
Unordered (sometimes) | Ordered
Unreliable | Reliable
Machine-to-Machine | Process-to-Process
Only on Local Area Net | Routed Anywhere
Asynchronous | Synchronous

## Slide 74: Glue: Adding Functionality
Physical Reality: Frames | Abstraction: Stream
Limited Size | Arbitrary Size
Unordered (sometimes) | Ordered
Unreliable | Reliable
Machine-to-Machine | Process-to-Process
Only on Local Area Net | Routed Anywhere
Asynchronous | Synchronous
Network Layer: IP

## Slide 75: Glue: Adding Functionality
Physical Reality: Frames | Abstraction: Stream
Limited Size | Arbitrary Size
Unordered (sometimes) | Ordered
Unreliable | Reliable
Machine-to-Machine | Process-to-Process
Only on Local Area Net | Routed Anywhere
Asynchronous | Synchronous
Transport Layer: TCP

## Slide 76: Summary: TCP
Syn | Syn-Ack | Ack to realize Connect/Listen Accept
  vs Open for a file
  Demultiplex to processes based on Port
Use sequence numbers to solve out-of-order delivery problem
Use acknowledgements to solve reliable delivery problem
  For better utilization, allow a window of unacknowledged packets
  Adjust window size in response to perceived congestion events
FIN | FIN ACK in both direction to tear down
  Upon close

## Slide 77: Summary: TCP
Use sequence numbers to solve out-of-order delivery problem
Use acknowledgements to solve reliable delivery problem
For better utilization, allow a window of unacknowledged packets
Adjust window size in response to perceived congestion events

## Slide 78: TCP State Machine
From Comer, Internetworking with TCP/IP