## Slide 1: CS162 Operating Systems and Systems Programming Lecture 7 Synchronization 1: Concurrency (cont’d), Lock Implementation
September 16th, 2021
Prof. Ion Stoica
http://cs162.eecs.Berkeley.edu

## Slide 2: Recall: Stack for Yielding Thread
How do we run a new thread?
run_new_thread() {
newThread = PickNewThread();
switch(curThread, newThread);
ThreadHouseKeeping(); /* Do any cleanup */
}
How does dispatcher switch to a new thread?
  Save anything next thread may trash: PC, regs, stack pointer
  Maintain isolation for each thread
yield
ComputePI
Stack growth
run_new_thread
kernel_yield
Trap to OS
switch

## Slide 3: What Do the Stacks Look Like?
Consider the following code blocks:
proc A() {
B();
}
proc B() {
while(TRUE) {
yield();
}
}
Suppose we have 2 threads:
  Threads S and T
Thread S
Stack growth
A
B(while)
yield
run_new_thread
switch
Thread T
A
B(while)
yield
run_new_thread
switch
Thread S's switch returns to Thread T's (and vice versa)

## Slide 4: Saving/Restoring state (often called “Context Switch)
Switch(tCur,tNew) {
/* Unload old thread */
TCB[tCur].regs.r7 = CPU.r7;
…
TCB[tCur].regs.r0 = CPU.r0;
TCB[tCur].regs.sp = CPU.sp;
TCB[tCur].regs.retpc = CPU.retpc; /*return addr*/
/* Load and execute new thread */
CPU.r7 = TCB[tNew].regs.r7;
…
CPU.r0 = TCB[tNew].regs.r0;
CPU.sp = TCB[tNew].regs.sp;
CPU.retpc = TCB[tNew].regs.retpc;
return; /* Return to CPU.retpc */
}

## Slide 5: Switch Details (continued)
What if you make a mistake in implementing switch?
  Suppose you forget to save/restore register 32
  Get intermittent failures depending on when context switch occurred and whether new thread uses register 32
  System will give wrong result without warning
Can you devise an exhaustive test to test switch code?
  No! Too many combinations and inter-leavings
Cautionary tale:
  For speed, Topaz kernel saved one instruction in switch()
  Carefully documented! Only works as long as kernel size < 1MB
  What happened?
    Time passed, People forgot
    Later, they added features to kernel (no one removes features!)
    Very weird behavior started happening
  Moral of story: Design for simplicity

## Slide 6: Aren't we still switching contexts?
Yes, but much cheaper than switching processes
  No need to change address space
Some numbers from Linux:
  Frequency of context switch: 10-100ms
  Switching between processes: 3-4 μsec.
  Switching between threads: 100 ns
Even cheaper: switch threads (using “yield”) in user-space!
Simple One-to-One
Threading Model
Many-to-One
Many-to-Many
What we are talking about in Today’s lecture

## Slide 7: Processes vs. Threads
Process 1
CPU sched.
OS
CPU
(1 core)
1 thread at a time
IO
state
Mem.
…
threads
Process N
IO
state
Mem.
…
threads
…
Switch overhead:
  Same process: low
  Different proc.: high
Protection
  Same proc: low
  Different proc: high
Sharing overhead
  Same proc: low
  Different proc: high
Parallelism: no
CPU
state
CPU
state
CPU
state
CPU
state

## Slide 8: Processes vs. Threads
Process 1
CPU sched.
OS
Core 1
4 threads at a time
IO
state
Mem.
…
threads
Process N
IO
state
Mem.
…
threads
…
CPU
state
CPU
state
CPU
state
CPU
state
Core 2
Core 3
Core 4
Switch overhead:
  Same process: low
  Different proc.: high
Protection
  Same proc: low
  Different proc: high
Sharing overhead
  Same proc: low
  Different proc, simultaneous core: medium
  Different proc, offloaded core: high
Parallelism: yes

## Slide 9: Simultaneous MultiThreading/Hyperthreading
Hardware scheduling technique
  Superscalar processors can execute multiple instructions that are independent.
  Hyperthreading duplicates register state to make a second “thread,” allowing more instructions to run.
Can schedule each thread as if were separate CPU
  But sub-linear speedup!
Original technique called “Simultaneous Multithreading”
  http://www.cs.washington.edu/research/smt/index.html
  SPARC, Pentium 4/Xeon (“Hyperthreading”), Power 5
Colored blocks show
instructions executed
Notes: Intel seems to be discarding SMT in Silvermont because of power problems

## Slide 10: What happens when thread blocks on I/O?
run_new_thread
kernel_read
Trap to OS
switch
What happens when a thread requests a block of data from the file system?
  User code invokes a system call
  Read operation is initiated
  Run new thread/switch
Thread communication similar
  Wait for Signal/Join
  Networking
CopyFile
read
Stack growth

## Slide 11: External Events
What happens if thread never does any I/O, never waits, and never yields control?
  Could the ComputePI program grab all resources and never release the processor?
    What if it didn’t print to console?
  Must find way that dispatcher can regain control!
Answer: utilize external events
  Interrupts: signals from hardware or software that stop the running code and jump to kernel
  Timer: like an alarm clock that goes off every some milliseconds
If we make sure that external events occur frequently enough, can ensure dispatcher runs
Notes: Patterson’s a nice guy, so he gives up the body after using it for awhile and let’s John Kubitowicz have it.
But Kubi’s not so nice, so he won’t give up control…
If you want to wake up for a final, you set your clock, or ask your roommate to pour water over your head – OS does the same

## Slide 12: Interrupt Controller
Interrupts invoked with interrupt lines from devices
Interrupt controller chooses interrupt request to honor
  Interrupt identity specified with ID line
  Mask enables/disables interrupts
  Priority encoder picks highest enabled interrupt
  Software Interrupt Set/Cleared by Software
CPU can disable all interrupts with internal flag
Non-Maskable Interrupt line (NMI) can’t be disabled
Network
IntID
Interrupt
Interrupt Mask
Control
Software
Interrupt
NMI
CPU
Priority Encoder
Timer
Int Disable

## Slide 13: Example: Network Interrupt
...
add $r1,$r2,$r3
subi $r4,$r1,#4
slli $r4,$r4,#2
...
PC saved
Disable All Ints
Kernel Mode
Restore PC
Enable all Ints
User Mode
Raise priority
(set mask)
Reenable All Ints
Save registers
Dispatch to Handler

Transfer Network Packet from hardware to Kernel Buffers

Restore registers
Clear current Int
Disable All Ints
Restore priority
(clear Mask)
RTI
“Interrupt Handler”
An interrupt is a hardware-invoked context switch
  No separate step to choose what to run next
  Always run the interrupt handler immediately
External Interrupt
Pipeline Flush
...
lw $r2,0($r4)
lw $r3,4($r4)
add $r2,$r2,$r3
sw 8($r4),$r2
...

## Slide 14: Use of Timer Interrupt to Return Control
Solution to our dispatcher problem
  Use the timer interrupt to force scheduling decisions
Timer Interrupt routine:
TimerInterrupt() { DoPeriodicHouseKeeping(); run_new_thread(); }
Some Routine
run_new_thread
TimerInterrupt
Interrupt
switch
Stack growth

## Slide 15: How do we initialize TCB and Stack?
Initialize Register fields of TCB
  Stack pointer made to point at stack
  PC return address  OS (asm) routine ThreadRoot()
  Two arg registers (a0 and a1) initialized to fcnPtr and fcnArgPtr, respectively
Initialize stack data?
  No. Important part of stack frame is in registers (ra)
  Think of stack frame as just before body of ThreadRoot() really gets started
ThreadRoot stub
Initial Stack
Stack growth

## Slide 16: How does Thread get started?
Eventually, run_new_thread() will select this TCB and return into beginning of ThreadRoot()
  This really starts the new thread
Stack growth
A
B(while)
yield
run_new_thread
switch
ThreadRoot
Other Thread
ThreadRoot stub
New Thread

## Slide 17: How does a thread get started?
How do we make a new thread?
  Setup TCB/kernel thread to point at new user stack and ThreadRoot code
  Put pointers to start function and args in registers
  This depends heavily on the calling convention (i.e. RISC-V vs x86)
Eventually, run_new_thread() will select this TCB and return into beginning of ThreadRoot()
  This really starts the new thread
Stack growth
A
B(while)
yield
run_new_thread
switch
Other Thread
ThreadRoot stub
New Thread
SetupNewThread(tNew) {
…
newStackPtr = TCB[tNew].regs.sp;
&ThreadRoot = TCB[tNew].regs.retpc;
fcnPtr = TCB[tNew].regs.r0; fcnArgPtr = TCB[tNew].regs.r1;
}
ThreadRoot

## Slide 18: What does ThreadRoot() look like?
ThreadRoot() is the root for the thread routine:
ThreadRoot(fcnPTR,fcnArgPtr) {
DoStartupHousekeeping();
UserModeSwitch(); /* enter user mode */
Call fcnPtr(fcnArgPtr);
ThreadFinish();
}
Startup Housekeeping
  Includes things like recording start time of thread
  Other statistics
Stack will grow and shrink with execution of thread
Final return from thread returns into ThreadRoot() which calls ThreadFinish()
  ThreadFinish() wake up sleeping threads
ThreadRoot
Running Stack
Stack growth
Thread Code *fcnPtr()

## Slide 19: Correctness with Concurrent Threads?
Non-determinism:
  Scheduler can run threads in any order
  Scheduler can switch threads at any time
  This can make testing very difficult
Independent Threads
  No state shared with other threads
  Deterministic, reproducible conditions
Cooperating Threads
  Shared state between multiple threads
Goal: Correctness by Design

## Slide 20: Recall: Possible Executions

## Slide 21: ATM Bank Server
ATM server problem:
  Service a set of requests
  Do so without corrupting database
  Don’t hand out too much money

## Slide 22: ATM bank server example
Suppose we wanted to implement a server process to handle requests from an ATM network:
BankServer() { while (TRUE) { ReceiveRequest(&op, &acctId, &amount); ProcessRequest(op, acctId, amount); } }
ProcessRequest(op, acctId, amount) { if (op == deposit) Deposit(acctId, amount); else if … }
Deposit(acctId, amount) { acct = GetAccount(acctId); /* may use disk I/O */ acct->balance += amount; StoreAccount(acct); /* Involves disk I/O */ }
How could we speed this up?
  More than one request being processed at once
  Event driven (overlap computation and I/O)
  Multiple threads (multi-proc, or overlap comp and I/O)

## Slide 23: Event Driven Version of ATM server
Suppose we only had one CPU
  Still like to overlap I/O with computation
  Without threads, we would have to rewrite in event-driven style
Example
BankServer() { while(TRUE) { event = WaitForNextEvent(); if (event == ATMRequest) StartOnRequest(); else if (event == AcctAvail) ContinueRequest(); else if (event == AcctStored) FinishRequest(); } }
  What if we missed a blocking I/O step?
  What if we have to split code into hundreds of pieces which could be blocking?
  This technique is used for graphical programming

## Slide 24: Can Threads Make This Easier?
Threads yield overlapped I/O and computation without “deconstructing” code into non-blocking fragments
  One thread per request
Requests proceeds to completion, blocking as required:
Deposit(acctId, amount) { acct = GetAccount(actId); /* May use disk I/O */ acct->balance += amount; StoreAccount(acct); /* Involves disk I/O */ }
Unfortunately, shared state can get corrupted: Thread 1 Thread 2 load r1, acct->balance load r1, acct->balance add r1, amount2 store r1, acct->balance add r1, amount1 store r1, acct->balance

## Slide 25: Problem is at the Lowest Level
Most of the time, threads are working on separate data, so scheduling doesn’t matter:
Thread A Thread B
x = 1; y = 2;
However, what about (Initially, y = 12):
Thread A Thread B
x = 1; y = 2;
x = y+1; y = y*2;
  What are the possible values of x?
Or, what are the possible values of x below?
Thread A Thread B
x = 1; x = 2;
  X could be 1 or 2 (non-deterministic!)
  Could even be 3 for serial processors:
    Thread A writes 0001, B writes 0010 → scheduling order ABABABBA yields 3!
Notes: X could be (13, 5, 3)

## Slide 26: Atomic Operations
To understand a concurrent program, we need to know what the underlying indivisible operations are!
Atomic Operation: an operation that always runs to completion or not at all
  It is indivisible: it cannot be stopped in the middle and state cannot be modified by someone else in the middle
  Fundamental building block – if no atomic operations, then have no way for threads to work together
On most machines, memory references and assignments (i.e. loads and stores) of words are atomic
  Consequently – weird example that produces “3” on previous slide can’t happen
Many instructions are not atomic
  Double-precision floating point store often not atomic
  VAX and IBM 360 had an instruction to copy a whole array

## Slide 27: Recall: Locks
Lock: prevents someone from doing something
  Lock before entering critical section and before accessing shared data
  Unlock when leaving, after accessing shared data
  Wait if locked
    Important idea: all synchronization involves waiting
Locks need to be allocated and initialized:
  structure Lock mylock or pthread_mutex_t mylock;
  lock_init(&mylock) or mylock = PTHREAD_MUTEX_INITIALIZER;
Locks provide two atomic operations:
  acquire(&mylock) – wait until lock is free; then mark it as busy
    After this returns, we say the calling thread holds the lock
  release(&mylock) – mark lock as free
    Should only be called by a thread that currently holds the lock
    After this returns, the calling thread no longer holds the lock

## Slide 28: Fix banking problem with Locks!
Thread C
Identify critical sections (atomic instruction sequences) and add locking:
Deposit(acctId, amount) {
acquire(&mylock) // Wait if someone else in critical section! acct = GetAccount(actId); acct->balance += amount; StoreAccount(acct);
release(&mylock) // Release someone into critical section }
Must use SAME lock (mylock) with all of the methods (Withdraw, etc…)
  Shared with all threads!
Thread A
Thread B
Thread A
Thread A
Thread C
Thread B
Thread B
Critical Section
acquire(&mylock)
release(&mylock)
Critical Section
Threads serialized by lock through critical section.
Only one thread at a time

## Slide 29: Recall: Definitions
Synchronization: using atomic operations to ensure cooperation between threads
  For now, only loads and stores are atomic
  We are going to show that its hard to build anything useful with only reads and writes
Mutual Exclusion: ensuring that only one thread does a particular thing at a time
  One thread excludes the other while doing its task
Critical Section: piece of code that only one thread can execute at once. Only one thread at a time will get into this section of code
  Critical section is the result of mutual exclusion
  Critical section and mutual exclusion are two ways of describing the same thing

## Slide 30: Another Concurrent Program Example
Two threads, A and B, compete with each other
  One tries to increment a shared counter
  The other tries to decrement the counter
Thread A Thread B
i = 0; i = 0; while (i < 10) while (i > -10) i = i + 1; i = i – 1; printf(“A wins!”); printf(“B wins!”);
Assume that memory loads and stores are atomic, but incrementing and decrementing are not atomic
  No difference between: “i=i+1” and “i++”
  Same instruction sequence, the ++ operator is just syntactic sugar
Who wins? Could be either
Is it guaranteed that someone wins? Why or why not?
What if both threads have their own CPU running at same speed? Is it guaranteed that it goes on forever?

## Slide 31: Hand Simulation Multiprocessor Example
Inner loop looks like this:
Thread A Thread B
r1=0 load r1, M[i]
r1=0 load r1, M[i]
r1=1 add r1, r1, 1
r1=-1 sub r1, r1, 1
M[i]=1 store r1, M[i]
M[i]=-1 store r1, M[i]
Hand Simulation:
  And we’re off. A gets off to an early start
  B says “hmph, better go fast” and tries really hard
  A goes ahead and writes “1”
  B goes and writes “-1”
  A says “HUH??? I could have sworn I put a 1 there”
Uncontrolled race condition: two threads attempting to access same data simultaneously with one of them performing a write
  Here “simultaneous” is defined even with one CPU as “could access at same time if only there were two CPUs

## Slide 32: So – does this fix it?
Put locks around increment/decrement:
Thread A Thread B
i = 0; i = 0; while (i < 10) while (i > -10)
acquire(&mylock) acquire(&mylock) i = i + 1; i = i – 1;
release(&mylock) release(&mylock) printf(“A wins!”); printf(“B wins!”);
What does this do? Is it better???
Each increment or decrement operation is now atomic. Good!
  Technically, no race conditions, since lock prevents simultaneous reads/writes
Program is likely still broken. Not so good…
  May or may not be what you intended (probably not)
  Still unclear who wins – it is a nondeterministic result: different on each run
When might something like this make sense?
  If each thread needed to get a unique integer for some reason

## Slide 33: Concurrency is Hard!
Even for practicing engineers trying to write mission-critical, bulletproof code!
  Threaded programs must work for all interleavings of thread instruction sequences
  Cooperating threads inherently non-deterministic and non-reproducible
  Really hard to debug unless carefully designed!
Therac-25: Radiation Therapy Machine with Unintended Overdoses (reading on course site)
  Concurrency errors caused the death of a number of patients by misconfiguring the radiation production
  Improper synchronization between input from operators and positioning software
Mars Pathfinder Priority Inversion (JPL Account)
Toyota Uncontrolled Acceleration (CMU Talk)
  256.6K Lines of C Code, ~9-11K global variables
  Inconsistent mutual exclusion on reads/writes

## Slide 34: Producer-Consumer with a Bounded Buffer
Problem Definition
  Producer(s) put things into a shared buffer
  Consumer(s) take them out
  Need synchronization to coordinate producer/consumer
Don’t want producer and consumer to have to work in lockstep, so put a fixed-size buffer between them
  Need to synchronize access to this buffer
  Producer needs to wait if buffer is full
  Consumer needs to wait if buffer is empty
Example 1: GCC compiler
  cpp | cc1 | cc2 | as | ld
Example 2: Coke machine
  Producer can put limited number of Cokes in machine
  Consumer can’t take Cokes out if machine is empty
Others: Web servers, Routers, ….
Consumer
Consumer
Producer
Consumer
Buffer
Producer

## Slide 35: Circular Buffer Data Structure (sequential case)
Insert: write & bump write ptr (enqueue)
Remove: read & bump read ptr (dequeue)
How to tell if Full (on insert) Empty (on remove)?
And what do you do if it is?
What needs to be atomic?
typedef struct buf {
int write_index;
int read_index;
<type> *entries[BUFSIZE];
} buf_t;
w
r
di
di+1
di+2

## Slide 36: Circular Buffer – first cut
mutex buf_lock = <initially unlocked>
Producer(item) {
acquire(&buf_lock);
while (buffer full) {}; // Wait for a free slot
enqueue(item); release(&buf_lock);
}
Consumer() {
acquire(&buf_lock);
while (buffer empty) {}; // Wait for arrival
item = dequeue(); release(&buf_lock);
return item
}
Will we ever come out of the wait loop?

## Slide 37: Circular Buffer – 2nd cut
mutex buf_lock = <initially unlocked>
Producer(item) {
acquire(&buf_lock);
while (buffer full) {release(&buf_lock); acquire(&buf_lock);}
enqueue(item); release(&buf_lock);
}
Consumer() {
acquire(&buf_lock);
while (buffer empty) {release(&buf_lock); acquire(&buf_lock);}
item = dequeue(); release(&buf_lock);
return item
}
What happens when one is waiting for the other?
- Multiple cores ?
- Single core ?


## Slide 38: Higher-level Primitives than Locks
What is right abstraction for synchronizing threads that share memory?
  Want as high a level primitive as possible
Good primitives and practices important!
  Since execution is not entirely sequential, really hard to find bugs, since they happen rarely
  UNIX is pretty stable now, but up until about mid-80s (10 years after started), systems running UNIX would crash every week or so – concurrency bugs
Synchronization is a way of coordinating multiple concurrent activities that are using shared state
  This lecture and the next presents a some ways of structuring sharing

## Slide 39: Recall: Semaphores
Semaphores are a kind of generalized lock
  First defined by Dijkstra in late 60s
  Main synchronization primitive used in original UNIX
Definition: a Semaphore has a non-negative integer value and supports the following two operations:
  Down() or P(): an atomic operation that waits for semaphore to become positive, then decrements it by 1
    Think of this as the wait() operation
  Up() or V(): an atomic operation that increments the semaphore by 1, waking up a waiting P, if any
    This of this as the signal() operation
  Note that P() stands for “proberen” (to test) and V() stands for “verhogen” (to increment) in Dutch

## Slide 40: Semaphores Like Integers Except…
Value=2
Value=1
Value=0
Semaphores are like integers, except:
  No negative values
  Only operations allowed are P and V – can’t read or write value, except initially
  Operations must be atomic
    Two P’s together can’t decrement value below zero
    Thread going to sleep in P won’t miss wakeup from V – even if both happen at same time
POSIX adds ability to read value, but technically not part of proper interface!
Semaphore from railway analogy
  Here is a semaphore initialized to 2 for resource control:
Value=1
Value=0
Value=2

## Slide 41: Two Uses of Semaphores
Mutual Exclusion (initial value = 1)
Also called “Binary Semaphore” or “mutex”.
Can be used for mutual exclusion, just like a lock:
    semaP(&mysem); // Critical section goes here semaV(&mysem);
Scheduling Constraints (initial value = 0)
Allow thread 1 to wait for a signal from thread 2
  thread 2 schedules thread 1 when a given event occurs
Example: suppose you had to implement ThreadJoin which must wait for thread to terminate:
    Initial value of semaphore = 0
    ThreadJoin { semaP(&mysem); }
    ThreadFinish { semaV(&mysem); }

## Slide 42: Revisit Bounded Buffer: Correctness constraints for solution
Correctness Constraints:
  Consumer must wait for producer to fill buffers, if none full (scheduling constraint)
  Producer must wait for consumer to empty buffers, if all full (scheduling constraint)
  Only one thread can manipulate buffer queue at a time (mutual exclusion)
Remember why we need mutual exclusion
  Because computers are stupid
  Imagine if in real life: the delivery person is filling the machine and somebody comes up and tries to stick their money into the machine
General rule of thumb: Use a separate semaphore for each constraint
  Semaphore fullBuffers; // consumer’s constraint
  Semaphore emptyBuffers;// producer’s constraint
  Semaphore mutex; // mutual exclusion

## Slide 43: Full Solution to Bounded Buffer (coke machine)
Semaphore fullSlots = 0; // Initially, no coke
Semaphore emptySlots = bufSize; // Initially, num empty slots
Semaphore mutex = 1; // No one using machine
Producer(item) { semaP(&emptySlots); // Wait until space semaP(&mutex); // Wait until machine free Enqueue(item); semaV(&mutex); semaV(&fullSlots); // Tell consumers there is // more coke }
Consumer() { semaP(&fullSlots); // Check if there’s a coke semaP(&mutex); // Wait until machine free item = Dequeue(); semaV(&mutex); semaV(&emptySlots); // tell producer need more return item; }
fullSlots signals coke
emptySlots
signals space
Critical sections using mutex protect integrity of the queue

## Slide 44: Discussion about Solution
Why asymmetry?
  Producer does: semaP(&emptyBuffer), semaV(&fullBuffer)
  Consumer does: semaP(&fullBuffer), semaV(&emptyBuffer)
Is order of P’s important?
  Yes! Can cause deadlock
Is order of V’s important?
  No, except that it might affect scheduling efficiency
What if we have 2 producers or 2 consumers?
  Do we need to change anything?
Decrease # of empty slots
Increase # of occupied slots
Increase # of empty slots
Decrease # of occupied slots
Producer(item) { semaP(&mutex); semaP(&emptySlots); Enqueue(item); semaV(&mutex); semaV(&fullSlots); } Consumer() { semaP(&fullSlots); semaP(&mutex); item = Dequeue(); semaV(&mutex); semaV(&emptySlots); return item; }

## Slide 45: Announcements
Please sign up for design reviews! Design docs due Friday.
HW1 due today!

## Slide 46: Where are we going with synchronization?
Hardware
Higher-level API
Programs
We are going to implement various higher-level synchronization primitives using atomic operations
  Everything is pretty painful if only atomic primitives are load and store
  Need to provide primitives useful at user-level
Load/Store Disable Ints Test&Set Compare&Swap
Locks Semaphores Monitors Send/Receive
Shared Programs

## Slide 47: Motivating Example: “Too Much Milk”
Great thing about OS’s – analogy between problems in OS and problems in real life
  Help you understand real life problems better
  But, computers are much stupider than people
Example: People need to coordinate:
Arrive home, put milk away
3:30
Buy milk
3:25
Arrive at store
Arrive home, put milk away
3:20
Leave for store
Buy milk
3:15
Leave for store
3:05
Look in Fridge. Out of milk
3:00
Look in Fridge. Out of milk
Arrive at store
3:10
Person B
Person A
Time
Notes: You’re sitting in class, hot day, milk does a body good. Go home, no milk, so go to store
Roommate leaves class late because prof is more long-winded than I am. Has same idea, but result is too much milk!
Problem: two cooperating threads, not cooperating properly

## Slide 48: Recall: What is a lock?
Lock: prevents someone from doing something
  Lock before entering critical section and before accessing shared data
  Unlock when leaving, after accessing shared data
  Wait if locked
    Important idea: all synchronization involves waiting
For example: fix the milk problem by putting a key on the refrigerator
  Lock it and take key if you are going to go buy milk
  Fixes too much: roommate angry if only wants OJ
Of Course – We don’t know how to make a lock yet
  Let’s see if we can answer this question!
#$@%@#$@

## Slide 49: Too Much Milk: Correctness Properties
Need to be careful about correctness of concurrent programs, since non-deterministic
  Impulse is to start coding first, then when it doesn’t work, pull hair out
  Instead, think first, then code
  Always write down behavior first
What are the correctness properties for the “Too much milk” problem???
  Never more than one person buys
  Someone buys if needed
First attempt: Restrict ourselves to use only atomic load and store operations as building blocks

## Slide 50: Too Much Milk: Solution #1
Use a note to avoid buying too much milk:
  Leave a note before buying (kind of “lock”)
  Remove note after buying (kind of “unlock”)
  Don’t buy if note (wait)
Suppose a computer tries this (remember, only memory read/write are atomic):
  if (noMilk) { if (noNote) { leave Note; buy milk; remove note; } }
Notes: * This is a fate worse than failure! Code that usually works is way worse than outright broken code

## Slide 51: Too Much Milk: Solution #1
Use a note to avoid buying too much milk:
  Leave a note before buying (kind of “lock”)
  Remove note after buying (kind of “unlock”)
  Don’t buy if note (wait)
Suppose a computer tries this (remember, only memory read/write are atomic):
Thread A Thread B
if (noMilk) { if (noMilk) { if (noNote) {
if (noNote) { leave Note;
buy Milk;
remove Note;
}
}
leave Note;
buy Milk;
remove Note; } }
Notes: * This is a fate worse than failure! Code that usually works is way worse than outright broken code

## Slide 52: Too Much Milk: Solution #1
Use a note to avoid buying too much milk:
  Leave a note before buying (kind of “lock”)
  Remove note after buying (kind of “unlock”)
  Don’t buy if note (wait)
Suppose a computer tries this (remember, only memory read/write are atomic):
  if (noMilk) { if (noNote) { leave Note; buy milk; remove note; } }
Result?
  Still too much milk but only occasionally!
  Thread can get context switched after checking milk and note but before buying milk!
Solution makes problem worse since fails intermittently
  Makes it really hard to debug…
  Must work despite what the dispatcher does!
Notes: * This is a fate worse than failure! Code that usually works is way worse than outright broken code

## Slide 53: Too Much Milk: Solution #1½
Clearly the Note is not quite blocking enough
  Let’s try to fix this by placing note first
Another try at previous solution:
  leave Note;
  if (noMilk) { if (noNote) { buy milk; } }
  remove Note;
What happens here?
  Well, with human, probably nothing bad
  With computer: no one ever buys milk

## Slide 54: Too Much Milk Solution #2
How about labeled notes?
  Now we can leave note before checking
Algorithm looks like this:
Thread A Thread B
leave note A; leave note B; if (noNote B) { if (noNoteA) { if (noMilk) { if (noMilk) { buy Milk; buy Milk; } } } } remove note A; remove note B;
Does this work?
Possible for neither thread to buy milk
  Context switches at exactly the wrong times can lead each to think that the other is going to buy
Really insidious:
  Extremely unlikely this would happen, but will at worse possible time
  Probably something like this in UNIX

## Slide 55: Too Much Milk Solution #2: problem!
I’m not getting milk, You’re getting milk
This kind of lockup is called “starvation!”

## Slide 56: Too Much Milk Solution #3
Here is a possible two-note solution:
Thread A Thread B
leave note A; leave note B; while (note B) {\\X if (noNote A) {\\Y do nothing; if (noMilk) { } buy milk; if (noMilk) { } buy milk; } } remove note B; remove note A;
Does this work? Yes. Both can guarantee that:
  It is safe to buy, or
  Other will buy, ok to quit
At X:
  If no note B, safe for A to buy,
  Otherwise wait to find out what will happen
At Y:
  If no note A, safe for B to buy
  Otherwise, A is either buying or waiting for B to quit

## Slide 57: Case 1
leave note B; if (noNote A) {\\Y
if (noMilk) { buy milk;
} } remove note B;
happened
before
leave note A; while (note B) {\\X
do nothing; };
if (noMilk) {
buy milk; } } remove note A;
“leave note A” happens before “if (noNote A)”

## Slide 58: Case 1
leave note A; while (note B) {\\X
do nothing; };
if (noMilk) {
buy milk; } } remove note A;
leave note B; if (noNote A) {\\Y
if (noMilk) { buy milk;
} } remove note B;
happened
before
“leave note A” happens before “if (noNote A)”

## Slide 59: Case 1
leave note A; while (note B) {\\X
do nothing; };
if (noMilk) {
buy milk; } } remove note A;
leave note B; if (noNote A) {\\Y
if (noMilk) { buy milk;
} } remove note B;
Wait for note B to be removed
happened
before
“leave note A” happens before “if (noNote A)”

## Slide 60: Case 2
leave note B; if (noNote A) {\\Y
if (noMilk) { buy milk;
} } remove note B;
happened
before
leave note A; while (note B) {\\X
do nothing; };
if (noMilk) {
buy milk; } } remove note A;
“if (noNote A)” happens before “leave note A”

## Slide 61: Case 2
leave note B; if (noNote A) {\\Y
if (noMilk) { buy milk;
} } remove note B;
happened
before
leave note A; while (note B) {\\X
do nothing; };
if (noMilk) {
buy milk; } } remove note A;
“if (noNote A)” happens before “leave note A”

## Slide 62: Case 2
leave note B; if (noNote A) {\\Y
if (noMilk) { buy milk;
} } remove note B;
happened
before
leave note A; while (note B) {\\X
do nothing; };
if (noMilk) {
buy milk; } } remove note A;
“if (noNote A)” happens before “leave note A”
Wait for note B to be removed

## Slide 63: Solution #3 discussion
Our solution protects a single “Critical-Section” piece of code for each thread:
if (noMilk) { buy milk; }
Solution #3 works, but it’s really unsatisfactory
  Really complex – even for this simple an example
    Hard to convince yourself that this really works
  A’s code is different from B’s – what if lots of threads?
    Code would have to be slightly different for each thread
  While A is waiting, it is consuming CPU time
    This is called “busy-waiting”
There’s got to be a better way!
  Have hardware provide higher-level primitives than atomic load & store
  Build even higher-level programming abstractions on this hardware support

## Slide 64: Too Much Milk: Solution #4?
Recall our target lock interface:
  acquire(&milklock) – wait until lock is free, then grab
  release(&milklock) – Unlock, waking up anyone waiting
  These must be atomic operations – if two threads are waiting for the lock and both see it’s free, only one succeeds to grab the lock
Then, our milk problem is easy:
acquire(&milklock);
if (nomilk)
buy milk;
release(&milklock);

## Slide 65: Back to: How to Implement Locks?
Lock: prevents someone from doing something
  Lock before entering critical section and before accessing shared data
  Unlock when leaving, after accessing shared data
  Wait if locked
    Important idea: all synchronization involves waiting
    Should sleep if waiting for a long time
Atomic Load/Store: get solution like Milk #3
  Pretty complex and error prone
Hardware Lock instruction
  Is this a good idea?
  What about putting a task to sleep?
    What is the interface between the hardware and scheduler?
  Complexity?
    Done in the Intel 432
    Each feature makes HW more complex and slow

## Slide 66: Naïve use of Interrupt Enable/Disable
How can we build multi-instruction atomic operations?
  Recall: dispatcher gets control in two ways.
    Internal: Thread does something to relinquish the CPU
    External: Interrupts cause dispatcher to take CPU
  On a uniprocessor, can avoid context-switching by:
    Avoiding internal events (although virtual memory tricky)
    Preventing external events by disabling interrupts
Consequently, naïve Implementation of locks: LockAcquire { disable Ints; } LockRelease { enable Ints; }
Problems with this approach:
  Can’t let user do this! Consider following:
    LockAcquire(); While(TRUE) {;}
  Real-Time system—no guarantees on timing!
    Critical Sections might be arbitrarily long
  What happens with I/O or other important events?
    “Reactor about to meltdown. Help?”

## Slide 67: Better Implementation of Locks by Disabling Interrupts
int value = FREE;
Acquire() { disable interrupts; if (value == BUSY) { put thread on wait queue; Go to sleep(); // Enable interrupts? } else { value = BUSY; } enable interrupts; }
Release() { disable interrupts; if (anyone on wait queue) { take thread off wait queue Place on ready queue; } else { value = FREE; } enable interrupts; }
Key idea: maintain a lock variable and impose mutual exclusion only during operations on that variable

## Slide 68: New Lock Implementation: Discussion
Why do we need to disable interrupts at all?
  Avoid interruption between checking and setting lock value
  Otherwise two threads could think that they both have lock
Note: unlike previous solution, the critical section (inside Acquire()) is very short
  User of lock can take as long as they like in their own critical section: doesn’t impact global machine behavior
  Critical interrupts taken in time!
Acquire() { disable interrupts; if (value == BUSY) { put thread on wait queue; Go to sleep(); // Enable interrupts? } else { value = BUSY; } enable interrupts; }
Critical
Section

## Slide 69: Interrupt Re-enable in Going to Sleep
What about re-enabling ints when going to sleep?
Acquire() { disable interrupts; if (value == BUSY) { put thread on wait queue; Go to sleep(); } else { value = BUSY; } enable interrupts; }

## Slide 70: Interrupt Re-enable in Going to Sleep
What about re-enabling ints when going to sleep?
Before Putting thread on the wait queue?
Acquire() { disable interrupts; if (value == BUSY) { put thread on wait queue; Go to sleep(); } else { value = BUSY; } enable interrupts; }
Enable Position

## Slide 71: Interrupt Re-enable in Going to Sleep
What about re-enabling ints when going to sleep?
Before Putting thread on the wait queue?
  Release can check the queue and not wake up thread
Acquire() { disable interrupts; if (value == BUSY) { put thread on wait queue; Go to sleep(); } else { value = BUSY; } enable interrupts; }
Enable Position

## Slide 72: Interrupt Re-enable in Going to Sleep
What about re-enabling ints when going to sleep?
Before Putting thread on the wait queue?
  Release can check the queue and not wake up thread
After putting the thread on the wait queue
Acquire() { disable interrupts; if (value == BUSY) { put thread on wait queue; Go to sleep(); } else { value = BUSY; } enable interrupts; }
Enable Position

## Slide 73: Interrupt Re-enable in Going to Sleep
What about re-enabling ints when going to sleep?
Before Putting thread on the wait queue?
  Release can check the queue and not wake up thread
After putting the thread on the wait queue
  Release puts the thread on the ready queue, but the thread still thinks it needs to go to sleep
  Misses wakeup and still holds lock (deadlock!)
Acquire() { disable interrupts; if (value == BUSY) { put thread on wait queue; Go to sleep(); } else { value = BUSY; } enable interrupts; }
Enable Position

## Slide 74: Interrupt Re-enable in Going to Sleep
What about re-enabling ints when going to sleep?
Before Putting thread on the wait queue?
  Release can check the queue and not wake up thread
After putting the thread on the wait queue
  Release puts the thread on the ready queue, but the thread still thinks it needs to go to sleep
  Misses wakeup and still holds lock (deadlock!)
Want to put it after sleep(). But – how?
Acquire() { disable interrupts; if (value == BUSY) { put thread on wait queue; Go to sleep(); } else { value = BUSY; } enable interrupts; }
Enable Position

## Slide 75: How to Re-enable After Sleep()?
In scheduler, since interrupts are disabled when you call sleep:
  Responsibility of the next thread to re-enable ints
  When the sleeping thread wakes up, returns to acquire and re-enables interrupts
  Thread A Thread B
  . . disable ints sleep
  sleep return enable ints
  . . .
  disable int sleep
  sleep return enable ints . .
context switch
context switch

## Slide 76: In-Kernel Lock: Simulation
INIT
int value = 0;
Acquire() { disable interrupts; if (value == 1) {
put thread on wait-queue;
go to sleep() //?? } else { value = 1; }
enable interrupts; }
Release() { disable interrupts; if anyone on wait queue { take thread off wait-queue Place on ready queue; } else { value = 0; } enable interrupts; }
lock.Acquire();
…
critical section;
…
lock.Release();
lock.Acquire();
…
critical section;
…
lock.Release();
Value: 0
waiters
owner
Thread A
Thread B
Running
READY
Ready

## Slide 77: In-Kernel Lock: Simulation
INIT
int value = 0;
Acquire() { disable interrupts; if (value == 1) {
put thread on wait-queue;
go to sleep() //?? } else { value = 1; }
enable interrupts; }
Release() { disable interrupts; if anyone on wait queue { take thread off wait-queue Place on ready queue; } else { value = 0; } enable interrupts; }
lock.Acquire();
…
critical section;
…
lock.Release();
lock.Acquire();
…
critical section;
…
lock.Release();
Thread A
Thread B
READY
Running
Value: 1
waiters
owner
Ready

## Slide 78: In-Kernel Lock: Simulation
INIT
int value = 0;
Acquire() { disable interrupts; if (value == 1) {
put thread on wait-queue;
go to sleep() //?? } else { value = 1; }
enable interrupts; }
Release() { disable interrupts; if anyone on wait queue { take thread off wait-queue Place on ready queue; } else { value = 0; } enable interrupts; }
lock.Acquire();
…
critical section;
…
lock.Release();
lock.Acquire();
…
critical section;
…
lock.Release();
Thread A
Thread B
READY
Running
Running
Value: 1
waiters
owner
Ready
Ready

## Slide 79: In-Kernel Lock: Simulation
INIT
int value = 0;
Acquire() { disable interrupts; if (value == 1) {
put thread on wait-queue;
go to sleep() //?? } else { value = 1; }
enable interrupts; }
lock.Acquire();
…
critical section;
…
lock.Release();
Release() { disable interrupts; if anyone on wait queue { take thread off wait-queue Place on ready queue; } else { value = 0; } enable interrupts; }
lock.Acquire();
…
critical section;
…
lock.Release();
Thread A
Thread B
READY
Running
Running
Value: 1
waiters
owner
Waiting
Ready

## Slide 80: In-Kernel Lock: Simulation
INIT
int value = 0;
Acquire() { disable interrupts; if (value == 1) {
put thread on wait-queue;
go to sleep() //?? } else { value = 1; }
enable interrupts; }
lock.Acquire();
…
critical section;
…
lock.Release();
Release() { disable interrupts; if anyone on wait queue { take thread off wait-queue Place on ready queue; } else { value = 0; } enable interrupts; }
lock.Acquire();
…
critical section;
…
lock.Release();
Thread A
Thread B
READY
Running
Value: 1
waiters
owner
Waiting
Ready

## Slide 81: In-Kernel Lock: Simulation
INIT
int value = 0;
Acquire() { disable interrupts; if (value == 1) {
put thread on wait-queue;
go to sleep() //?? } else { value = 1; }
enable interrupts; }
Running
Release() { disable interrupts; if anyone on wait queue { take thread off wait-queue Place on ready queue; } else { value = 0; } enable interrupts; }
lock.Acquire();
…
critical section;
…
lock.Release();
lock.Acquire();
…
critical section;
…
lock.Release();
Thread A
Thread B
READY
Running
Value: 1
waiters
owner
Ready
Ready

## Slide 82: Conclusion
Concurrency accomplished by multiplexing CPU time:
  Unloading current thread (PC, registers)
  Loading new thread (PC, registers)
  Such context switching may be voluntary (yield(), I/O) or involuntary (interrupts)
TCB + Stacks hold complete state of thread for restarting
Atomic Operation: an operation that always runs to completion or not at all
Synchronization: using atomic operations to ensure cooperation between threads
Mutual Exclusion: ensuring that only one thread does a particular thing at a time
  One thread excludes the other while doing its task
Critical Section: piece of code that only one thread can execute at once. Only one thread at a time will get into this section of code
Locks: synchronization mechanism for enforcing mutual exclusion on critical sections to construct atomic operations
Semaphores: synchronization mechanism for enforcing resource constraints