## Slide 1: CS162 Operating Systems and Systems Programming Lecture 16 Memory 4: Demand Paging Policies
March 15th, 2022
Prof. Anthony Joseph and John Kubiatowicz
http://cs162.eecs.Berkeley.edu

## Slide 2: What TLB Organization Makes Sense?
Needs to be really fast
  Critical path of memory access
    In simplest view: before the cache
    Thus, this adds to access time (reducing cache speed)
  Seems to argue for Direct Mapped or Low Associativity
However, needs to have very few conflicts!
  With TLB, the Miss Time extremely high! (PT traversal)
  Cost of Conflict (Miss Time) is high
  Hit Time – dictated by clock cycle
Thrashing: continuous conflicts between accesses
  What if use low order bits of virtual page number as index into TLB?
    First page of code, data, stack may map to same entry
    Need 3-way associativity at least?
  What if use high order bits as index?
    TLB mostly unused for small programs
CPU
TLB
Cache
[Physically
indexed]
Memory

## Slide 3: TLB organization: include protection
How big does TLB actually have to be?
  Usually small: 128-512 entries (larger now)
  Not very big, can support higher associativity
Small TLBs usually organized as fully-associative cache
  Lookup is by Virtual Address
  Returns Physical Address + other info
What happens when fully-associative is too slow?
  Put a small (4-16 entry) direct-mapped cache in front
  Called a “TLB Slice”
Example for MIPS R3000:
0xFA00 0x0003 Y N Y R/W 34 0x0040 0x0010 N Y Y R 0 0x0041 0x0011 N Y Y R 0
Virtual Address Physical Address Dirty Ref Valid Access ASID

## Slide 4: Example: R3000 pipeline includes TLB “stages”
Inst Fetch
Dcd/ Reg
ALU / E.A
Memory
Write Reg
TLB I-Cache RF Operation WB
E.A. TLB D-Cache
MIPS R3000 Pipeline
ASID
V. Page Number
Offset
12
20
6
0xx User segment (caching based on PT/TLB entry)
100 Kernel physical space, cached
101 Kernel physical space, uncached
11x Kernel virtual space
Allows context switching among
64 user processes without TLB flush
Virtual Address Space
TLB
  64 entry, on-chip, fully associative, software TLB fault handler

## Slide 5: Reducing translation time for physically-indexed caches
As described, TLB lookup is in serial with cache lookup
  Consequently, speed of TLB can impact speed of access to cache
Machines with TLBs go one step further: overlap TLB lookup with cache access
  Works because offset available early
  Offset in virtual address exactly covers the “cache index” and “byte select”
  Thus can select the cached byte(s) in parallel to perform address translation
Virtual Address
TLB Lookup
V
Access
Rights
PA
V page no.
offset
10
P page no.
offset
10
Physical Address
Offset
Virtual Page #
index
tag / page #
byte
virtual address:
physical address:

## Slide 6: Overlapping TLB & Cache Access
Here is how this might work with a 4K cache:
What if cache size is increased to 8KB?
  Overlap not complete
  Need to do something else. See CS152/252
Another option: Virtual Caches would make this faster
  Tags in cache are virtual addresses
  Translation only happens on cache misses
TLB
4K Cache
10
2
00
4 bytes
index
1 K
page #
disp
20
assoc
lookup
32
Hit/
Miss
FN
Data
Hit/
Miss
=
FN

## Slide 7: Current Intel x86 (Skylake, Cascade Lake)

## Slide 8: Current Example: Memory Hierarchy
Caches (all 64 B line size)
  L1 I-Cache: 32 KiB/core, 8-way set assoc.
  L1 D Cache: 32 KiB/core, 8-way set assoc., 4-5 cycles load-to-use, Write-back policy
  L2 Cache: 1 MiB/core, 16-way set assoc., Inclusive, Write-back policy, 14 cycles latency
  L3 Cache: 1.375 MiB/core, 11-way set assoc., shared across cores, Non-inclusive victim cache, Write-back policy, 50-70 cycles latency
TLB
  L1 ITLB, 128 entries; 8-way set assoc. for 4 KB pages
    8 entries per thread; fully associative, for 2 MiB / 4 MiB page
  L1 DTLB 64 entries; 4-way set associative for 4 KB pages
    32 entries; 4-way set associative, 2 MiB / 4 MiB page translations:
    4 entries; 4-way associative, 1G page translations:
  L2 STLB: 1536 entries; 12-way set assoc. 4 KiB + 2 MiB pages
    16 entries; 4-way set associative, 1 GiB page translations:

## Slide 9: What happens on a Context Switch?
Need to do something, since TLBs map virtual addresses to physical addresses
  Address Space just changed, so TLB entries no longer valid!
Options?
  Invalidate TLB: simple but might be expensive
    What if switching frequently between processes?
  Include ProcessID in TLB
    This is an architectural solution: needs hardware
What if translation tables change?
  For example, to move page from memory to disk or vice versa…
  Must invalidate TLB entry!
    Otherwise, might think that page is still in memory!
  Called “TLB Consistency”
Aside: with Virtually-Indexed cache, need to flush cache!
  Rember, everyone has their own version of the address “0”!

## Slide 10: Putting Everything Together: Address Translation
Virtual Address:
Offset
Virtual
P2 index
Virtual
P1 index
PageTablePtr
Page Table
(1st level)
Page Table
(2nd level)
Physical
Memory:
Offset
Physical Address:
Physical
Page #

## Slide 11: Putting Everything Together: TLB
Page Table
(2nd level)
PageTablePtr
Page Table
(1st level)
Offset
Virtual Address:
Offset
Virtual
P2 index
Virtual
P1 index
Physical
Memory:
Physical Address:
…
TLB:
Physical
Page #
Physical
Page #

## Slide 12: Putting Everything Together: Cache
Page Table
(2nd level)
PageTablePtr
Page Table
(1st level)
Virtual Address:
Offset
Virtual
P2 index
Virtual
P1 index
…
TLB:
Offset
Physical
Memory:
Physical Address:
…
tag:
block:
cache:
index
byte
tag
Physical
Page #

## Slide 13: Page Fault
The Virtual-to-Physical Translation fails
  PTE marked invalid, Priv. Level Violation, Access violation, or does not exist
  Causes an Fault / Trap
    Not an interrupt because synchronous to instruction execution
  May occur on instruction fetch or data access
  Protection violations typically terminate the instruction
Other Page Faults engage operating system to fix the situation and retry the instruction
  Allocate an additional stack page, or
  Make the page accessible - Copy on Write,
  Bring page in from secondary storage to memory – demand paging
Fundamental inversion of the hardware / software boundary

## Slide 14: Demand Paging
Modern programs require a lot of physical memory
  Memory per system growing faster than 25%-30%/year
But they don’t use all their memory all of the time
  90-10 rule: programs spend 90% of their time in 10% of their code
  Wasteful to require all of user’s code to be in memory
Solution: use main memory as “cache” for disk
On-Chip
Cache
Control
Datapath
Secondary
Storage
(Disk)
Processor
Main
Memory
(DRAM)
Second
Level
Cache
(SRAM)
Tertiary
Storage
(Tape)
paging
caching

## Slide 15: Page Fault  Demand Paging
virtual address
MMU
PT
instruction
physical address
page#
frame#
offset
page fault
Operating System
exception
Page Fault Handler
load page from disk
update PT entry
Process
scheduler
retry
frame#
offset

## Slide 16: Recall 61C: Average Memory Access Time
Used to compute access time probabilistically:
AMAT = Hit RateL1 x Hit TimeL1 + Miss RateL1 x Miss TimeL1
Hit RateL1 + Miss RateL1 = 1 Hit TimeL1 = Time to get value from L1 cache. Miss TimeL1 = Hit TimeL1 + Miss PenaltyL1 Miss PenaltyL1 = AVG Time to get value from lower level (DRAM)
So, AMAT = Hit TimeL1 + Miss RateL1 x Miss PenaltyL1
What about more levels of hierarchy?
AMAT = Hit TimeL1 + Miss RateL1 x Miss PenaltyL1
Miss PenaltyL1 = AVG time to get value from lower level (L2) = Hit TimeL2 + Miss RateL2 x Miss PenaltyL2 Miss PenaltyL2 = Average Time to fetch from below L2 (DRAM)
AMAT = Hit TimeL1 +
Miss RateL1 x (Hit TimeL2 + Miss RateL2 x Miss PenaltyL2)
And so on … (can do this recursively for more levels!)
Proc
L1 Cache
L2 Cache
DRAM
Proc
L1 Cache
DRAM

## Slide 17: Recall: Caching Applied to Address Translation
Question is one of page locality: does it exist?
  Instruction accesses spend a lot of time on the same page (accesses sequential)
  Stack accesses have definite locality of reference
  Data accesses have less page locality, but still some…
Can we have a TLB hierarchy?
  Sure: multiple levels at different sizes/speeds
Data Read or Write
(untranslated)
CPU
Physical
Memory
TLB
Translate
(MMU)
No
Virtual
Address
Physical
Address
Yes
Cached?
Save
Result

## Slide 18: Management & Access to the Memory Hierarchy
L3 Cache (shared)
Registers
Secondary Storage (Disk)
Processor
Main
Memory
(DRAM)
1
10,000,000
(10 ms)
Speed (ns):
10-30
100
100Bs
Size (bytes):
MBs
GBs
TBs
Registers
L1 Cache
L1 Cache
L2 Cache
L2 Cache
0.3
3
10kBs
100kBs
Secondary Storage (SSD)
100,000 (0.1 ms)
100GBs
Managed in Hardware
Managed in Software - OS
PT
PT
PT
PT
TLB
TLB
Accessed in Hardware
?
Notes: The design goal is to present the user with as much memory as is available in the cheapest technology (points to the disk).
While by taking advantage of the principle of locality, we like to provide the user an average access speed that is very close to the speed that is offered by the fastest technology.
(We will go over this slide in details in the next lecture on caches).
+1 = 16 min. (X:56)

## Slide 19: Page Fault  Demand Paging
virtual address
MMU
PT
instruction
physical address
page#
frame#
offset
page fault
Operating System
exception
Page Fault Handler
load page from disk
update PT entry
Process
scheduler
retry
frame#
offset

## Slide 20: Demand Paging as Caching, …
What “block size”? - 1 page (e.g, 4 KB)
What “organization” ie. direct-mapped, set-assoc., fully-associative?
  Fully associative since arbitrary virtual  physical mapping
How do we locate a page?
  First check TLB, then page-table traversal
What is page replacement policy? (i.e. LRU, Random…)
  This requires more explanation… (kinda LRU)
What happens on a miss?
  Go to lower level to fill miss (i.e. disk)
What happens on a write? (write-through, write back)
  Definitely write-back – need dirty bit!

## Slide 21: Illusion of Infinite Memory
Page
Table
TLB
Disk is larger than physical memory 
  In-use virtual memory can be bigger than physical memory
  Combined memory of running processes much larger than physical memory
    More programs fit into memory, allowing more concurrency
Principle: Transparent Level of Indirection (page table)
  Supports flexible placement of physical data
    Data could be on disk or somewhere across network
  Variable location of data transparent to user program
    Performance issue, not correctness issue
Physical
Memory
512 MB
Disk
500GB

Virtual
Memory
4 GB

## Slide 22: Review: What is in a PTE?
What is in a Page Table Entry (or PTE)?
  Pointer to next-level page table or to actual page
  Permission bits: valid, read-only, read-write, write-only
Example: Intel x86 architecture PTE:
  2-level page tabler (10, 10, 12-bit offset)
  Intermediate page tables called “Directories”
  P: Present (same as “valid” bit in other architectures)
  W: Writeable
  U: User accessible
  PWT: Page write transparent: external cache write-through
  PCD: Page cache disabled (page cannot be cached)
  A: Accessed: page has been accessed recently
  D: Dirty (PTE only): page has been modified recently
  PS: Page Size: PS=14MB page (directory only). Bottom 22 bits of virtual address serve as offset
Page Frame Number
(Physical Page Number)
Free
(OS)
0
PS
D
A
PCD
PWT
U
W
P
0
1
2
3
4
5
6
7
8
11-9
31-12

## Slide 23: Demand Paging Mechanisms
Cache
PTE makes demand paging implementatable
  Valid  Page in memory, PTE points at physical page
  Not Valid  Page not in memory; use info in PTE to find it on disk when necessary
Suppose user references page with invalid PTE?
  Memory Management Unit (MMU) traps to OS
    Resulting trap is a “Page Fault”
  What does OS do on a Page Fault?:
    Choose an old page to replace
    If old page modified (“D=1”), write contents back to disk
    Change its PTE and any cached TLB to be invalid
    Load new page into memory from disk
    Update page table entry, invalidate TLB for new entry
    Continue thread from original faulting location
  TLB for new page will be loaded when thread continued!
  While pulling pages off disk for one process, OS runs another process from ready queue
    Suspended process sits on wait queue

## Slide 24: Origins of Paging
Disks provide most of the storage
Relatively small memory, for many processes
P
. . .
Many clients on dumb terminals running different programs
Keep memory full of the frequently accesses pages
Keep most of the address space on disk
Actively swap pages to/from

## Slide 25: Very Different Situation Today
Powerful system
Huge memory
Huge disk
Single user

## Slide 26: A Picture on one machine
Memory stays about 75% used, 25% for dynamics
A lot of it is shared 1.9 GB

## Slide 27: Many Uses of Virtual Memory and “Demand Paging” …
Extend the stack
  Allocate a page and zero it
Extend the heap (sbrk of old, today mmap)
Process Fork
  Create a copy of the page table
  Entries refer to parent pages – NO-WRITE
  Shared read-only pages remain shared
  Copy page on write
Exec
  Only bring in parts of the binary in active use
  Do this on demand
MMAP to explicitly share region (or to access a file as RAM)

## Slide 28: Classic: Loading an executable into memory
.exe
  lives on disk in the file system
  contains contents of code & data segments, relocation entries and symbols
  OS loads it into memory, initializes registers (and initial stack pointer)
  program sets up stack and heap upon initialization: crt0 (C runtime init)
disk (huge)
memory
code
data
info
exe

## Slide 29: Create Virtual Address Space of the Process
Utilized pages in the VAS are backed by a page block on disk
  Called the backing store or swap file
  Typically in an optimized block store, but can think of it like a file
disk (huge)
memory
code
data
heap
stack
kernel
process VAS
sbrk
kernel code & data
user page
frames
user pagetable

## Slide 30: Create Virtual Address Space of the Process
User Page table maps entire VAS
All the utilized regions are backed on disk
  swapped into and out of memory as needed
For every process
disk (huge, TB)
memory
code
data
heap
stack
kernel
process VAS (GBs)
kernel code & data
user page
frames
user pagetable
code
data
heap
stack

## Slide 31: Create Virtual Address Space of the Process
User Page table maps entire VAS
  Resident pages to the frame in memory they occupy
  The portion of it that the HW needs to access must be resident in memory
disk (huge, TB)
memory
code
data
heap
stack
kernel
VAS
[per process]
kernel code & data
user page
frames
user pagetable
code
data
heap
stack
PT

## Slide 32: Provide Backing Store for VAS
User Page table maps entire VAS
Resident pages mapped to memory frames
For all other pages, OS must record where to find them on disk
disk (huge, TB)
memory
code
data
heap
stack
kernel
kernel code & data
user page
frames
user pagetable
code
data
heap
stack
VAS
[per process]

## Slide 33: What Data Structure Maps Non-Resident Pages to Disk?
FindBlock(PID, page#) → disk_block
  Some OSs utilize spare space in PTE for paged blocks
  Like the PT, but purely software
Where to store it?
  In memory – can be compact representation if swap storage is contiguous on disk
  Could use hash table (like Inverted PT)
Usually want backing store for resident pages too
May map code segment directly to on-disk image
  Saves a copy of code to swap file
May share code segment with multiple instances of the program

## Slide 34: Provide Backing Store for VAS
disk (huge, TB)
memory
kernel code & data
user page
frames
user pagetable
code
data
heap
stack
code
data
heap
stack
kernel
VAS 1
PT 1
code
data
heap
stack
kernel
VAS 2
PT 2
heap
stack
data

## Slide 35: On page Fault …
disk (huge, TB)
memory
kernel code
& data
user page
frames
user pagetable
code
data
heap
stack
code
data
heap
stack
kernel
VAS 1
PT 1
code
data
heap
stack
kernel
VAS 2
PT 2
heap
stack
data
active process & PT

## Slide 36: On page Fault … find & start load
disk (huge, TB)
memory
kernel code & data
user page
frames
user pagetable
code
data
heap
stack
code
data
heap
stack
kernel
VAS 1
PT 1
code
data
heap
stack
kernel
VAS 2
PT 2
heap
stack
data
active process & PT

## Slide 37: On page Fault … schedule other P or T
disk (huge, TB)
memory
kernel code & data
user page
frames
user pagetable
code
data
heap
stack
code
data
heap
stack
kernel
VAS 1
PT 1
code
data
heap
stack
kernel
VAS 2
PT 2
heap
stack
data
active process & PT

## Slide 38: On page Fault … update PTE
disk (huge, TB)
memory
kernel code & data
user page
frames
user pagetable
code
data
heap
stack
code
data
heap
stack
kernel
VAS 1
PT 1
code
data
heap
stack
kernel
VAS 2
PT 2
heap
stack
data
active process & PT

## Slide 39: Eventually reschedule faulting thread
disk (huge, TB)
memory
kernel code & data
user page
frames
user pagetable
code
data
heap
stack
code
data
heap
stack
kernel
VAS 1
PT 1
code
data
heap
stack
kernel
VAS 2
PT 2
heap
stack
data
active process & PT

## Slide 40: Summary: Steps in Handling a Page Fault

## Slide 41: Some questions we need to answer!
During a page fault, where does the OS get a free frame?
  Keeps a free list
  Unix runs a “reaper” if memory gets too full
    Schedule dirty pages to be written back on disk
    Zero (clean) pages which haven’t been accessed in a while
  As a last resort, evict a dirty page first
How can we organize these mechanisms?
  Work on the replacement policy
How many page frames/process?
  Like thread scheduling, need to “schedule” memory resources:
    Utilization? fairness? priority?
  Allocation of disk paging bandwidth

## Slide 42: Working Set Model
As a program executes it transitions through a sequence of “working sets” consisting of varying sized subsets of the address space
Time
Address

## Slide 43: Cache Behavior under WS model
Amortized by fraction of time the Working Set is active
Transitions from one WS to the next
Capacity, Conflict, Compulsory misses
Applicable to memory caches and pages. Others ?
Hit Rate
Cache Size
new working set fits
0
1

## Slide 44: Another model of Locality: Zipf
Likelihood of accessing item of rank r is α 1/ra
Although rare to access items below the top few, there are so many that it yields a “heavy tailed” distribution
Substantial value from even a tiny cache
Substantial misses from even a very large cache
Chart: P access(rank) = 1/rank
pop a=1 | 0.19278 | 0.096388 | 0.064259 | 0.048194 | 0.038555 | 0.032129 | 0.027539 | 0.024097 | 0.02142 | 0.019278 | 0.017525 | 0.016065 | 0.014829 | 0.01377 | 0.012852 | 0.012048 | 0.01134 | 0.01071 | 0.010146 | 0.0096388 | 0.0091798 | 0.0087625 | 0.0083815 | 0.0080323 | 0.007711 | 0.0074144 | 0.0071398 | 0.0068848 | 0.0066474 | 0.0064259 | 0.0062186 | 0.0060242 | 0.0058417 | 0.0056699 | 0.0055079 | 0.0053549 | 0.0052102 | 0.005073 | 0.004943 | 0.0048194 | 0.0047018 | 0.0045899 | 0.0044832 | 0.0043813 | 0.0042839 | 0.0041908 | 0.0041016 | 0.0040162 | 0.0039342 | 0.0038555
Hit Rate(cache) | 0.19278 | 0.28916 | 0.35342 | 0.40162 | 0.44017 | 0.4723 | 0.49984 | 0.52394 | 0.54536 | 0.56463 | 0.58216 | 0.59822 | 0.61305 | 0.62682 | 0.63967 | 0.65172 | 0.66306 | 0.67377 | 0.68392 | 0.69356 | 0.70274 | 0.7115 | 0.71988 | 0.72791 | 0.73562 | 0.74304 | 0.75018 | 0.75706 | 0.76371 | 0.77014 | 0.77635 | 0.78238 | 0.78822 | 0.79389 | 0.7994 | 0.80475 | 0.80996 | 0.81504 | 0.81998 | 0.8248 | 0.8295 | 0.83409 | 0.83857 | 0.84296 | 0.84724 | 0.85143 | 0.85553 | 0.85955 | 0.86348 | 0.86734

## Slide 45: Demand Paging Cost Model
Since Demand Paging like caching, can compute average access time! (“Effective Access Time”)
  EAT = Hit Rate x Hit Time + Miss Rate x Miss Time
  EAT = Hit Time + Miss Rate x Miss Penalty
Example:
  Memory access time = 200 nanoseconds
  Average page-fault service time = 8 milliseconds
  Suppose p = Probability of miss, 1-p = Probably of hit
  Then, we can compute EAT as follows:
EAT = 200ns + p x 8 ms
= 200ns + p x 8,000,000ns
If one access out of 1,000 causes a page fault, then EAT = 8.2 μs:
  This is a slowdown by a factor of 40!
What if want slowdown by less than 10%?
  EAT < 200ns x 1.1  p < 2.5 x 10-6
  This is about 1 page fault in 400,000!

## Slide 46: What Factors Lead to Misses in Page Cache?
Compulsory Misses:
  Pages that have never been paged into memory before
  How might we remove these misses?
    Prefetching: loading them into memory before needed
    Need to predict future somehow! More later
Capacity Misses:
  Not enough memory. Must somehow increase available memory size.
  Can we do this?
    One option: Increase amount of DRAM (not quick fix!)
    Another option: If multiple processes in memory: adjust percentage of memory allocated to each one!
Conflict Misses:
  Technically, conflict misses don’t exist in virtual memory, since it is a “fully-associative” cache
Policy Misses:
  Caused when pages were in memory, but kicked out prematurely because of the replacement policy
  How to fix? Better replacement policy

## Slide 47: Page Replacement Policies
Why do we care about Replacement Policy?
  Replacement is an issue with any cache
  Particularly important with pages
    The cost of being wrong is high: must go to disk
    Must keep important pages in memory, not toss them out
FIFO (First In, First Out)
  Throw out oldest page. Be fair – let every page live in memory for same amount of time.
  Bad – throws out heavily used pages instead of infrequently used
RANDOM:
  Pick random page for every replacement
  Typical solution for TLB’s. Simple hardware
  Pretty unpredictable – makes it hard to make real-time guarantees
MIN (Minimum):
  Replace page that won’t be used for the longest time
  Great (provably optimal), but can’t really know future…
  But past is a good predictor of the future …

## Slide 48: Replacement Policies (Con’t)
LRU (Least Recently Used):
  Replace page that hasn’t been used for the longest time
  Programs have locality, so if something not used for a while, unlikely to be used in the near future.
  Seems like LRU should be a good approximation to MIN.
How to implement LRU? Use a list:
  On each use, remove page from list and place at head
  LRU page is at tail
Problems with this scheme for paging?
  Need to know immediately when page used so that can change position in list…
  Many instructions for each hardware access
In practice, people approximate LRU (more later)
Page 6
Page 7
Page 1
Page 2
Head
Tail (LRU)

## Slide 49: Example: FIFO (strawman)
Suppose we have 3 page frames, 4 virtual pages, and following reference stream:
  A B C A B D A D B C B
Consider FIFO Page replacement:
FIFO: 7 faults
When referencing D, replacing A is bad choice, since need A again right away
C
B
A
D
C
B
A
B
C
B
D
A
D
B
A
C
B
A
3
2
1
Ref:
Page:

## Slide 50: Example: MIN / LRU
Suppose we have the same reference stream:
  A B C A B D A D B C B
Consider MIN Page replacement:
MIN: 5 faults
  Where will D be brought in? Look for page not referenced farthest in future
What will LRU do?
  Same decisions as MIN here, but won’t always be true!
C
D
C
B
A
B
C
B
D
A
D
B
A
C
B
A
3
2
1
Ref:
Page:

## Slide 51: Is LRU guaranteed to perform well?
Consider the following: A B C D A B C D A B C D
LRU Performs as follows (same as FIFO here):
  Every reference is a page fault!
Fairly contrived example of working set of N+1 on N frames
D
C
B
A
D
C
B
A
D
C
B
A
C
B
A
D
C
B
A
D
C
B
A
D
3
2
1
Ref:
Page:

## Slide 52: When will LRU perform badly?
Consider the following: A B C D A B C D A B C D
LRU Performs as follows (same as FIFO here):
  Every reference is a page fault!
MIN Does much better:
D
C
B
A
D
C
B
A
D
C
B
A
C
B
A
D
C
B
A
D
C
B
A
D
3
2
1
Ref:
Page:
B
C
D
C
B
A
B
A
D
C
B
A
D
C
B
A
C
D
3
2
1
Ref:
Page:

## Slide 53: Graph of Page Faults Versus The Number of Frames
One desirable property: When you add memory the miss rate drops (stack property)
  Does this always happen?
  Seems like it should, right?
No: Bélády’s anomaly
  Certain replacement algorithms (FIFO) don’t have this obvious property!

## Slide 54: Adding Memory Doesn’t Always Help Fault Rate
Does adding memory reduce number of page faults?
  Yes for LRU and MIN
  Not necessarily for FIFO! (Called Bélády’s anomaly)
After adding memory:
  With FIFO, contents can be completely different
  In contrast, with LRU or MIN, contents of memory with X pages are a subset of contents with X+1 Page
D
C
E
B
A
D
C
B
A
D
C
B
A
E
B
A
D
C
B
A
E
3
2
1
Ref:
Page:
C
D
4
E
D
B
A
E
C
B
A
D
C
B
A
E
B
A
D
C
B
A
E
3
2
1
Ref:
Page:

## Slide 55: Approximating LRU: Clock Algorithm
Set of all pages
in Memory
Single Clock Hand:
  Advances only on page fault!
  Check for pages not used recently
  Mark pages as not used recently
Clock Algorithm: Arrange physical pages in circle with single clock hand
  Approximate LRU (approximation to approximation to MIN)
  Replace an old page, not the oldest page
Details:
  Hardware “use” bit per physical page (called “accessed” in Intel architecture):
    Hardware sets use bit on each reference
    If use bit isn’t set, means not referenced in a long time
    Some hardware sets use bit in the TLB; must be copied back to PTE when TLB entry gets replaced
  On page fault:
    Advance clock hand (not real time)
    Check use bit: 1 used recently; clear and leave alone 0 selected candidate for replacement

## Slide 56: Clock Algorithm: More details
Will always find a page or loop forever?
  Even if all use bits set, will eventually loop all the way around  FIFO
What if hand moving slowly?
  Good sign or bad sign?
    Not many page faults
    or find page quickly
What if hand is moving quickly?
  Lots of page faults and/or lots of reference bits set
One way to view clock algorithm:
  Crude partitioning of pages into two groups: young and old
  Why not partition into more than 2 groups?
Set of all pages
in Memory
Single Clock Hand

## Slide 57: Nth Chance version of Clock Algorithm
Nth chance algorithm: Give page N chances
  OS keeps counter per page: # sweeps
  On page fault, OS checks use bit:
    1  clear use and also clear counter (used in last sweep)
    0  increment counter; if count=N, replace page
  Means that clock hand has to sweep by N times without page being used before page is replaced
How do we pick N?
  Why pick large N? Better approximation to LRU
    If N ~ 1K, really good approximation
  Why pick small N? More efficient
    Otherwise might have to look a long way to find free page
What about “modified” (or “dirty”) pages?
  Takes extra overhead to replace a dirty page, so give dirty pages an extra chance before replacing?
  Common approach:
    Clean pages, use N=1
    Dirty pages, use N=2 (and write back to disk when N=1)

## Slide 58: Recall: Meaning of PTE bits
Which bits of a PTE entry are useful to us for the Clock Algorithm? Remember Intel PTE:
  The “Present” bit (called “Valid” elsewhere):
    P==0: Page is invalid and a reference will cause page fault
    P==1: Page frame number is valid and MMU is allowed to proceed with translation
  The “Writable” bit (could have opposite sense and be called “Read-only”):
    W==0: Page is read-only and cannot be written.
    W==1: Page can be written
  The “Accessed” bit (called “Use” elsewhere):
    A==0: Page has not been accessed (or used) since last time software set A0
    A==1: Page has been accessed (or used) since last time software set A0
  The “Dirty” bit (called “Modified” elsewhere):
    D==0: Page has not been modified (written) since PTE was loaded
    D==1: Page has changed since PTE was loaded
Page Frame Number
(Physical Page Number)
Free
(OS)
0
PS
D
A
PCD
PWT
U
W
P
0
1
2
3
4
5
6
7
8
11-9
31-12
PTE:

## Slide 59: Clock Algorithms Variations
Do we really need hardware-supported “modified” bit?
  No. Can emulate it using read-only bit
    Need software DB of which pages are allowed to be written (needed this anyway)
    We will tell MMU that pages have more restricted permissions than the actually do to force page faults (and allow us notice when page is written)
  Algorithm (Clock-Emulated-M):
    Initially, mark all pages as read-only (W0), even writable data pages. Further, clear all software versions of the “modified” bit  0 (page not dirty)
    Writes will cause a page fault. Assuming write is allowed, OS sets software “modified” bit  1, and marks page as writable (W1).
    Whenever page written back to disk, clear “modified” bit  0, mark read-only

## Slide 60: Clock Algorithms Variations (continued)
Do we really need a hardware-supported “use” bit?
  No. Can emulate it similar to above (e.g. for read operation)
    Kernel keeps a “use” bit and “modified” bit for each page
  Algorithm (Clock-Emulated-Use-and-M):
    Mark all pages as invalid, even if in memory. Clear emulated “use” bits  0 and “modified” bits  0 for all pages (not used, not dirty)
    Read or write to invalid page traps to OS to tell use page has been used
    OS sets “use” bit  1 in software to indicate that page has been “used”. Further: 1) If read, mark page as read-only, W0 (will catch future writes) 2) If write (and write allowed), set “modified” bit  1, mark page as writable (W1)
    When clock hand passes, reset emulated “use” bit  0 and mark page as invalid again
    Note that “modified” bit left alone until page written back to disk
Remember, however, clock is just an approximation of LRU!
  Can we do a better approximation, given that we have to take page faults on some reads and writes to collect use information?
  Need to identify an old page, not oldest page!
  Answer: second chance list

## Slide 61: Second-Chance List Algorithm (VAX/VMS)
Split memory in two: Active list (RW), SC list (Invalid)
Access pages in Active list at full speed
Otherwise, Page Fault
  Always move overflow page from end of Active list to front of Second-chance list (SC) and mark invalid
  Desired Page On SC List: move to front of Active list, mark RW
  Not on SC list: page in to front of Active list, mark RW; page out LRU victim at end of SC list
Directly
Mapped Pages
Marked: RW
List: FIFO
Second
Chance List
Marked: Invalid
List: LRU
LRU victim
Page-in
From disk
New
Active Pages
Access
New
SC Victims
Overflow

## Slide 62: Second-Chance List Algorithm (continued)
How many pages for second chance list?
  If 0  FIFO
  If all  LRU, but page fault on every page reference
Pick intermediate value. Result is:
  Pro: Few disk accesses (page only goes to disk if unused for a long time)
  Con: Increased overhead trapping to OS (software / hardware tradeoff)
With page translation, we can adapt to any kind of access the program makes
  Later, we will show how to use page translation / protection to share memory between threads on widely separated machines
History: The VAX architecture did not include a “use” bit. Why did that omission happen???
  Strecker (architect) asked OS people, they said they didn’t need it, so didn’t implement it
  He later got blamed, but VAX did OK anyway

## Slide 63: Summary
Replacement policies
  FIFO: Place pages on queue, replace page at end
  MIN: Replace page that will be used farthest in future
  LRU: Replace page used farthest in past
Clock Algorithm: Approximation to LRU
  Arrange all pages in circular list
  Sweep through them, marking as not “in use”
  If page not “in use” for one pass, than can replace
Nth-chance clock algorithm: Another approximate LRU
  Give pages multiple passes of clock hand before replacing
Second-Chance List algorithm: Yet another approximate LRU
  Divide pages into two groups, one of which is truly LRU and managed on page faults.
Working Set:
  Set of pages touched by a process recently
Thrashing: a process is busy swapping pages in and out
  Process will thrash if working set doesn’t fit in memory
  Need to swap out a process