## Slide 1: CS162 Operating Systems and Systems Programming Lecture 17 General I/O, Storage Devices

## Slide 2: Course Map
Introduction
OS Concepts
Concurrency
Scheduling
Memory Management
Devices and file systems
Reliability, networking and cloud

## Slide 3: Recall: Five Components of a Computer

## Slide 4: CPU: You need to get out more!
Input/output is the mechanism through which the computer communicates with the outside world

## Slide 5: Want Standard Interfaces to Devices
Block Devices: e.g. disk drives, tape drives, DVD-ROM
  Access blocks of data
  Commands include open(), read(), write(), seek()
  Raw I/O or file-system access
Character Devices: e.g. keyboards, mice, serial ports, some USB devices
  Single characters at a time
  Commands include get(), put()
Network Devices: e.g. Ethernet, Wireless, Bluetooth
  Different enough from block/character to have own interface
  Unix and Windows include socket interface
    Separates network protocol from network operation
    Includes select() functionality
  Usage: pipes, FIFOs, streams, queues, mailboxes

## Slide 6: IO Subsystem: Abstraction, abstraction, abstraction
Processor
Memory
OS Memory
Process 1
Process 2
Process 3
OS Hardware Virtualization
Virtual Machine Abstraction
IO Layer
IO Devices

## Slide 7: IO Subsystem: Abstraction, abstraction, abstraction
This code
  FILE fd = fopen("/dev/something", "rw"); for (int i = 0; i < 10; i++) { fprintf(fd, "Count %d\n", i); } close(fd);
  Why? Because code that controls devices (“device driver”) implements standard interface
We will try to get a flavor for what is involved in actually controlling devices in rest of lecture
  Can only scratch surface!

## Slide 8: Requirements of I/O layer
But… thousands of devices, each slightly different
    OS: How can we standardize the interfaces to these devices?
Devices unreliable: media failures and transmission errors
    OS: How can we make them reliable???
Devices unpredictable and/or slow
    OS: How can we manage them if we don’t know what they will do or how they will perform?

## Slide 9: Simplified IO architecture
Follows a hierarchical structure because of cost: the faster the bus, the more expensive it is

## Slide 10: Intel’s Z270 Chipset

## Slide 11: Sky Lake I/O: PCH
Platform Controller Hub
  Connected to processor with proprietary bus
    Direct Media Interface
Types of I/O on PCH:
  USB, Ethernet
  Thunderbolt 3
  Audio, BIOS support
  More PCI Express (lower speed than on Processor)
  SATA (for Disks)
Sky Lake
System Configuration

## Slide 12: Example: Device Transfer Rates in Mb/s (Sun Enterprise 6000)
Device rates vary over 12 orders of magnitude!!!

## Slide 13: Two questions
What is a bus?
How does the processor talk to the devices?

## Slide 14: What’s a bus?
Common set of wires for communication among hardware devices plus protocols for carrying out data transfer transactions
Split into three parts: data bus, address bus, and control bus
Protocol: initiator requests access, arbitration to grant, identification of recipient, handshake to convey address, length, data

## Slide 15: Why a Bus?
Buses let us connect devices over a single set of wires, connections, and protocols
  relationships with 1 set of wires (!)
Downside: Only one transaction at a time
  The rest must wait
  “Arbitration” aspect of bus protocol ensures the rest wait

## Slide 16: PCI Bus Evolution
PCI started life out as a parallel bus
But a parallel bus has many limitations
  Multiplexing address/data for many requests
  Slowest devices must be able to tell what’s happening (e.g., for arbitration)
  Bus speed is set to that of the slowest device

## Slide 17: PCI Express “Bus”
No longer a parallel bus
Really a collection of fast serial channels or “lanes”
Devices can use as many as they need to achieve a desired bandwidth
Slow devices don’t have to share with fast ones
One of the successes of device abstraction in Linux was the ability to migrate from PCI to PCI Express
  The physical interconnect changed completely, but the old API still worked

## Slide 18: How does the processor talk to devices?
Remember, it’s all about abstractions!
It’s a file!
(What the user sees)
Interface
(What the OS sees)
Internals
(What is needed to implement the abstraction)
Hardware interface device presents to OS
Hardware interface device presents to OS
Microcontroller
Memory
Other chips
Device Controller

## Slide 19: How does the processor talk to devices?
Interface
(What the OS sees)
Registers
Status
Command
Data
  Port-Mapped I/O:
  Privileged in/out instructions
    Example from the Intel architecture: out 0x21,AL
  Memory-mapped I/O: load/store instructions
    Registers/memory appear in physical address space
    I/O accomplished with load and store instructions

## Slide 20: Port-Mapped I/O in Pintos Speaker Driver
Pintos: threads/io.h
Pintos: devices/speaker.c

## Slide 21: A simple protocol
  Protocol does a lot of polling!
  How can we lower this overhead?
  CPU is responsible for moving data

## Slide 22: Polling vs Interrupt-driven IO
Use hardware interrupts:
  Allows CPU to process another task. Will get notified when task is done
  Interrupt handler will read data & error code
Is it always better to use interrupts?

## Slide 23: From programmed IO to direct memory access
With programmed IO (simple protocol):
  CPU issues read request
  Device interrupts CPU with data
  CPU writes data to memory
  Pros: simple hardware. Cons: Poor CPU is always busy!
With direct-memory-access (DMA):
  CPU sets up DMA request
    Gives controller access to memory bus
  Device puts data on bus & RAM accepts it
  Device interrupts CPU when done
Device
CPU
CPU
RAM
Device
RAM

## Slide 24: DMA in more detail
1
2
3

## Slide 25: How can the OS handle one all devices
How do we fit devices with specific interfaces into OS, which should remain general?
  Build a “device neutral” OS and hide details of devices from most of OS
Abstraction to the rescue!
  Device Drivers encapsulate all specifics of device interaction
  Implement device neutral interfaces

## Slide 26: Device Drivers
Device Driver: Device-specific code in the kernel that interacts directly with the device hardware
  Supports a standard, internal interface
  Special device-specific configuration supported with the ioctl() system call
Device Drivers typically divided into two pieces:
  Top half: accessed in call path from system calls
    implements a set of standard, cross-device calls like open(), close(), read(), write(), ioctl(), strategy()
    This is the kernel’s interface to the device driver
    Top half will start I/O to device, may put thread to sleep until finished
  Bottom half: run as interrupt routine
    Gets input or transfers next block of output
    May wake sleeping threads if I/O now complete
Your body is 90% water, the OS is 70% device-drivers

## Slide 27: Putting it together: Life Cycle of An I/O Request
Device Driver
Top Half
Device Driver
Bottom Half
Device
Hardware
Kernel I/O
Subsystem
User
Program

## Slide 28: Conclusion
I/O Devices Types:
  Many different speeds (0.1 bytes/sec to GBytes/sec)
  Different Access Patterns:
    Block Devices, Character Devices, Network Devices
I/O Controllers: Hardware that controls actual device
  Processor Accesses through I/O instructions, load/store to special physical memory
Notification mechanisms
  Interrupts
  Polling: Report results through status register that processor looks at periodically
Device drivers interface to I/O devices
  Provide clean Read/Write interface to OS above
  Manipulate devices through PIO, DMA & interrupt handling