## Slide 1: CS162 Operating Systems and Systems Programming Lecture 19 General IO (Continued) & File Systems
Professor Natacha Crooks.
Special Guest: Tux
https://cs162.org/
Slides based on prior slide decks from David Culler, Ion Stoica, John Kubiatowicz, Alison Norman and Lorenzo Alvisi

## Slide 2: A History of Tux
Tux, the friendly penguin has been Linux logo since 1996
Why? Linus Torvalds … just really liked penguins despite being bitten by a penguin in Australia
By 2007, the zoo in Canberra where Torvalds was first nibbled by a penguin had erected a sign commemorating the episode, mentioning "It is our belief that the original Tux is still housed in this enclosure."

## Slide 3: A History of Tux

## Slide 4: Recall : Simplified IO architecture
Follows a hierarchical structure because of cost:
the faster the bus, the more expensive

## Slide 5: Recall: How does processor talk to devices?
Remember, it’s all about abstractions!
Interface
(What the OS sees)
Internals
(What is needed to implement the abstraction)
Hardware interface device presents to OS
Hardware interface device presents to OS
Microcontroller
Memory
Other chips
Device Controller
Status
Command
Data

## Slide 6: Recall: Device Drivers
Device-specific code in the kernel that interacts directly with the device hardware
  Supports a standard, internal interface
  Special device-specific configuration supported with ioctl()
  Top half: accessed in call path from system calls.
    Implements a set of standard, cross-device calls
    Bottom half: run as interrupt routine
    Gets input or transfers next block of output
    May wake sleeping threads if I/O now complete
Your body is 90% water, the OS is 70% device-drivers

## Slide 7: Recall: Life Cycle of An I/O Request
Device Driver
Top Half
Device Driver
Bottom Half
Device
Hardware
Kernel I/O
Subsystem
User
Program

## Slide 8: Ways of Measuring Performance
Latency - time to complete a task
Measured in units of time (s, ms, us, …, hours, years)
Throughput or Bandwidth – rate at which tasks are performed
Measured in units of things per unit time (ops/s, GFLOP/s)
Start up or Overhead – time to initiate an operation
Most I/O operations are roughly linear in b bytes
  Latency(b) = Overhead + b/TransferCapacity

## Slide 9: Storage Devices
Magnetic disks
  Storage that rarely becomes corrupted
  Large capacity at low cost
  Block level random access (except for SMR – later!)
  Slow performance for random access
  Better performance for sequential access
Flash memory
  Storage that rarely becomes corrupted
  Capacity at intermediate cost (5-20x disk)
  Block level random access
  Good performance for reads; worse for random writes
  Wear patterns issue

## Slide 10: Hard Disk Drives (HDDs)
Read/Write Head Side View
IBM Personal Computer 1986
30MB Hard Disk for 500 dollars

## Slide 11: The Amazing Magnetic Disk
Store data magnetically on thin metallic film bonded to rotating disk of glass, ceramic, or aluminum

## Slide 12: The Amazing Magnetic Disk
Track: concentric circle on surface
Sectors: slice of a track
  Smallest addressable unit
  Are units of transfers
Cylinder all the tracks under the head at a given point on all surfaces

## Slide 13: The Amazing Magnetic Disk
Sector
Track
Cylinder
Head
Platter
Track lengths vary across disk: outside tracks have more sectors per track, higher bandwidth
Disk is organized into regions of tracks with the same number of sector/tracks
Usually, only outer half of radius is used

## Slide 14: Reading/Writing Data
  Seek time: position the head/arm over the proper track
  Rotational latency: wait for desired sector to rotate under r/w head
  Transfer time: transfer a block of bits (sector) under r/w head

## Slide 15: Reading/Writing Data
Software
Queue
(Device Driver)
Hardware
Controller
Media Time
(Seek+Rot+Xfer)
Request
Result
Request Time =
Queueing Time + Controller Time + Seek + Rotational + Transfer

## Slide 16: Typical Numbers for Magnetic Disk
Parameter | Info/Range
Space/Density | Space: 14TB (Seagate), 8 platters, in 3½ inch form factor! Areal Density: ≥ 1 Terabit/square inch! (PMR, Helium, …)
Average Seek Time | Typically 4-6 milliseconds
Average Rotational Latency | Most laptop/desktop disks rotate at 3600-7200 RPM (16-8 ms/rotation). Server disks up to 15,000 RPM. Average latency is halfway around disk so 4-8 milliseconds
Controller Time | Depends on controller hardware
Transfer Time | Typically 50 to 250 MB/s. Depends on: Transfer size (usually a sector): 512B – 1KB per sector Rotation speed: 3600 RPM to 15000 RPM Recording density: bits per inch on a track Diameter: ranges from 1 in to 5.25 in
Cost | Used to drop by a factor of two every 1.5 years (or faster), now slowing down

## Slide 17: Disk Performance Example
Key to using disk effectively (especially for file systems) is to minimize seek and rotational delays
Do access patterns influence how fast can read/write to disk?
  Avg seek time of 5ms,
  7200RPM 
  Time for rotation: 60000 (ms/min)/7200(rev/min) ~= 8ms
  Transfer rate of 50MByte/s, block size of 4Kbyte  4096 bytes/50×106 (bytes/s) = 81.92 × 10-6 sec 
  0.082 ms for 1 sector

## Slide 18: Disk Performance Example
Read block from random place on disk (random reads):
  Seek (5ms) + Rot. Delay (4ms) + Transfer (0.082ms) = 9.082ms
  Approx 9ms to fetch/put data: 4096 bytes/9.082×10-3 s  451KB/s
Read block from random place in same cylinder:
  Rot. Delay (4ms) + Transfer (0.082ms) = 4.082ms
  Approx 4ms to fetch/put data: 4096 bytes/4.082×10-3 s  1.03MB/s
Read next block on same track (sequential reads):
  Transfer (0.082ms): 4096 bytes/0.082×10-3 s  50MB/sec

## Slide 19: When is Disk Performance Highest?
When there are big sequential reads, or
When there is so much work to do that they can be piggy backed (reordering queues—one moment)
OK to be inefficient when things are mostly idle
Bursts are both a threat and an opportunity
<your idea for optimization goes here>
  Waste space for speed?

## Slide 20: Disk Scheduling (1/3)
Disk can do only one request at a time; What order do you choose to do queued requests?
2,3
2,1
3,10
7,2
5,2
2,2
Head
User
Requests
1
4
2
Disk Head
3

## Slide 21: Disk Scheduling (1/3)
FIFO Order
  Fair among requesters, but order of arrival may be to random spots on the disk
SSTF: Shortest seek time first
  Pick the request that’s closest on the disk
  Con: SSTF good at reducing seeks, but may lead to starvation
2,3
2,1
3,10
7,2
5,2
2,2
Head
User
Requests

## Slide 22: Disk Scheduling (2/3)
SCAN: Implements an Elevator Algorithm: take the closest request in the direction of travel
  No starvation, but retains flavor of SSTF
2,3
2,1
3,10
7,2
5,2
2,2
Head
User
Requests

## Slide 23: Disk Scheduling (3/3)
C-SCAN: Circular-Scan: only goes in one direction
  Skips any requests on the way back
  Fairer than SCAN, not biased towards pages in middle

## Slide 24: Lots of Intelligence in the Controller
Sectors contain sophisticated error correcting codes
  Disk head magnet has a field wider than track
  Hide corruptions due to neighboring track writes
Sector sparing
  Remap bad sectors transparently to spare sectors on the same surface
Slip sparing
  Remap all sectors (when there is a bad sector) to preserve sequential behavior
Track skewing
  Sector numbers offset from one track to the next, to allow for disk head movement for sequential ops

## Slide 25: Hard Drive Prices over Time

## Slide 26: Example of Current HDDs
Seagate Exos X18 (2020)
  18 TB hard disk
    9 platters, 18 heads
    Helium filled: reduce friction and power
  4.16ms average seek time
  4096 byte physical sectors
  7200 RPMs
  Dual 6 Gbps SATA /12Gbps SAS interface
    270MB/s MAX transfer rate
    Cache size: 256MB
  Price: $ 562 (~ $0.03/GB)
IBM Personal Computer/AT (1986)
  30 MB hard disk
  30-40ms seek time
  0.7-1 MB/s (est.)
  Price: $500 ($17K/GB, 340,000x more expensive !!)

## Slide 27: Solid State Drives
1995 – Replace rotating magnetic media with non-volatile memory (battery backed DRAM)
2009 – Use flash memory
  Sector (4 KB page) addressable, but stores 4-64 “pages” per memory block
  Trapped electrons distinguish between 1 and 0
No moving parts (no rotate/seek motors)
  Eliminates seek and rotational delay (0.1-0.2ms access time)
  Very low power and lightweight
  Limited “write cycles”

## Slide 28: The Flash Cell
Encode bit by trapping electrons into a cell
Single-level cell (SLC)
  Single bit is stored within a transistor
  Faster, more lasting (50k to 100k writes before wear out)
Multi-level cell (MLC)
  Two/three bits are encoded into different levels of charge
  Wear out much faster (1k to 10k writes)

## Slide 29: Of banks, blocks, cells
Bank
Block
Block
Page
Page
Page
Page
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Cell
Flash chips organized in banks
  Banks can be accessed in parallel
Blocks 128 KB/256KB
  (64 to 258 pages)
Pages Few KB
Cells 1 to 4 bits
Distinction between blocks and pages important in operations!

## Slide 30: Low-level flash operations
How do you read?
  Chip supports reading pages
  10s of microseconds, independently of the previously read page
What about writing? More complicated!
  Must first erase the block
    Erase quite expensive (milliseconds)
  Once block has been erased, can then program a page
    Change 1s to 0s within a page.
    100s of microseconds.
  Blocks can only be erased a limited number of times!

## Slide 31: Low-level flash operations
INVALID
ERASED
VALID

## Slide 32: Low-level flash operations
Assume block of 4 pages. All valid.
Want to write Page 0
Step 1: erase full block
Step 2: program page 0

## Slide 33: SSD Architecture
Recall that SSDs uses low-level Flash operations to provide same interface as HDD
  read and write chunk (4KB) at a time
Reads are easy, but for writes, can only overwrite data one block (256KB) at a time!
Why not just erase and rewrite new version of entire 256KB block?
  Erasure is very slow (milliseconds)
  Each block has a finite lifetime, can only be erased and rewritten about 10K times
  Heavily used blocks likely to wear out quickly

## Slide 34: SSD Architecture (Simplified)

## Slide 35: Flash Translation Layer (FTL)
Add a layer of indirection: the flash translation layer
  Translates request for logical blocks (device interface) to low-level Flash blocks and pages
Reduce write amplification
  Ratio of the total write traffic in bytes issues by the flash chip by the FTL devided by the total write traffic issued by the OS to the device
Avoid wear out
  A single block should not be erased too often

## Slide 36: FTL – Two Systems Principles
FTL uses indirection and copy-on-write
Maintains mapping tables in DRAM
  Map virtual block numbers (which OS uses) to physical page numbers (which flash mem. controller uses)
  Can now freely relocate data w/o OS knowing
Copy on Write/ Log-structured FTL
  Don’t overwrite a page when OS updates its data
  Instead, write new version in a free page
  Update FTL mapping to point to new location

## Slide 37: FTL Example
Write(a0)
Block 0
Block 1
Mapping Table
a0->0,0
a0
V
E
E
E
Block 0
Block 1
Mapping Table:
E
E
E
E
Initial
State
Write(a1)
Block 0
Block 1
Mapping Table:
a0->0,0/a1->0,1
a0
a1
V
V
E
E
Write(a1)
Block 0
Block 1
Mapping Table:
a0->0,0/a1->1,0
a0
a1
V
V
a1
V
E
Write(a0)
Block 0
Block 1
Mapping Table:
a0->1,1/a1->1,0
a0
a1
V
V
a1
a0
V
V
Garbage Collect
Block 0
Block 1
Mapping Table:
a0->1,1/a1->1,0
E
E
a1
a0
V
V

## Slide 38: Some “Current” (large) 3.5in SSDs
Seagate Exos SSD: 15.36TB (2017)
  Seq reads 860MB/s
  Seq writes 920MB/s
  Price (Amazon): $5495 ($0.36/GB)
Nimbus SSD: 100TB (2019)
  Seq reads/writes: 500MB/s
  Random Read Ops (IOPS): 100K
  Unlimited writes for 5 years!
  Price: ~ $40K? ($0.4/GB)
    However, 50TB drive costs $12500 ($0.25/GB)

## Slide 39: HDD vs. SSD Comparison
HDD | SDD
Require seek + rotation | No seeks
Not parallel (one head) | Parallel
Brittle (moving parts) | No moving parts
Random reads take 10s milliseconds | Random reads take 10s microseconds
Slow (Mechanical) | Wears out
Cheap/large storage | Expensive/smaller storage

## Slide 40: Recall: I/O and Storage Layers
High Level I/O
Low Level I/O
Syscall
File System
I/O Driver
Streams
File Descriptors
open(), read(), write(), close(), …
Files/Directories/Indexes
Commands and Data Transfers
Disks, Flash, Controllers, DMA
Open File Descriptions

## Slide 41: From Storage to File Systems
I/O API and
syscalls
Variable-Size Buffer
File System
Block
Logical Index, Typically 4 KB
Hardware Devices
Memory Address
HDD
Sector(s)
Physical Index,
512B or 4KB
SSD
Flash Trans. Layer
Phys. Block
Phys Index., 4KB
Sector(s)
Sector(s)
Erasure Page

## Slide 42: Building a File System
Layer of OS that transforms block interface of disks (or other block devices) into Files, Directories, etc.

## Slide 43: Building a File System
OS as an illusionist: Take limited hardware interface (array of blocks) and provide a more convenient/useful interface with:
Naming: Find file by name, not block numbers
Organize file names with directories
Organization: Map files to blocks
Protection: Enforce access restrictions
Reliability: Keep files intact despite crashes, failures, etc.

## Slide 44: User vs. System View of a File
User’s view:
  Durable Data Structures
System’s view (system call interface):
  Collection of Bytes (UNIX)
  Doesn’t matter to system what kind of data structures you want to store on disk!
System’s view (inside OS):
  Collection of blocks (a block is a logical transfer unit, while a sector is the physical transfer unit)
  Block size  sector size; in UNIX, block size is 4KB

## Slide 45: Translation from User to System View
What happens if user says: “give me bytes 2 – 12?”
  Fetch block corresponding to those bytes
  Return just the correct portion of the block
What about writing bytes 2 – 12?
  Fetch block, modify relevant portion, write out block
Everything inside file system is in terms of whole-size blocks
File
System
File (Bytes)

## Slide 46: Disk Management
Basic entities on a disk:
  File: user-visible group of blocks arranged sequentially in logical space
  Directory: user-visible index mapping names to files
The disk is accessed as linear array of sectors
Old: Physical Position [cylinder, surface, sector]
  New: Logical Block Addressing (LBA)
    Every sector has integer address
    Controller translates from address  physical position
    Shields OS from structure of disk

## Slide 47: What Does the File System Need?
Track free disk blocks
  Need to know where to put newly written data
Track which blocks contain data for which files
  Need to know where to read a file from
Track files in a directory
  Find list of file's blocks given its name
Where do we maintain all of this?
  Somewhere on disk