## Slide 1: CS162 Operating Systems and Systems Programming Lecture 14 Caching (Finished), Demand Paging
March 12th, 2018
Profs. Anthony D. Joseph & Jonathan Ragan-Kelley
http://cs162.eecs.Berkeley.edu
[substitute Prof. David E. Culler]
Notes: Ok, so let’s get started! This is lecture 14 and I will continue talking about caching, picking up where Anthony left off on Monday.
And towards the end of the lecture, I will introduce demand paging, which is also a form of caching.

## Slide 2: Tribute
Sir Maurice Wilkes, inventor of EDSAC, Microprogramming, and the Translation Look-aside Buffer

## Slide 3: Recall: Caching Concept
Cache: a repository for copies that can be accessed more quickly than the original
  Make frequent case fast and infrequent case less dominant
Caching underlies many techniques used today to make computers fast
  Can cache: memory locations, address translations, pages, file blocks, file names, network routes, etc…
Notes: Ok, so as I said, this lecture is really about accelerating accesses. We will try to optimize anything and everything we can to achieve that.
Let’s start with recalling some of the concepts Anthony talked about in the last lecture.
Actually, the concept of caching might go back to your 61C or even 61A, where it was first introduced to you.
In simple words, Cache is a repository for copies that can be accessed more quickly than the original.
And I like this idea here in this picture, we have a desk where we place documents, pages that we need to access more frequently on the desk, and infrequently we need to get up, go to the cabinet to fetch a new file or something.
Well, that is the key thing about caching: make frequent cases fast, and infrequent cases less dominant/less expensive.
In our world, we see cache behind many techniques to make systems fast. We can cache memory locations, address translations, pages, file names, blocks, network routes, for instance.

## Slide 4: Big Really Basic Concept #1
“Large” memories are “slow”, “Fast” memories are “small”
How do we create the illusion of a ”large fast” memory? – on average.

## Slide 5: Recall: In Machine Structures (eg. 61C) …
Caching is the key to memory system performance
Average Access time=(Hit Rate x HitTime) + (Miss Rate x MissTime)
HitRate + MissRate = 1
HitRate = 90% => Avg. Access Time=(0.9 x 10) + (0.1 x 100)=19ns
HitRate = 99% => Avg. Access Time=(0.99 x 10) + (0.01 x 100)=10.9 ns
Processor
Main
Memory
(DRAM)
100ns
10ns
Second
Level
Cache
(SRAM)
Processor
Main
Memory
(DRAM)
100ns
Access time = 100ns
Notes: So, the role of a cache is to reduce the average memory access time. So, here we have a processor; if it directly needs to go to memory to access something, it takes 100ns.
Remember, processors are superfast, they compute in small cycles, and hence 100ns is a really long time for them.
If we add a second level cache, we can instead access the same data in 10ns, i.e.,10 times faster than directly going to memory.
To quantify the gain due to a cache, we can compute the average access time: and its simply the hit-rate (times we find it in the cache). …
So, we get an illusion that we can access the main memory at such a fast speed, due to caching.

## Slide 6: Big Really Really Basic Concept #2
How many distinct values can be expressed in K bits?
How many addresses can be expressed in K bits?
How large a “namespace” can be addressed by N bits?
K bits
Address Space
“datum”
address
2K addresses
K

## Slide 7: Big Basic Concept #3
A program operates in a Virtual Address Space distinct from the Physical Address Space of the hardware in the machine.
264
~ 1.8×1019
64 bits
Virtual Address Space
Virtual address
Physical Address Space
238
~ 256×109
38 bits
Physical address
map
?

## Slide 8: Recall: How is the Translation Accomplished?
What, exactly happens inside MMU?
Hardware Tree Traversal
  For each virtual address traverses the page table in hardware
  Generates a “Page Fault” if it encounters invalid PTE
    Fault handler will decide what to do
    More on this next lecture
  Pros: Relatively fast (but still many memory accesses!)
  Cons: Inflexible, Complex hardware
Another possibility: Software
  Each traversal done in software
  Pros: Very flexible
  Cons: Every translation must invoke Fault!
In fact, need way to cache translations for either case!
CPU
MMU
Virtual
Addresses
Physical
Addresses

## Slide 9: How to map VA => PA ?
What should be the unit of mapping? How?
How many?
64 bits
Virtual address
38 bits
Physical address
map
?
Virtual addr 0
Physical addr 0
Virtual addr 1
Physical addr 1
Virtual addr m-1
Physical addr m-1

## Slide 10: Caching Applied to Address Translation
Question is one of page locality: does it exist?
  Instruction accesses spend a lot of time on the same page (since accesses sequential)
  Stack accesses have definite locality of reference
  Data accesses have less page locality, but still some…
Data Read or Write
(untranslated)
CPU
Physical
Memory
TLB
Translate
(MMU)
No
Virtual
Address
Physical
Address
Yes
Cached?
Save
Result
Notes: Remember how we used caching for address translation?

## Slide 11: What Actually Happens on a TLB Miss? (1/2)
Hardware traversed page tables:
  On TLB miss, hardware in MMU looks at current page table to fill TLB (may walk multiple levels)
    If PTE valid, hardware fills TLB and processor never knows
    If PTE marked as invalid, causes Page Fault, after which kernel decides what to do afterwards
Software traversed Page tables (like MIPS)
  On TLB miss, processor receives TLB fault
  Kernel traverses page table to find PTE
    If PTE valid, fills TLB and returns from fault
    If PTE marked as invalid, internally calls Page Fault handler

## Slide 12: What Actually Happens on a TLB Miss? (2/2)
Most chip sets provide hardware traversal
  Modern operating systems tend to have more TLB faults since they use translation for many things
  Examples:
    shared segments
    user-level portions of an operating system

## Slide 13: What happens on a Context Switch?
Need to do something, since TLBs map virtual addresses to physical addresses
  Address Space just changed, so TLB entries no longer valid!
Options?
  Invalidate TLB: simple but might be expensive
    What if switching frequently between processes?
  Include ProcessID in TLB
    This is an architectural solution: needs hardware
What if translation tables change?
  For example, to move page from memory to disk or vice versa…
  Must invalidate TLB entry!
    Otherwise, might think that page is still in memory!

## Slide 14: Really really basic question #4
How many virtual-to-physical translations occur per instruction ?
How much time do we have to do them?
How many memory references occur per instruction?
What is the difference between an interrupt and a fault (or trap) ?
  Both care called Exceptions.
Which kind is a Page Fault?
A TLB miss?

## Slide 15: Recall: UserKernel (System Call)
Can’t let inmate (user) get out of padded cell on own
  Would defeat purpose of protection!
  So, how does the user program get back into kernel?
System call: Voluntary procedure call into kernel
  Hardware for controlled UserKernel transition
  Can any kernel routine be called?
    No! Only specific ones.
  System call ID encoded into system call instruction
    Index forces well-defined interface with kernel
But on a page-fault there is no “system call” instruction

## Slide 16: Transparent Exceptions: TLB/Page fault (1/2)
How to transparently restart faulting instructions?
  (Consider load or store that gets TLB or Page fault)
  Could we just skip faulting instruction?
    No: need to perform load or store after reconnecting physical page
Software
Load TLB
Faulting
Inst 1
Faulting
Inst 1
Faulting
Inst 2
Faulting
Inst 2
Fetch page/
Load TLB
User
OS
TLB Faults

## Slide 17: Transparent Exceptions: TLB/Page fault (2/2)
Hardware must help out by saving:
  Faulting instruction and partial state
    Need to know which instruction caused fault
    Is single PC sufficient to identify faulting position????
  Processor State: sufficient to restart user thread
    Save/restore registers, stack, etc
What if an instruction has side-effects?
Software
Load TLB
Faulting
Inst 1
Faulting
Inst 1
Faulting
Inst 2
Faulting
Inst 2
Fetch page/
Load TLB
User
OS
TLB Faults

## Slide 18: Consider weird things that can happen
What if an instruction has side effects?
  Options:
    Unwind side-effects (easy to restart)
    Finish off side-effects (messy!)
  Example 1: mov (sp)+,10
    What if page fault occurs when write to stack pointer?
    Did sp get incremented before or after the page fault?
  Example 2: strcpy (r1), (r2)
    Source and destination overlap: can’t unwind in principle!
    IBM S/370 and VAX solution: execute twice – once read-only
What about “RISC” processors?
  For instance delayed branches?
    Example: bne somewhere ld r1,(sp)
    Precise exception state consists of two PCs: PC and nPC (next PC)
  Delayed exceptions:
    Example: div r1, r2, r3 ld r1, (sp)
    What if takes many cycles to discover divide by zero, but load has already caused page fault?

## Slide 19: Precise Exceptions
Precise  state of the machine is preserved as if program executed up to the offending instruction
  All previous instructions completed
  Offending instruction and all following instructions act as if they have not even started
  Same system code will work on different implementations
  Difficult in the presence of pipelining, out-of-order execution, ...
  MIPS takes this position
Imprecise  system software has to figure out what is where and put it all back together
Performance goals often lead to forsaking precise interrupts
  system software developers, user, markets etc. usually wish they had not done this
Modern techniques for out-of-order execution and branch prediction help implement precise interrupts

## Slide 20: Recall: TLB Organization
Needs to be really fast
  Critical path of memory access
    In simplest view: before the cache
    Thus, this adds to access time (reducing cache speed)
  Seems to argue for Direct Mapped or Low Associativity
However, needs to have very few conflicts!
  With TLB, the Miss Time extremely high!
  This argues that cost of Conflict (Miss Time) is much higher than slightly increased cost of access (Hit Time)
Thrashing: continuous conflicts between accesses
  What if use low order bits of page as index into TLB?
    First page of code, data, stack may map to same entry
    Need 3-way associativity at least?
  What if use high order bits as index?
    TLB mostly unused for small programs
CPU
TLB
Cache
Memory

## Slide 21: Basic Concept #5
If we use K bits out of an N bit address, how many of the 2N “things” in the address space can re refer too?
Which ones?

## Slide 22: Reducing translation time further
As described, TLB lookup is in serial with cache lookup:
Machines with TLBs go one step further: they overlap TLB lookup with cache access.
  Works because offset available early
Virtual Address
TLB Lookup
V
Access
Rights
PA
V page no.
offset
10
P page no.
offset
10
Physical Address
CPU
TLB
Cache
Memory

## Slide 23: Overlapping TLB & Cache Access (1/2)
Main idea:
  Offset in virtual address exactly covers the “cache index” and “byte select”
  Thus can select the cached byte(s) in parallel to perform address translation
Offset
Virtual Page #
index
tag / page #
byte
virtual address
physical address

## Slide 24: Overlapping TLB & Cache Access
Here is how this might work with a 4K cache:
What if cache size is increased to 8KB?
  Overlap not complete
  Need to do something else. See CS152/252
Another option: Virtual Caches
  Tags in cache are virtual addresses
  Translation only happens on cache misses
TLB
4K Cache
10
2
00
4 bytes
index
1 K
page #
disp
20
assoc
lookup
32
Hit/
Miss
FN
Data
Hit/
Miss
=
FN

## Slide 25: Putting Everything Together: Address Translation
Physical Address:
Offset
Physical
Page #
Virtual Address:
Offset
Virtual
P2 index
Virtual
P1 index
PageTablePtr
Page Table
(1st level)
Page Table
(2nd level)
Physical
Memory:

## Slide 26: Putting Everything Together: TLB
Page Table
(2nd level)
PageTablePtr
Page Table
(1st level)
Offset
Physical
Page #
Virtual Address:
Offset
Virtual
P2 index
Virtual
P1 index
Physical
Memory:
Physical Address:
…
TLB:

## Slide 27: Putting Everything Together: Cache
Page Table
(2nd level)
PageTablePtr
Page Table
(1st level)
Virtual Address:
Offset
Virtual
P2 index
Virtual
P1 index
…
TLB:
Offset
Physical
Memory:
Physical Address:
Physical
Page #
…
tag:
block:
cache:
index
byte
tag

## Slide 28: Next Up: What happens when …
virtual address
MMU
PT
instruction
physical address
page#
frame#
offset
page fault
Operating System
exception
Page Fault Handler
load page from disk
update PT entry
Process
scheduler
retry
frame#
offset

## Slide 29: Break

## Slide 30: Where are all places that caching arises in OSes?
Direct use of caching techniques
  TLB (cache of PTEs)
  Paged virtual memory (memory as cache for disk)
  File systems (cache disk blocks in memory)
  DNS (cache hostname => IP address translations)
  Web proxies (cache recently accessed pages)
Which pages to keep in memory?
  All-important “Policy” aspect of virtual memory
  Will spend a bit more time on this in a moment

## Slide 31: Impact of caches on Operating Systems (1/2)
Indirect - dealing with cache effects (e.g., sync state across levels)
  Maintaining the correctness of various caches
  E.g., TLB consistency:
    With PT across context switches ?
    Across updates to the PT ?
Process scheduling
  Which and how many processes are active ? Priorities ?
  Large memory footprints versus small ones ?
  Shared pages mapped into VAS of multiple processes ?

## Slide 32: Impact of caches on Operating Systems (2/2)
Impact of thread scheduling on cache performance
  Rapid interleaving of threads (small quantum) may degrade cache performance
    Increase average memory access time (AMAT) !!!
Designing operating system data structures for cache performance

## Slide 33: Working Set Model
As a program executes it transitions through a sequence of “working sets” consisting of varying sized subsets of the address space
Time
Address

## Slide 34: Cache Behavior under WS model
Amortized by fraction of time the Working Set is active
Transitions from one WS to the next
Capacity, Conflict, Compulsory misses
Applicable to memory caches and pages. Others ?
Hit Rate
Cache Size
new working set fits
0
1

## Slide 35: Another model of Locality: Zipf
Likelihood of accessing item of rank r is α 1/ra
Although rare to access items below the top few, there are so many that it yields a “heavy tailed” distribution
Substantial value from even a tiny cache
Substantial misses from even a very large cache
Chart: P access(rank) = 1/rank
pop a=1 | 0.19278 | 0.096388 | 0.064259 | 0.048194 | 0.038555 | 0.032129 | 0.027539 | 0.024097 | 0.02142 | 0.019278 | 0.017525 | 0.016065 | 0.014829 | 0.01377 | 0.012852 | 0.012048 | 0.01134 | 0.01071 | 0.010146 | 0.0096388 | 0.0091798 | 0.0087625 | 0.0083815 | 0.0080323 | 0.007711 | 0.0074144 | 0.0071398 | 0.0068848 | 0.0066474 | 0.0064259 | 0.0062186 | 0.0060242 | 0.0058417 | 0.0056699 | 0.0055079 | 0.0053549 | 0.0052102 | 0.005073 | 0.004943 | 0.0048194 | 0.0047018 | 0.0045899 | 0.0044832 | 0.0043813 | 0.0042839 | 0.0041908 | 0.0041016 | 0.0040162 | 0.0039342 | 0.0038555
Hit Rate(cache) | 0.19278 | 0.28916 | 0.35342 | 0.40162 | 0.44017 | 0.4723 | 0.49984 | 0.52394 | 0.54536 | 0.56463 | 0.58216 | 0.59822 | 0.61305 | 0.62682 | 0.63967 | 0.65172 | 0.66306 | 0.67377 | 0.68392 | 0.69356 | 0.70274 | 0.7115 | 0.71988 | 0.72791 | 0.73562 | 0.74304 | 0.75018 | 0.75706 | 0.76371 | 0.77014 | 0.77635 | 0.78238 | 0.78822 | 0.79389 | 0.7994 | 0.80475 | 0.80996 | 0.81504 | 0.81998 | 0.8248 | 0.8295 | 0.83409 | 0.83857 | 0.84296 | 0.84724 | 0.85143 | 0.85553 | 0.85955 | 0.86348 | 0.86734

## Slide 36: Demand Paging
Modern programs require a lot of physical memory
  Memory per system growing faster than 25%-30%/year
But they don’t use all their memory all of the time
  90-10 rule: programs spend 90% of their time in 10% of their code
  Wasteful to require all of user’s code to be in memory
Solution: use main memory as cache for disk
On-Chip
Cache
Control
Datapath
Secondary
Storage
(Disk)
Processor
Main
Memory
(DRAM)
Second
Level
Cache
(SRAM)
Tertiary
Storage
(Tape)
Caching

## Slide 37: Illusion of Infinite Memory (1/2)
Page
Table
TLB
Disk is larger than physical memory 
  In-use virtual memory can be bigger than physical memory
  Combined memory of running processes much larger than physical memory
    More programs fit into memory, allowing more concurrency
Physical
Memory
512 MB
Disk
500GB
∞
Virtual
Memory
4 GB

## Slide 38: Illusion of Infinite Memory (2/2)
Page
Table
TLB
Principle: Transparent Level of Indirection (page table)
  Supports flexible placement of physical data
    Data could be on disk or somewhere across network
  Variable location of data transparent to user program
    Performance issue, not correctness issue
Physical
Memory
512 MB
Disk
500GB
∞
Virtual
Memory
4 GB

## Slide 39: Since Demand Paging is Caching, Must Ask…
What is block size?
  1 page
What is organization of this cache (i.e. direct-mapped, set-associative, fully-associative)?
  Fully associative: arbitrary virtual  physical mapping
How do we find a page in the cache when look for it?
  First check TLB, then page-table traversal
What is page replacement policy? (i.e. LRU, Random…)
  This requires more explanation… (kinda LRU)
What happens on a miss?
  Go to lower level to fill miss (i.e. disk)
What happens on a write? (write-through, write back)
  Definitely write-back – need dirty bit!

## Slide 40: Recall: What is in a Page Table Entry
What is in a Page Table Entry (or PTE)?
  Pointer to next-level page table or to actual page
  Permission bits: valid, read-only, read-write, write-only
Example: Intel x86 architecture PTE:
  Address same format previous slide (10, 10, 12-bit offset)
  Intermediate page tables called “Directories”
  P: Present (same as “valid” bit in other architectures)
  W: Writeable
  U: User accessible
  PWT: Page write transparent: external cache write-through
  PCD: Page cache disabled (page cannot be cached)
  A: Accessed: page has been accessed recently
  D: Dirty (PTE only): page has been modified recently
  L: L=14MB page (directory only). Bottom 22 bits of virtual address serve as offset
Page Frame Number
(Physical Page Number)
Free
(OS)
0
L
D
A
PCD
PWT
U
W
P
0
1
2
3
4
5
6
7
8
11-9
31-12

## Slide 41: Demand Paging Mechanisms
Cache
PTE helps us implement demand paging
  Valid  Page in memory, PTE points at physical page
  Not Valid  Page not in memory; use info in PTE to find it on disk when necessary
Suppose user references page with invalid PTE?
  Memory Management Unit (MMU) traps to OS
    Resulting trap is a “Page Fault”
  What does OS do on a Page Fault?:
    Choose an old page to replace
    If old page modified (“D=1”), write contents back to disk
    Change its PTE and any cached TLB to be invalid
    Load new page into memory from disk
    Update page table entry, invalidate TLB for new entry
    Continue thread from original faulting location
  TLB for new page will be loaded when thread continued!
  While pulling pages off disk for one process, OS runs another process from ready queue
    Suspended process sits on wait queue

## Slide 42: Summary: Steps in Handling a Page Fault

## Slide 43: Summary
A cache of translations called a “Translation Lookaside Buffer” (TLB)
  Relatively small number of PTEs and optional process IDs (< 512)
  Fully Associative (Since conflict misses expensive)
  On TLB miss, page table must be traversed and if located PTE is invalid, cause Page Fault
  On change in page table, TLB entries must be invalidated
  TLB is logically in front of cache (need to overlap with cache access)
Precise Exception specifies a single instruction for which:
  All previous instructions have completed (committed state)
  No following instructions nor actual instruction have started
Can manage caches in hardware or software or both
  Goal is highest hit rate, even if it means more complex cache management
Notes: No fancy replacement policy is needed for the direct mapped cache.
As a matter of fact, that is what cause direct mapped trouble to begin with: only one place to go in the cache--causes conflict misses.
No fancy replacement policy is needed for the direct mapped cache.
As a matter of fact, that is what cause direct mapped trouble to begin with: only one place to go in the cache--causes conflict misses.
Besides working at Sun, I also teach people how to fly whenever I have time.
Statistic have shown that if a pilot crashed after an engine failure, he or she is more likely to get killed in a multi-engine light airplane than a single engine airplane.
The joke among us flight instructors is that: sure, when the engine quit in a single engine stops, you have one option: sooner or later, you land. Probably sooner.
But in a multi-engine airplane with one engine stops, you have a lot of options. It is the need to make a decision that kills those people.