## Slide 1: CS162 Operating Systems and Systems Programming Lecture 9 Synchronization (Con’t) Monitors and Readers/Writers example
February 19th, 2019
Prof. John Kubiatowicz
http://cs162.eecs.Berkeley.edu

## Slide 2: Recall: Implement Locks by Disabling Interrupts
Key idea: maintain a lock variable and impose mutual exclusion only during operations on that variable
Really only works in kernel – why?
int mylock = FREE;
Acquire(&mylock) – wait until lock is free, then grab
Release(&mylock) – Unlock, waking up anyone waiting
Acquire(int *lock) { disable interrupts; if (*lock == BUSY) { put thread on wait queue; Go to sleep() && Enab ints!
// Ints disabled on wakeup } else { *lock = BUSY; } enable interrupts; }
Release(int *lock) { disable interrupts; if (anyone on wait queue) { take thread off wait queue Place on ready queue; } else { *lock = FREE; } enable interrupts; }

## Slide 3: Recall: Two Implementations for T&S Lock
Brief busy-wait only to protect lock implementation
  Note: sleep has to be sure to reset the guard variable
Must understand value of guard on exiting sleep
  Post – sleep guard value must be specified!
  Only Acquire_Ver2() parallel to “disable interrupts” case!
Acquire_Ver2() {
// Short busy-wait time while (test&set(guard)); if (mylock == BUSY) {
put thread on wait queue;
go to sleep() & guard = 0;
// guard == 1 on wakeup! } else { mylock = BUSY; }
guard = 0; // Success or fail! }
int guard = 0;
int mylock = FREE;
Acquire_Ver1() {
// Short busy-wait time while (test&set(guard)); if (mylock == BUSY) {
put thread on wait queue;
go to sleep() & guard = 0;
// guard == 0 on wakeup! } else { mylock = BUSY; guard = 0; // Only success } }

## Slide 4: In-Kernel Lock: Simulation
INIT
int value = 0;
Acquire() { disable interrupts; if (value == 1) {
put thread on wait-queue;
go to sleep() //?? } else { value = 1; }
enable interrupts; }
Release() { disable interrupts; if anyone on wait queue { take thread off wait-queue Place on ready queue; } else { value = 0; } enable interrupts; }
lock.Acquire();
…
critical section;
…
lock.Release();
lock.Acquire();
…
critical section;
…
lock.Release();
Value: 0
waiters
owner
Thread A
Thread B
Running
READY
Ready

## Slide 5: In-Kernel Lock: Simulation
INIT
int value = 0;
Acquire() { disable interrupts; if (value == 1) {
put thread on wait-queue;
go to sleep() //?? } else { value = 1; }
enable interrupts; }
Release() { disable interrupts; if anyone on wait queue { take thread off wait-queue Place on ready queue; } else { value = 0; } enable interrupts; }
lock.Acquire();
…
critical section;
…
lock.Release();
lock.Acquire();
…
critical section;
…
lock.Release();
Thread A
Thread B
READY
Running
Value: 1
waiters
owner
Ready

## Slide 6: In-Kernel Lock: Simulation
INIT
int value = 0;
Acquire() { disable interrupts; if (value == 1) {
put thread on wait-queue;
go to sleep() //?? } else { value = 1; }
enable interrupts; }
Release() { disable interrupts; if anyone on wait queue { take thread off wait-queue Place on ready queue; } else { value = 0; } enable interrupts; }
lock.Acquire();
…
critical section;
…
lock.Release();
lock.Acquire();
…
critical section;
…
lock.Release();
Thread A
Thread B
READY
Running
Running
Value: 1
waiters
owner
Ready
Ready

## Slide 7: In-Kernel Lock: Simulation
INIT
int value = 0;
Acquire() { disable interrupts; if (value == 1) {
put thread on wait-queue;
go to sleep() //?? } else { value = 1; }
enable interrupts; }
lock.Acquire();
…
critical section;
…
lock.Release();
Release() { disable interrupts; if anyone on wait queue { take thread off wait-queue Place on ready queue; } else { value = 0; } enable interrupts; }
lock.Acquire();
…
critical section;
…
lock.Release();
Thread A
Thread B
READY
Running
Running
Value: 1
waiters
owner
Waiting
Ready

## Slide 8: In-Kernel Lock: Simulation
INIT
int value = 0;
Acquire() { disable interrupts; if (value == 1) {
put thread on wait-queue;
go to sleep() //?? } else { value = 1; }
enable interrupts; }
lock.Acquire();
…
critical section;
…
lock.Release();
Release() { disable interrupts; if anyone on wait queue { take thread off wait-queue Place on ready queue; } else { value = 0; } enable interrupts; }
lock.Acquire();
…
critical section;
…
lock.Release();
Thread A
Thread B
READY
Running
Value: 1
waiters
owner
Waiting
Ready

## Slide 9: In-Kernel Lock: Simulation
INIT
int value = 0;
Acquire() { disable interrupts; if (value == 1) {
put thread on wait-queue;
go to sleep() //?? } else { value = 1; }
enable interrupts; }
Running
Release() { disable interrupts; if anyone on wait queue { take thread off wait-queue Place on ready queue; } else { value = 0; } enable interrupts; }
lock.Acquire();
…
critical section;
…
lock.Release();
lock.Acquire();
…
critical section;
…
lock.Release();
Thread A
Thread B
READY
Running
Value: 1
waiters
owner
Ready
Ready

## Slide 10: Review: Semaphores
Definition: a Semaphore has a non-negative integer value and supports the following two operations:
  P(): an atomic operation that waits for semaphore to become positive, then decrements it by 1
    Think of this as the wait() operation
  V(): an atomic operation that increments the semaphore by 1, waking up a waiting P, if any
    This of this as the signal() operation
  Only time can set integer directly is at initialization time
Semaphore from railway analogy
  Here is a semaphore initialized to 2 for resource control:
Value=2
Value=1
Value=0
Value=1
Value=0
Value=2

## Slide 11: Review: Full Solution to Bounded Buffer
Semaphore fullSlots = 0; // Initially, no coke
Semaphore emptySlots = bufSize; // Initially, num empty slots
Semaphore mutex = 1; // No one using machine
Producer(item) { emptySlots.P(); // Wait until space mutex.P(); // Wait until machine free Enqueue(item); mutex.V(); fullSlots.V(); // Tell consumers there is // more coke }
Consumer() { fullSlots.P(); // Check if there’s a coke mutex.P(); // Wait until machine free item = Dequeue(); mutex.V(); emptySlots.V(); // tell producer need more return item; }

## Slide 12: Review: Discussion about Solution
Why asymmetry?
  Producer does: emptyBuffer.P(), fullBuffer.V()
  Consumer does: fullBuffer.P(), emptyBuffer.V()
Is order of P’s important?
  Yes! Can cause deadlock
Is order of V’s important?
  No, except that it might affect scheduling efficiency
What if we have 2 producers or 2 consumers?
  Still Works fine…

## Slide 13: Motivation for Monitors and Condition Variables
Semaphores are a huge step up; just think of trying to do the bounded buffer with only loads and stores
  Problem is that semaphores are dual purpose:
    They are used for both mutex and scheduling constraints
    Example: the fact that flipping of P’s in bounded buffer gives deadlock is not immediately obvious. How do you prove correctness to someone?
Cleaner idea: Use locks for mutual exclusion and condition variables for scheduling constraints
Definition: Monitor: a lock and zero or more condition variables for managing concurrent access to shared data
  Some languages like Java provide this natively
  Most others use actual locks and condition variables

## Slide 14: Monitor with Condition Variables
Lock: the lock provides mutual exclusion to shared data
  Always acquire before accessing shared data structure
  Always release after finishing with shared data
  Lock initially free
Condition Variable: a queue of threads waiting for something inside a critical section
  Key idea: make it possible to go to sleep inside critical section by atomically releasing lock at time we go to sleep
  Contrast to semaphores: Can’t wait inside critical section

## Slide 15: Simple Monitor Example (version 1)
Here is an (infinite) synchronized queue
Lock lock; Queue queue;
AddToQueue(item) { lock.Acquire(); // Lock shared data queue.enqueue(item); // Add item lock.Release(); // Release Lock }
RemoveFromQueue() { lock.Acquire(); // Lock shared data item = queue.dequeue();// Get next item or null lock.Release(); // Release Lock return(item); // Might return null }
Not very interesting use of “Monitor”
  It only uses a lock with no condition variables
  Cannot put consumer to sleep if no work!

## Slide 16: Condition Variables
How do we change the RemoveFromQueue() routine to wait until something is on the queue?
  Could do this by keeping a count of the number of things on the queue (with semaphores), but error prone
Condition Variable: a queue of threads waiting for something inside a critical section
  Key idea: allow sleeping inside critical section by atomically releasing lock at time we go to sleep
  Contrast to semaphores: Can’t wait inside critical section
Operations:
  Wait(&lock): Atomically release lock and go to sleep. Re-acquire lock later, before returning.
  Signal(): Wake up one waiter, if any
  Broadcast(): Wake up all waiters
Rule: Must hold lock when doing condition variable ops!
  In Birrell paper, he says can perform signal() outside of lock – IGNORE HIM (this is only an optimization)

## Slide 17: Complete Monitor Example (with cond. variable)
Here is an (infinite) synchronized queue
Lock lock; Condition dataready; Queue queue;
AddToQueue(item) { lock.Acquire(); // Get Lock queue.enqueue(item); // Add item dataready.signal(); // Signal any waiters lock.Release(); // Release Lock }
RemoveFromQueue() { lock.Acquire(); // Get Lock while (queue.isEmpty()) { dataready.wait(&lock); // If nothing, sleep } item = queue.dequeue(); // Get next item lock.Release(); // Release Lock return(item); }

## Slide 18: Administrivia
Project 1 Design Document
  Due tomorrow (Wednesday, 2/20) @ 11:59PM
Midterm on Thursday 2/28 8pm-10pm
  Room assignments TBD
Closed book, no calculators, one double-side letter-sized page of handwritten notes
  Covers Lectures 1-11 (up through Deadlock), readings, homework 1, and project 1

## Slide 19: Mesa vs. Hoare monitors
Need to be careful about precise definition of signal and wait. Consider a piece of our dequeue code:
while (queue.isEmpty()) { dataready.wait(&lock); // If nothing, sleep } item = queue.dequeue(); // Get next item
  Why didn’t we do this?
if (queue.isEmpty()) { dataready.wait(&lock); // If nothing, sleep } item = queue.dequeue(); // Get next item
Answer: depends on the type of scheduling
  Hoare-style: Named after British logician Tony Hoare
  Mesa-style: Named after Xerox-Park Mesa Operating System

## Slide 20: Hoare monitors
Signaler gives up lock, CPU to waiter; waiter runs immediately
Waiter gives up lock, processor back to signaler when it exits critical section or if it waits again
Most textbooks
lock.Acquire()
…
if (queue.isEmpty()) { dataready.wait(&lock); } …
lock.Release();
…
lock.Acquire()
…
dataready.signal();
…
lock.Release();
Lock, CPU
Lock, CPU

## Slide 21: Mesa monitors
Signaler keeps lock and processor
Waiter placed on ready queue with no special priority
Practically, need to check condition again after wait
Most real operating systems
lock.Acquire()
…
while (queue.isEmpty()) { dataready.wait(&lock); } …
lock.Release();
…
lock.Acquire()
…
dataready.signal();
…
lock.Release();
schedule waiting thread
Put waiting thread on ready queue

## Slide 22: Mesa Monitor: Why “while()”?
Why do we use “while()” instead of “if() with Mesa monitors?
  Example illustrating what happens if we use “if()”, e.g.,
if (queue.isEmpty()) { dataready.wait(&lock); // If nothing, sleep }
We’ll use the synchronized (infinite) queue example
AddToQueue(item) {
lock.Acquire(); queue.enqueue(item); dataready.signal(); lock.Release();
}
RemoveFromQueue() { lock.Acquire(); if (queue.isEmpty()) { dataready.wait(&lock); } item = queue.dequeue(); lock.Release(); return(item);
}
Replace “while” with “if”

## Slide 23: Mesa Monitor: Why “while()”?
RemoveFromQueue() { lock.Acquire(); if (queue.isEmpty()) {
dataready.wait(&lock);
} item = queue.dequeue(); lock.Release();
return(item);
}
T1 (Running)
queue
lock: FREE
dataready
queue
Monitor
NULL
App. Shared State
CPU State
Running: T1
Ready
queue  NULL
…

## Slide 24: Mesa Monitor: Why “while()”?
RemoveFromQueue() { lock.Acquire(); if (queue.isEmpty()) {
dataready.wait(&lock);
} item = queue.dequeue(); lock.Release();
return(item);
}
T1 (Running)
lock: BUSY (T1)
dataready
queue
NULL
queue
Monitor
App. Shared State
CPU State
Running: T1
Ready
queue  NULL
…

## Slide 25: Mesa Monitor: Why “while()”?
RemoveFromQueue() { lock.Acquire(); if (queue.isEmpty()) {
dataready.wait(&lock);
} item = queue.dequeue(); lock.Release();
return(item);
}
T1 (Waiting)
lock: FREE
dataready
queue
T1
queue
Monitor
App. Shared State
CPU State
Running:
Ready
queue  NULL
…
wait(&lock) puts thread on dataready queue and releases lock

## Slide 26: Mesa Monitor: Why “while()”?
RemoveFromQueue() { lock.Acquire(); if (queue.isEmpty()) {
dataready.wait(&lock);
} item = queue.dequeue(); lock.Release();
return(item);
}
T1 (Waiting)
lock: FREE
dataready
queue
T1
AddToQueue(item) { lock.Acquire();
queue.enqueue(item); dataready.signal(); lock.Release(); }
T2 (Running)
queue
Monitor
App. Shared State
CPU State
Running: T2
Ready
queue  NULL
…

## Slide 27: Mesa Monitor: Why “while()”?
RemoveFromQueue() { lock.Acquire(); if (queue.isEmpty()) {
dataready.wait(&lock);
} item = queue.dequeue(); lock.Release();
return(item);
}
T1 (Waiting)
AddToQueue(item) { lock.Acquire();
queue.enqueue(item); dataready.signal(); lock.Release(); }
T2 (Running)
Monitor
App. Shared State
CPU State
Running: T2
Ready
queue  NULL
…
queue
add
item
lock: BUSY (T2)
dataready
queue
T1

## Slide 28: Mesa Monitor: Why “while()”?
RemoveFromQueue() { lock.Acquire(); if (queue.isEmpty()) {
dataready.wait(&lock);
} item = queue.dequeue(); lock.Release();
return(item);
}
T1 (Ready)
AddToQueue(item) { lock.Acquire();
queue.enqueue(item); dataready.signal(); lock.Release(); }
T2 (Running)
Monitor
App. Shared State
CPU State
Running: T2
Ready
queue  T1
…
queue
lock: BUSY (T2)
dataready
queue
NULL
signal() wakes up T1 and moves it on ready queue

## Slide 29: Mesa Monitor: Why “while()”?
RemoveFromQueue() { lock.Acquire(); if (queue.isEmpty()) {
dataready.wait(&lock);
} item = queue.dequeue(); lock.Release();
return(item);
}
T1 (Ready)
AddToQueue(item) { lock.Acquire();
queue.enqueue(item); dataready.signal(); lock.Release(); }
T2 (Running)
Monitor
App. Shared State
CPU State
Running: T2
Ready
queue  T1, T3
…
queue
lock: BUSY (T2)
dataready
queue
NULL
RemoveFromQueue() { lock.Acquire(); if (queue.isEmpty()) {
dataready.wait(&lock);
} item = queue.dequeue(); lock.Release();
return(item);
}
T3 (Ready)

## Slide 30: Mesa Monitor: Why “while()”?
RemoveFromQueue() { lock.Acquire(); if (queue.isEmpty()) {
dataready.wait(&lock);
} item = queue.dequeue(); lock.Release();
return(item);
}
T1 (Ready)
AddToQueue(item) { lock.Acquire();
queue.enqueue(item); dataready.signal(); lock.Release(); }
T2 (Terminate)
Monitor
App. Shared State
CPU State
Running:
Ready
queue  T1, T3
…
queue
lock: FREE
dataready
queue
NULL
RemoveFromQueue() { lock.Acquire(); if (queue.isEmpty()) {
dataready.wait(&lock);
} item = queue.dequeue(); lock.Release();
return(item);
}
T3 (Ready)

## Slide 31: Mesa Monitor: Why “while()”?
RemoveFromQueue() { lock.Acquire(); if (queue.isEmpty()) {
dataready.wait(&lock);
} item = queue.dequeue(); lock.Release();
return(item);
}
T1 (Ready)
Monitor
App. Shared State
CPU State
Running: T3
Ready
queue  T1
…
queue
lock: FREE
dataready
queue
NULL
RemoveFromQueue() { lock.Acquire(); if (queue.isEmpty()) {
dataready.wait(&lock);
} item = queue.dequeue(); lock.Release();
return(item);
}
T3 (Running)
T3 scheduled first!

## Slide 32: Mesa Monitor: Why “while()”?
RemoveFromQueue() { lock.Acquire(); if (queue.isEmpty()) {
dataready.wait(&lock);
} item = queue.dequeue(); lock.Release();
return(item);
}
T1 (Ready)
Monitor
App. Shared State
CPU State
Running: T3
Ready
queue  T1
…
queue
lock: BUSY (T3)
dataready
queue
NULL
RemoveFromQueue() { lock.Acquire(); if (queue.isEmpty()) {
dataready.wait(&lock);
} item = queue.dequeue(); lock.Release();
return(item);
}
T3 (Running)

## Slide 33: Mesa Monitor: Why “while()”?
RemoveFromQueue() { lock.Acquire(); if (queue.isEmpty()) {
dataready.wait(&lock);
} item = queue.dequeue(); lock.Release();
return(item);
}
T1 (Ready)
Monitor
App. Shared State
CPU State
Running: T3
Ready
queue  T1
…
queue
lock: BUSY (T3)
dataready
queue
NULL
RemoveFromQueue() { lock.Acquire(); if (queue.isEmpty()) {
dataready.wait(&lock);
} item = queue.dequeue(); lock.Release();
return(item);
}
T3 (Running)
remove
item

## Slide 34: Mesa Monitor: Why “while()”?
RemoveFromQueue() { lock.Acquire(); if (queue.isEmpty()) {
dataready.wait(&lock);
} item = queue.dequeue(); lock.Release();
return(item);
}
T1 (Ready)
Monitor
App. Shared State
CPU State
Running:
Ready
queue  T1
…
queue
lock: FREE
dataready
queue
NULL
RemoveFromQueue() { lock.Acquire(); if (queue.isEmpty()) {
dataready.wait(&lock);
} item = queue.dequeue(); lock.Release();
return(item);
}
T3 (Finished)

## Slide 35: Mesa Monitor: Why “while()”?
RemoveFromQueue() { lock.Acquire(); if (queue.isEmpty()) {
dataready.wait(&lock);
} item = queue.dequeue(); lock.Release();
return(item);
}
T1 (Running)
Monitor
App. Shared State
CPU State
Running: T1
Ready
queue  NULL
…
queue
lock: BUSY (T1)
dataready
queue
NULL

## Slide 36: Mesa Monitor: Why “while()”?
RemoveFromQueue() { lock.Acquire(); if (queue.isEmpty()) {
dataready.wait(&lock);
} item = queue.dequeue(); lock.Release();
return(item);
}
T1 (Running)
Monitor
App. Shared State
CPU State
Running: T1
Ready
queue  NULL
…
queue
lock: BUSY (T1)
dataready
queue
NULL
ERROR: Nothing in the queue!

## Slide 37: Mesa Monitor: Why “while()”?
RemoveFromQueue() { lock.Acquire(); while (queue.isEmpty())
{
dataready.wait(&lock);
} item = queue.dequeue(); lock.Release();
return(item);
}
T1 (Running)
Monitor
App. Shared State
CPU State
Running: T1
Ready
queue  NULL
…
queue
lock: BUSY (T1)
dataready
queue
NULL
Replace “if” with “while”

## Slide 38: Mesa Monitor: Why “while()”?
RemoveFromQueue() { lock.Acquire(); while (queue.isEmpty())
{
dataready.wait(&lock);
} item = queue.dequeue(); lock.Release();
return(item);
}
T1 (Ready)
Monitor
App. Shared State
CPU State
Running: T1
Ready
queue  NULL
…
queue
lock: BUSY (T1)
dataready
queue
NULL
Check again:
Is queue empty?

## Slide 39: Mesa Monitor: Why “while()”?
RemoveFromQueue() { lock.Acquire(); while (queue.isEmpty())
{
dataready.wait(&lock);
} item = queue.dequeue(); lock.Release();
return(item);
}
T1 (Waiting)
Monitor
App. Shared State
CPU State
Running: T1
Ready
queue  NULL
…
queue
lock: FREE
dataready
queue
T1
Yup!
Back to Sleep

## Slide 40: Readers/Writers Problem
Motivation: Consider a shared database
  Two classes of users:
    Readers – never modify database
    Writers – read and modify database
  Is using a single lock on the whole database sufficient?
    Like to have many readers at the same time
    Only one writer at a time
R
R
R
W

## Slide 41: Basic Readers/Writers Solution
Correctness Constraints:
  Readers can access database when no writers
  Writers can access database when no readers or writers
  Only one thread manipulates state variables at a time
Basic structure of a solution:
  Reader() Wait until no writers Access data base Check out – wake up a waiting writer
  Writer() Wait until no active readers or writers Access database Check out – wake up waiting readers or writer
  State variables (Protected by a lock called “lock”):
    int AR: Number of active readers; initially = 0
    int WR: Number of waiting readers; initially = 0
    int AW: Number of active writers; initially = 0
    int WW: Number of waiting writers; initially = 0
    Condition okToRead = NIL
    Condition okToWrite = NIL

## Slide 42: Code for a Reader
Reader() { // First check self into system lock.Acquire();
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist okToRead.wait(&lock); // Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! lock.release();
// Perform actual read-only access AccessDatabase(ReadOnly);
// Now, check out of system lock.Acquire(); AR--; // No longer active if (AR == 0 && WW > 0) // No other active readers okToWrite.signal(); // Wake up one writer lock.Release(); }
Why Release the Lock here?

## Slide 43: Code for a Writer
Writer() { // First check self into system lock.Acquire();
while ((AW + AR) > 0) { // Is it safe to write? WW++; // No. Active users exist okToWrite.wait(&lock); // Sleep on cond var WW--; // No longer waiting }
AW++; // Now we are active! lock.release();
// Perform actual read/write access AccessDatabase(ReadWrite);
// Now, check out of system lock.Acquire(); AW--; // No longer active if (WW > 0){ // Give priority to writers okToWrite.signal(); // Wake up one writer } else if (WR > 0) { // Otherwise, wake reader okToRead.broadcast(); // Wake all readers } lock.Release(); }
Why Give priority to writers?
Why broadcast() here instead of signal()?

## Slide 44: Simulation of Readers/Writers Solution
Use an example to simulate the solution
Consider the following sequence of operators:
  R1, R2, W1, R3
Initially: AR = 0, WR = 0, AW = 0, WW = 0

## Slide 45: Simulation of Readers/Writers Solution
R1 comes along (no waiting threads)
AR = 0, WR = 0, AW = 0, WW = 0
Reader() { lock.Acquire();
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist okToRead.wait(&lock); // Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! lock.release();
AccessDBase(ReadOnly);
lock.Acquire(); AR--; if (AR == 0 && WW > 0) okToWrite.signal(); lock.Release(); }

## Slide 46: Simulation of Readers/Writers Solution
R1 comes along (no waiting threads)
AR = 0, WR = 0, AW = 0, WW = 0
Reader() { lock.Acquire();
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist okToRead.wait(&lock); // Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! lock.release();
AccessDBase(ReadOnly);
lock.Acquire(); AR--; if (AR == 0 && WW > 0) okToWrite.signal(); lock.Release(); }

## Slide 47: Simulation of Readers/Writers Solution
R1 comes along (no waiting threads)
AR = 1, WR = 0, AW = 0, WW = 0
Reader() { lock.Acquire();
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist okToRead.wait(&lock); // Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! lock.release();
AccessDBase(ReadOnly);
lock.Acquire(); AR--; if (AR == 0 && WW > 0) okToWrite.signal(); lock.Release(); }

## Slide 48: Simulation of Readers/Writers Solution
R1 comes along (no waiting threads)
AR = 1, WR = 0, AW = 0, WW = 0
Reader() { lock.Acquire();
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist okToRead.wait(&lock); // Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! lock.release();
AccessDBase(ReadOnly);
lock.Acquire(); AR--; if (AR == 0 && WW > 0) okToWrite.signal(); lock.Release(); }
Why release the
lock here???

## Slide 49: Simulation of Readers/Writers Solution
R1 accessing dbase (no other threads)
AR = 1, WR = 0, AW = 0, WW = 0
Reader() { lock.Acquire();
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist okToRead.wait(&lock); // Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! lock.release();
AccessDBase(ReadOnly);
lock.Acquire(); AR--; if (AR == 0 && WW > 0) okToWrite.signal(); lock.Release(); }

## Slide 50: Simulation of Readers/Writers Solution
R2 comes along (R1 accessing dbase)
AR = 1, WR = 0, AW = 0, WW = 0
Reader() { lock.Acquire();
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist okToRead.wait(&lock); // Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! lock.release();
AccessDBase(ReadOnly);
lock.Acquire(); AR--; if (AR == 0 && WW > 0) okToWrite.signal(); lock.Release(); }

## Slide 51: Simulation of Readers/Writers Solution
R2 comes along (R1 accessing dbase)
AR = 1, WR = 0, AW = 0, WW = 0
Reader() { lock.Acquire();
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist okToRead.wait(&lock); // Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! lock.release();
AccessDBase(ReadOnly);
lock.Acquire(); AR--; if (AR == 0 && WW > 0) okToWrite.signal(); lock.Release(); }

## Slide 52: Simulation of Readers/Writers Solution
R2 comes along (R1 accessing dbase)
AR = 2, WR = 0, AW = 0, WW = 0
Reader() { lock.Acquire();
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist okToRead.wait(&lock); // Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! lock.release();
AccessDBase(ReadOnly);
lock.Acquire(); AR--; if (AR == 0 && WW > 0) okToWrite.signal(); lock.Release(); }

## Slide 53: Simulation of Readers/Writers Solution
R2 comes along (R1 accessing dbase)
AR = 2, WR = 0, AW = 0, WW = 0
Reader() { lock.Acquire();
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist okToRead.wait(&lock); // Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! lock.release();
AccessDBase(ReadOnly);
lock.Acquire(); AR--; if (AR == 0 && WW > 0) okToWrite.signal(); lock.Release(); }

## Slide 54: Simulation of Readers/Writers Solution
R1 and R2 accessing dbase
AR = 2, WR = 0, AW = 0, WW = 0
Reader() { lock.Acquire();
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist okToRead.wait(&lock); // Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! lock.release();
AccessDBase(ReadOnly);
lock.Acquire(); AR--; if (AR == 0 && WW > 0) okToWrite.signal(); lock.Release(); }
Assume readers take a while to access database
  Situation: Locks released, only AR is non-zero

## Slide 55: Simulation of Readers/Writers Solution
Writer() { lock.Acquire();
while ((AW + AR) > 0) { // Is it safe to write? WW++; // No. Active users exist okToWrite.wait(&lock);// Sleep on cond var WW--; // No longer waiting }
AW++; lock.release();
AccessDBase(ReadWrite);
lock.Acquire(); AW--; if (WW > 0){ okToWrite.signal(); } else if (WR > 0) { okToRead.broadcast(); } lock.Release(); }
W1 comes along (R1 and R2 are still accessing dbase)
AR = 2, WR = 0, AW = 0, WW = 0

## Slide 56: Simulation of Readers/Writers Solution
Writer() { lock.Acquire();
while ((AW + AR) > 0) { // Is it safe to write? WW++; // No. Active users exist okToWrite.wait(&lock);// Sleep on cond var WW--; // No longer waiting }
AW++; lock.release();
AccessDBase(ReadWrite);
lock.Acquire(); AW--; if (WW > 0){ okToWrite.signal(); } else if (WR > 0) { okToRead.broadcast(); } lock.Release(); }
W1 comes along (R1 and R2 are still accessing dbase)
AR = 2, WR = 0, AW = 0, WW = 0

## Slide 57: Simulation of Readers/Writers Solution
Writer() { lock.Acquire();
while ((AW + AR) > 0) { // Is it safe to write? WW++; // No. Active users exist okToWrite.wait(&lock);// Sleep on cond var WW--; // No longer waiting }
AW++; lock.release();
AccessDBase(ReadWrite);
lock.Acquire(); AW--; if (WW > 0){ okToWrite.signal(); } else if (WR > 0) { okToRead.broadcast(); } lock.Release(); }
W1 comes along (R1 and R2 are still accessing dbase)
AR = 2, WR = 0, AW = 0, WW = 1
W1 cannot start because of readers

## Slide 58: Simulation of Readers/Writers Solution
R3 comes along (R1 and R2 accessing dbase, W1 waiting)
AR = 2, WR = 0, AW = 0, WW = 1
Reader() { lock.Acquire();
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist okToRead.wait(&lock); // Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! lock.release();
AccessDBase(ReadOnly);
lock.Acquire(); AR--; if (AR == 0 && WW > 0) okToWrite.signal(); lock.Release(); }

## Slide 59: Simulation of Readers/Writers Solution
R3 comes along (R1 and R2 accessing dbase, W1 waiting)
AR = 2, WR = 0, AW = 0, WW = 1
Reader() { lock.Acquire();
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist okToRead.wait(&lock); // Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! lock.release();
AccessDBase(ReadOnly);
lock.Acquire(); AR--; if (AR == 0 && WW > 0) okToWrite.signal(); lock.Release(); }

## Slide 60: Simulation of Readers/Writers Solution
R3 comes along (R1 and R2 accessing dbase, W1 waiting)
AR = 2, WR = 1, AW = 0, WW = 1
Reader() { lock.Acquire();
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist okToRead.wait(&lock); // Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! lock.release();
AccessDBase(ReadOnly);
lock.Acquire(); AR--; if (AR == 0 && WW > 0) okToWrite.signal(); lock.Release(); }

## Slide 61: Simulation of Readers/Writers Solution
R3 comes along (R1, R2 accessing dbase, W1 waiting)
AR = 2, WR = 1, AW = 0, WW = 1
Reader() { lock.Acquire();
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist okToRead.wait(&lock); // Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! lock.release();
AccessDBase(ReadOnly);
lock.Acquire(); AR--; if (AR == 0 && WW > 0) okToWrite.signal(); lock.Release(); }
R3 cannot start because of writers (both AW & WW)

## Slide 62: Simulation of Readers/Writers Solution
R1 and R2 accessing dbase, W1 and R3 waiting
AR = 2, WR = 1, AW = 0, WW = 1
Reader() { lock.Acquire();
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist okToRead.wait(&lock); // Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! lock.release();
AccessDBase(ReadOnly);
lock.Acquire(); AR--; if (AR == 0 && WW > 0) okToWrite.signal(); lock.Release(); }
Status:
R1 and R2 still reading
W1 and R3 waiting on okToWrite and okToRead, respectively

## Slide 63: Simulation of Readers/Writers Solution
R2 finishes (R1 accessing dbase, W1 and R3 waiting)
AR = 2, WR = 1, AW = 0, WW = 1
Reader() { lock.Acquire();
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist okToRead.wait(&lock); // Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! lock.release();
AccessDBase(ReadOnly);
lock.Acquire(); AR--; if (AR == 0 && WW > 0) okToWrite.signal(); lock.Release(); }

## Slide 64: Simulation of Readers/Writers Solution
R2 finishes (R1 accessing dbase, W1 and R3 waiting)
AR = 1, WR = 1, AW = 0, WW = 1
Reader() { lock.Acquire();
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist okToRead.wait(&lock); // Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! lock.release();
AccessDBase(ReadOnly);
lock.Acquire(); AR--; if (AR == 0 && WW > 0) okToWrite.signal(); lock.Release(); }

## Slide 65: Simulation of Readers/Writers Solution
R2 finishes (R1 accessing dbase, W1 and R3 waiting)
AR = 1, WR = 1, AW = 0, WW = 1
Reader() { lock.Acquire();
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist okToRead.wait(&lock); // Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! lock.release();
AccessDBase(ReadOnly);
lock.Acquire(); AR--; if (AR == 0 && WW > 0) okToWrite.signal(); lock.Release(); }

## Slide 66: Simulation of Readers/Writers Solution
R2 finishes (R1 accessing dbase, W1 and R3 waiting)
AR = 1, WR = 1, AW = 0, WW = 1
Reader() { lock.Acquire();
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist okToRead.wait(&lock); // Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! lock.release();
AccessDBase(ReadOnly);
lock.Acquire(); AR--; if (AR == 0 && WW > 0) okToWrite.signal(); lock.Release(); }

## Slide 67: Simulation of Readers/Writers Solution
R1 finishes (W1 and R3 waiting)
AR = 1, WR = 1, AW = 0, WW = 1
Reader() { lock.Acquire();
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist okToRead.wait(&lock); // Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! lock.release();
AccessDBase(ReadOnly);
lock.Acquire(); AR--; if (AR == 0 && WW > 0) okToWrite.signal(); lock.Release(); }

## Slide 68: Simulation of Readers/Writers Solution
R1 finishes (W1, R3 waiting)
AR = 0, WR = 1, AW = 0, WW = 1
Reader() { lock.Acquire();
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist okToRead.wait(&lock); // Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! lock.release();
AccessDBase(ReadOnly);
lock.Acquire(); AR--; if (AR == 0 && WW > 0) okToWrite.signal(); lock.Release(); }

## Slide 69: Simulation of Readers/Writers Solution
R1 finishes (W1, R3 waiting)
AR = 0, WR = 1, AW = 0, WW = 1
Reader() { lock.Acquire();
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist okToRead.wait(&lock); // Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! lock.release();
AccessDBase(ReadOnly);
lock.Acquire(); AR--; if (AR == 0 && WW > 0) okToWrite.signal(); lock.Release(); }

## Slide 70: Simulation of Readers/Writers Solution
R1 signals a writer (W1 and R3 waiting)
AR = 0, WR = 1, AW = 0, WW = 1
Reader() { lock.Acquire();
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist okToRead.wait(&lock); // Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! lock.release();
AccessDBase(ReadOnly);
lock.Acquire(); AR--; if (AR == 0 && WW > 0) okToWrite.signal(); lock.Release(); }
All readers done,
Signal writer W1

## Slide 71: Simulation of Readers/Writers Solution
Writer() { lock.Acquire();
while ((AW + AR) > 0) { // Is it safe to write? WW++; // No. Active users exist okToWrite.wait(&lock);// Sleep on cond var WW--; // No longer waiting }
AW++; lock.release();
AccessDBase(ReadWrite);
lock.Acquire(); AW--; if (WW > 0){ okToWrite.signal(); } else if (WR > 0) { okToRead.broadcast(); } lock.Release(); }
W1 gets signal (R3 still waiting)
AR = 0, WR = 1, AW = 0, WW = 1
Receive signal from R1

## Slide 72: Simulation of Readers/Writers Solution
Writer() { lock.Acquire();
while ((AW + AR) > 0) { // Is it safe to write? WW++; // No. Active users exist okToWrite.wait(&lock);// Sleep on cond var WW--; // No longer waiting }
AW++; lock.release();
AccessDBase(ReadWrite);
lock.Acquire(); AW--; if (WW > 0){ okToWrite.signal(); } else if (WR > 0) { okToRead.broadcast(); } lock.Release(); }
W1 gets signal (R3 still waiting)
AR = 0, WR = 1, AW = 0, WW = 0

## Slide 73: Simulation of Readers/Writers Solution
Writer() { lock.Acquire();
while ((AW + AR) > 0) { // Is it safe to write? WW++; // No. Active users exist okToWrite.wait(&lock);// Sleep on cond var WW--; // No longer waiting }
AW++; lock.release();
AccessDBase(ReadWrite);
lock.Acquire(); AW--; if (WW > 0){ okToWrite.signal(); } else if (WR > 0) { okToRead.broadcast(); } lock.Release(); }
W1 gets signal (R3 still waiting)
AR = 0, WR = 1, AW = 1, WW = 0

## Slide 74: Simulation of Readers/Writers Solution
Writer() { lock.Acquire();
while ((AW + AR) > 0) { // Is it safe to write? WW++; // No. Active users exist okToWrite.wait(&lock);// Sleep on cond var WW--; // No longer waiting }
AW++; lock.release();
AccessDBase(ReadWrite);
lock.Acquire(); AW--; if (WW > 0){ okToWrite.signal(); } else if (WR > 0) { okToRead.broadcast(); } lock.Release(); }
W1 accessing dbase (R3 still waiting)
AR = 0, WR = 1, AW = 1, WW = 0

## Slide 75: Simulation of Readers/Writers Solution
Writer() { lock.Acquire();
while ((AW + AR) > 0) { // Is it safe to write? WW++; // No. Active users exist okToWrite.wait(&lock);// Sleep on cond var WW--; // No longer waiting }
AW++; lock.release();
AccessDBase(ReadWrite);
lock.Acquire(); AW--; if (WW > 0){ okToWrite.signal(); } else if (WR > 0) { okToRead.broadcast(); } lock.Release(); }
W1 finishes (R3 still waiting)
AR = 0, WR = 1, AW = 1, WW = 0

## Slide 76: Simulation of Readers/Writers Solution
Writer() { lock.Acquire();
while ((AW + AR) > 0) { // Is it safe to write? WW++; // No. Active users exist okToWrite.wait(&lock);// Sleep on cond var WW--; // No longer waiting }
AW++; lock.release();
AccessDBase(ReadWrite);
lock.Acquire(); AW--; if (WW > 0){ okToWrite.signal(); } else if (WR > 0) { okToRead.broadcast(); } lock.Release(); }
W1 finishes (R3 still waiting)
AR = 0, WR = 1, AW = 0, WW = 0

## Slide 77: Simulation of Readers/Writers Solution
Writer() { lock.Acquire();
while ((AW + AR) > 0) { // Is it safe to write? WW++; // No. Active users exist okToWrite.wait(&lock);// Sleep on cond var WW--; // No longer waiting }
AW++; lock.release();
AccessDBase(ReadWrite);
lock.Acquire(); AW--; if (WW > 0){ okToWrite.signal(); } else if (WR > 0) { okToRead.broadcast(); } lock.Release(); }
W1 finishes (R3 still waiting)
AR = 0, WR = 1, AW = 0, WW = 0

## Slide 78: Simulation of Readers/Writers Solution
Writer() { lock.Acquire();
while ((AW + AR) > 0) { // Is it safe to write? WW++; // No. Active users exist okToWrite.wait(&lock);// Sleep on cond var WW--; // No longer waiting }
AW++; lock.release();
AccessDBase(ReadWrite);
lock.Acquire(); AW--; if (WW > 0){ okToWrite.signal(); } else if (WR > 0) { okToRead.broadcast(); } lock.Release(); }
W1 signaling readers (R3 still waiting)
AR = 0, WR = 1, AW = 0, WW = 0
No waiting writers,
Signal reader R3

## Slide 79: Simulation of Readers/Writers Solution
Reader() { lock.Acquire();
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist okToRead.wait(&lock); // Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! lock.release();
AccessDBase(ReadOnly);
lock.Acquire(); AR--; if (AR == 0 && WW > 0) okToWrite.signal(); lock.Release(); }
R3 gets signal (no waiting threads)
AR = 0, WR = 1, AW = 0, WW = 0
Receive signal from W1

## Slide 80: Simulation of Readers/Writers Solution
Reader() { lock.Acquire();
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist okToRead.wait(&lock); // Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! lock.release();
AccessDBase(ReadOnly);
lock.Acquire(); AR--; if (AR == 0 && WW > 0) okToWrite.signal(); lock.Release(); }
R3 gets signal (no waiting threads)
AR = 0, WR = 0, AW = 0, WW = 0

## Slide 81: Simulation of Readers/Writers Solution
R3 accessing dbase (no waiting threads)
AR = 1, WR = 0, AW = 0, WW = 0
Reader() { lock.Acquire();
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist okToRead.wait(&lock); // Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! lock.release();
AccessDBase(ReadOnly);
lock.Acquire(); AR--; if (AR == 0 && WW > 0) okToWrite.signal(); lock.Release(); }

## Slide 82: Simulation of Readers/Writers Solution
R3 finishes (no waiting threads)
AR = 1, WR = 0, AW = 0, WW = 0
Reader() { lock.Acquire();
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist okToRead.wait(&lock); // Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! lock.release();
AccessDBase(ReadOnly);
lock.Acquire(); AR--; if (AR == 0 && WW > 0) okToWrite.signal(); lock.Release(); }

## Slide 83: Simulation of Readers/Writers Solution
R3 finishes (no waiting threads)
AR = 0, WR = 0, AW = 0, WW = 0
Reader() { lock.Acquire();
while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist okToRead.wait(&lock); // Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active! lock.release();
AccessDbase(ReadOnly);
lock.Acquire(); AR--; if (AR == 0 && WW > 0) okToWrite.signal(); lock.Release(); }
All DONE!
DBase is Idle

## Slide 84: Questions
Can readers starve? Consider Reader() entry code:
  while ((AW + WW) > 0) { // Is it safe to read? WR++; // No. Writers exist okToRead.wait(&lock); // Sleep on cond var WR--; // No longer waiting }
AR++; // Now we are active!
What if we erase the condition check in Reader exit?
AR--; // No longer active if (AR == 0 && WW > 0) // No other active readers okToWrite.signal(); // Wake up one writer
Further, what if we turn the signal() into broadcast()
AR--; // No longer active okToWrite.broadcast(); // Wake up sleepers
Finally, what if we use only one condition variable (call it “okContinue”) instead of two separate ones?
  Both readers and writers sleep on this variable
  Must use broadcast() instead of signal()

## Slide 85: Use of Single CV: okContinue
Reader() { // check into system lock.Acquire();
while ((AW + WW) > 0) { WR++; okContinue.wait(&lock); WR--; }
AR++; lock.release();
// read-only access AccessDbase(ReadOnly);
// check out of system lock.Acquire(); AR--; if (AR == 0 && WW > 0) okContinue.signal(); lock.Release(); }
Writer() { // check into system lock.Acquire();
while ((AW + AR) > 0) { WW++; okContinue.wait(&lock); WW--; }
AW++; lock.release();
// read/write access AccessDbase(ReadWrite);
// check out of system lock.Acquire(); AW--; if (WW > 0){ okContinue.signal(); } else if (WR > 0) { okContinue.broadcast(); } lock.Release(); }
What if we turn okToWrite and okToRead into okContinue (i.e. use only one condition variable instead of two)?

## Slide 86: Use of Single CV: okContinue
Reader() { // check into system lock.Acquire();
while ((AW + WW) > 0) { WR++; okContinue.wait(&lock); WR--; }
AR++; lock.release();
// read-only access AccessDbase(ReadOnly);
// check out of system lock.Acquire(); AR--; if (AR == 0 && WW > 0) okContinue.signal(); lock.Release(); }
Writer() { // check into system lock.Acquire();
while ((AW + AR) > 0) { WW++; okContinue.wait(&lock); WW--; }
AW++; lock.release();
// read/write access AccessDbase(ReadWrite);
// check out of system lock.Acquire(); AW--; if (WW > 0){ okContinue.signal(); } else if (WR > 0) { okContinue.broadcast(); } lock.Release(); }
Consider this scenario:
R1 arrives
W1, R2 arrive while R1 still reading  W1 and R2 wait for R1 to finish
Assume R1’s signal is delivered to R2 (not W1)

## Slide 87: Use of Single CV: okContinue
Reader() { // check into system lock.Acquire();
while ((AW + WW) > 0) { WR++; okContinue.wait(&lock); WR--; }
AR++; lock.release();
// read-only access AccessDbase(ReadOnly);
// check out of system lock.Acquire(); AR--; if (AR == 0 && WW > 0) okContinue.broadcast(); lock.Release(); }
Writer() { // check into system lock.Acquire();
while ((AW + AR) > 0) { WW++; okContinue.wait(&lock); WW--; }
AW++; lock.release();
// read/write access AccessDbase(ReadWrite);
// check out of system lock.Acquire(); AW--; if (WW > 0 || WR > 0){ okContinue.broadcast(); } lock.Release(); }
Need to change to broadcast()!
Must broadcast() to sort things out!

## Slide 88: Can we construct Monitors from Semaphores?
Locking aspect is easy: Just use a mutex
Can we implement condition variables this way?
  Wait() { semaphore.P(); }
  Signal() { semaphore.V(); }
  Doesn’t work: Wait() may sleep with lock held
Does this work better?
  Wait(Lock lock) { lock.Release(); semaphore.P(); lock.Acquire(); } Signal() { semaphore.V(); }
  No: Condition vars have no history, semaphores have history:
    What if thread signals and no one is waiting? NO-OP
    What if thread later waits? Thread Waits
    What if thread V’s and noone is waiting? Increment
    What if thread later does P? Decrement and continue

## Slide 89: Construction of Monitors from Semaphores (con’t)
Problem with previous try:
  P and V are commutative – result is the same no matter what order they occur
  Condition variables are NOT commutative
Does this fix the problem?
  Wait(Lock lock) { lock.Release(); semaphore.P(); lock.Acquire(); } Signal() { if semaphore queue is not empty semaphore.V(); }
  Not legal to look at contents of semaphore queue
  There is a race condition – signaler can slip in after lock release and before waiter executes semaphore.P()
It is actually possible to do this correctly
  Complex solution for Hoare scheduling in book
  Can you come up with simpler Mesa-scheduled solution?

## Slide 90: Monitor Conclusion
Monitors represent the logic of the program
  Wait if necessary
  Signal when change something so any waiting threads can proceed
Basic structure of monitor-based program:
  lock while (need to wait) { condvar.wait(); } unlock do something so no need to wait lock
  condvar.signal();
  unlock
Check and/or update state variables
Wait if necessary
Check and/or update
state variables

## Slide 91: C-Language Support for Synchronization
C language: Pretty straightforward synchronization
  Just make sure you know all the code paths out of a critical section
  int Rtn() { lock.acquire(); … if (exception) { lock.release(); return errReturnCode; } … lock.release(); return OK; }
  Watch out for setjmp/longjmp!
    Can cause a non-local jump out of procedure
    In example, procedure E calls longjmp, poping stack back to procedure B
    If Procedure C had lock.acquire, problem!
Proc A
Proc B
Calls setjmp
Proc C
lock.acquire
Proc D
Proc E
Calls longjmp
Stack growth

## Slide 92: C++ Language Support for Synchronization
Languages with exceptions like C++
  Languages that support exceptions are problematic (easy to make a non-local exit without releasing lock)
  Consider:
  void Rtn() { lock.acquire(); … DoFoo(); … lock.release(); } void DoFoo() { … if (exception) throw errException; … }
  Notice that an exception in DoFoo() will exit without releasing the lock!

## Slide 93: C++ Language Support for Synchronization (con’t)
Must catch all exceptions in critical sections
  Catch exceptions, release lock, and re-throw exception: void Rtn() { lock.acquire(); try { … DoFoo(); … } catch (…) { // catch exception lock.release(); // release lock throw; // re-throw the exception } lock.release(); } void DoFoo() { … if (exception) throw errException; … }
  Even Better: auto_ptr<T> facility. See C++ Spec.
    Can deallocate/free lock regardless of exit method

## Slide 94: Java Language Support for Synchronization
Java has explicit support for threads and thread synchronization
Bank Account example: class Account { private int balance; // object constructor public Account (int initialBalance) { balance = initialBalance; } public synchronized int getBalance() { return balance; } public synchronized void deposit(int amount) { balance += amount; } }
  Every object has an associated lock which gets automatically acquired and released on entry and exit from a synchronized method.

## Slide 95: Java Language Support for Synchronization (con’t)
Java also has synchronized statements:
synchronized (object) { … }
  Since every Java object has an associated lock, this type of statement acquires and releases the object’s lock on entry and exit of the body
  Works properly even with exceptions:
  synchronized (object) { … DoFoo(); … } void DoFoo() { throw errException; }

## Slide 96: Java Language Support for Synchronization (con’t 2)
In addition to a lock, every object has a single condition variable associated with it
  How to wait inside a synchronization method of block:
    void wait(long timeout); // Wait for timeout
    void wait(long timeout, int nanoseconds); //variant
    void wait();
  How to signal in a synchronized method or block:
    void notify(); // wakes up oldest waiter
    void notifyAll(); // like broadcast, wakes everyone
  Condition variables can wait for a bounded length of time. This is useful for handling exception cases:
  t1 = time.now(); while (!ATMRequest()) { wait (CHECKPERIOD); t2 = time.new(); if (t2 – t1 > LONG_TIME) checkMachine(); }
  Not all Java VMs equivalent!
    Different scheduling policies, not necessarily preemptive!

## Slide 97: Summary
Semaphores: Like integers with restricted interface
  Two operations:
    P(): Wait if zero; decrement when becomes non-zero
    V(): Increment and wake a sleeping task (if exists)
    Can initialize value to any non-negative value
  Use separate semaphore for each constraint
Monitors: A lock plus one or more condition variables
  Always acquire lock before accessing shared data
  Use condition variables to wait inside critical section
    Three Operations: Wait(), Signal(), and Broadcast()
Monitors represent the logic of the program
  Wait if necessary
  Signal when change something so any waiting threads can proceed