## Slide 1: CS162 Operating Systems and Systems Programming Lecture 20 Device Drivers, Storage Devices, Performance
April 4th, 2023
Prof. John Kubiatowicz
http://cs162.eecs.Berkeley.edu

## Slide 2: Recall: How does the Processor Talk to the Device?
CPU interacts with a Controller
  Contains a set of registers that can be read and written
  May contain memory for request queues, etc.
Processor accesses registers in two ways:
  Port-Mapped I/O: in/out instructions
    Example from the Intel architecture: out 0x21,AL
  Memory-mapped I/O: load/store instructions
    Registers/memory appear in physical address space
    I/O accomplished with load and store instructions
Device
Controller
read
write
control
status
Addressable
Memory
and/or
Queues
Registers
(port 0x20)
Hardware
Controller
Memory Mapped
Region: 0x8f008020
Bus
Interface
Address +
Data
Interrupt Request
Processor Memory Bus
CPU
Regular
Memory
Interrupt
Controller
Bus
Adaptor
Bus
Adaptor
Other Devices
or Buses

## Slide 3: Recall: Example Memory-Mapped Display Controller
Memory-Mapped:
  Hardware maps control registers and display memory into physical address space
    Addresses set by HW jumpers or at boot time
  Simply writing to display memory (also called the “frame buffer”) changes image on screen
    Addr: 0x8000F000 — 0x8000FFFF
  Writing graphics description to cmd queue
    Say enter a set of triangles describing some scene
    Addr: 0x80010000 — 0x8001FFFF
  Writing to the command register may cause on-board graphics hardware to do something
    Say render the above scene
    Addr: 0x0007F004
Can protect with address translation
Display
Memory
0x8000F000
0x80010000
Physical
Address
Space
Status
0x0007F000
Command
0x0007F004
Graphics
Command
Queue
0x80020000

## Slide 4: Recall: Transferring Data To/From Controller
Programmed I/O:
  Each byte transferred via processor in/out or load/store
  Pro: Simple hardware, easy to program
  Con: Consumes processor cycles proportional to data size
Direct Memory Access:
  Give controller access to memory bus
  Ask it to transfer data blocks to/from memory directly
Sample interaction with DMA controller (from OSC book):
1
2
3

## Slide 5: Recall: Transferring Data To/From Controller
Programmed I/O:
  Each byte transferred via processor in/out or load/store
  Pro: Simple hardware, easy to program
  Con: Consumes processor cycles proportional to data size
Direct Memory Access:
  Give controller access to memory bus
  Ask it to transfer data blocks to/from memory directly
Sample interaction with DMA controller (from OSC book):
4
5
6

## Slide 6: Recall: I/O Device Notifying the OS
The OS needs to know when:
  The I/O device has completed an operation
  The I/O operation has encountered an error
I/O Interrupt:
  Device generates an interrupt whenever it needs service
  Pro: handles unpredictable events well
  Con: interrupts relatively high overhead
Polling:
  OS periodically checks a device-specific status register
    I/O device puts completion information in status register
  Pro: low overhead
  Con: may waste many cycles on polling if infrequent or unpredictable I/O operations
Actual devices combine both polling and interrupts
  For instance – High-bandwidth network adapter:
    Interrupt for first incoming packet
    Poll for following packets until hardware queues are empty
Notes: After the OS has issued a command to the I/O device either via a special I/O instruction or by writing to a location in the I/O address space, the OS needs to be notified when:
(a) The I/O device has completed the operation.
(b) Or when the I/O device has encountered an error.
This can be accomplished in two different ways: Polling and I/O interrupt.
+1 = 58 min. (Y:38)

## Slide 7: Kernel Device Structure
The System Call Interface
Process
Management
Memory Management
Filesystems
Device Control
Networking
Architecture
Dependent
Code
Memory Manager
Device Control
Network Subsystem
File System Types
Block Devices
IF drivers
Concurrency, multitasking
Virtual memory
Files and dirs: the VFS
TTYs and device access
Connectivity

## Slide 8: Recall: Device Drivers
Device Driver: Device-specific code in the kernel that interacts directly with the device hardware
  Supports a standard, internal interface
  Same kernel I/O system can interact easily with different device drivers
  Special device-specific configuration supported with the ioctl() system call
Device Drivers typically divided into two pieces:
  Top half: accessed in call path from system calls
    implements a set of standard, cross-device calls like open(), close(), read(), write(), ioctl(), strategy()
    This is the kernel’s interface to the device driver
    Top half will start I/O to device, may put thread to sleep until finished
  Bottom half: run as interrupt routine
    Gets input or transfers next block of output
    May wake sleeping threads if I/O now complete

## Slide 9: Recall: Life Cycle of An I/O Request
Device Driver
Top Half
Device Driver
Bottom Half
Device
Hardware
Kernel I/O
Subsystem
User
Program

## Slide 10: The Goal of the I/O Subsystem
Provide Uniform Interfaces, Despite Wide Range of Different Devices
  This code works on many different devices:
  FILE fd = fopen("/dev/something", "rw"); for (int i = 0; i < 10; i++) { fprintf(fd, "Count %d\n", i); } close(fd);
  Why? Because code that controls devices (“device driver”) implements standard interface
We will try to get a flavor for what is involved in actually controlling devices in rest of lecture
  Can only scratch surface!

## Slide 11: Want Standard Interfaces to Devices
Block Devices: e.g. disk drives, tape drives, DVD-ROM
  Access blocks of data
  Commands include open(), read(), write(), seek()
  Raw I/O or file-system access
  Memory-mapped file access possible
Character Devices: e.g. keyboards, mice, serial ports, some USB devices
  Single characters at a time
  Commands include get(), put()
  Libraries layered on top allow line editing
Network Devices: e.g. Ethernet, Wireless, Bluetooth
  Different enough from block/character to have own interface
  Unix and Windows include socket interface
    Separates network protocol from network operation
    Includes select() functionality
  Usage: pipes, FIFOs, streams, queues, mailboxes

## Slide 12: How Does User Deal with Timing?
Blocking Interface: “Wait”
  When request data (e.g. read() system call), put process to sleep until data is ready
  When write data (e.g. write() system call), put process to sleep until device is ready for data
Non-blocking Interface: “Don’t Wait”
  Returns quickly from read or write request with count of bytes successfully transferred
  Read may return nothing, write may write nothing
Asynchronous Interface: “Tell Me Later”
  When request data, take pointer to user’s buffer, return immediately; later kernel fills buffer and notifies user
  When send data, take pointer to user’s buffer, return immediately; later kernel takes data and notifies user

## Slide 13: Administrivia
Midterm 2 has been graded (before Spring break)
  Statistics: Min: 10.5, Max: 93.7, Mean: 52.38, Std Dev: 14.9
  Final regrade requests are due tomorrow
Project 2: Due tomorrow!
Homework 5: Released today!
Midterm 3: April 27th
Special Topics Lecture: May 2nd
  Topics requested by you…!
Midterm 2

## Slide 14: Storage Devices
Magnetic disks
  Storage that rarely becomes corrupted
  Large capacity at low cost
  Block level random access (except for SMR – later!)
  Slow performance for random access
  Better performance for sequential access
Flash memory
  Storage that rarely becomes corrupted
  Capacity at intermediate cost (5-20x disk)
  Block level random access
  Good performance for reads; worse for random writes
  Erasure requirement in large blocks
  Wear patterns issue

## Slide 15: Hard Disk Drives (HDDs)
IBM/Hitachi Microdrive
Western Digital Drive
http://www.storagereview.com/guide/
Read/Write Head
Side View
IBM Personal Computer/AT (1986)
  30 MB hard disk - $500
  30-40ms seek time
  0.7-1 MB/s (est.)

## Slide 16: The Amazing Magnetic Disk
cylinder
Unit of Transfer: Sector (512B or 4096B)
  Ring of sectors form a track
  Stack of tracks form a cylinder
  Heads position on cylinders

## Slide 17: The Amazing Magnetic Disk
Unit of Transfer: Sector (512B or 4096B)
  Ring of sectors form a track
  Stack of tracks form a cylinder
  Heads position on cylinders
Disk Tracks ~ 1µm (micron) wide
  Wavelength of light is ~ 0.5µm
  Resolution of human eye: 50µm
  100K tracks on a typical 2.5” disk
Separated by unused guard regions
  Reduces likelihood neighboring tracks are corrupted during writes (still a small non-zero chance)

## Slide 18: The Amazing Magnetic Disk
Track length varies across disk
  Outside: More sectors per track, higher bandwidth
  Disk is organized into regions of tracks with same # of sectors/track
  Only outer half of radius is used
    Most of the disk area in the outer regions of the disk
OS Unit of Transfer: Block
  Typically more than one Sector
  Example: 4KB, 16KB
Disks so big that some companies (like Google) reportedly only use part of disk for active data
  Rest is archival data

## Slide 19: Shingled Magnetic Recording (SMR)
Overlapping tracks yields greater density, capacity
Restrictions on writing, complex DSP for reading

## Slide 20: Magnetic Disk Performance
Cylinders: all the tracks under the head at a given point on all surfaces
Read/write data is a three-stage process:
  Seek time: position the head/arm over the proper cylinder
  Rotational latency: wait for desired sector to rotate under r/w head
  Transfer time: transfer a block of bits (sector) under r/w head
Sector
Track
Cylinder
Head
Platter
Software
Queue
(Device Driver)
Hardware
Controller
Media Time
(Seek+Rot+Xfer)
Request
Result
Disk Latency = Queueing Time + Controller time +
Seek Time + Rotation Time + Xfer Time

## Slide 21: Typical Numbers for Magnetic Disk
Parameter | Info/Range
Space/Density | Space: 18TB (Seagate), 9 platters, in 3½ inch form factor! Areal Density: ≥ 1 Terabit/square inch! (PMR, Helium, …)
Average Seek Time | Typically 4-6 milliseconds
Average Rotational Latency | Most laptop/desktop disks rotate at 3600-7200 RPM (16-8 ms/rotation). Server disks up to 15,000 RPM. Average latency is halfway around disk so 4-8 milliseconds
Controller Time | Depends on controller hardware
Transfer Time | Typically 50 to 270 MB/s. Depends on: Transfer size (usually a sector): 512B – 1KB per sector Rotation speed: 3600 RPM to 15000 RPM Recording density: bits per inch on a track Diameter: ranges from 1 in to 5.25 in
Cost | Used to drop by a factor of two every 1.5 years (or faster), now slowing down

## Slide 22: Disk Performance Example
Assumptions:
  Ignoring queuing and controller times for now
  Avg seek time of 5ms
  7200RPM  Time for rotation: 60000 (ms/min) / 7200(rev/min) = 8ms Avg time to find block = ½ × 8ms = 4ms
  Transfer rate of 50MByte/s, block size of 4Kbyte  4096 bytes/50×106 (bytes/s) = 81.92 × 10-6 sec  0.082 ms for 1 sector
Read block from random place on disk:
  Seek (5ms) + Rot. Delay (4ms) + Transfer (0.082ms) = 9.082ms
  Approx 9ms to fetch/put data: 4096 bytes/9.082×10-3 s  451KB/s
Read block from random place in same cylinder:
  Rot. Delay (4ms) + Transfer (0.082ms) = 4.082ms
  Approx 4ms to fetch/put data: 4096 bytes/4.082×10-3 s  1.03MB/s
Read next block on same track:
  Transfer (0.082ms): 4096 bytes/0.082×10-3 s  50MB/sec
Key to using disk effectively is to minimize seek and rotational delays

## Slide 23: Lots of Intelligence in the Controller
Sectors contain sophisticated error correcting codes
  Disk head magnet has a field wider than track
  Hide corruptions due to neighboring track writes
Sector sparing
  Remap bad sectors transparently to spare sectors on the same surface
Slip sparing
  Remap all sectors (when there is a bad sector) to preserve sequential behavior
Track skewing
  Sector numbers offset from one track to the next, to allow for disk head movement for sequential ops

## Slide 24: When is Disk Performance Highest?
When there are big sequential reads, or
When there is so much work to do that they can be piggy backed (reordering queues—one moment)
OK to be inefficient when things are mostly idle
Bursts are both a threat and an opportunity
<your idea for optimization goes here>
  Waste space for speed?
Other techniques:
  Reduce overhead through user level drivers
  Reduce the impact of I/O delays by doing other useful work in the meantime

## Slide 25: Disk Scheduling (1/3)
Disk can do only one request at a time; What order do you choose to do queued requests?
FIFO Order
  Fair among requesters, but order of arrival may be to random spots on the disk  Very long seeks
SSTF: Shortest seek time first
  Pick the request that’s closest on the disk
  Although called SSTF, today must include rotational delay in calculation, since rotation can be as long as seek
  Con: SSTF good at reducing seeks, but may lead to starvation
2,3
2,1
3,10
7,2
5,2
2,2
Head
User
Requests
1
4
2
Disk Head
3

## Slide 26: Disk Scheduling (2/3)
Disk can do only one request at a time; What order do you choose to do queued requests?
SCAN: Implements an Elevator Algorithm: take the closest request in the direction of travel
  No starvation, but retains flavor of SSTF
2,3
2,1
3,10
7,2
5,2
2,2
Head
User
Requests

## Slide 27: Disk Scheduling (3/3)
Disk can do only one request at a time; What order do you choose to do queued requests?
C-SCAN: Circular-Scan: only goes in one direction
  Skips any requests on the way back
  Fairer than SCAN, not biased towards pages in middle
2,3
2,1
3,10
7,2
5,2
2,2
Head
User
Requests

## Slide 28: Example of Current HDDs
Seagate Exos X18 (2020)
  18 TB hard disk
    9 platters, 18 heads
    Helium filled: reduce friction and power
  4.16 ms average seek time
  4096 byte physical sectors
  7200 RPMs
  Dual 6 Gbps SATA /12Gbps SAS interface
    270MB/s MAX transfer rate
    Cache size: 256MB
  Price: $ 562 (~ $0.03/GB)
IBM Personal Computer/AT (1986)
  30 MB hard disk
  30-40 ms seek time
  0.7-1 MB/s (est.)
  Price: $500 ($17K/GB)
600K x
10 x
300 x
567K x

## Slide 29: Solid State Disks (SSDs)
1995 – Replace rotating magnetic media with non-volatile memory (battery backed DRAM)
2009 – Use NAND Multi-Level Cell (2 or 3-bit/cell) flash memory
  Sector (4 KB page) addressable, but stores 4-64 “pages” per memory block
  Trapped electrons distinguish between 1 and 0
No moving parts (no rotate/seek motors)
  Eliminates seek and rotational delay (0.1-0.2ms access time)
  Very low power and lightweight
  Limited “write cycles”
Rapid advances in capacity and cost ever since!

## Slide 30: FLASH Memory
Like a normal transistor but:
  Has a floating gate that can hold charge
  To write: raise or lower wordline high enough to cause charges to tunnel
  To read: turn on wordline as if normal transistor
    presence of charge changes threshold and thus measured current
Two varieties:
  NAND: denser, must be read and written in blocks
  NOR: much less dense, fast to read and write
V-NAND: 3D stacking (Samsung claims 1TB possible in 1 chip)
Samsung 2015:
512GB, NAND Flash

## Slide 31: Flash Memory (Con’t)
Data read and written in page-sized chunks (e.g. 4K)
  Cannot be addressed at byte level
  Random access at block level for reads (no locality advantage)
  Writing of new blocks handled in order (kinda like a log)
Before writing, must be erased (256K block at a time)
  Requires free-list management
  CANNOT write over existing block (Copy-on-Write is normal case)

## Slide 32: SSD Architecture – Reads
  Read 4 KB Page: ~25 usec
  No seek or rotational latency
  Transfer time: transfer a 4KB page
    SATA: 300-600MB/s => ~4 x103 b / 400 x 106 bps => 10 us
  Latency = Queuing Time + Controller time + Xfer Time
  Highest Bandwidth: Sequential OR Random reads
Host
Buffer
Manager
(software
Queue)
Flash
Memory
Controller
DRAM
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
NAND
SATA

## Slide 33: SSD Architecture – Writes
Writing data is complex! (~200μs – 1.7ms)
  Can only write empty pages in a block
  Erasing a block takes ~1.5ms
  Controller maintains pool of empty blocks by coalescing used pages (read, erase, write), also reserves some % of capacity
Rule of thumb: writes 10x reads, erasure 10x writes
https://en.wikipedia.org/wiki/Solid-state_drive

## Slide 34: SSD Architecture – Writes
SSDs provide same interface as HDDs to OS – read and write chunk (4KB) at a time
But can only overwrite data 256KB at a time!
Why not just erase and rewrite new version of entire 256KB block?
  Erasure is very slow (milliseconds)
  Each block has a finite lifetime, can only be erased and rewritten about 10K times
  Heavily used blocks likely to wear out quickly

## Slide 35: Solution – Two Systems Principles
Layer of Indirection
  Maintain a Flash Translation Layer (FTL) in SSD
  Map virtual block numbers (which OS uses) to physical page numbers (which flash mem. controller uses)
  Can now freely relocate data w/o OS knowing
Copy on Write
  Don’t overwrite a page when OS updates its data
  Instead, write new version in a free page
  Update FTL mapping to point to new location

## Slide 36: Flash Translation Layer
No need to erase and rewrite entire 256KB block when making small modifications
SSD controller can assign mappings to spread workload across pages
  Wear Levelling
What to do with old versions of pages?
  Garbage Collection in background
  Erase blocks with old pages, add to free list

## Slide 37: Some “Current” (large) 3.5in SSDs
Seagate Exos SSD: 15.36TB (2017)
  Dual 12Gb/s interface
  Seq reads 860MB/s
  Seq writes 920MB/s
  Random Reads (IOPS): 102K
  Random Writes (IOPS): 15K
  Price (Amazon): $5495 ($0.36/GB)
Nimbus SSD: 100TB (2019)
  Dual port: 12Gb/s interface
  Seq reads/writes: 500MB/s
  Random Read Ops (IOPS): 100K
  Unlimited writes for 5 years!
  Price: ~ $40K? ($0.4/GB)
    However, 50TB drive costs $12500 ($0.25/GB)

## Slide 38: HDD vs. SSD Comparison
SSD prices drop faster than HDD

## Slide 39: Amusing calculation: Is a full Kindle heavier than an empty one?
Actually, “Yes”, but not by much
Flash works by trapping electrons:
  So, erased state lower energy than written state
Assuming that:
  Kindle has 4GB flash
  ½ of all bits in full Kindle are in high-energy state
  High-energy state about 10-15 joules higher
  Then: Full Kindle is 1 attogram (10-18gram) heavier (Using E = mc2)
Of course, this is less than most sensitive scale can measure (it can measure 10-9 grams)
Of course, this weight difference overwhelmed by battery discharge, weight from getting warm, ….
Source: John Kubiatowicz (New York Times, Oct 24, 2011)

## Slide 40: SSD Summary
Pros (vs. hard disk drives):
  Low latency, high throughput (eliminate seek/rotational delay)
  No moving parts:
    Very light weight, low power, silent, very shock insensitive
  Read at memory speeds (limited by controller and I/O bus)
Cons
  Small storage (0.1-0.5x disk), expensive (3-20x disk)
    Hybrid alternative: combine small SSD with large HDD

## Slide 41: SSD Summary
Pros (vs. hard disk drives):
  Low latency, high throughput (eliminate seek/rotational delay)
  No moving parts:
    Very light weight, low power, silent, very shock insensitive
  Read at memory speeds (limited by controller and I/O bus)
Cons
  Small storage (0.1-0.5x disk), expensive (3-20x disk)
    Hybrid alternative: combine small SSD with large HDD
  Asymmetric block write performance: read pg/erase/write pg
    Controller garbage collection (GC) algorithms have major effect on performance
  Limited drive lifetime
    1-10K writes/page for MLC NAND
    Avg failure rate is 6 years, life expectancy is 9–11 years
These are changing rapidly!
No longer true!

## Slide 42: Nano-Tube Memory (NANTERO)
Yet another possibility: Nanotube memory
  NanoTubes between two electrodes, slight conductivity difference between ones and zeros
  No wearout!
Better than DRAM?
  Speed of DRAM, no wearout, non-volatile!
  Nantero promises 512Gb/dice for 8Tb/chip! (with 16 die stacking)

## Slide 43: Conclusion (1/2)
Notification mechanisms
  Interrupts
  Polling: Report results through status register that processor looks at periodically
Device drivers interface to I/O devices
  Provide clean Read/Write interface to OS above
  Manipulate devices through PIO, DMA & interrupt handling
  Three types: block, character, and network
Direct Memory Access (DMA)
  Permit devices to directly access memory
  Free up processor from transferring every byte

## Slide 44: Conclusion (2/2)
Disk Performance:
  Queuing time + Controller + Seek + Rotational + Transfer
  Rotational latency: on average ½ rotation
  Transfer time: spec of disk depends on rotation speed and bit storage density
Devices have complex interaction and performance characteristics
  Response time (Latency) = Queue + Overhead + Transfer
    Effective BW = BW * T/(S+T)
  HDD: Queuing time + controller + seek + rotation + transfer
  SSD: Queuing time + controller + transfer (erasure & wear)
Systems (e.g., file system) designed to optimize performance and reliability
  Relative to performance characteristics of underlying device
Next time: Bursts & High Utilization introduce queuing delays
Next time: Queuing Latency:
  M/M/1 and M/G/1 queues: simplest to analyze
  As utilization approaches 100%, latency  
  Tq = Tser x ½(1+C) x /(1 – ))