CS162:
Operating Systems and
Systems Programming
Lecture 11:
Caching & Demand Paging (start)
8 July 2015
Charles Reiss
https://cs162.eecs.berkeley.edu/

---
Recall: Address Translation Comparison
	Advantages	Disadvantages
Segmentation	Fast context switching: Segment mapping maintained by CPU	External fragmentation
Paging (single-level page)	No external fragmentation, fast easy allocation	Large table size ~ virtual memory / Internal fragmentation
Paged segmentation	Table size ~ # of pages in virtual memory, fast + easy allocation	Multiple memory references per page access
Two-level pages
Inverted Table	Table size ~ # of pages in physical memory	Hash function more complex

---
Recall: Paging Tricks: Examples
1. Demand Paging
  1. Swapping for pages
  2. Keep only active pages in memory
  3. When exception occurs for page not in memory, load from disk and retry
2. Copy on Write
  1. Remember fork() – copy of address space
  2. Instead of real copy, mark pages read-only
  3. Allocate new pages on protection fault
3. Zero-Fill On Demand
  1. New pages should be zeroed out – slow!
  2. Instead, pages start invalid – create new zero page when accessed

---
Diversion: Protection without HW
1. Example: emulator
  1. Add any permissions checks, but very slow
2. Faster: Programming language restrictions (think Java)
3. Faster: binary translation / software fault isolation
  1. Insert checks before every dangerous operation
    1. Load, store, ...
  2. Either compile/link-time or runtime
  3. Can separately verify checks are present

---
Diversion: Protection without HW
1. OS that runs only "managed" languages: Singularity (Microsoft Research; defunct?)
  1. Like C#, Java, …
  2. Which don't allow pointers to other process's addresses or the OS's addresses
2. No address translation/protection – rely on language runtime to limit what programs can access

---
Diversion: Protection without HW
1. Binary Translation
  1. MIPS: ~5% overhead
  2. (but with caveats)
2. Separate base and bound for code, data
3. All jumps and loads/stores use particular registers
  1. Cecks before putting any values into these registers
  2. Checks are of the form address & mask == value
4. Static checker that assembly follows rules

---
Caching: Definition
1. Cache: repository for copies that can be accessed quicker than originals
2. Goal: Improve performance
3. Lots of things can be cached
  1. Memory (61C), Address Translations (today), Files, File Names, …

---
Why cache? Much faster storage
Processor-DRAM Memory Gap (latency)
1000
“Moore’s Law”
100
10
“Less’ Law?”
1
Time
CPU
µProc
60%/yr.
(2X/1.5yr)
DRAM
9%/yr.
(2X/10 yrs)
DRAM
1980
1981
1983
1984
1985
1986
1987
1988
1989
1990
1991
1992
1993
1994
1995
1996
1997
1998
1999
2000
1982
Processor-Memory
Performance Gap:
(grows 50% / year)
Performance

---
Why cache? Address Translation
Three DRAM accesses per access?
  1. Even three cache accesses per access is too slow
1. Solution: Translation cache (called TLB)
page #0
page #1
page #3
page #4
page #5
V,R
V,R
page #2
V,R,W
V,R,W
N
V,R,W
Offset
Physical Address
Virtual
Address:
Offset
Virtual
Page #
Virtual
Seg #
Base0
Limit0
V
Base1
Limit1
V
Base2
Limit2
V
Base3
Limit3
N
Base4
Limit4
V
Base5
Limit5
N
Base6
Limit6
N
Base7
Limit7
V
Access
Error
>
Physical
Page #
Check Perm
Access
Error

---
Average Access Time
1. Average access time =
   (Hit Rate x Hit Time) + (Miss Rate x Miss Time)
2. Intuition: Caching is good when most accesses are for a small portion of the items
3. Most accesses → Relatively high hit rate
4. Small portion → Hits can be faster than misses
  1. Small data storage is faster

---
New text doesn't fit with diagram on bottom as well
Locality
1. Temporal Locality (Time)
  1. Recently accessed items will be accessed soon
2. Spatial Localtiy (Space)
  1. Items adjacent to recently accessed items will be accessed soon
Address Space
0
2n - 1
Probability
of reference
Lower Level
Memory
Upper Level
Memory
To Processor
From Processor
Blk X
Blk Y

---
Recall: The Memory Hierarchy
Goal: speed of fastest technology with capacity of cheapest
On-Chip
Cache
Registers
Control
Datapath
Secondary
Storage
(Disk)
Processor
Main
Memory
(DRAM)
Second
Level
Cache
(SRAM)
1s
10,000,000s
   (10s ms)
Speed (ns):
10s-100s
100s
100s
Gs
Size (bytes):
Ks-Ms
Ms
Tertiary
Storage
(Tape)
10,000,000,000s
   (10s sec)
Ts

---
Types of Cache Misses
1. Compulsory ("cold start"): first access to a block
  1. Insignificant in any long-lived program
2. Capacity: not enough space in cache
3. Conflict: memory locations map to same cache location
4. Coherence (invalidation): memory updated externally
  1. Example: multiple cores, I/O

---
Types of Cache Misses
1. Compulsory ("cold start"): first access to a block
  1. Insignificant in any long-lived program
2. Capacity: not enough space in cache
3. Conflict: memory locations map to same cache location
4. Coherence (invalidation): memory updated externally
  1. Example: multiple cores, I/O
Not affected by changes in cache design (mostly)

---
Types of Cache Misses
1. Compulsory ("cold start"): first access to a block
  1. Insignificant in any long-lived program
2. Capacity: not enough space in cache
3. Conflict: memory locations map to same cache location
4. Coherence (invalidation): memory updated externally
  1. Example: multiple cores, I/O
Eliminated by increasing cache size (enough)

---
Types of Cache Misses
1. Compulsory ("cold start"): first access to a block
  1. Insignificant in any long-lived program
2. Capacity: not enough space in cache
3. Conflict: memory locations map to same cache location
4. Coherence (invalidation): memory updated externally
  1. Example: multiple cores, I/O
Eliminated by increasing associativity

---
Finding Blocks in (Memory) Cache
1. Index used to lookup set of candidates
2. Tag used to identify actual copy
  1. None in set match → cache miss
3. Block is minimum unit of caching
  1. Data select → part of block to get
Block
offset
Block Address
Tag
Index
Set Select
Data Select

---
Review: Direct Mapped Cache
Example: 2^10 byte capacity; 2^5 byte blocks; 32-bit addresses
  1. Upper (32 – 10) bits are tag
  2. Lower 5 bits are offset
  3. Remaining bits are index
Ex: 0x50
:
0x50
Valid Bit
:
 Cache Tag
Byte 32
0
1
2
3
:
 Cache Data
Byte 0
Byte 1
Byte 31
:
Byte 33
Byte 63
:
Byte 992
Byte 1023
:
31
Ex: 0x00
Cache Index
0
4
31
Cache Tag
Offset
9
Ex: 0x01

---
Review: Direct Mapped Cache
Example: 2^10 byte capacity; 2^5 byte blocks; 32-bit addresses
  1. Upper (32 – 10) bits are tag
  2. Lower 5 bits are offset
  3. Remaining bits are index
:
0x50
Valid Bit
:
 Cache Tag
Byte 32
0
1
2
3
:
 Cache Data
Byte 0
Byte 1
Byte 31
:
Byte 33
Byte 63
:
Byte 992
Byte 1023
:
31
Cache Index
0
4
31
Cache Tag
Byte Select
9
[Speaker Notes: Let’s use a specific example with realistic numbers: assume we have a 1 KB direct mapped cache with block size equals to 32 bytes. In other words, each block associated with the cache tag will have 32 bytes in it (Row 1). With Block Size equals to 32 bytes, the 5 least significant bits of the address will be used as byte select within the cache block. Since the cache size is 1K byte, the upper 32 minus 10 bits, or 22 bits of the address will be stored as cache tag. The rest of the address bits in the middle, that is bit 5 through 9, will be used as Cache Index to select the proper cache entry. +2 = 30 min. (Y:10)]

---
Review: Direct Mapped Cache
Review: Direct Mapped Cache
Example: 2^10 byte capacity; 2^5 byte blocks; 32-bit addresses
  1. Check index to find set of one potential block
  2. Compare tag to verify block
  3. Use byte select to choose byte within block
Ex: 0x50
:
0x50
Valid Bit
:
 Cache Tag
Byte 32
0
1
2
3
:
 Cache Data
Byte 0
Byte 1
Byte 31
:
Byte 33
Byte 63
:
Byte 992
Byte 1023
:
31
Ex: 0x00
Cache Index
0
4
31
Cache Tag
Byte Select
9
Ex: 0x01
[Speaker Notes: Let’s use a specific example with realistic numbers: assume we have a 1 KB direct mapped cache with block size equals to 32 bytes. In other words, each block associated with the cache tag will have 32 bytes in it (Row 1). With Block Size equals to 32 bytes, the 5 least significant bits of the address will be used as byte select within the cache block. Since the cache size is 1K byte, the upper 32 minus 10 bits, or 22 bits of the address will be stored as cache tag. The rest of the address bits in the middle, that is bit 5 through 9, will be used as Cache Index to select the proper cache entry. +2 = 30 min. (Y:10)]

---
Review: Set Associative Cache
Review: Set Associative Cache
N-way set associative: N entries per cache index
Example: 2-way set associative
Cache Index
0
4
31
Cache Tag
Byte Select
8
Cache Data
Cache Block 0
Cache Tag
Valid
:
:
:
Cache Data
Cache Block 0
Cache Tag
Valid
:
:
:
Mux
0
1
Sel1
Sel0
OR
Hit
Compare
Compare
Cache Block
[Speaker Notes: This is called a 2-way set associative cache because there are two cache entries for each cache index. Essentially, you have two direct mapped cache works in parallel. This is how it works: the cache index selects a set from the cache. The two tags in the set are compared in parallel with the upper bits of the memory address. If neither tag matches the incoming address tag, we have a cache miss. Otherwise, we have a cache hit and we will select the data on the side where the tag matches occur. This is simple enough. What is its disadvantages? +1 = 36 min. (Y:16)]

---
Review: Fully Associative Cache
Review: Fully Associative Cache
Fully associative: every block can hold address
  1. Compare cache tags to all blocks
  2. No index
:
 Cache Data
Byte 0
Byte 1
Byte 31
:
Byte 32
Byte 33
Byte 63
:
Valid Bit
:
:
 Cache Tag
0
4
Cache Tag (27 bits long)
Byte Select
31
=
=
=
=
=
Ex: 0x01
[Speaker Notes: While the direct mapped cache is on the simple end of the cache design spectrum, the fully associative cache is on the most complex end. It is the N-way set associative cache carried to the extreme where N in this case is set to the number of cache entries in the cache. In other words, we don’t even bother to use any address bits as the cache index. We just store all the upper bits of the address (except Byte select) that is associated with the cache block as the cache tag and have one comparator for every entry. The address is sent to all entries at once and compared in parallel and only the one that matches are sent to the output. This is called an associative lookup. Needless to say, it is very hardware intensive. Usually, fully associative cache is limited to 64 or less entries. Since we are not doing any mapping with the cache index, we will never push any other item out of the cache because multiple memory locations map to the same cache location. Therefore, by definition, conflict miss is zero for a fully associative cache. This, however, does not mean the overall miss rate will be zero. Assume we have 64 entries here. The first 64 items we accessed can fit in. But when we try to bring in the 65th item, we will need to throw one of them out to make room for the new item. This bring us to the third type of cache misses: Capacity Miss. +3 = 41 min. (Y:21)]

---
Review: Where can a block go?
Example: Block 12 placed in 8 block cache
0 1 2 3 4 5 6 7
Block
no.
Direct mapped:
block 12 can go only into block 4 (12 mod 8)
Set associative:
block 12 can go anywhere in set 0 (12 mod 4)
0 1 2 3 4 5 6 7
Block
no.
Set
0
Set
1
Set
2
Set
3
Fully associative:
block 12 can go anywhere
0 1 2 3 4 5 6 7
Block
no.
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
32-Block Address Space:
1 1 1 1 1 1 1 1 1 1 2 2 2 2 2 2 2 2 2 2 3 3
Block
no.

---
Review: Which block to replace?
1. Direct mapped – no choice
2. Associative:
  1. Random
  2. LRU (least recently used)
3. Empirical miss rates for CPU caches:
	2-way		4-way		8-way
Size	LRU	Rand	LRU	Rand	LRU	Rand
16 KB	5.2%	5.7%	4.7%	5.3%	4.4%	5.0%
64 KB	1.9%	2.0%	1.5%	1.7%	1.4%	1.5%
256 KB	1.15%	1.17%	1.13%	1.13%	1.12%	1.12%

---
Review: Write Policies
1. Write-through: Hold in cache until removed
  1. Simple to implement
  2. Writes can become bottleneck
2. Write-back: Always write to cache
  1. Dirty bit
  2. Better for repeated writes
  3. Reads may trigger write
  4. Coherence policy

---
Caching in Address Translation
TLB
Physical
Memory
CPU
Cached?
Translate
(MMU)
Data Read or Write
(untranslated)
No
Virtual
Address
Physical
Address
Yes
Save
Result

---
Caching in Address Translation
1. Locality in page acceses?
  1. Yes! Same reasons as CPU cache locality.
2. TLB – cache of page table entries
3. TLB design options:
  1. Associativity?
  2. Hierarchy?
  3. Size?

---
Recall: What happens in the MMU?
Virtual
Addresses
Physical
Addresses
CPU
MMU
1. Reads the page table, triggers interrupts
2. Always: translations are cached – what about when nothing cached yet?
3. Option 1: Hardware traversal (example: x86)
  1. Hardware reads page tables
  2. Invoke page fault handler if invalid/non-present PTE
4. Option 2: Software traversal (example: MIPS)
  1. Invoke software handler

---
TLBs and Context Switches
1. Do nothing?
  1. Might use old process's address space
2. Option 1: Invalidate entire TLB
3. Option 2: ProcessID in TLB
  1. Called "tagged TLB"
4. Same problem if translation table changes
  1. Examples: swapping, copy-on-write

---
TLB and page table changes
1. Consider copy-on-write.
2. Process A calls fork().
3. OS marks its pages as read-only.
4. After returning from fork it tries to write to its stack.
5. Triggers protection fault. OS makes a copy of the stack page, updates page table.
6. Restarts instruction.

---
TLB and page table changes
What if TLB has the read/write version
of the page cached?
1. Consider copy-on-write.
2. Process A calls fork().
3. OS marks its pages as read-only.
4. After returning from fork it tries to write to its stack.
5. Triggers protection fault. OS makes a copy of the stack page, updates page table.
6. Restarts instruction.

---
TLB and page table changes
What if TLB has the read-only version
of the page cached?
1. Consider copy-on-write.
2. Process A calls fork().
3. OS marks its pages as read-only.
4. After returning from fork it tries to write to its stack.
5. Triggers protection fault. OS makes a copy of the stack page, updates page table.
6. Restarts instruction.

---
How does hardware invalidate TLB entries?
1. Could maybe keep track of where the page table is and watch for writes to it... but this is really complicated with two (or more)-level page tables and tagged TLBs...
3. Instead, the operating system needs to do it!
  1. Means the TLB is not a transparent cache (for the OS)

---
TLB and page table changes
1. Consider copy-on-write.
2. Process A calls fork().
3. OS marks its pages as read-only. Tells MMU to clear those TLB entries.
4. After returning from fork it tries to write to its stack.
5. Triggers protection fault. OS makes a copy of the stack page, updates page table. Tells MMU to clear that TLB entry.
6. Restarts instruction.

---
Designing a TLB
Critical path of every memory access
  1. Caches need physical addresses. (Why?)
  2. Very high miss time
1. So low associativity?
  1. Problem: conflict misses
  2. Code + data + stack indexes easily coincide:
    1. code @	0x0040 0000
    2. data @	0x1000 0000
    3. stack @	0x7FFF 0FFC
CPU
TLB
Cache
Memory

---
Typical TLB Organization
1. 128-512 entries
2. Often highly associative
  1. Sometimes very small, less-associative cache in front (e.g. 4-16 entry direct mapped "TLB slice")
3. Virtual address → physical address + other info
  1. Or virtual addresss + Process ID
  2. physical address + other info ~ Page Table Entry

---
TLB Example: MIPS R3000
Page numbers
Permissions + other bits from page table
Including info to help paging (later)
ASID = Address Space ID ~ Process ID
Entry only valid when that "PID" running
0xFA00	0x0003	Y	N	Y	R/W	34
0x0040	0x0010	N	Y	Y	R	0
0x0041	0x0011	N	Y	Y	R	0
Virtual Address Physical Address Dirty Ref Valid Access ASID

---
R3000 TLB Overhead
Dcd/ Reg
Inst Fetch
ALU / E.A
Memory
Write Reg
 TLB I-Cache RF Operation WB
 E.A. TLB D-Cache
1. Half-cycle TLB
2. One cycle extra latency on every instruction

---
Overlapping TLB and cache (1)
Idea: cache access shouldn't need need physical page # immediately
virtual address
physical address
byte
Cache access starts with index + byte
1. TLB access finishes in time to compare tag
Offset
Virtual Page #
index
tag / page #

---
Overlapping TLB and cache (2)
1. Larger cache?
  1. Can only overlap set lookup
2. Alternative: Virtual addresses in caches
TLB
4K Cache
10
2
00
4 bytes
index
1 K
page #
disp
20
assoc
lookup
32
Hit/
Miss
FN
Data
Hit/
Miss
=
FN

---
Putting Everything Together: Address Translation
Putting Everything Together: Address Translation
Physical
Memory:
Virtual Address:
Virtual
P1 index
Virtual
P2 index
Offset
Physical Address:
Physical
Page #
Offset
PageTablePtr
Page Table
(1st level)
Page Table
(2nd level)

---
Putting Everything Together: TLB
Putting Everything Together: TLB
Physical
Memory:
Virtual Address:
Virtual
P1 index
Virtual
P2 index
Offset
PageTablePtr
Physical Address:
Physical
Page #
Offset
Page Table
(1st level)
Page Table
(2nd level)
…
TLB:

---
Putting Everything Together: Cache
Putting Everything Together: Cache
Physical
Memory:
Virtual Address:
Virtual
P1 index
Virtual
P2 index
Offset
PageTablePtr
Physical Address:
Physical
Page #
Offset
Page Table
(1st level)
cache:
Page Table
(2nd level)
TLB:
…
…
tag:
block:
index
byte
tag

---
Other Examples of Caching
1. Demand paging (later)
  1. Leave unused parts of process memory on disk/SSD
2. File systems
  1. Contents of files
  2. Directory structure
3. Networking
  1. Hostname to IP address translations
  2. Web pages

---
Other Examples of Caching
1. Demand paging (later)
  1. Leave unused parts of process memory on disk/SSD
2. File systems
  1. Contents of files
  2. Directory structure
3. Networking
  1. Hostname to IP address translations
  2. Web pages

---
Logistics
1. Homework 1 due today
2. Project 1 Checkpoint 1 due today
4. Midterm next week class time
  1. Up to and including demand paging

---
Break

---
The Working Set Model
Theory: Programs transition through sequence of "working sets" – subsets of their address spaces
Time
Address

---
Cache Behavior and Working Sets
1
new working set fits
0
Cache Size
Hit Rate

---
Zipf/Power Law Model
P access(rank) = 1/rank
Rank
Popularity (% accesses)
Estimated Hit Rate
1. "Heavy-tailed" distribution
  1. Lots of rare items – lots of unavoidable misses
  2. A few very common items – caching very helpful

---
Demand Paging
1. Main memory as cache for SSD/disks
2. Idea: Illusion memory has the capacity of disk
On-Chip
Cache
Control
Datapath
Secondary
Storage
(Disk)
Processor
Main
Memory
(DRAM)
Second
Level
Cache
(SRAM)
Tertiary
Storage
(Tape)
Caching

---
Illusion of "infinite" memory
1. How? Transparent layer of indirection
  1. the page table + page fault handlers
Page
Table
TLB
Physical
Memory
512 MB
Disk
500GB
∞
Virtual
Memory
4 GB

---
Illusion of "infinite" memory
For performance? No – Disk is 10000x slower (latency) than DRAM.
For correctness? Yes. Just looks like slower memory.
1. How? Transparent layer of indirection
  1. the page table + page fault handlers
Page
Table
TLB
Physical
Memory
512 MB
Disk
500GB
∞
Virtual
Memory
4 GB

---
Memory as a Cache for Disk
1. Block size: 1 page
2. Associativity: fully associative
3. Write policy: write-back (disk writes are slow)
4. Replacement policy: LRU approximation (later)

---
Illusion of "infinite" memory
1. How? Transparent layer of indirection
  1. the page table + page fault handlers
Page
Table
TLB
Physical
Memory
512 MB
Disk
500GB
∞
Virtual
Memory
4 GB

---
Illusion of "infinite" memory
For performance? No – Disk is 10000x slower (latency) than DRAM.
For correctness? Yes. Just looks like slower memory.
1. How? Transparent layer of indirection
  1. the page table + page fault handlers
Page
Table
TLB
Physical
Memory
512 MB
Disk
500GB
∞
Virtual
Memory
4 GB

---
Recall: x86-32 Page Table Entry
1. 10/10/12-bit split of virtual address
2. top-level page tables called directories
Page Frame Number
(Physical Page Number)
Free
(OS)
0
L
D
A
PCD
PWT
U
W
P
31-12
11-9
8
7
6
5
4
3
2
1
0
}
  1. PFN: physical page number of page or next page table
  2. P: Present bit (= Valid)
  3. W: Writable
  4. U: User-accessible
  5. A: Accessed – set when page is accessed
  6. D: Dirty – set when page is modified
  7. L: If 1, points to 4MB "hugepage" instead of next page table
  8. PWT: Write-through caching behavior (for memory-mapped IO)
  9. PCD: Disable caching (for memory-mapped IO)
Pointer
}
Protection bits
}
Feedback to OS

---
Recall: x86-32 Page Table Entry
1. 10/10/12-bit split of virtual address
2. top-level page tables called directories
Page Frame Number
(Physical Page Number)
Free
(OS)
0
L
D
A
PCD
PWT
U
W
P
31-12
11-9
8
7
6
5
4
3
2
1
0
}
  1. PFN: physical page number of page or next page table
  2. P: Present bit (= Valid)
  3. W: Writable
  4. U: User-accessible
  5. A: Accessed – set when page is accessed
  6. D: Dirty – set when page is modified
  7. L: If 1, points to 4MB "hugepage" instead of next page table
  8. PWT: Write-through caching behavior (for memory-mapped IO)
  9. PCD: Disable caching (for memory-mapped IO)
Pointer
= 0 if page is on disk
(or actually invalid)
}
Protection bits
}
Feedback to OS

---
Recall: x86-32 Page Table Entry
1. 10/10/12-bit split of virtual address
2. top-level page tables called directories
Page Frame Number
(Physical Page Number)
Free
(OS)
0
L
D
A
PCD
PWT
U
W
P
31-12
11-9
8
7
6
5
4
3
2
1
0
}
  1. PFN: physical page number of page or next page table
  2. P: Present bit (= Valid)
  3. W: Writable
  4. U: User-accessible
  5. A: Accessed – set when page is accessed
  6. D: Dirty – set when page is modified
  7. L: If 1, points to 4MB "hugepage" instead of next page table
  8. PWT: Write-through caching behavior (for memory-mapped IO)
  9. PCD: Disable caching (for memory-mapped IO)
Pointer
}
Protection bits
}
Feedback to OS
Dirty bit for write-back!
(Could also be done in SW)

---
Recall: x86-32 Page Table Entry
1. 10/10/12-bit split of virtual address
2. top-level page tables called directories
Page Frame Number
(Physical Page Number)
Free
(OS)
0
L
D
A
PCD
PWT
U
W
P
31-12
11-9
8
7
6
5
4
3
2
1
0
}
  1. PFN: physical page number of page or next page table
  2. P: Present bit (= Valid)
  3. W: Writable
  4. U: User-accessible
  5. A: Accessed – set when page is accessed
  6. D: Dirty – set when page is modified
  7. L: If 1, points to 4MB "hugepage" instead of next page table
  8. PWT: Write-through caching behavior (for memory-mapped IO)
  9. PCD: Disable caching (for memory-mapped IO)
Pointer
}
Protection bits
}
Feedback to OS
Accessed bit to help approximate LRU

---
Demand Paging: Page Replacement
1. Process accesses page on disk
2. Memory Management Unit (MMU) traps to OS – Page Fault
3. OS chooses a page to replace
  1. If it's modified (D=1), writes it back to disk
4. OS load new page into memory
5. OS update page table entries (replaced + new page)
  1. Invalidates TLB for them, too
6. OS restart process from just before access

---
Demand Paging: Page Replacement
1. Process accesses page on disk
2. Memory Management Unit (MMU) traps to OS – Page Fault
3. OS chooses a page to replace
  1. If it's modified (D=1), writes it back to disk
4. OS load new page into memory
5. OS update page table entries (replaced + new page)
  1. Invalidates TLB for them, too
6. OS restart process from just before access
Takes a long time!
Put process on wait queue while waiting for disk

---
Demand Paging: Page Replacement
1. Process accesses page on disk
2. Memory Management Unit (MMU) traps to OS – Page Fault
3. OS chooses a page to replace
  1. If it's modified (D=1), writes it back to disk
4. OS load new page into memory
5. OS update page table entries (replaced + new page)
  1. Invalidate old TLB entries for them, too
6. OS restart process from just before access
Invalidate, but don't update
Rely on TLB miss handling

---
Summary: TLB
1. Cache for page-table entries
2. Lookup by virtual page number
3. Possibly "tagged" with process ID
4. Explicit invalidation by OS

---
Summary: Demand Paging
1. Illusion of infinite memory
2. Memory is just a cache for program's real data on disk
3. Much more tommorrow