## Slide 1: Congestion Control
CS 168 Discussion
Week 7

## Slide 2: RECAP: How does TCP set rate?
How much data can be outstanding?
  min{RWND, CWND}
RWND: do not overload the receiver
  Maintained by receiver
  Advertised to sender
CWND: do not overload the network
  Maintained by sender with Slow Start and AIMD

## Slide 3: Managing CWND: Ver.1
Let’s ignore timeout and Slow Start for now.
  We are in Congestion Avoidance phase
A new ACK: CWND += 1/CWND
  Additive increase
Three duplicate ACKs: CWND /= 2
  Multiplicative decrease
  Quiz: why three?

## Slide 4: Worksheet 1(a)
t (s) | ACK (due to) | CWND | xmit
1.0 | 102 (101) | 10+1/10 | 111
1.2 | 102 (103) | 10+1/10 | -

## Slide 5: Worksheet 1(a)
t (s) | ACK (due to) | CWND | xmit
1.0 | 102 (101) | 10+1/10 | 111
1.2 | 102 (103) | 10+1/10 | -
1.3 | 102 (104) | 10+1/10 | -

## Slide 6: Worksheet 1(a)
t (s) | ACK (due to) | CWND | xmit
1.0 | 102 (101) | 10+1/10 | 111
1.2 | 102 (103) | 10+1/10 | -
1.3 | 102 (104) | 10+1/10 | -
1.4 | 102 (105) | 5 | 102
Fast Retransmit

## Slide 7: Worksheet 1(a)
t (s) | ACK (due to) | CWND | xmit
1.0 | 102 (101) | 10+1/10 | 111
1.2 | 102 (103) | 10+1/10 | -
1.3 | 102 (104) | 10+1/10 | -
1.4 | 102 (105) | 5 | 102
1.5 | 102 (106) | 5 | -
1.6 | 102 (107) | 5 | -
1.7 | 102 (108) | 5 | -
1.8 | 102 (109) | 5 | -
1.9 | 102 (110) | 5 | -
2.0 | 102 (110) | 5 | -
Cannot send any more packets, since # of unACKed > CWND

## Slide 8: Worksheet 1(a)
t (s) | ACK (due to) | CWND | xmit
1.0 | 102 (101) | 10+1/10 | 111
1.2 | 102 (103) | 10+1/10 | -
1.3 | 102 (104) | 10+1/10 | -
1.4 | 102 (105) | 5 | 102
1.5 | 102 (106) | 5 | -
1.6 | 102 (107) | 5 | -
1.7 | 102 (108) | 5 | -
1.8 | 102 (109) | 5 | -
1.9 | 102 (110) | 5 | -
2.0 | 102 (110) | 5 | -
2.4 | 112 (102) | 5+1/5 | 112-116
A new ACK triggers a burst

## Slide 9: Managing CWND: Ver.1
No activity, followed by a sudden burst
  Burst is bad!
    Especially when CWND is large (e.g., 1000s of packets)
  For others: congestion at a small time scale
  For you: packets are more likely to be dropped
Why does this happen?
  We overestimate the # of in-flight packets!

## Slide 10: Worksheet 1(a)
t (s) | ACK (due to) | CWND | xmit | # of unACKed | Actually in-flight
1.0 | 102 (101) | 10+1/10 | 111 | 10 | 10
1.2 | 102 (103) | 10+1/10 | - | 10 | 9
1.3 | 102 (104) | 10+1/10 | - | 10 | 8
1.4 | 102 (105) | 5 | 102 | 10 | 7
1.5 | 102 (106) | 5 | - | 10 | 6
1.6 | 102 (107) | 5 | - | 10 | 5
1.7 | 102 (108) | 5 | - | 10 | 4
1.8 | 102 (109) | 5 | - | 10 | 3
1.9 | 102 (110) | 5 | - | 10 | 2
2.0 | 102 (110) | 5 | - | 10 | 1
2.4 | 112 (102) | 5+1/5 | 112-116 | 5 | 5

## Slide 11: Managing CWND: Ver.2
Idea: an ACK implies that the receiver got an packet
  The packet is not in-flight any longer.
  Give temporary credits so as to keep the packets flow!
On triple dupACKs, enter “Fast Recovery”.
  ssthresh = cwnd / 2
  cwnd = ssthresh + 3
  On dupACK, cwnd = cwnd + 1
  On new ACK, exit Fast Recovery and set cwnd=ssthresh

## Slide 12: Worksheet 1(b)
t (s) | ACK (due to) | CWND | xmit
1.0 | 102 (101) | 10+1/10 | 111
1.2 | 102 (103) | 10+1/10 | -
1.3 | 102 (104) | 10+1/10 | -
1.4 | 102 (105) | 8 | 102
8 = 5 + 3

## Slide 13: Worksheet 1(b)
t (s) | ACK (due to) | CWND | xmit
1.0 | 102 (101) | 10+1/10 | 111
1.2 | 102 (103) | 10+1/10 | -
1.3 | 102 (104) | 10+1/10 | -
1.4 | 102 (105) | 8 | 102
1.5 | 102 (106) | 9 | -
1.6 | 102 (107) | 10 | -
1.7 | 102 (108) | 11 | 112
1.8 | 102 (109) | 12 | 113
1.9 | 102 (110) | 13 | 114
2.0 | 102 (111) | 14 | 115
Packets starts to flow

## Slide 14: Worksheet 1(b)
t (s) | ACK (due to) | CWND | xmit
1.0 | 102 (101) | 10+1/10 | 111
1.2 | 102 (103) | 10+1/10 | -
1.3 | 102 (104) | 10+1/10 | -
1.4 | 102 (105) | 8 | 102
1.5 | 102 (106) | 9 | -
1.6 | 102 (107) | 10 | -
1.7 | 102 (108) | 11 | 112
1.8 | 102 (109) | 12 | 113
1.9 | 102 (110) | 13 | 114
2.0 | 102 (111) | 14 | 115
2.4 | 112 (102) | 5 | 116
Back to Congestion Avoidance

## Slide 15: Worksheet 1(b)
t (s) | ACK (due to) | CWND | xmit | # of unACKed | Actually in-flight
1.0 | 102 (101) | 10+1/10 | 111 | 10 | 10
1.2 | 102 (103) | 10+1/10 | - | 10 | 9
1.3 | 102 (104) | 10+1/10 | - | 10 | 8
1.4 | 102 (105) | 8 | 102 | 10 | 7
1.5 | 102 (106) | 9 | - | 10 | 6
1.6 | 102 (107) | 10 | - | 10 | 5
1.7 | 102 (108) | 11 | 112 | 11 | 5
1.8 | 102 (109) | 12 | 113 | 12 | 5
1.9 | 102 (110) | 13 | 114 | 13 | 5
2.0 | 102 (111) | 14 | 115 | 14 | 5
2.4 | 112 (102) | 5 | 116 | 5 | 5
Temporary credits…
reflect the right CWND

## Slide 16: The Big Picture
slow start
congstn. avoid.
fast recovery
cwnd > ssthresh
timeout
dupACK=3
timeout
dupACK=3
new ACK
dupACK
new ACK
timeout
new ACK
dupACK
dupACK
See Fig 3.52 in the textbook for more details

## Slide 17
A
Loss
time
cwnd
1
RTT
½ Wmax RTTs between drops
Avg. ¾ Wmax packets per RTTs

## Slide 18: Worksheet 2(b) and 2(c)
(b) 1.22Mbps
  1.22 * 10^4 / (0.1 * 0.1)
(c) RTT
  2 > sqrt(2)

## Slide 19: Worksheet 2 (d)
The loss probability p is predictable.
  It can be dynamic depending on the level of congestion.
Loss is indicated by triple dupACK.
  TCP retransmission timeout deviates from “sawtooth”
Only the network is the bottleneck.
  What if the receiver is the bottleneck at a given time?
…