## Slide 1: A Complete End-to-End View

## Slide 2
Laptop
Wifi
AP
BERKELEY
DHCP Server/
Gateway Router
DNS Server (9.9.9.9)
www.google.com
AT&T
GOOGLE

## Slide 3: Step 1: Setting up the Network
To get an IP address, broadcast DHCP message that is picked by the DHCP server
DHCP Discovery

## Slide 4: Step 1: Setting up the Network
It is a UDP packet sent on source port 68 and destination port 67
DHCP Discovery
UDP

## Slide 5: Step 1: Setting up the Network
IP contains:
Source Address: 0.0.0.0
  We do not yet have an IP address
Destination Address: 255.255.255.255
  We broadcast the request
DHCP Discovery
UDP
IP

## Slide 6: Step 1: Setting up the Network
Add a Link Layer Frame (even Wifi has same format as Ethernet Frame)
Destination MAC address is FF:FF:FF:FF:FF:FF
  To broadcast
DHCP Discovery
UDP
IP
LL

## Slide 7: Step 1: Setting up the Network
Machine running DHCP server picks up the request
Link Layer driver in the server shreds the LL header
IP Layer of the kernel shreds the IP header
UDP layer shreds the UDP header, after demultiplexing the packet to the server application running on port 67.
DHCP Discovery
UDP
IP
LL

## Slide 8: Step 1: Setting up the Network
Prepares an offer containing:
  IP address of the requesting entity
  DNS server’s IP address
  Default Gateway’s IP address
  Subnet Mask
Encapsulated by UDP, IP and LL frames
DHCP Offer
UDP
IP
LL

## Slide 9: Step 1: Setting up the Network
Prepares an offer containing:
  IP address of the requesting entity
  DNS server’s IP address
  Default Gateway’s IP address
  Subnet Mask
Encapsulated by UDP, IP and LL frames
DHCP Offer
UDP
IP
LL

## Slide 10: Step 1: Setting up the Network
Next Steps:
  Client accepts an offer by broadcasting a “Request message
  The server sends back an ACK

## Slide 11: If Ethernet Instead of Wifi?
The basic protocol remains same upto network
Wifi and Ethernet use the same LL header
Preamble and CRC added by Physical layer varies
Technology used to transmit the packets varies
  e.g. CSMA/CD for Ethernet CSMA/CA for Wifi, stronger reliability for Wifi etc
DHCP Discovery
UDP
IP
LL

## Slide 12: Step 2: Getting Destination IP Address
Send a DNS request to the local DNS server to obtain IP address www.google.com
DNS Request

## Slide 13: Step 2:Getting Destination IP Address
It is a UDP packet sent on destination port 53
DNS Request
UDP

## Slide 14: Step 2:Getting Destination IP Address
IP contains:
Source Address: Obtained by DHCP
Destination Address: Local DNS server’s IP address (9.9.9.9), also contained DHCP response
DNS Request
UDP
IP

## Slide 15: Step 2: Getting Destination IP Address
Add a LL frame
Destination MAC address??
It knows that 9.9.9.9 is outside the subnet, since it knows the netmask from DHCP response
Needs to route to the Default Gateway Router
But its MAC address unknown
DNS Request
UDP
IP
LL

## Slide 16: ARP
Broadcast an ARP request message
ARP response from the Gateway Router contains the MAC address
ARP
LL

## Slide 17: Step 2: Getting Destination IP Address
DNS request then processed by local server
  Does the recursive querying to root, TLD and authoritative DNS server
DNS response with www.google.com’s IP address
Can save on complete iterative querying by local server if response if cached

## Slide 18: Step 3: Requesting the Page
Use HTTP to communicate with the destination’s application
TCP is the transport protocol used
Encapsulated by IP and LL frames
HTTP
TCP
IP
LL

## Slide 19: How is a Packet Transmitted?

## Slide 20: Same network layer functionalities irrespective of transport or application layer protocols

## Slide 21: Inter-Domain
Laptop
Wifi
AP
BERKELEY
DHCP Server/
Gateway Router
DNS Server (9.9.9.9)
www.google.com
AT&T
GOOGLE
BGP
BGP

## Slide 22: Intra-Domain
Laptop
Wifi
AP
BERKELEY
DHCP Server/
Gateway Router
DNS Server (9.9.9.9)
www.google.com
AT&T
GOOGLE
DV/LS

## Slide 23: Link Layer Technology Varies
Laptop
Wifi
AP
BERKELEY
DHCP Server/
Gateway Router
DNS Server (9.9.9.9)
www.google.com
AT&T
GOOGLE
Ethernet
ATM

## Slide 24: Transmitting Packet: All Layers View
Application
Transport
Network
Link Layer/Phy
a
a
a
a
a
a
a
a
a
a
Application
Transport
a
a
a
Network
Link Layer/Phy
a
a
a
a
a
a
a
A
B
C
D
b
Network
Link Layer/Phy
a
a
a
a
a
a
b
c
Network
Link Layer/Phy
a
a
a
a
a
a
c
Source
Dest
Router
Router