## Slide 1: CS252 Graduate Computer Architecture Fall 2015 Lecture 15: Memory Protection and Address Translation
Krste Asanovic
krste@eecs.berkeley.edu
http://inst.eecs.berkeley.edu/~cs252/fa15

## Slide 2: Memory Management
Can separate into orthogonal functions:
  Translation (mapping of virtual address to physical address)
  Protection (permission to access word in memory)
  Virtual memory (transparent extension of memory space using slower disk or flash storage)
But most modern computer systems provide support for all the above functions with a single page-based memory-management system

## Slide 3: Bare Machine
In a bare machine, the only kind of address is a physical address, corresponding to address lines of actual hardware memory.
PC
Inst. Cache
D
Decode
E
M
Data Cache
W
+
Main Memory (DRAM)
Memory Controller
Physical Address
Physical Address
Physical Address
Physical Address
Physical Address

## Slide 4: Managing Memory in Bare Machines
Early machines only ran one program at a time, with this program having unrestricted access to all memory and all I/O devices
  This simple memory management model was also used in turn by the first minicomputer and first microcomputer systems
Subroutine libraries became popular, were written in location-independent form
  Different programs use different combination of routines
To run program on bare machines, use linker or loader program to relocate library modules to actual locations in physical memory

## Slide 5: Motivating Dynamic Address Translation
In early machines, I/O was slow and each I/O transfer involved CPU (programmed I/O)
  Higher throughput possible if CPU and I/O of 2 or more programs were overlapped
  multiprogramming with DMA I/O devices, interrupts
Location-independent programs
  Programming and storage management ease
   need for a base register
Protection
  Independent programs should not affect each other inadvertently
   need for a bound register
Multiprogramming drives requirement for resident supervisor software to manage context switches between multiple programs
Physical Memory
Program 1
Program 2
OS

## Slide 6: Simple Base and Bound Translation
Load X
Program Address Space
Bound
Register
Bounds
Violation?
Physical Memory
Current
Segment
Base
Register
+
Physical
Address
Logical
Address
Base and bounds registers are visible/accessible only when processor is running in the supervisor mode
Base Physical Address
Segment Length
≥

## Slide 7: Separate Areas for Program and Data
Physical Address
Physical Address
Load X
Program Address Space
Physical Memory
Data Segment
Data Bound Register
Data Base Register
+
Bounds Violation?
Program Bound Register
Program Base Register
+
Program Segment
Logical Address
Logical Address
What is an advantage of this separation?
What about more base/bound pairs?
(Scheme used on all Cray vector supercomputers prior to X1, 2002)
≥
≥
Bounds Violation?
Program Counter
Notes: Permits sharing of program segments.

## Slide 8: Base and Bound Machine
Can fold addition of base register into (register+immediate) address calculation using a carry-save adder (sums three numbers with only a few gate delays more than adding two numbers)
PC
Inst. Cache
D
Decode
E
M
Data Cache
W
+
Main Memory (DRAM)
Memory Controller
Physical Address
Physical Address
Physical Address
Physical Address
Data Bound Register
Data Base Register
+
Logical Address
Bounds Violation?
Physical Address
Program Base Register
+
Logical Address
Bounds Violation?
≥
≥
Program Bound Register

## Slide 9: External Fragmentation with Segments
72K
Job 1
32K
Job 2
24K
8K
Job 1
32K
Job 2
24K
Job 3
64K
Job 3 starts
Job 1
32K
24K
Job 3
64K
8K
Job 2 finishes
Job 4
32K
Job 4 arrives
Can’t run Job 4, as not enough contiguous space. Must compact.

## Slide 10: Paged Memory Systems
Program-generated (virtual or logical) address split into:
Virtual Address Space Pages for Job 1
Page Table
for Job 1
Page Table contains physical address of start of each fixed-sized page in virtual address space
Physical Memory
Pages
Page Number
Offset
0
1
2
3
0
1
2
3
1
0
3
2
Paging makes it possible to store a large contiguous virtual memory space using non-contiguous physical memory pages
Notes: Relaxes the contiguous allocation requirement.

## Slide 11: Private Address Space per User
Virtual Address Space Pages for Job 1
Page Table
for Job 1
Physical Memory
Pages
0
1
2
3
0
1
2
3
1
0
1
3
3
3
2
0
0
2
2
1
Operating
System
Pages
Virtual Address Space Pages for Job 2
Page Table
for Job 2
0
1
2
3
0
1
2
3
Virtual Address Space Pages for Job 3
Page Table
for Job 3
0
1
2
3
0
1
2
3
Notes: Relaxes the contiguous allocation requirement.

## Slide 12: Paging Simplifies Allocation
Fixed-size pages can be kept on OS free list and allocated as needed to any process
Process memory usage can easily grow and shrink dynamically
Paging suffers from internal fragmentation where not all bytes on a page are used
  Much less of an issue than external fragmentation or compaction for common page sizes (4-8KB)

## Slide 13: Page Tables Live in Memory
Virtual Address Space Pages for Job 1
Physical Memory
Pages
0
1
2
3
Page Table
for Job 1
1
0
1
3
3
2
0
2
Virtual Address Space Pages for Job 2
0
1
2
3
Page Table
for Job 2
Simple linear page tables are too large, so hierarchical page tables are commonly used (see later)
Common for modern OS to place page tables in kernel’s virtual memory (page tables can be swapped to secondary storage)
Notes: Relaxes the contiguous allocation requirement.

## Slide 14: Coping with Limited Primary Storage
Paging reduces fragmentation, but still many problems would not fit into primary memory, have to copy data to and from secondary storage (drum, disk)
Two early approaches:
  Manual overlays, programmer explicitly copies code and data in and out of primary memory
    Tedious coding, error-prone (jumping to non-resident code?)
  Software interpretive coding (Brooker 1960). Dynamic interpreter detects variables that are swapped out to drum and brings them back in
    Simple for programmer, but inefficient
Not just ancient black arts, e.g., IBM Cell microprocessor using in Playstation-3 had explicitly managed local store!

## Slide 15: Demand Paging in Atlas (1962)
Secondary
(Drum)
32x6 pages
Primary
32 Pages
512 words/page
Central
Memory
User sees 32 x 6 x 512 words
of storage
“A page from secondary
storage is brought into the primary storage whenever it is (implicitly) demanded by the processor.”
Tom Kilburn
Primary memory as a cache
for secondary memory
Notes: Single-level Store

## Slide 16: Hardware Organization of Atlas
Initial
Address
Decode
16 ROM pages
0.4-1 sec
2 subsidiary pages
1.4 sec
Main
32 pages
1.4 sec
Drum (4)
192 pages
8 Tape decks
88 sec/word
48-bit words
512-word pages
1 Page Address Register (PAR) per page frame
Compare the effective page address against all 32 PARs
match  normal access
no match  page fault
save the state of the partially executed instruction
Effective
Address
system code
(not swapped)
system data
(not swapped)
0
31
PARs
<effective PN , status>

## Slide 17: Atlas Demand Paging Scheme
On a page fault:
Input transfer into a free page is initiated
The Page Address Register (PAR) is updated
If no free page is left, a page is selected to be replaced (based on usage)
The replaced page is written on the drum
  to minimize drum latency effect, the first empty page on the drum was selected
The page table is updated to point to the new location of the page on the drum

## Slide 18: Size of Linear Page Table
With 32-bit addresses, 4-KB pages & 4-byte PTEs:
  220 PTEs, i.e, 4 MB page table per user
  4 GB of swap needed to back up full virtual address space
Larger pages?
  Internal fragmentation (Not all memory in page is used)
  Larger page fault penalty (more time to read from disk)
What about 64-bit virtual address space???
  Even 1MB pages would require 244 8-byte PTEs (35 TB!)
What is the “saving grace” ?
Notes: Virtual address space is large but only a small fraction of the
pages are populated. So we can use a sparse representation
of the table.

## Slide 19: Hierarchical Page Table
Level 1
Page Table
Level 2
Page Tables
Data Pages
page in primary memory
page in secondary memory
Root of the Current
Page Table
p1
offset
p2
Virtual Address from CPU
(Processor
Register)
PTE of a nonexistent page
p1 p2 offset
0
11
12
21
22
31
10-bit
L1 index
10-bit
L2 index
Physical Memory

## Slide 20: Two-Level Page Tables in Physical Memory
VA1
User 1
User1/VA1
User2/VA1
Level 1 PT User 1
Level 1 PT User 2
VA1
User 2
Level 2 PT User 2
Virtual Address Spaces
Physical Memory

## Slide 21: Address Translation & Protection
Every instruction and data access needs address
translation and protection checks
A good VM design needs to be fast (~ one cycle) and space efficient
Physical Address
Virtual Address
Address
Translation
Virtual Page No. (VPN)
offset
Physical Page No. (PPN)
offset
Exception?
Kernel/User Mode
Read/Write
Protection Check

## Slide 22: Translation-Lookaside Buffers (TLB)
Address translation is very expensive!
  In a two-level page table, each reference becomes several memory accesses
Solution: Cache translations in TLB
TLB hit  Single-Cycle Translation
TLB miss  Page-Table Walk to refill
VPN offset
V R W D tag PPN
physical address
PPN offset
virtual address
hit?
(VPN = virtual page number)
(PPN = physical page number)
Notes: 3 memory references
2 page faults (disk accesses) + ..
Actually used in IBM before paged memory.

## Slide 23: TLB Designs
Typically 32-128 entries, usually fully associative
  Each entry maps a large page, hence less spatial locality across pages  more likely that two entries conflict
  Sometimes larger TLBs (256-512 entries) are 4-8 way set-associative
  Larger systems sometimes have multi-level (L1 and L2) TLBs
Random or FIFO replacement policy
TLB Reach: Size of largest virtual address space that can be simultaneously mapped by TLB
  Example: 64 TLB entries, 4KB pages, one page per entry
  TLB Reach = _____________________________________________?
64 entries * 4 KB = 256 KB (if contiguous)

## Slide 24: Handling a TLB Miss
Software (MIPS, Alpha)
  TLB miss causes an exception and the operating system walks the page tables and reloads TLB. A privileged “untranslated” addressing mode used for walk.
  Software TLB miss can be very expensive on out-of-order superscalar processor as requires a flush of pipeline to jump to trap handler.
Hardware (SPARC v8, x86, PowerPC, RISC-V)
  A memory management unit (MMU) walks the page tables and reloads the TLB.
  If a missing (data or PT) page is encountered during the TLB reloading, MMU gives up and signals a Page Fault exception for the original instruction.
NOTE: A given ISA can use either TLB miss strategy

## Slide 25: Hierarchical Page Table Walk: SPARC v8
31 11 0
Virtual Address
Index 1 Index 2 Index 3 Offset
31 23 17 11 0
Context
Table
Register
Context
Register
root ptr
PTP
PTP
PTE
Context Table
L1 Table
L2 Table
L3 Table
Physical Address
PPN Offset
MMU does this table walk in hardware on a TLB miss

## Slide 26: Page-Based Virtual-Memory Machine (Hardware Page-Table Walk)
Assumes page tables held in untranslated physical memory
PC
Inst. TLB
Inst. Cache
D
Decode
E
M
Data Cache
W
+
Page Fault?
Protection violation?
Data TLB
Main Memory (DRAM)
Memory Controller
Physical Address
Physical Address
Physical Address
Physical Address
Page-Table Base Register
Virtual Address
Physical Address
Virtual Address
Hardware Page Table Walker
Miss?
Miss?
Page Fault?
Protection violation?

## Slide 27: Page Fault Handler
When the referenced page is not in DRAM:
  The missing page is located (or created)
  It is brought in from disk, and page table is updated
    Another job may be run on the CPU while the first job waits for the requested page to be read from disk
  If no free pages are left, a page is swapped out
    Pseudo-LRU replacement policy, implemented in software
Since it takes a long time to transfer a page (msecs), page faults are handled completely in software by OS
  Untranslated addressing mode is essential to allow kernel to access page tables
Keeping TLBs coherent with page table changes might require expensive “TLB shootdown”
  Interrupt other processors to invalidate stale TLB entries
  Some mainframes had hardware TLB coherence

## Slide 28: Handling VM-related exceptions
Handling a TLB miss needs a hardware or software mechanism to refill TLB
Handling page fault (e.g., page is on disk) needs restartable exception so software handler can resume after retrieving page
  Precise exceptions are easy to restart
  Can be imprecise but restartable, but this complicates OS software
A protection violation may abort process
  But often handled the same as a page fault
PC
Inst TLB
Inst. Cache
D
Decode
E
M
Data TLB
Data Cache
W
+
TLB miss? Page Fault?
Protection violation?
TLB miss? Page Fault?
Protection violation?

## Slide 29: Acknowledgements
This course is partly inspired by previous MIT 6.823 and Berkeley CS252 computer architecture courses created by my collaborators and colleagues:
  Arvind (MIT)
  Joel Emer (Intel/MIT)
  James Hoe (CMU)
  John Kubiatowicz (UCB)
  David Patterson (UCB)