## Slide 1: CS 61C: Great Ideas in Computer Architecture (Machine Structures) Lecture 28: Single-Cycle CPU Datapath Control Part 1
Guest Lecturer: Sagar Karandikar
http://inst.eecs.berkeley.edu/~cs61c/

## Slide 2: Technology In the News
http://research.microsoft.com/apps/pubs/default.aspx?id=212001
FPGAs are “programmable” hardware used by computer architects and digital circuit designers, lie somewhere between CPUs and custom chips (ASICs).
“Microsoft published a paper at ISCA about using FPGAs in datacenters
Microsoft “Catapult”, ISCA 2014
for page ranking processing for Bing. In a test deployment, MS reported up to 95% more throughput for only 10% more power. The added TCO was less than 30%. Microsoft used Altera Stratix V FPGAs in a PCIe form-factor with 8GB of DDR3 RAM on each board. The FPGAs were connected using a 10Gb SAS network.” - AnandTech

## Slide 3: Review
CPU design involves Datapath, Control
  5 Stages for MIPS Instructions
    Instruction Fetch
    Instruction Decode & Register Read
    ALU (Execute)
    Memory
    Register Write
Datapath timing: single long clock cycle or one short clock cycle per stage

## Slide 4: Datapath and Control
Datapath based on data transfers required to perform instructions
Controller causes the right transfers to happen
PC
instruction
memory
+4
rt
rs
rd
registers
Data
memory
imm
ALU
Controller
opcode, funct
==
zero

## Slide 5: CPU Clocking (1/2)
For each instruction, how do we control the flow of information though the datapath?
Single Cycle CPU: All stages of an instruction completed within one long clock cycle
  Clock cycle sufficiently long to allow each instruction to complete all stages without interruption within one cycle
1. Instruction
Fetch
2. Decode/
Register
Read
3. Execute
4. Memory
5. Reg.
Write

## Slide 6: CPU Clocking (2/2)
Alternative multiple-cycle CPU: only one stage of instruction per clock cycle
  Clock is made as long as the slowest stage
  Several significant advantages over single cycle execution: Unused stages in a particular instruction can be skipped OR instructions can be pipelined (overlapped)
1. Instruction
Fetch
2. Decode/
Register
Read
3. Execute
4. Memory
5. Register
Write

## Slide 7: Agenda
Stages of the Datapath
Datapath Instruction Walkthroughs
Datapath Design

## Slide 8: Five Components of a Computer
Processor
Computer
Control
Datapath
Memory
(passive)
(where
programs,
data live
when
running)
Devices
Input
Output
Keyboard, Mouse
Display, Printer
Disk (where
programs,
data live when not running)

## Slide 9: Processor Design: 5 steps
  Step 1: Analyze instruction set to determine datapath requirements
  Meaning of each instruction is given by register transfers
  Datapath must include storage element for ISA registers
  Datapath must support each register transfer
  Step 2: Select set of datapath components & establish clock methodology
  Step 3: Assemble datapath components that meet the requirements
  Step 4: Analyze implementation of each instruction to determine setting of control points that realizes the register transfer
  Step 5: Assemble the control logic

## Slide 10: The MIPS Instruction Formats
All MIPS instructions are 32 bits long. 3 formats:
  R-type
  I-type
  J-type
The different fields are:
  op: operation (“opcode”) of the instruction
  rs, rt, rd: the source and destination register specifiers
  shamt: shift amount
  funct: selects the variant of the operation in the “op” field
  address / immediate: address offset or immediate value
  target address: target address of jump instruction
op
target address
0
26
31
6 bits
26 bits
op
rs
rt
rd
shamt
funct
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
op
rs
rt
address/immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits

## Slide 11: The MIPS-lite Subset
ADDU and SUBU
  addu rd,rs,rt
  subu rd,rs,rt
OR Immediate:
  ori rt,rs,imm16
LOAD and STORE Word
  lw rt,rs,imm16
  sw rt,rs,imm16
BRANCH:
  beq rs,rt,imm16
op
rs
rt
rd
shamt
funct
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits

## Slide 12: Register Transfer Level (RTL)
Colloquially called “Register Transfer Language”
RTL gives the meaning of the instructions
All start by fetching the instruction itself
{op , rs , rt , rd , shamt , funct}  MEM[ PC ]
{op , rs , rt , Imm16}  MEM[ PC ]
Inst Register Transfers
ADDU R[rd]  R[rs] + R[rt]; PC  PC + 4
SUBU R[rd]  R[rs] – R[rt]; PC  PC + 4
ORI R[rt]  R[rs] | zero_ext(Imm16); PC  PC + 4
LOAD R[rt]  MEM[ R[rs] + sign_ext(Imm16)]; PC  PC + 4
STORE MEM[ R[rs] + sign_ext(Imm16) ]  R[rt]; PC  PC + 4
BEQ if ( R[rs] == R[rt] ) PC  PC + 4 + {sign_ext(Imm16), 2’b00}
else PC  PC + 4

## Slide 13: Step 1: Requirements of the Instruction Set
Memory (MEM)
  Instructions & data (will use one for each)
Registers (R: 32, 32-bit wide registers)
  Read RS
  Read RT
  Write RT or RD
Program Counter (PC)
Extender (sign/zero extend)
Add/Sub/OR/etc unit for operation on register(s) or extended immediate (ALU)
Add 4 (+ maybe extended immediate) to PC
Compare registers?

## Slide 14: Step 2: Components of the Datapath
Combinational Elements
Storage Elements + Clocking Methodology
Building Blocks
32
32
A
B
32
Sum
CarryOut
CarryIn
Adder
32
A
B
32
Y
32
Select
MUX
Multiplexer
32
32
A
B
32
Result
OP
ALU
ALU
Adder

## Slide 15: ALU Needs for MIPS-lite + Rest of MIPS
Addition, subtraction, logical OR, ==:
  ADDU R[rd] = R[rs] + R[rt]; ...
  SUBU R[rd] = R[rs] – R[rt]; ...
  ORI R[rt] = R[rs] | zero_ext(Imm16)...
  BEQ if ( R[rs] == R[rt] )...
Test to see if output == 0 for any ALU operation gives == test. How?
P&H also adds AND, Set Less Than (1 if A < B, 0 otherwise)
ALU follows Chapter 5

## Slide 16: Storage Element: Idealized Memory
“Magic” Memory
  One input bus: Data In
  One output bus: Data Out
Memory word is found by:
  For Read: Address selects the word to put on Data Out
  For Write: Set Write Enable = 1: address selects the memory word to be written via the Data In bus
Clock input (CLK)
  CLK input is a factor ONLY during write operation
  During read operation, behaves as a combinational logic block: Address valid  Data Out valid after “access time”
Clk
Data In
Write Enable
32
32
DataOut
Address

## Slide 17: Storage Element: Register (Building Block)
Similar to D Flip Flop except
  N-bit input and output
  Write Enable input
Write Enable:
  Negated (or deasserted) (0): Data Out will not change
  Asserted (1): Data Out will become Data In on positive edge of clock
clk
Data In
Write Enable
N
N
Data Out

## Slide 18: Storage Element: Register File
Register File consists of 32 registers:
  Two 32-bit output busses:
  busA and busB
  One 32-bit input bus: busW
Register is selected by:
  RA (number) selects the register to put on busA (data)
  RB (number) selects the register to put on busB (data)
  RW (number) selects the register to be written via busW (data) when Write Enable is 1
Clock input (clk)
  Clk input is a factor ONLY during write operation
  During read operation, behaves as a combinational logic block:
    RA or RB valid  busA or busB valid after “access time.”
Clk
busW
Write Enable
32
32
busA
32
busB
5
5
5
RW
RA
RB
32 x 32-bit
Registers

## Slide 19: Administrivia
No classes on Tuesday – If you have discussion on Tuesday, go to a M/W discussion.
Project 3-1 out Sunday
  Free to choose new partners, but not forced
  Start early!
Heads Up: No Lab Thanksgiving Week

## Slide 20: Step 3a: Instruction Fetch Unit
Register Transfer Requirements  Datapath Assembly
Instruction Fetch
Read Operands and Execute Operation
Common RTL operations
  Fetch the Instruction: mem[PC]
  Update the program counter:
    Sequential Code: PC  PC + 4
    Branch and Jump: PC  “something else”
32
Instruction Word
Address
Instruction
Memory
PC
clk
Next Address
Logic

## Slide 21: Step 3b: Add & Subtract
R[rd] = R[rs] op R[rt] (addu rd,rs,rt)
  Ra, Rb, and Rw come from instruction’s Rs, Rt, and Rd fields
  ALUctr and RegWr: control logic after decoding the instruction
… Already defined the register file & ALU
32
Result
ALUctr
clk
busW
RegWr
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 x 32-bit
Registers
Rs
Rt
Rd
ALU
op
rs
rt
rd
shamt
funct
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits

## Slide 22: Clocking Methodology
Storage elements clocked by same edge
Flip-flops (FFs) and combinational logic have some delays
  Gates: delay from input change to output change
  Signals at FF D input must be stable before active clock edge to allow signal to travel within the FF (set-up time), and we have the usual clock-to-Q delay
“Critical path” (longest path through logic) determines length of clock period
Clk
.
.
.
.
.
.
.
.
.
.
.
.

## Slide 23: Register-Register Timing: One Complete Cycle
Clk
PC
Rs, Rt, Rd,
Op, Func
ALUctr
Instruction Memory Access Time
Old Value
New Value
RegWr
Old Value
New Value
Delay through Control Logic
busA, B
Register File Access Time
Old Value
New Value
busW
ALU Delay
Old Value
New Value
Old Value
New Value
New Value
Old Value
Register Write
Occurs Here
32
ALUctr
clk
busW
RegWr
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
ALU
5
Rd

## Slide 24: Putting it All Together:A Single Cycle Datapath
imm16
32
ALUctr
clk
busW
RegWr
32
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
Rt
Rd
RegDst
Extender
32
16
imm16
ALUSrc
ExtOp
MemtoReg
clk
Data In
32
MemWr
Equal
Instruction<31:0>
<21:25>
<16:20>
<11:15>
<0:15>
Imm16
Rd
Rt
Rs
clk
PC
00
4
nPC_sel
PC Ext
Adr
Inst
Memory
Adder
Adder
Mux
0
1
0
1
=
ALU
0
1
WrEn
Adr
Data
Memory
5

## Slide 25: Processor Design: 3 of 5 steps
  Step 1: Analyze instruction set to determine datapath requirements
  Meaning of each instruction is given by register transfers
  Datapath must include storage element for ISA registers
  Datapath must support each register transfer
  Step 2: Select set of datapath components & establish clock methodology
  Step 3: Assemble datapath components that meet the requirements
  Step 4: Analyze implementation of each instruction to determine setting of control points that realizes the register transfer
  Step 5: Assemble the control logic