## Slide 1: CS 61C: Great Ideas in Computer Architecture More MIPS, MIPS Functions
Instructors:
John Wawrzynek & Vladimir Stojanovic
http://inst.eecs.Berkeley.edu/~cs61c/fa15

## Slide 2: Levels of Representation/Interpretation
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
High Level Language Program (e.g., C)
Assembly Language Program (e.g., MIPS)
Machine Language Program (MIPS)
Hardware Architecture Description (e.g., block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Architecture Implementation
Anything can be represented as a number, i.e., data or instructions
Logic Circuit Description (Circuit Schematic Diagrams)

## Slide 3: From last lecture …
Computer “words” and “vocabulary” are called instructions and instruction set respectively
MIPS is example RISC instruction set used in CS61C
Rigid format: 1 operation, 2 source operands, 1 destination
  add,sub,mul,div,and,or,sll,srl,sra
  lw,sw,lb,sb to move data to/from registers from/to memory
  beq, bne, j, slt, slti for decision/flow control
Simple mappings from arithmetic expressions, array access, in C to MIPS instructions

## Slide 4: Review: Components of a Computer
Processor
Control
Datapath
Program Counter
Registers
Arithmetic & Logic Unit
(ALU)
Memory
Input
Output
Bytes
Enable?
Read/Write
Address
Write Data
ReadData
Processor-Memory Interface
I/O-Memory Interfaces
Program
Data

## Slide 5: How Program is Stored
Memory
Bytes
Program
Data
One MIPS Instruction = 32 bits

## Slide 6: Assembler to Machine Code (more later in course)
foo.S
bar.S
Assembler
Assembler
foo.o
bar.o
Linker
lib.o
a.out
Assembler source files (text)
Machine code object files
Pre-built object file libraries
Machine code executable file
Assembler converts human-readable assembly code to instruction bit patterns

## Slide 7: Executing a Program
Processor
Control
Datapath
PC
Registers
Arithmetic & Logic Unit
(ALU)
Memory
Bytes
Instruction
Address
Read Instruction Bits
Program
Data
The PC (program counter) is internal register inside processor holding byte address of next instruction to be executed.
Instruction is fetched from memory, then control unit executes instruction using datapath and memory system, and updates program counter (default is add +4 bytes to PC, to move to next sequential instruction)

## Slide 8: Review if-else Statement
Assuming translations below, compile
f → $s0 g → $s1 h → $s2
i → $s3 j → $s4
if (i == j) bne $s3,$s4,Else
f = g + h; add $s0,$s1,$s2
else j Exit
f = g – h; Else: sub $s0,$s1,$s2
Exit:

## Slide 9: Control-flow Graphs: A visualization
bne $s3,$s4,Else
add $s0,$s1,$s2
j Exit
Else: sub $s0,$s1,$s2
Exit:
bne $s3, $s4, Else
add $s0, $s1, $s2
j Exit
Else: sub $s0, $s1, $s2
Exit: …

## Slide 10: Clickers/Peer Instruction
What is the code above?
A: while loop
B: do … while loop
C: for loop
D: A or C
E: Not a loop
addi $s0,$zero,0
Start: slt $t0,$s0,$s1
beq $t0,$zero,Exit
sll $t1,$s0,2 addu $t1,$t1,$s5 lw $t1,0($t1)
add $s4,$s4,$t1
addi $s0,$s0,1
j Start
Exit:

## Slide 11: Administrivia
Fill-out the form to link bitbucket and edX accounts
  Look-out for post on Piazza
Advertising Guerrilla sections again
  Tuesdays and Saturdays every two weeks
CE applications approved for all students

## Slide 12: CS61C In the News
MIPS Creator CI20 dev board now available
  A lot like Raspberry Pi but with MIPS CPU
  Supports Linux and Android
1.2GHz 32-bit MIPS with integrated graphics
http://liliputing.com/2015/01/mips-creator-ci20-dev-board-now-available-for-65.html

## Slide 13: CS61C In the News pt. 2
RISC-V ANGEL:
Try RISC-V in a browser
http://riscv.org/angel/

## Slide 14: Six Fundamental Steps in Calling a Function
Put parameters in a place where function can access them
Transfer control to function
Acquire (local) storage resources needed for function
Perform desired task of the function
Put result value in a place where calling code can access it and restore any registers you used
Return control to point of origin, since a function can be called from several points in a program

## Slide 15: MIPS Function Call Conventions
Registers faster than memory, so use them
$a0–$a3: four argument registers to pass parameters ($4 - $7)
$v0,$v1: two value registers to return values ($2,$3)
$ra: one return address register to return to the point of origin ($31)
Notes: $at – assembler temporary register, used for pseudo instructions

## Slide 16: Instruction Support for Functions (1/4)
... sum(a,b);... /* a,b:$s0,$s1 */ } int sum(int x, int y) { return x+y; }
address (shown in decimal) 1000 1004 1008 1012 1016 … 2000 2004
C
M I P S
In MIPS, all instructions are 4 bytes, and stored in memory just like data. So here we show the addresses of where the programs are stored.

## Slide 17: Instruction Support for Functions (2/4)
... sum(a,b);... /* a,b:$s0,$s1 */ } int sum(int x, int y) { return x+y; }
address (shown in decimal) 1000 add $a0,$s0,$zero # x = a 1004 add $a1,$s1,$zero # y = b 1008 addi $ra,$zero,1016 #$ra=1016 1012 j sum #jump to sum 1016 … # next instruction … 2000 sum: add $v0,$a0,$a1 2004 jr $ra # new instr. “jump register”
C
M I P S

## Slide 18: Instruction Support for Functions (3/4)
... sum(a,b);... /* a,b:$s0,$s1 */ } int sum(int x, int y) { return x+y; }
2000 sum: add $v0,$a0,$a1 2004 jr $ra # new instr. “jump register”
Question: Why use jr here? Why not use j?
Answer: sum might be called by many places, so we can’t return to a fixed place. The calling proc to sum must be able to say “return here” somehow.
C
M I P S

## Slide 19: Instruction Support for Functions (4/4)
Single instruction to jump and save return address: jump and link (jal)
Before: 1008 addi $ra,$zero,1016 #$ra=1016 1012 j sum #goto sum
After: 1008 jal sum # $ra=1012,goto sum
Why have a jal?
  Make the common case fast: function calls very common.
  Don’t have to know where code is in memory with jal!

## Slide 20: MIPS Function Call Instructions
Invoke function: jump and link instruction (jal)
(really should be laj “link and jump”)
  “link” means form an address or link that points to calling site to allow function to return to proper address
  Jumps to address and simultaneously saves the address of the following instruction in register $ra
  jal FunctionLabel
Return from function: jump register instruction (jr)
  Unconditional jump to address specified in register
  jr $ra

## Slide 21: Notes on Functions
Calling program (caller) puts parameters into registers $a0-$a3 and uses jal X to invoke (callee) at address labeled X
Must have register in computer with address of currently executing instruction
  Instead of Instruction Address Register (better name), historically called Program Counter (PC)
  It’s a program’s counter; it doesn’t count programs!
What value does jal X place into $ra? ????
jr $ra puts address inside $ra back into PC
Notes: PC+4

## Slide 22: Where Are Old Register Values Saved to Restore Them After Function Call?
Need a place to save old values before call function, restore them when return, and delete
Ideal is stack: last-in-first-out queue (e.g., stack of plates)
  Push: placing data onto stack
  Pop: removing data from stack
Stack in memory, so need register to point to it
$sp is the stack pointer in MIPS ($29)
Convention is grow from high to low addresses
  Push decrements $sp, Pop increments $sp

## Slide 23: Example
int Leaf (int g, int h, int i, int j)
{
int f;
f = (g + h) – (i + j);
return f;
}
Parameter variables g, h, i, and j in argument registers $a0, $a1, $a2, and $a3, and f in $s0
Assume need one temporary register $t0

## Slide 24: Stack Before, During, After Function
Need to save old values of $s0 and $t0
Contents of $s0
Contents of $t0

## Slide 25: MIPS Code for Leaf()
Leaf: addi $sp,$sp,-8 # adjust stack for 2 items
sw $t0, 4($sp) # save $t0 for use afterwards
sw $s0, 0($sp) # save $s0 for use afterwards
add $s0,$a0,$a1 # f = g + h
add $t0,$a2,$a3 # t0 = i + j
sub $v0,$s0,$t0 # return value (g + h) – (i + j)
lw $s0, 0($sp) # restore register $s0 for caller
lw $t0, 4($sp) # restore register $t0 for caller
addi $sp,$sp,8 # adjust stack to delete 2 items
jr $ra # jump back to calling routine

## Slide 26: What If a Function Calls a Function? Recursive Function Calls?
Would clobber values in $a0 to $a3 and $ra
What is the solution?
Notes: Save $ra on the stack

## Slide 27: Nested Procedures (1/2)
int sumSquare(int x, int y) { return mult(x,x)+ y; }
Something called sumSquare, now sumSquare is calling mult
So there’s a value in $ra that sumSquare wants to jump back to, but this will be overwritten by the call to mult
Need to save sumSquare return address before call to mult

## Slide 28: Nested Procedures (2/2)
In general, may need to save some other info in addition to $ra.
When a C program is run, there are 3 important memory areas allocated:
  Static: Variables declared once per program, cease to exist only after execution completes - e.g., C globals
  Heap: Variables declared dynamically via malloc
  Stack: Space to be used by procedure during execution; this is where we can save register values

## Slide 29: Optimized Function Convention
To reduce expensive loads and stores from spilling and restoring registers, MIPS divides registers into two categories:
Preserved across function call
  Caller can rely on values being unchanged
  $sp, $gp, $fp, “saved registers” $s0- $s7
Not preserved across function call
  Caller cannot rely on values being unchanged
  Return value registers $v0,$v1, Argument registers $a0-$a3, “temporary registers” $t0-$t9,$ra

## Slide 30: Clickers/Peer Instruction
Which statement is FALSE?
B: jal saves PC+1 in $ra
C: The callee can use temporary registers ($ti) without saving and restoring them
D: The caller can rely on save registers ($si) without fear of callee changing them
A: MIPS uses jal to invoke a function and jr to return from a function
Notes: B: Print It saves PC+4 …because instructions in this system are 4-bytes long and the actual address increments by 4 bytes even though it appears to only increment by one instruction.

## Slide 31: Allocating Space on Stack
C has two storage classes: automatic and static
  Automatic variables are local to function and discarded when function exits
  Static variables exist across exits from and entries to procedures
Use stack for automatic (local) variables that don’t fit in registers
Procedure frame or activation record: segment of stack with saved registers and local variables
Some MIPS compilers use a frame pointer ($fp) to point to first word of frame

## Slide 32: Stack Before, During, After Call

## Slide 33: Using the Stack (1/2)
So we have a register $sp which always points to the last used space in the stack.
To use stack, we decrement this pointer by the amount of space we need and then fill it with info.
So, how do we compile this?
  int sumSquare(int x, int y) { return mult(x,x)+ y; }

## Slide 34: Using the Stack (2/2)
Hand-compile sumSquare: addi $sp,$sp,-8 # space on stack sw $ra, 4($sp) # save ret addr sw $a1, 0($sp) # save y add $a1,$a0,$zero # mult(x,x) jal mult # call mult lw $a1, 0($sp) # restore y add $v0,$v0,$a1 # mult()+y lw $ra, 4($sp) # get ret addr addi $sp,$sp,8 # restore stack jr $ra mult: ...
  int sumSquare(int x, int y) { return mult(x,x)+ y; }
“push”
“pop”

## Slide 35: Basic Structure of a Function
entry_label: addi $sp,$sp, -framesize sw $ra, framesize-4($sp) # save $ra save other regs if need be
...
restore other regs if need be lw $ra, framesize-4($sp) # restore $ra addi $sp,$sp, framesize jr $ra
Epilogue
Prologue
Body (call other functions…)
ra
memory

## Slide 36: Where is the Stack in Memory?
MIPS convention
Stack starts in high memory and grows down
  Hexadecimal (base 16) : 7fff fffchex
MIPS programs (text segment) in low end
  0040 0000hex
static data segment (constants and other static variables) above text for static variables
  MIPS convention global pointer ($gp) points to static
Heap above static for data structures that grow and shrink ; grows up to high addresses

## Slide 37: MIPS Memory Allocation

## Slide 38: Register Allocation and Numbering

## Slide 39: And in Conclusion…
Functions called with jal, return with jr $ra.
The stack is your friend: Use it to save anything you need. Just leave it the way you found it!
Instructions we know so far…
  Arithmetic: add, addi, sub, addu, addiu, subu
  Memory: lw, sw, lb, sb
  Decision: beq, bne, slt, slti, sltu, sltiu
  Unconditional Branches (Jumps): j, jal, jr
Registers we know so far
  All of them!
  $a0-$a3 for function arguments, $v0-$v1 for return values
  $sp, stack pointer, $fp frame pointer, $ra return address

## Slide 40: Bonus Slides

## Slide 41: Recursive Function Factorial
int fact (int n)
{
if (n < 1) return (1);
else return (n * fact(n-1));
}

## Slide 42: Recursive Function Factorial
Fact: # adjust stack for 2 items
addi $sp,$sp,-8
# save return address
sw $ra, 4($sp) # save argument n
sw $a0, 0($sp) # test for n < 1
slti $t0,$a0,1
# if n >= 1, go to L1
beq $t0,$zero,L1 # Then part (n==1) return 1
addi $v0,$zero,1 # pop 2 items off stack
addi $sp,$sp,8 # return to caller
jr $ra
L1:
# Else part (n >= 1) # arg. gets (n – 1)
addi $a0,$a0,-1 # call fact with (n – 1)
jal Fact
# return from jal: restore n
lw $a0, 0($sp) # restore return address
lw $ra, 4($sp) # adjust sp to pop 2 items
addi $sp, $sp,8 # return n * fact (n – 1)
mul $v0,$a0,$v0 # return to the caller
jr $ra
mul is a pseudo instruction
Notes: Slti: set dst to 1 if src is less than imm (signed immediate)