## Slide 1: CS 61C: Great Ideas in Computer Architecture Running a Program - CALL (Compiling, Assembling, Linking, and Loading)
Instructors:
John Wawrzynek & Vladimir Stojanovic
http://inst.eecs.Berkeley.edu/~cs61c/fa15

## Slide 2: Review
I-Format: instructions with immediates, lw/sw (offset is immediate), and beq/bne
  But not the shift instructions
  Branches use PC-relative addressing
J-Format: j and jal (but not jr)
  Jumps use absolute addressing
R-Format: all other instructions
opcode
rs
rt
immediate
I:
opcode
target address
J:
opcode
funct
rs
rt
rd
shamt
R:

## Slide 3: Integer Multiplication (1/3)
Paper and pencil example (unsigned):
  Multiplicand 1000 8
  Multiplier x1001 9 1000 0000 0000 +1000 01001000 72
m bits x n bits = m + n bit product

## Slide 4: Integer Multiplication (2/3)
In MIPS, we multiply registers, so:
  32-bit value x 32-bit value = 64-bit value
Syntax of Multiplication (signed):
  mult register1, register2
  Multiplies 32-bit values in those registers & puts 64-bit product in special result registers:
    puts product upper half in hi, lower half in lo
  hi and lo are 2 registers separate from the 32 general purpose registers
  Use mfhi register & mflo register to move from hi, lo to another register

## Slide 5: Integer Multiplication (3/3)
Example:
  in C: a = b * c;
  in MIPS:
    let b be $s2; let c be $s3; and let a be $s0 and $s1 (since it may be up to 64 bits)
  mult $s2,$s3 # b*c
  mfhi $s0 # upper half of # product into $s0 mflo $s1 # lower half of # product into $s1
Note: Often, we only care about the lower half of the product
  Pseudo-inst. mul expands to mult/mflo

## Slide 6: Integer Division (1/2)
Paper and pencil example (unsigned):
  1001 Quotient Divisor 1000|1001010 Dividend -1000 10 101 1010 -1000 10 Remainder (or Modulo result)
Dividend = Quotient x Divisor + Remainder

## Slide 7: Integer Division (2/2)
Syntax of Division (signed):
  div register1, register2
  Divides 32-bit register 1 by 32-bit register 2:
  puts remainder of division in hi, quotient in lo
Implements C division (/) and modulo (%)
Example in C: a = c / d; b = c % d;
in MIPS: a↔$s0; b↔$s1; c↔$s2; d↔$s3
  div $s2,$s3 # lo=c/d, hi=c%d
  mflo $s0 # get quotient mfhi $s1 # get remainder

## Slide 8: Levels of Representation/Interpretation
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
High Level Language Program (e.g., C)
Assembly Language Program (e.g., MIPS)
Machine Language Program (MIPS)
Hardware Architecture Description (e.g., block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Architecture Implementation
Anything can be represented as a number, i.e., data or instructions
Logic Circuit Description (Circuit Schematic Diagrams)
+ How to take a program and run it

## Slide 9: Language Execution Continuum
An Interpreter is a program that executes other programs.
Language translation gives us another option
In general, we interpret a high-level language when efficiency is not critical and translate to a lower-level language to increase performance
Easy to program
Inefficient to interpret
Difficult to program
Efficient to interpret
Scheme Java C++
C
Assembly
Machine code
Java bytecode

## Slide 10: Interpretation vs Translation
How do we run a program written in a source language?
  Interpreter: Directly executes a program in the source language
  Translator: Converts a program from the source language to an equivalent program in another language
For example, consider a Python program foo.py

## Slide 11: Interpretation
Python interpreter is just a program that reads a python program and performs the functions of that python program.
Python program: foo.py
Python interpreter

## Slide 12: Interpretation
Any good reason to interpret machine language in software?
MARS– useful for learning / debugging
Apple Macintosh conversion
  Switched from Motorola 680x0 instruction architecture to PowerPC.
    Similar issue with switch to x86
  Could require all programs to be re-translated from high level language
  Instead, let executables contain old and/or new machine code, interpret old code in software if necessary (emulation)

## Slide 13: Interpretation vs. Translation? (1/2)
Generally easier to write interpreter
Interpreter closer to high-level, so can give better error messages (e.g., MARS)
  Translator reaction: add extra information to help debugging (line numbers, names)
Interpreter slower (10x?), code smaller (2x?)
Interpreter provides instruction set independence: run on any machine

## Slide 14: Interpretation vs. Translation? (2/2)
Translated/compiled code almost always more efficient and therefore higher performance:
  Important for many applications, particularly operating systems.
Translation/compilation helps “hide” the program “source” from the users:
  One model for creating value in the marketplace (eg. Microsoft keeps all their source code secret)
  Alternative model, “open source”, creates value by publishing the source code and fostering a community of developers.

## Slide 15: Steps in compiling a C program
C program: foo.c
Compiler
Executable (mach lang pgm): a.out
Memory
Assembly program: foo.s
Assembler
Object (mach lang module): foo.o
Linker
Loader
lib.o

## Slide 16: Compiler
Input: High-Level Language Code (e.g., foo.c)
Output: Assembly Language Code (e.g., foo.s for MIPS)
Note: Output may contain pseudo-instructions
Pseudo-instructions: instructions that assembler understands but not in machine For example:
  move $s1,$s2  add $s1,$s2,$zero

## Slide 17: Where Are We Now?
C program: foo.c
Compiler
Executable (mach lang pgm): a.out
Memory
Assembly program: foo.s
Assembler
Object (mach lang module): foo.o
Linker
Loader
lib.o
CS164

## Slide 18: Assembler
Input: Assembly Language Code (MAL) (e.g., foo.s for MIPS)
Output: Object Code, information tables (TAL) (e.g., foo.o for MIPS)
Reads and Uses Directives
Replace Pseudo-instructions
Produce Machine Language
Creates Object File

## Slide 19: Assembler Directives (p. A-51.. A-53)
Give directions to assembler, but do not produce machine instructions
  .text: Subsequent items put in user text segment (machine code)
  .data: Subsequent items put in user data segment (binary rep of data in source file)
  .globl sym: declares sym global and can be referenced from other files
  .asciiz str: Store the string str in memory and null-terminate it
  .word w1…wn: Store the n 32-bit quantities in successive memory words

## Slide 20: Pseudo-instruction Replacement
Assembler treats convenient variations of machine language instructions as if real instructions Pseudo: Real:
subu $sp,$sp,32 addiu $sp,$sp,-32
sd $a0, 32($sp) sw $a0, 32($sp) sw $a1, 36($sp)
mul $t7,$t6,$t5 mult $t6,$t5 mflo $t7
addu $t0,$t6,1 addiu $t0,$t6,1
ble $t0,100,loop slti $at,$t0,101 bne $at,$0,loop
la $a0, str lui $at,left(str) ori $a0,$at,right(str)

## Slide 21: Clicker/Peer Instruction
Which of the following is a correct TAL instruction sequence for la $v0, FOO?*
%hi(label), tells assembler to fill upper 16 bits of label’s addr
%lo(label), tells assembler to fill lower 16 bits of label’s addr
A: ori $v0, %hi(FOO)
addiu $v0, %lo(FOO)
B: ori $v0, %lo(FOO)
lui $v0, %hi(FOO)
C: lui $v0, %lo(FOO)
ori $v0, %hi(FOO)
D: lui $v0, %hi(FOO)
addiu $v0, %lo(FOO)
E: la $v0, FOO is already a TAL instruction
*Assume the address of FOO is 0xABCD0124

## Slide 22: Administrivia
HW1 out, due 9/27 @ 23:59:59
Proj 1 due today @ 23:59:59
  Make sure you test your code on hive machines, that’s where we’ll grade them
Proj 2 Team Registration on Piazza
Please fill-out Bitbucket EdX form on Piazza

## Slide 23: Producing Machine Language (1/3)
Simple Case
  Arithmetic, Logical, Shifts, and so on
  All necessary info is within the instruction already
What about Branches?
  PC-Relative
  So once pseudo-instructions are replaced by real ones, we know by how many instructions to branch
So these can be handled

## Slide 24: Producing Machine Language (2/3)
“Forward Reference” problem
  Branch instructions can refer to labels that are “forward” in the program:
  Solved by taking 2 passes over the program
    First pass remembers position of labels
    Second pass uses label positions to generate code
or $v0, $0, $0 L1: slt $t0, $0, $a1 beq $t0, $0, L2 addi $a1, $a1, -1 j L1 L2: add $t1, $a0, $a1

## Slide 25: Producing Machine Language (3/3)
What about jumps (j and jal)?
  Jumps require absolute address
  So, forward or not, still can’t generate machine instruction without knowing the position of instructions in memory
What about references to static data?
  la gets broken up into lui and ori
  These will require the full 32-bit address of the data
These can’t be determined yet, so we create two tables…

## Slide 26: Symbol Table
List of “items” in this file that may be used by other files
What are they?
  Labels: function calling
  Data: anything in the .data section; variables which may be accessed across files

## Slide 27: Relocation Table
List of “items” this file needs the address of later
What are they?
  Any label jumped to: j or jal
    internal
    external (including lib files)
  Any piece of data in static section
    such as the la instruction

## Slide 28: Object File Format
object file header: size and position of the other pieces of the object file
text segment: the machine code
data segment: binary representation of the static data in the source file
relocation information: identifies lines of code that need to be fixed up later
symbol table: list of this file’s labels and static data that can be referenced
debugging information
A standard format is ELF (except MS) http://www.skyfree.org/linux/references/ELF_Format.pdf

## Slide 29: Where Are We Now?
C program: foo.c
Compiler
Executable (mach lang pgm): a.out
Memory
Assembly program: foo.s
Assembler
Object (mach lang module): foo.o
Linker
Loader
lib.o

## Slide 30: Linker (1/3)
Input: Object code files, information tables (e.g., foo.o,libc.o for MIPS)
Output: Executable code (e.g., a.out for MIPS)
Combines several object (.o) files into a single executable (“linking”)
Enable separate compilation of files
  Changes to one file do not require recompilation of the whole program
    Windows NT source was > 40 M lines of code!
  Old name “Link Editor” from editing the “links” in jump and link instructions

## Slide 31: Linker (2/3)
.o file 1
text 1
data 1
info 1
.o file 2
text 2
data 2
info 2
Linker
a.out
Relocated text 1
Relocated text 2
Relocated data 1
Relocated data 2

## Slide 32: Linker (3/3)
Step 1: Take text segment from each .o file and put them together
Step 2: Take data segment from each .o file, put them together, and concatenate this onto end of text segments
Step 3: Resolve references
  Go through Relocation Table; handle each entry
  That is, fill in all absolute addresses

## Slide 33: Four Types of Addresses
PC-Relative Addressing (beq, bne)
  never relocate
Absolute Function Address (j, jal)
  always relocate
External Function Reference (usually jal)
  always relocate
Static Data Reference (often lui and ori)
  always relocate

## Slide 34: Absolute Addresses in MIPS
Which instructions need relocation editing?
  J-format: jump, jump and link
  Loads and stores to variables in static area, relative to global pointer
  What about conditional branches?
  PC-relative addressing preserved even if code moves
j/jal
xxxxx
lw/sw
$gp
$x
address
beq/bne
$rs
$rt
address

## Slide 35: Resolving References (1/2)
Linker assumes first word of first text segment is at address 0x04000000.
  (More later when we study “virtual memory”)
Linker knows:
  length of each text and data segment
  ordering of text and data segments
Linker calculates:
  absolute address of each label to be jumped to (internal or external) and each piece of data being referenced

## Slide 36: Resolving References (2/2)
To resolve references:
  search for reference (data or label) in all “user” symbol tables
  if not found, search library files (for example, for printf)
  once absolute address is determined, fill in the machine code appropriately
Output of linker: executable file containing text and data (plus header)

## Slide 37: Where Are We Now?
C program: foo.c
Compiler
Executable (mach lang pgm): a.out
Memory
Assembly program: foo.s
Assembler
Object (mach lang module): foo.o
Linker
Loader
lib.o

## Slide 38: Loader Basics
Input: Executable Code (e.g., a.out for MIPS)
Output: (program is run)
Executable files are stored on disk
When one is run, loader’s job is to load it into memory and start it running
In reality, loader is the operating system (OS)
  loading is one of the OS tasks

## Slide 39: Loader … what does it do?
Reads executable file’s header to determine size of text and data segments
Creates new address space for program large enough to hold text and data segments, along with a stack segment
Copies instructions and data from executable file into the new address space
Copies arguments passed to the program onto the stack
Initializes machine registers
  Most registers cleared, but stack pointer assigned address of 1st free stack location
Jumps to start-up routine that copies program’s arguments from stack to registers & sets the PC
  If main routine returns, start-up routine terminates program with the exit system call

## Slide 40: Clicker/Peer Instruction
At what point in process are all the machine code bits determined for the following assembly instructions:
1) addu $6, $7, $8
2) jal fprintf
A: 1) & 2) After compilation
B: 1) After compilation, 2) After assembly
C: 1) After assembly, 2) After linking
D: 1) After assembly, 2) After loading
E: 1) After compilation, 2) After linking

## Slide 41: Break

## Slide 42: Example: C  Asm  Obj  Exe  Run
#include <stdio.h>
int main (int argc, char *argv[]) {
int i, sum = 0;
for (i = 0; i <= 100; i++) sum = sum + i * i;
printf ("The sum of sq from 0 .. 100 is %d\n", sum);
}
C Program Source Code: prog.c
“printf” lives in “libc”

## Slide 43: Compilation: MAL
.text
.align 2
.globl main
main:
subu $sp,$sp,32
sw $ra, 20($sp)
sd $a0, 32($sp)
sw $0, 24($sp)
sw $0, 28($sp)
loop:
lw $t6, 28($sp)
mul $t7, $t6,$t6
lw $t8, 24($sp)
addu $t9,$t8,$t7
sw $t9, 24($sp)
addu $t0, $t6, 1
sw $t0, 28($sp)
ble $t0,100, loop
la $a0, str
lw $a1, 24($sp)
jal printf
move $v0, $0
lw $ra, 20($sp)
addiu $sp,$sp,32
jr $ra
.data
.align 0
str:
.asciiz "The sum of sq from 0 .. 100 is %d\n"
Where are
7 pseudo- instructions?

## Slide 44: Compilation: MAL
.text
.align 2
.globl main
main:
subu $sp,$sp,32
sw $ra, 20($sp)
sd $a0, 32($sp)
sw $0, 24($sp)
sw $0, 28($sp)
loop:
lw $t6, 28($sp)
mul $t7, $t6,$t6
lw $t8, 24($sp)
addu $t9,$t8,$t7
sw $t9, 24($sp)
addu $t0, $t6, 1
sw $t0, 28($sp)
ble $t0,100, loop
la $a0, str
lw $a1, 24($sp)
jal printf
move $v0, $0
lw $ra, 20($sp)
addiu $sp,$sp,32
jr $ra
.data
.align 0
str:
.asciiz "The sum of sq from 0 .. 100 is %d\n"
7 pseudo- instructions underlined

## Slide 45: Assembly step 1:
00 addiu $29,$29,-32
04 sw $31,20($29)
08 sw $4, 32($29)
0c sw $5, 36($29)
10 sw $0, 24($29)
14 sw $0, 28($29)
18 lw $14, 28($29)
1c multu $14, $14
20 mflo $15
24 lw $24, 24($29)
28 addu $25,$24,$15
2c sw $25, 24($29)
30 addiu $8,$14, 1
34 sw $8,28($29)
38 slti $1,$8, 101
3c bne $1,$0, loop
40 lui $4, l.str
44 ori $4,$4,r.str
48 lw $5,24($29)
4c jal printf
50 add $2, $0, $0
54 lw $31,20($29)
58 addiu $29,$29,32
5c jr $31
Remove pseudoinstructions, assign addresses

## Slide 46: Assembly step 2
Symbol Table
  Label address (in module) type
  main: 0x00000000 global text
  loop: 0x00000018 local text
  str: 0x00000000 local data
Relocation Information
  Address Instr. type Dependency 0x00000040 lui l.str 0x00000044 ori r.str 0x0000004c jal printf
Create relocation table and symbol table

## Slide 47: Assembly step 3
00 addiu $29,$29,-32
04 sw $31,20($29)
08 sw $4, 32($29)
0c sw $5, 36($29)
10 sw $0, 24($29)
14 sw $0, 28($29)
18 lw $14, 28($29)
1c multu $14, $14
20 mflo $15
24 lw $24, 24($29)
28 addu $25,$24,$15
2c sw $25, 24($29)
30 addiu $8,$14, 1
34 sw $8,28($29)
38 slti $1,$8, 101
3c bne $1,$0, -10
40 lui $4, l.str
44 ori $4,$4,r.str
48 lw $5,24($29)
4c jal printf
50 add $2, $0, $0
54 lw $31,20($29)
58 addiu $29,$29,32
5c jr $31
Resolve local PC-relative labels

## Slide 48: Assembly step 4
Generate object (.o) file:
  Output binary representation for
    text segment (instructions)
    data segment (data)
    symbol and relocation tables
  Using dummy “placeholders” for unresolved absolute and external references

## Slide 49: Text segment in object file
0x000000 00100111101111011111111111100000
0x000004 10101111101111110000000000010100
0x000008 10101111101001000000000000100000
0x00000c 10101111101001010000000000100100
0x000010 10101111101000000000000000011000
0x000014 10101111101000000000000000011100
0x000018 10001111101011100000000000011100
0x00001c 10001111101110000000000000011000
0x000020 00000001110011100000000000011001
0x000024 00100101110010000000000000000001
0x000028 00101001000000010000000001100101
0x00002c 10101111101010000000000000011100
0x000030 00000000000000000111100000010010
0x000034 00000011000011111100100000100001
0x000038 00010100001000001111111111110111
0x00003c 10101111101110010000000000011000
0x000040 00111100000001000000000000000000
0x000044 10001111101001010000000000000000
0x000048 00001100000100000000000011101100
0x00004c 00100100000000000000000000000000
0x000050 10001111101111110000000000010100
0x000054 00100111101111010000000000100000
0x000058 00000011111000000000000000001000
0x00005c 00000000000000000001000000100001

## Slide 50: Link step 1: combine prog.o, libc.o
Merge text/data segments
Create absolute memory addresses
Modify & merge symbol and relocation tables
Symbol Table
  Label Address
  main: 0x00000000
  loop: 0x00000018
  str: 0x10000430
  printf: 0x000003b0 …
Relocation Information
  Address Instr. Type Dependency 0x00000040 lui l.str 0x00000044 ori r.str 0x0000004c jal printf …

## Slide 51: Link step 2:
00 addiu $29,$29,-32
04 sw $31,20($29)
08 sw $4, 32($29)
0c sw $5, 36($29)
10 sw $0, 24($29)
14 sw $0, 28($29)
18 lw $14, 28($29)
1c multu $14, $14
20 mflo $15
24 lw $24, 24($29)
28 addu $25,$24,$15
2c sw $25, 24($29)
30 addiu $8,$14, 1
34 sw $8,28($29)
38 slti $1,$8, 101
3c bne $1,$0, -10
40 lui $4, 4096
44 ori $4,$4,1072
48 lw $5,24($29)
4c jal 812
50 add $2, $0, $0
54 lw $31,20($29)
58 addiu $29,$29,32
5c jr $31
Edit Addresses in relocation table
  (shown in TAL for clarity, but done in binary )

## Slide 52: Link step 3:
Output executable of merged modules
  Single text (instruction) segment
  Single data segment
  Header detailing size of each segment
NOTE:
  The preceeding example was a much simplified version of how ELF and other standard formats work, meant only to demonstrate the basic principles.

## Slide 53: Static vs Dynamically linked libraries
What we’ve described is the traditional way: statically-linked approach
  The library is now part of the executable, so if the library updates, we don’t get the fix (have to recompile if we have source)
  It includes the entire library even if not all of it will be used
  Executable is self-contained
An alternative is dynamically linked libraries (DLL), common on Windows & UNIX platforms

## Slide 54: Dynamically linked libraries
Space/time issues
  + Storing a program requires less disk space
  + Sending a program requires less time
  + Executing two programs requires less memory (if they share a library)
  – At runtime, there’s time overhead to do link
Upgrades
  + Replacing one file (libXYZ.so) upgrades every program that uses library “XYZ”
  – Having the executable isn’t enough anymore
Overall, dynamic linking adds quite a bit of complexity to the compiler, linker, and operating system. However, it provides many benefits that often outweigh these
en.wikipedia.org/wiki/Dynamic_linking

## Slide 55: Dynamically linked libraries
The prevailing approach to dynamic linking uses machine code as the “lowest common denominator”
  The linker does not use information about how the program or library was compiled (i.e., what compiler or language)
  This can be described as “linking at the machine code level”
  This isn’t the only way to do it ...

## Slide 56: In Conclusion…
C program: foo.c
Compiler
Executable (mach lang pgm): a.out
Memory
Assembly program: foo.s
Assembler
Object (mach lang module): foo.o
Linker
Loader
lib.o
Compiler converts a single HLL file into a single assembly language file.
Assembler removes pseudo-instructions, converts what it can to machine language, and creates a checklist for the linker (relocation table). A .s file becomes a .o file.
  Does 2 passes to resolve addresses, handling internal forward references
Linker combines several .o files and resolves absolute addresses.
  Enables separate compilation, libraries that need not be compiled, and resolves remaining addresses
Loader loads executable into memory and begins execution.