## Slide 1: CS 61C: Great Ideas in Computer Architecture (Machine Structures) Caches Part 3
Instructors:
John Wawrzynek & Vladimir Stojanovic
http://inst.eecs.berkeley.edu/~cs61c/

## Slide 2: You Are Here!
Parallel Requests
  Assigned to computer
  e.g., Search “Katz”
Parallel Threads
  Assigned to core
  e.g., Lookup, Ads
Parallel Instructions
  >1 instruction @ one time
  e.g., 5 pipelined instructions
Parallel Data
  >1 data item @ one time
  e.g., Add of 4 pairs of words
Hardware descriptions
  All gates @ one time
Programming Languages
Smart Phone
Warehouse Scale Computer
Software Hardware
Harness Parallelism &
Achieve High Performance
Logic Gates
Core
Core
…
Memory (Cache)
Input/Output
Computer
Main Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A3+B3
A2+B2
A1+B1
A0+B0
Today’s
Lecture

## Slide 3: Review from Last Lecture
Cache Organization
Cache Capacity
Cache Addressing
Cache write policies
AMAT (average memory access time)

## Slide 4: Different Organizations of an Eight-Block Cache
Total size of $ in blocks is equal to number of sets × associativity. For fixed $ size and fixed block size, increasing associativity decreases number of sets while increasing number of elements per set. With eight blocks, an 8-way set-associative $ is same as a fully associative $.

## Slide 5: Total Cache Capacity =
Associativity × # of sets × block_size
Bytes = blocks/set × sets × Bytes/block
Byte Offset
Tag
Index
C = N × S × B
address_size = tag_size + index_size + offset_size
= tag_size + log2(S) + log2(B)

## Slide 6: Write Policy Choices
Cache hit:
  write through: writes both cache & memory on every access
    Generally higher memory traffic but simpler pipeline & cache design
  write back: writes cache only, memory `written only when dirty entry evicted
    A dirty bit per line reduces write-back traffic
    Must handle 0, 1, or 2 accesses to memory for each load/store
Cache miss:
  no write allocate: only write to main memory
  write allocate (aka fetch on write): fetch into cache
Common combinations:
  write through and no write allocate
  write back with write allocate

## Slide 7: Average Memory Access Time (AMAT)
Average Memory Access Time (AMAT) is the average time to access memory considering both hits and misses in the cache
  AMAT = Time for a hit + Miss rate × Miss penalty
Notes: AMAT = 1 + 0.02x50 = 2

## Slide 8: Today
Cache Replacement Policies
Understanding Cache misses
Increasing Cache Performance
Performance of multi-level Caches (L1,L2, …)
Real world example caches

## Slide 9: Four-Way Set-Associative Cache
28 = 256 sets each with four ways (each with one block)
31 30 . . . 13 12 11 . . . 2 1 0
Byte offset
Data
Tag
V
0
1
2
.
.
.
253
254
255
Data
Tag
V
0
1
2
.
.
.
253
254
255
Data
Tag
V
0
1
2
.
.
.
253
254
255
Index
Data
Tag
V
0
1
2
.
.
.
253
254
255
8
Index
22
Tag
Hit
Data
32
4x1 select
Way 0
Way 1
Way 2
Way 3
Notes: This is called a 4-way set associative cache because there are four cache entries for each cache index. Essentially, you have four direct mapped cache working in parallel.
This is how it works: the cache index selects a set from the cache. The four tags in the set are compared in parallel with the upper bits of the memory address.
If no tags match the incoming address tag, we have a cache miss.
Otherwise, we have a cache hit and we will select the data from the way where the tag matches occur.
This is simple enough. What is its disadvantages?
+1 = 36 min. (Y:16)

## Slide 10: Costs of Set-Associative Caches
N-way set-associative cache costs
  N comparators (delay and area)
  MUX delay (set selection) before data is available
  Data available after set selection (and Hit/Miss decision). DM $: block is available before the Hit/Miss decision
    In Set-Associative, not possible to just assume a hit and continue and recover later if it was a miss
When miss occurs, which way’s block selected for replacement?
  Least Recently Used (LRU): one that has been unused the longest (principle of temporal locality)
    Must track when each way’s block was used relative to other blocks in the set
    For 2-way SA $, one bit per set → set to 1 when a block is referenced; reset the other way’s bit (i.e., “last used”)
Notes: First of all, a N-way set associative cache will need N comparators instead of just one comparator (use the right side of the diagram for direct mapped cache).
A N-way set associative cache will also be slower than a direct mapped cache because of this extra multiplexer delay.
Finally, for a N-way set associative cache, the data will be available AFTER the hit/miss signal becomes valid because the hit/mis is needed to control the data MUX.
For a direct mapped cache, that is everything before the MUX on the right or left side, the cache block will be available BEFORE the hit/miss signal (AND gate output) because the data does not have to go through the comparator.
This can be an important consideration because the processor can now go ahead and use the data without knowing if it is a Hit or Miss. Just assume it is a hit.
Since cache hit rate is in the upper 90% range, you will be ahead of the game 90% of the time and for those 10% of the time that you are wrong, just make sure you can recover.
You cannot play this speculation game with a N-way set-associative cache because as I said earlier, the data will not be available to you until the hit/miss signal is valid.
+2 = 38 min. (Y:18)

## Slide 11: Cache Replacement Policies
Random Replacement
  Hardware randomly selects a cache evict
Least-Recently Used
  Hardware keeps track of access history
  Replace the entry that has not been used for the longest time
  For 2-way set-associative cache, need one bit for LRU replacement
Example of a Simple “Pseudo” LRU Implementation
  Assume 64 Fully Associative entries
  Hardware replacement pointer points to one cache entry
  Whenever access is made to the entry the pointer points to:
    Move the pointer to the next entry
  Otherwise: do not move the pointer
  (example of “not-most-recently used” replacement policy)
:
Entry 0
Entry 1
Entry 63
Replacement
Pointer

## Slide 12: Benefits of Set-Associative Caches
Largest gains are in going from direct mapped to 2-way (20%+ reduction in miss rate)
Notes: As cache sizes grow, the relative improvement from associativity increases only slightly; since the overall miss rate of a larger cache is lower, the opportunity for improving the miss rate decreases and the absolute improvement in miss rate from associativity shrinks significantly.

## Slide 13: Sources of Cache Misses (3 C’s)
Compulsory (cold start, first reference):
  1st access to a block, not a lot you can do about it.
    If running billions of instructions, compulsory misses are insignificant
Capacity:
  Cache cannot contain all blocks accessed by the program
    Misses that would not occur with infinite cache
Conflict (collision):
  Multiple memory locations mapped to same cache set
    Misses that would not occur with ideal fully associative cache
Notes: (Capacity miss) That is the cache misses are due to the fact that the cache is simply not large enough to contain all the blocks that are accessed by the program.
The solution to reduce the Capacity miss rate is simple: increase the cache size.
Here is a summary of other types of cache miss we talked about.
First is the Compulsory misses. These are the misses that we cannot avoid. They are caused when we first start the program.
Then we talked about the conflict misses. They are the misses that caused by multiple memory locations being mapped to the same cache location.
There are two solutions to reduce conflict misses. The first one is, once again, increase the cache size. The second one is to increase the associativity.
For example, say using a 2-way set associative cache instead of directed mapped cache.
But keep in mind that cache miss rate is only one part of the equation. You also have to worry about cache access time and miss penalty. Do NOT optimize miss rate alone.
Finally, there is another source of cache miss we will not cover today. Those are referred to as invalidation misses caused by another process, such as IO , update the main memory so you have to flush the cache to avoid inconsistency between memory and cache.
+2 = 43 min. (Y:23)

## Slide 14: How to Calculate 3C’s using Cache Simulator
Compulsory: set cache size to infinity and fully associative, and count number of misses
Capacity: Change cache size from infinity, usually in powers of 2, and count misses for each reduction in size
  16 MB, 8 MB, 4 MB, … 128 KB, 64 KB, 16 KB
Conflict: Change from fully associative to n-way set associative while counting misses
  Fully associative, 16-way, 8-way, 4-way, 2-way, 1-way

## Slide 15: 3Cs Analysis
Three sources of misses (SPEC2000 integer and floating-point benchmarks)
  Compulsory misses 0.006%; not visible
  Capacity misses, function of cache size
  Conflict portion depends on associativity and cache size

## Slide 16: Administrivia
Project 3-2, delayed. Posted Sunday 10/25 now due 11/1.
Lab 7 will help you with the CPU project (do it before the project).
No Midterm I regrade requests after 10/25 (Sunday).

## Slide 17: CPU-Cache Interaction (5-stage pipeline)
PC
addr
inst
Primary
Instruction
Cache
0x4
Add
IR
D
bubble
hit?
  PCen
Decode,
Register
Fetch
wdata
R
addr
wdata
rdata
Primary
Data
Cache
we
A
B
Y
Y
ALU
MD1
MD2
Cache Refill Data from Lower Levels of Memory Hierarchy
hit?
Stall entire CPU on data cache miss
To Memory Control
M
E
Notes: How are writes to istream handled?

## Slide 18: Improving Cache Performance
Reduce the time to hit in the cache
  E.g., Smaller cache
Reduce the miss rate
  E.g., Bigger cache
Reduce the miss penalty
  E.g., Use multiple cache levels
  AMAT = Time for a hit + Miss rate x Miss penalty

## Slide 19: Cache Design Space
Several interacting dimensions
  Cache size
  Block size
  Associativity
  Replacement policy
  Write-through vs. write-back
  Write allocation
Optimal choice is a compromise
  Depends on access characteristics
    Workload
    Use (I-cache, D-cache)
  Depends on technology / cost
Simplicity often wins
Associativity
Cache Size
Block Size
Bad
Good
Less
More
Factor A
Factor B
Computer architects expend considerable effort optimizing organization of cache hierarchy – big impact on performance and power!
Notes: No fancy replacement policy is needed for the direct mapped cache.
As a matter of fact, that is what cause direct mapped trouble to begin with: only one place to go in the cache--causes conflict misses.
No fancy replacement policy is needed for the direct mapped cache.
As a matter of fact, that is what cause direct mapped trouble to begin with: only one place to go in the cache--causes conflict misses.
Besides working at Sun, I also teach people how to fly whenever I have time.
Statistic have shown that if a pilot crashed after an engine failure, he or she is more likely to get killed in a multi-engine light airplane than a single engine airplane.
The joke among us flight instructors is that: sure, when the engine quit in a single engine stops, you have one option: sooner or later, you land. Probably sooner.
But in a multi-engine airplane with one engine stops, you have a lot of options. It is the need to make a decision that kills those people.

## Slide 20: Primary Cache Parameters
Block size
  how many bytes of data in each cache entry?
Associativity
  how many ways in each set?
  Direct-mapped => Associativity = 1
  Set-associative => 1 < Associativity < #Entries
  Fully associative => Associativity = #Entries
Capacity (bytes) = Total #Entries * Block size
#Entries = #Sets * Associativity

## Slide 21: Clickers/Peer Instruction: For fixed capacity and fixed block size, how does increasing associativity effect AMAT?
A: Increases hit time, decreases miss rate
B: Decreases hit time, decreases miss rate
C: Increases hit time, increases miss rate
D: Decreases hit time, increases miss rate

## Slide 22: Increasing Associativity?
Hit time as associativity increases?
  Increases, with large step from direct-mapped to >=2 ways, as now need to mux correct way to processor
  Smaller increases in hit time for further increases in associativity
Miss rate as associativity increases?
  Goes down due to reduced conflict misses, but most gain is from 1->2->4-way with limited benefit from higher associativities
Miss penalty as associativity increases?
  Unchanged, replacement policy runs in parallel with fetching missing line from memory

## Slide 23: Increasing #Entries?
Hit time as #entries increases?
  Increases, since reading tags and data from larger memory structures
Miss rate as #entries increases?
  Goes down due to reduced capacity and conflict misses
  Architects rule of thumb: miss rate drops ~2x for every ~4x increase in capacity (only a gross approximation)
Miss penalty as #entries increases?
  Unchanged
At some point, increase in hit time for a larger cache may overcome the improvement in hit rate, yielding a decrease in performance

## Slide 24: Clickers: Impact of larger blocks on AMAT
For fixed total cache capacity and associativity, what is effect of larger blocks on each component of AMAT:
  A: Decrease, B: Unchanged, C: Increase
Hit Time?
Miss Rate?
Miss Penalty?

## Slide 25: Clickers: Impact of larger cache blocks on misses?
For fixed total cache capacity and associativity, what is effect of larger blocks on each type of miss rate:
  A: Decrease, B: Unchanged, C: Increase
Compulsory?
Capacity?
Conflict?

## Slide 26: Increasing Block Size?
Hit time as block size increases?
  Hit time unchanged, but might be slight hit-time reduction as number of tags is reduced, so faster to access memory holding tags
Miss rate as block size increases?
  Goes down at first due to spatial locality, then increases due to increased conflict misses due to fewer blocks in cache
Miss penalty as block size increases?
  Rises with longer block size, but with fixed constant initial latency that is amortized over whole block

## Slide 27: How to Reduce Miss Penalty?
Could there be locality on misses from a cache?
Use multiple cache levels!
With Moore’s Law, more room on die for bigger L1 caches and for second-level (L2) cache
And in some cases even an L3 cache!
IBM mainframes have ~1GB L4 cache off-chip.

## Slide 28: Review: Memory Hierarchy
Processor
Size of memory at each level
Increasing distance from processor, decreasing speed
Level 1
Level 2
Level n
Level 3
. . .
Inner
Outer
Levels in memory hierarchy
As we move to outer levels the latency goes up and price per bit goes down.

## Slide 29: From Lecture 11: In the News
At ISSCC 2015 in San Francisco this year, latest IBM mainframe chip details
z13 designed in 22nm SOI technology with seventeen metal layers, 4 billion transistors/chip
8 cores/chip, with 2MB L2 cache, 64MB L3 cache, and 480MB L4 off-chip cache.
5GHz clock rate, 6 instructions per cycle, 2 threads/core
Up to 24 processor chips in shared memory node

## Slide 30: IBM z13 Memory Hierarchy

## Slide 31: Local vs. Global Miss Rates
Local miss rate – the fraction of references to one level of a cache that miss
  Local Miss rate L2$ = L2$ Misses / L1$ Misses = L2$ Misses / total_L2_accesses
Global miss rate – the fraction of references that miss in all levels of a multilevel cache
    L2$ local miss rate >> than the global miss rate

## Slide 32
L1 Cache: 32KB I$, 32KB D$
L2 Cache: 256 KB
L3 Cache: 4 MB

## Slide 33: Local vs. Global Miss Rates
Local miss rate – the fraction of references to one level of a cache that miss
  Local Miss rate L2$ = $L2 Misses / L1$ Misses
Global miss rate – the fraction of references that miss in all levels of a multilevel cache
    L2$ local miss rate >> than the global miss rate
  Global Miss rate = L2$ Misses / Total Accesses
  = (L2$ Misses / L1$ Misses) × (L1$ Misses / Total Accesses)
  = Local Miss rate L2$ × Local Miss rate L1$
  AMAT = Time for a hit + Miss rate × Miss penalty
  AMAT = Time for a L1$ hit + (local) Miss rate L1$ × (Time for a L2$ hit + (local) Miss rate L2$ × L2$ Miss penalty)

## Slide 34: Clickers/Peer Instruction
Overall, what are L2 and L3 local miss rates?
A: L2 > 50%, L3 > 50%
B: L2 ~ 50%, L3 < 50%
C: L2 ~ 50%, L3 ~ 50%
D: L2 < 50%, L3 < 50%
E: L2 > 50%, L3 ~50%

## Slide 36: CPI/Miss Rates/DRAM Access SpecInt2006
Instructions and Data
Data Only
Data Only

## Slide 37: In Conclusion, Cache Design Space
Several interacting dimensions
  Cache size
  Block size
  Associativity
  Replacement policy
  Write-through vs. write-back
  Write-allocation
Optimal choice is a compromise
  Depends on access characteristics
    Workload
    Use (I-cache, D-cache)
  Depends on technology / cost
Simplicity often wins
Associativity
Cache Size
Block Size
Bad
Good
Less
More
Factor A
Factor B