## Slide 1: CS 61C: Great Ideas in Computer Architecture (Machine Structures) Lecture 24 More I/O: DMA, Disks, Networking
Instructors: John Wawrzynek & Vladimir Stojanovic
http://inst.eecs.berkeley.edu/~cs61c/
Notes: Hookup sound

## Slide 2: Virtual Memory Review

## Slide 3: Modern Virtual Memory Systems Illusion of a large, private, uniform store
Protection & Privacy
  * Many processes, each with their own private address space and one or more shared address spaces
Demand Paging
  * Many processes share DRAM.
  * Provides ability to run programs with large address space. Pages that aren’t yet allocated or pages that don’t fit swap to secondary storage.
  * Hides differences in machine configurations
The price is address translation on
each memory reference
OS
Prog1
Primary
Memory
Swapping Store (Disk)
VA
PA
mapping
TLB
Notes: Portability on machines with different memory configurations.

## Slide 4: Private (Virtual) Address Space per Program
Each prog has a page table
Page table contains an entry for each prog page
VA1
Prog 1
Page Table
VA1
Prog 2
Page Table
VA1
Prog 3
Page Table
Physical Memory
free
OS
pages
Notes: Pages are fixed sized chunks. So no fragmentation in terms of pages

## Slide 5: Translation Lookaside Buffers (TLB)
Address translation is very expensive!
  In a two-level page table, each reference becomes several memory accesses
Solution: Cache translations in TLB
TLB hit  Single-Cycle Translation
TLB miss  Page-Table Walk to refill
VPN offset
V R W D tag PPN
physical address
PPN offset
virtual address
hit?
(VPN = virtual page number)
(PPN = physical page number)
Notes: 3 memory references
2 page faults (disk accesses) + ..
Actually used in IBM before paged memory.

## Slide 6: Page-Based Virtual-Memory Machine (Hardware Page-Table Walk)
PC
Inst. TLB
Inst. Cache
D
Decode
E
M
Data Cache
W
+
Page Fault?
Protection violation?
Page Fault?
Protection violation?
Page tables held in untranslated physical memory
Data TLB
Main Memory (DRAM)
Memory Controller
Physical Address
Physical Address
Physical Address
Physical Address
Page-Table Base Register
Virtual Address
Physical Address
Virtual Address
Hardware Page Table Walker
Miss?
Miss?

## Slide 7: Clicker Question from Last Week
Let’s try to extrapolate from caches… Which one is false?
A. # offset bits in V.A. = log2(page size)
B. # offset bits in P.A. = log2(page size)
C. # VPN bits in V.A. = log2(# of physical pages)
D. # PPN bits in P.A. = log2(# of physical pages)
E. A single-level page table contains a PTE for every possible VPN in a particular Virtual Address Space
Notes: C. it’s the # of virtual pages, which is != to # of physical pages

## Slide 8: Review: I/O
“Memory mapped I/O”: Device control/data registers mapped to CPU address space
CPU synchronizes with I/O device:
  Polling
  Interrupts
“Programmed I/O”:
  CPU execs lw/sw instructions for all data movement to/from devices
  CPU spends time doing 2 things:
    Getting data from device to main memory
    Using data to compute

## Slide 9: Working with real devices
“Memory mapped I/O”: Device control/data registers mapped to CPU address space
CPU synchronizes with I/O device:
  Polling
  Interrupts
“Programmed I/O”: DMA
  CPU execs lw/sw instructions for all data movement to/from devices
  CPU spends time doing 2 things:
    Getting data from device to main memory
    Using data to compute

## Slide 10: Agenda
Direct Memory Access (DMA)
Disks
Networking

## Slide 11: What’s wrong with Programmed I/O?
Not ideal because …
  CPU has to execute all transfers, could be doing other work
  Device speeds don’t align well with CPU speeds
  Energy cost of using beefy general-purpose CPU where simpler hardware would suffice
Until now CPU has sole control of main memory

## Slide 12: PIO vs. DMA

## Slide 13: Direct Memory Access (DMA)
Allows I/O devices to directly read/write main memory
New Hardware: the DMA Engine
DMA engine contains registers written by CPU:
  Memory address to place data
  # of bytes
  I/O device #, direction of transfer
  unit of transfer, amount to transfer per burst

## Slide 14: Operation of a DMA Transfer
[From Section 5.1.4 Direct Memory Access in Modern Operating Systems by Andrew S. Tanenbaum, Herbert Bos, 2014]

## Slide 15: DMA: Incoming Data
Receive interrupt from device
CPU takes interrupt, begins transfer
  Instructs DMA engine/device to place data @ certain address
Device/DMA engine handle the transfer
  CPU is free to execute other things
Upon completion, Device/DMA engine interrupt the CPU again

## Slide 16: DMA: Outgoing Data
CPU decides to initiate transfer, confirms that external device is ready
CPU begins transfer
  Instructs DMA engine/device that data is available @ certain address
Device/DMA engine handle the transfer
  CPU is free to execute other things
Device/DMA engine interrupt the CPU again to signal completion

## Slide 17: DMA: Some new problems
Where in the memory hierarchy do we plug in the DMA engine? Two extremes:
  Between L1 and CPU:
    Pro: Free coherency
    Con: Trash the CPU’s working set with transferred data
  Between Last-level cache and main memory:
    Pro: Don’t mess with caches
    Con: Need to explicitly manage coherency

## Slide 18: DMA: Some new problems
How do we arbitrate between CPU and DMA Engine/Device access to memory? Three options:
  Burst Mode
    Start transfer of data block, CPU cannot access memory in the meantime
  Cycle Stealing Mode
    DMA engine transfers a byte, releases control, then repeats - interleaves processor/DMA engine accesses
  Transparent Mode
    DMA transfer only occurs when CPU is not using the system bus

## Slide 19: Administrivia
Upcoming Lecture Schedule
  11/24: I/O: DMA, Disks, Networking (today)
  11/26: Thanksgiving Holiday
  12/01: Dependability: Parity, ECC, RAID
    Last day of new material
  12/03: Summary, What’s Next? (+ HKN reviews)

## Slide 20: Administrivia
Last HW (5) Virtual Memory
  Due 12/06 (Sunday after end of classes)
Last project (5): Spark
  5-1: posted, due today!
  5-2: due 12/06 (Sunday after end of classes)
Final Exam is Friday (12/18)
  7-10PM, RSF Field House
  More info soon on review sessions, etc.

## Slide 21: Agenda
Direct Memory Access (DMA)
Disks
Networking

## Slide 22: Computer Memory Hierarchy
Today

## Slide 23: Magnetic Disk – common I/O device
A kind of computer memory
  Information stored by magnetizing ferrite material on surface of rotating disk
    similar to tape recorder except digital rather than analog data
A type of non-volatile storage
  retains its value without applying power to disk.
Two Types of Magnetic Disk
  Hard Disk Drives (HDD) – faster, more dense, non-removable.
  Floppy disks – slower, less dense, removable (now replaced by USB “flash drive”).
Purpose in computer systems (Hard Drive):
  Working file system + long-term backup for files
  Secondary “backing store” for main-memory. Large, inexpensive, slow level in the memory hierarchy (virtual memory)

## Slide 24: Photo of Disk Head, Arm, Actuator
Actuator
Arm
Head
Platters (1-12)
{
Spindle

## Slide 25: Disk Device Terminology
Several platters, with information recorded magnetically on both surfaces (usually)
Bits recorded in tracks, which in turn divided into sectors (e.g., 512 Bytes)
Actuator moves head (end of arm) over track (“seek”), wait for sector rotate under head, then read or write
Outer
Track
Inner
Track
Sector
Actuator
Head
Arm
Platter
Video of hard disk in action
Notes: arm interaction with platter

## Slide 26
Hard Drives are Sealed. Why?
The closer the head to the disk, the smaller the “spot size” and thus the denser the recording.
  Measured in Gbit/in^2
  ~900 Gbit/in^2 is state of the art
  Started out at 2 Kbit/in^2
  ~450,000,000x improvement in ~60 years
Disks are sealed to keep the dust out.
  Heads are designed to “fly” at around 3-20nm above the surface of the disk.
  99.999% of the head/arm weight is supported by the air bearing force (air cushion) developed between the disk and the head.
3-20nm

## Slide 27: Disk Device Performance (1/2)
Disk Access Time = Seek Time + Rotation Time + Transfer Time + Controller Overhead
  Seek Time = time to position the head assembly at the proper cylinder
  Rotation Time = time for the disk to rotate to the point where the first sectors of the block to access reach the head
  Transfer Time = time taken by the sectors of the block and any gaps between them to rotate past the head
Platter
Arm
Actuator
Head
Sector
Inner
Track
Outer
Track
Controller
Spindle
Notes: Use analogy to records

## Slide 28: Disk Device Performance (2/2)
Average values to plug into the formula:
Rotation Time: Average distance of sector from head?
  1/2 time of a rotation
    7200 Revolutions Per Minute  120 Rev/sec
    1 revolution = 1/120 sec  8.33 milliseconds
    1/2 rotation (revolution)  4.17 ms
Seek time: Average no. tracks to move arm?
  Number of tracks/3 (see CS186 for the math)
  Then, seek time = number of tracks moved × time to move across one track

## Slide 29: But wait!
Performance estimates are different in practice:
Many disks have on-disk caches, which are completely hidden from the outside world
  Previous formula completely replaced with on-disk cache access time

## Slide 30: Where does Flash memory come in?
~10 years ago: Microdrives and Flash memory (e.g., CompactFlash) went head-to-head
  Both non-volatile (retains contents without power supply)
  Flash benefits: lower power, no crashes (no moving parts, need to spin µdrives up/down)
  Disk cost = fixed cost of motor + arm mechanics, but actual magnetic media cost very low
  Flash cost = most cost/bit of flash chips
  Over time, cost/bit of flash came down, became cost competitive

## Slide 31: Flash Memory / SSD Technology
NMOS transistor with an additional conductor between gate and source/drain which “traps” electrons. The presence/absence is a 1 or 0
Memory cells can withstand a limited number of program-erase cycles. Controllers use a technique called wear leveling to distribute writes as evenly as possible across all the flash blocks in the SSD.

## Slide 32: What did Apple put in its iPods?
Samsung flash 16 GB
shuffle nano classic touch
Toshiba 1.8-inch HDD 80, 120, 160 GB
Toshiba flash 2 GB
Toshiba flash 32, 64 GB

## Slide 33: Flash Memory in Smart Phones
iPhone 6: up to 128 GB

## Slide 34: Flash Memory in Laptops – Solid State Drive (SSD)
capacities up to 512GB

## Slide 35: iClicker Question
We have the following disk:
  15000 Cylinders, 1 ms to cross 1000 Cylinders
  15000 RPM = 4 ms per rotation
  Want to copy 1 MB, transfer rate of 1000 MB/s
  1 ms controller processing time
What is the access time using our model?
Disk Access Time = Seek Time + Rotation Time + Transfer Time + Controller Processing Time
A | B | C | D | E
10.5 ms | 9 ms | 8.5 ms | 11.4 ms | 12 ms

## Slide 36: iClicker Question
We have the following disk:
  15000 Cylinders, 1 ms to cross 1000 Cylinders
  15000 RPM = 4 ms per rotation
  Want to copy 1 MB, transfer rate of 1000 MB/s
  1 ms controller processing time
What is the access time?
Seek = # cylinders/3 * time = 15000/3 * 1ms/1000 cylinders = 5ms
Rotation = time for ½ rotation = 4 ms / 2 = 2 ms
Transfer = Size / transfer rate = 1 MB / (1000 MB/s) = 1 ms
Controller = 1 ms
Total = 5 + 2 + 1 + 1 = 9 ms
Notes: on the order of 10 million times slower than the cpu

## Slide 37: Break

## Slide 38: Agenda
Direct Memory Access (DMA)
Disks
Networking

## Slide 39: Networks: Talking to the Outside World
Originally sharing I/O devices between computers
  E.g., printers
Then communicating between computers
  E.g., file transfer protocol
Then communicating between people
  E.g., e-mail
Then communicating between networks of computers
  E.g., file sharing, www, …
Notes: Original printers were the size of bathrooms - HAD to share
FTP was the first time file sharing happened
Communicating between people has become dominant, pervasive, ubiquitous
- Also IM
Last bullet is where a lot of research is happening

## Slide 40: The Internet (1962)
History
  1963: JCR Licklider, while at DoD’s ARPA, writes a memo describing desire to connect the computers at various research universities: Stanford, Berkeley, UCLA, ...
  1969 : ARPA deploys 4 “nodes” @ UCLA, SRI, Utah, & UCSB
  1973 Robert Kahn & Vint Cerf invent TCP, now part of the Internet Protocol Suite
Internet growth rates
  Exponential since start!
www.computerhistory.org/internet_history
www.greatachievements.org/?id=3736 en.wikipedia.org/wiki/Internet_Protocol_Suite
“Lick”
Vint Cerf
“Revolutions like this don't come along very often”

## Slide 41: The World Wide Web (1989)
“System of interlinked hypertext documents on the Internet”
History
  1945: Vannevar Bush describes hypertext system called “memex” in article
  1989: Sir Tim Berners-Lee proposed and implemented the first successful communication between a Hypertext Transfer Protocol (HTTP) client and server using the internet.
  ~2000 Dot-com entrepreneurs rushed in, 2001 bubble burst
Today : Access anywhere!
en.wikipedia.org/wiki/History_of_the_World_Wide_Web
Tim Berners-Lee
World’s First web server in 1990

## Slide 42: Shared vs. Switch-Based Networks
Shared vs. Switched:
  Shared: 1 at a time (CSMA/CD)
  Switched: pairs (“point-to-point” connections) communicate at same time
Aggregate bandwidth (BW) in switched network is many times that of shared:
  point-to-point faster since no arbitration, simpler interface
Node
Node
Node
Shared
Crossbar
Switch
Node
Node
Node
Node
Notes: CSMA/CD = Carrier Sense Multiple Access / Collision Detection
Bus: On collision, have to wait random amount of time
Buses not used very much, inefficient.
Switches are much more efficient
Bandwidth is like throughput

## Slide 43: What makes networks work?
links connecting switches and/or routers to each other and to computers or devices
Computer
network
interface
switch
switch
switch
ability to name the components and to route packets of information - messages - from a source to a destination
Layering, redundancy, protocols, and encapsulation as means of abstraction (61C big idea)
Notes: Computer has Network Interface Card (NIC)
Sends message through the series of switches, which get the message to recipient
Usually draw the series of switches as the “Internet Cloud”
- Represents an abstraction, “don’t know” implementation
- Send the message through the network, and it will get to where it needs to go
Switches use routing tables to know how to get the message to the recipient

## Slide 44: Software Protocol to Send and Receive
SW Send steps
  1: Application copies data to OS buffer
  2: OS calculates checksum, starts timer
  3: OS sends data to network interface HW and says start
SW Receive steps
  3: OS copies data from network interface HW to OS buffer
  2: OS calculates checksum, if OK, send ACK; if not, delete message (sender resends when timer expires)
  1: If OK, OS copies data to user address space, & signals application to continue
Header
Payload
Checksum
Trailer
CMD/ Address /Data
Net ID
Net ID
Len
ACK
INFO
Dest
Src
Notes: Timer is counting down on Time To Live (TTL)
- You can see this in Pings

## Slide 45: Networks are like Ogres
https://www.youtube.com/watch?v=_bMcXVe8zIs

## Slide 46: Protocols for Networks of Networks?
What does it take to send packets across the globe?
Bits on wire or air
Packets on wire or air
Delivery packets within a single physical network
Deliver packets across multiple networks
Ensure the destination received the data
Create data at the sender and make use of the data at the receiver

## Slide 47: Protocol for Networks of Networks?
Lots to do and at multiple levels!
Use abstraction to cope with complexity of communication
Networks are like ogres onions
  Hierarchy of layers:
    Application (chat client, game, etc.)
    Transport (TCP, UDP)
    Network (IP)
    Data Link Layer (ethernet)
    Physical Link (copper, wireless, etc.)
Notes: WS companies used TCP/IP even over LAN
Because early Ethernet controllers were cheap, but not reliable

## Slide 48: Protocol Family Concept
Protocol: packet structure and control commands to manage communication
Protocol families (suites): a set of cooperating protocols that implement the network stack
Key to protocol families is that communication occurs logically at the same level of the protocol, called peer-to-peer… …but is implemented via services at the next lower level
Encapsulation: carry higher level information within lower level “envelope”

## Slide 49: Inspiration…
Dear John,
Your days are numbered.
--Pat
CEO A writes letter to CEO B
  Folds letter and hands it to assistant
Assistant:
  Puts letter in envelope with CEO B’s full name
  Takes to FedEx
FedEx Office
  Puts letter in larger envelope
  Puts name and street address on FedEx envelope
  Puts package on FedEx delivery truck
FedEx delivers to other company

## Slide 50: The Path of the Letter
CEO
Aide
FedEx
CEO
Aide
FedEx
Location
Fedex Envelope (FE)
Letter
Envelope
Semantic Content
Identity
“Peers” on each side understand the same things
No one else needs to
Lowest level has most packaging

## Slide 51: The Path Through FedEx
Truck
Sorting
Office
Airport
FE
Sorting
Office
Airport
Truck
Sorting
Office
Airport
Crate
Crate
FE
New
Crate
Crate
FE
Deepest Packaging (Envelope+FE+Crate)
at the Lowest Level of Transport

## Slide 52: Protocol Family Concept
Message
Message
T
H
Message
T
H
Message
T
H
T
H
Actual
Actual
Physical
Message
T
H
Message
T
H
Actual
Actual
Logical
Logical
Each lower level of stack “encapsulates” information from layer above by adding header and trailer.

## Slide 53: Most Popular Protocol for Network of Networks
Transmission Control Protocol/Internet Protocol (TCP/IP)
This protocol family is the basis of the Internet, a WAN (wide area network) protocol
  IP makes best effort to deliver
    Packets can be lost, corrupted
  TCP guarantees delivery
  TCP/IP so popular it is used even when communicating locally: even across homogeneous LAN (local area network)
Notes: WS companies used TCP/IP even over LAN
Because early Ethernet controllers were cheap, but not reliable
TCP and IP fundamentally different but very connected
TCP hires IP guys
- GO!
- IP guy falls into a hole
- TCP hires another IP guy
- GO!
-IP gus falls into a hole
- Hire another!

## Slide 54: TCP/IP packet, Ethernet packet, protocols
Message
Application sends message
TCP data
TCP Header
IP Header
IP Data
EH
Ethernet Hdr
Ethernet Hdr
TCP breaks into 64KiB segments, adds 20B header
IP adds 20B header, sends to network
If Ethernet, broken into 1500B packets with headers, trailers

## Slide 55: “And in conclusion…”
I/O gives computers their 5 senses
I/O speed range is 100-million to one
Polling vs. Interrupts
DMA to avoid wasting CPU time on data transfers
Disks for persistent storage, replaced by flash
Networks: computer-to-computer I/O
  Protocol suites allow networking of heterogeneous components. Abstraction!!!
Acknowledgement: Some Networking slides adapted from CS168