## Slide 1: CS 61C: Great Ideas in Computer Architecture (a.k.a. Machine Structures) Lecture 1: Course Introduction
Instructors:
Krste Asanović, Randy H. Katz
http://inst.eecs.berkeley.edu/~cs61c/

## Slide 2: Agenda
Thinking about Machine Structures
Great Ideas in Computer Architecture
What You Need to Know About This Class
Everything is a Number

## Slide 3: Agenda
Thinking about Machine Structures
Great Ideas in Computer Architecture
What You Need to Know About This Class
Everything is a Number

## Slide 4: Most Popular Programming Languages 2016-7
What do you think is the most “popular” programming language in use today?
Notes: C# up, Ruby down …

## Slide 5: Why You Need to Learn C!

## Slide 6: CS61C is NOT really about C Programming
It is about the hardware-software interface
  What does the programmer need to know to achieve the highest possible performance
C is close to the underlying hardware, unlike languages like Python and Java!
  Allows us to talk about key hardware features in higher level terms
  Allows programmer to explicitly harness underlying hardware parallelism for higher performance and power efficiency

## Slide 7: Old School CS61C
Notes: This image is a fake!
Although the photograph displayed could represent what some people in the early 1950s contemplated a "home computer" might look like (based on the technology of the day), it isn't, as the accompanying text claims, a RAND Corporation illustration from 1954 of a prototype "home computer." The picture is actually an entry submitted to a Fark.com image modification competition, taken from an original photo of a <A HREF="http://home.att.net/~jeff1_satobserve/photo17.htm" TARGET=sub>submarine</A> submarine maneuvering room console found on the U.S. Navy web site, converted to grayscale, and modified to replace a modern display panel and TV screen with pictures of a decades-old teletype/printer and television (as well as to add the gray-suited man to the left-hand side of the photo):

## Slide 8: New School CS61C (1/2)
Personal Mobile Devices
Network Edge
Devices

## Slide 9: New School CS61C (2/2)

## Slide 10: New-School Machine Structures
Parallel Requests
  Assigned to computer
  e.g., Search “cats”
Parallel Threads
  Assigned to core
  e.g., Lookup, Ads
Parallel Instructions
  >1 instruction @ one time
  e.g., 5 pipelined instructions
Parallel Data
  >1 data item @ one time
  e.g., Add of 4 pairs of words
Hardware descriptions
  All gates functioning in parallel at same time
Smart Phone
Warehouse-Scale Computer
Software Hardware
Harness Parallelism &
Achieve High Performance
Logic Gates
Core
Core
…
Memory (Cache)
Input/Output
Computer
Main Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A3+B3
A2+B2
A1+B1
A0+B0
10

## Slide 11: Agenda
Thinking about Machine Structures
Great Ideas in Computer Architecture
What You Need to Know About This Class
Everything is a Number

## Slide 12: Five Great Ideas in Computer Architecture
Abstraction (Layers of Representation/Interpretation)
Moore’s Law (Designing through trends)
Principle of Locality (Memory Hierarchy)
Parallelism
Dependability via Redundancy

## Slide 13: Great Idea #1: Abstraction (Levels of Representation/Interpretation)
Anything can be represented as a number, i.e., data or instructions
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
High Level Language Program (e.g., C)
Assembly Language Program (e.g., MIPS)
Machine Language Program (MIPS)
Hardware Architecture Description (e.g., block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Logic Circuit Description (Circuit Schematic Diagrams)
Architecture Implementation

## Slide 14: #2: Moore’s Law
Gordon Moore Intel Cofounder B.S. Cal 1950!
Predicts:
2X Transistors / chip every 2 years

## Slide 15: Jim Gray’s Storage Latency Analogy: How Far Away is the Data?
Registers
On Chip Cache
On Board Cache
Main Memory
Disk
1
2
10
100
Tape /Optical
Robot
10
9
10
6
Sacramento
This Campus
This Room
My Head
10 min
1.5 hr
2 Years
1 min
Pluto
2,000 Years
Andromeda
(ns)
Jim Gray Turing Award
B.S. Cal 1966
Ph.D. Cal 1969!
Fall 2017-- Lecture #1

## Slide 16: Great Idea #3: Principle of Locality/ Memory Hierarchy
8/29/17

## Slide 17: Great Idea #4: Parallelism

## Slide 18: Great Idea #5: Dependability via Redundancy
Redundancy so that a failing piece doesn’t make the whole system fail
1+1=2
1+1=2
1+1=1
1+1=2
2 of 3 agree
FAIL!
Increasing transistor density reduces the cost of redundancy

## Slide 19: Great Idea #5: Dependability via Redundancy
Applies to everything from datacenters to storage to memory to instructors
  Redundant datacenters so that can lose 1 datacenter but Internet service stays online
  Redundant disks so that can lose 1 disk but not lose data (Redundant Arrays of Independent Disks/RAID)
  Redundant memory bits of so that can lose 1 bit but no data (Error Correcting Code/ECC Memory)

## Slide 20: Break!

## Slide 21: Why is Architecture Exciting Today?
CPU Clock Speed +15%/year
CPU Speed Flat
Notes: Goal: fast programs, low cost (power dissipation)
Moore’s law
Past: clock speed increased every year  programs automatically got faster
Today: Clock speed stays constant  only creativity can make programs faster
  E.g. parallel processing
  61C: learn how to increase speed by over 100x for some algorithms
  Combination of architectural innovations and programming innovations

## Slide 22: Old Conventional Wisdom
Moore’s Law + Dennard Scaling = faster, cheaper, lower-power general-purpose computers each year
In glory days, 1%/week performance improvement!
Dumb to compete by designing parallel or specialized computers
By time you’ve finished design, next generation of general-purpose will beat you

## Slide 23: New Conventional Wisdom
Google TPU2
Specialized Engine for NN training
Deployed in cloud
45 TFLOPS/chip
Serious heatsinks!

## Slide 24: Agenda
Thinking about Machine Structures
Great Ideas in Computer Architecture
What You Need to Know About This Class
Everything is a Number

## Slide 25: Course Information
Course Web: http://inst.eecs.Berkeley.edu/~cs61c/
Instructors: Krste Asanović and Randy H. Katz
Teaching Staff:
  Co-Head TAs: Steven Ho, Steven Chen, and Peijei Li
  TAs: Nikhil Athreya, Connor Brennan, Irene Dea, Dylan Dreyer, Julian Early, Derek Feng, Haoan Jing, Tejas Kannan, Daniel Ho, Lisa Lee, Ehimare Okayomon, Srinivasa Pranav, Nicholas Riasanovsky, William Sheu
  Tutors:, Ryan Hayes, Anna Li, Sameer Suresh, Morgan Reschenberg, Keyhan Vakil, Nicolas Zoghb
Textbooks: Average 15 pages of reading/week (can rent!)
  Patterson & Hennessey, Computer Organization and Design, RISC-V ed.
  Kernighan & Ritchie, The C Programming Language, 2nd Edition
  Barroso & Holzle, The Datacenter as a Computer, 2nd Edition, FREE!
Piazza:
  Every announcement, discussion, clarification happens there!

## Slide 26: CS61c House Rules in a Nutshell
Webcast? Yes!
Labs and discussion after NEXT Tuesday’s lecture
Wait listed? Enroll in any available section/lab, swap later
Excused Absences: Let us know by second week
Midterms are in class 26 September and 31 October; Final is 14 December at 7-10 PM
Labs and Projects (4+1 Extra Credit) are partnered
  Discussion is Good, but Co-Developing/Sharing/Borrowing Project Code or Circuits is Bad
  No Public Repos Please: Don’t Look, Don’t Publish
Join Piazza for more details … see http://inst.eecs.berkeley.edu/~cs61c/fa17/

## Slide 27: EPA!
Effort
  Attending prof and TA office hours, completing all assignments, turning in HW, doing reading quizzes
Participation
  Attending discussion and asking great questions
Altruism
  Helping others in lab or on Piazza
EPA! points have the potential to bump students up to the next grade level! (but actual EPA! scores are internal)

## Slide 28: Peer Instruction
Increase real-time learning in lecture, test understanding of concepts vs. details
As complete a “segment” ask multiple-choice question
  1-2 minutes to decide yourself
  2 minutes in pairs/triples to reach consensus.
  Teach others!
  2 minute discussion of answers, questions, clarifications
No need for iClickers; we will distribute color cards for you to use!

## Slide 29: Collaboration in Black and White
Good Collaboration
  High level discussion and brainstorming, stopping short of code snippets
Bad Collaboration
  Sitting together and co-writing code, inspecting each other’s code, taking (or giving) code whether in exchange or wholesale copying
This should be obvious, but …
  Don’t hire someone to do your assignments
  Don’t ask someone outside of the class (a parent, a student from a previous semester, sourceforge) to help you
  Don’t use search engines to look for solutions on-line or in someone’s unprotected GitHub (and don’t put your course project solutions in unprotected GitHubs please!)
  It is supposed to be your own work after all!

## Slide 30: Architecture of a typical Lecture
Attention
Time (minutes)
10
35
60
78
90
Administrivia
“And in conclusion…”
Full
Fun/News

## Slide 31: Break!

## Slide 32: Agenda
Thinking about Machine Structures
Great Ideas in Computer Architecture
What You Need to Know About This Class
Everything is a Number

## Slide 33: Computer Data
Computers represent data as binary values
Unit element: bit
  Just two possible values, 0 or 1
  Can be efficiently stored/communicated/manipulated in hardware
Use many bits to store more complex information, e.g.
  Byte: 8 bits, can represent 28 = 256 different values
  Word, e.g. 4 bytes (32 bits) to represent 232 different values
  64-bit floating point numbers
  Text files, databases, … (many bytes)
  Computer program
Notes: Bits hold whatever you assign them
No special hardware for storing numbers or text
Even the program is held in the same memory as data (and communicated over the same wires)
  Proposed in late 1940ties by John von Neurmann and other contributors, notably …
  So common today, it’s hard to think that it could be different
  Implemented first in England, in the Manchester Mark I
E.g. big program, small data or vice versa: it does not matter
Question: how does the computer know if a memory location contains a number or a string? Good question! We’ll get to that in the next lecture.
For now, let’s look at how to represent numbers (specifically: integers) with bits.

## Slide 34: Binary Number Conversion
Binary  Decimal
1001010two = ?ten
Decimal  Binary
74ten = ?two
Binary Digit | Decimal Value
0 | 0 x 20 = 0
1 | 1 x 21 = 2
0 | 0 x 22 = 0
1 | 0 x 23 = 8
0 | 0 x 24 = 0
0 | 0 x 25 = 0
1 | 1 x 26 = 64
 | S = 74ten
Decimal | Binary (odd?)
74 | 0
/2 = 37 | 1
/2 = 18 | 0
/2 = 9 | 1
/2 = 4 | 0
/2 = 2 | 0
/2 = 1 | 1
Collect  | 1001010two
Notes: Computers work with binary numbers.
Digits are only 0 or 1. Not 0 … 9, like in decimal.
Since we work close to the hardware, we occasionally deal with binary numbers.
Frequently we want to convert between decimal and binary. Many ways to do this. Here I show you a simple approach. If you are familiar with something else, use that.
B->D
Binary number goes in left column. LSB at the top.
Determine decimal value of each digit.
Sum up the individual values.
D->B
Start with decimal value.
Binary digit is 1 if decimal is odd, 0 otherwise.
Divide by 10, ignore fraction. Repeat down to 1.
Collect binary digits. MSB is at bottom.

## Slide 35: Hexadecimal
Problem: many digits
  e.g. 7643ten = 1110111011011two
Solutions:
  Grouping: 1 1101 1101 1011two
  Hexadecimal: 1DDBhex
  Octal: 1 110 111 011 011two
  16733oct
Binary | Hex
0000 | 0
0001 | 1
0010 | 2
0011 | 3
0100 | 4
0101 | 5
0110 | 6
0111 | 7
1000 | 8
1001 | 9
1010 | A
1011 | B
1100 | C
1101 | D
1110 | E
1111 | F
Notes: Binary numbers have many digits:
In binary, everybody is “rich”!
Computer do not care (nor do they mix up long sequences of bits).
Human’s need “crutches”.
Hexadecimal is most common: map 4 bits to a single character.

## Slide 36: The Computer Knows it, too
Output Decimal: 1234
Hex: 4d2
Octal: 2322
Literals (not supported by all compilers):
0x4d2 = 1234 (hex)
0b10011010010 = 1234 (binary)
02322 = 1234 (octal, prefix 0 - zero)
Notes: No need to manually convert. Just use the right base when entering literals.
Example is for C.

## Slide 37: Large Numbers
E.g. 1GiByte disk versus 1GByte disk
Marketing exploits this: 1TB disk  100GB less than 1TiB
Decimal
Suffix | Multiplier | Value
K | 103 | 1000
M | 106 | 1000,000
G | 109 | 1000,000,000
T | 1012 | 1000,000,000,000
Binary (IEC)
Suffix | Multiplier | Value
Ki | 210 | 1024
Mi | 220 | 1048,576
Gi | 230 | 1073,741,824
Ti | 240 | 1099,511,627,776
https://en.wikipedia.org/wiki/Byte
Notes: One km = 1 kilo meters, or just one kilometer
For binary, we often prefer base 2.
Then a kilobyte is 1024 bytes. To make that clear, we use Ki, not just K. A KiBi is 1024 Bytes.
KiBi, MeBi, GiBi, TeBi
E.g. 1GiByte disk contains > 109 bytes.
But some disks are sold with 1GByte capacity, “saving” 73MBytes.
Clever marketing

## Slide 38: Signed Integer Representation
Sign & magnitude (8-bit example):
Rules for addition, a + b:
If (a>0 and b>0): add
If (a>0 and b<0): subtract
…
+0, -0  are they equal? comparator must handle special case!
Cumbersome
”Complicated” hardware: reduced speed / increased power
Is there a better way?
sign | 7-bit magnitude (0 … 127)
Notes: Familiar decimal notation: just prepend minus sign to signify negative value.
It’s like an extra bit reserved to indicating the sign.
No change to magnitude.
Could do the same with binary numbers.
Unfortunately the result is a nightmare:
rules of addition depend on signs of operands
two representations for zero: + and minus. Cannot just compare bits to determine equality!
It’s possible to build computers that use signed-magnitude integers.
But this adds complexity to the hardware doing arithmetic.
Just like programmer hates slow algorithms, computer architect hates slow hardware.
Complexity reduces speed (maximum frequency at which operations can be performed). Or increases power dissipation. And size. And cost.
Fortunately there is a better way!

## Slide 39: 4-bit Example
 | 7
+ | -3
 | 4
 | 7 | 
+ | -3 | + 16
 | 4 | + 16
 | 7
+ | 13
 | 4 + 16
 | 0111 | 
+ | 1101 | 
 | 1 0100 | 0100 + 1 0000
Decimal
Binary
Map negative  positive numbers
  Example for N=4-bit: -3  24 – 3 = 13
  “Two’s complement”
  No special rules for adding positive and negative numbers
-8 | -7 | … | -1 | 0 | 1 | … | 7 |  |  |  | 
 |  |  |  | 0 | 1 | … | 7 | 8 | 9 | … | 15
+ 24 = 16

## Slide 40: Two’s Complement
Signed Decimal | Unsigned Decimal | Binary Two’s Complement
-128 | 128 | 1000 0000
-127 | 129 | 1000 0001
… | … | …
-2 | 254 | 1111 1110
-1 | 255 | 1111 1111
0 | 0 | 0000 0000
1 | 1 | 0000 0001
… | … | ...
127 | 127 | 0111 1111
Note: Most significant bit (MSB) equals sign
+256
+0

## Slide 41: Unary Negation (Two’s Complement) 4-bit Example (-8ten … +7ten)
Brute Force & Tedious
Clever & Elegant
16ten
10000two
- 3ten
- 0011two
13ten
1101two
16ten
10000two
- 13ten
- 1101two
3ten
0011two
”largest” 4-bit number + 1
15ten
01111two
- 3ten
- 0011two
12ten
1100two
invert
+ 1ten
+ 0001two
13ten
1101two
Notes: How do we determine the bit pattern of a negative number?
We cannot just flip the MSB!
Turns out it’s very simple.
To go from unsigned to signed, we had to add 2^N. For signed to two’s complement, we subtract from 2^N. Here N=4, hence we subtract from 16.
Of course we can do it also convert the negative two’s complement number back to the corresponding positive value. And get what we started from.
The subtraction is tedious: since all but the MSB are 0, we have to do a lot of “borrowing”.
Let’s try something different.
Subtract from 15, 2^N-1. Now all digits are one and the subtraction is trivial. In fact, in binary it’s just an inversion.
Well, that was easy. Only the result was wrong.
But that’s easily fixed by adding the one we missed by subtracting from 15 instead of 16.
Adding 1 is easy. The result is the same as with the brute force method.
If you build a computer, which approach do you use?

## Slide 42: Your Turn
What is the decimal value of the following binary 8-bit 2’s complement number?
  1110 0001two
Answer | Value
A | 33ten
B | -31ten
C | 225ten
D | -33ten
E | None of the above
Notes: -31

## Slide 43: Addition 4-bit Example
Unsigned
Signed (Two’s Complement)
3ten
0011two
+ 4ten
+ 0100two
7ten
0111two
3ten
0011two
+ 11ten
+ 1011two
14ten
1110two
3ten
0011two
+ 4ten
+ 0100two
7ten
0111two
3ten
0011two
+ -5ten
+ 1011two
-2ten
1110two
No special rules for two’s complement signed addition
Notes: Now let’s try addition.
Note there are no special rules for negative numbers.
Everything just comes out right.

## Slide 44: Overflow 4-bit Example
Unsigned
Signed (Two’s Complement)
13ten
1101two
+ 14ten
+ 1110two
27ten
1 1011two
7ten
0111two
+ 1ten
+ 0001two
8ten
0 1000two
-3ten
1101two
+ -2ten
+ 1110two
-5ten
1 1011two
7ten
0111two
+ 1ten
+ 0001two
-8ten
0 1000two
Carry-out  Overflow
Carry-out  Overflow
carry-out but no overflow
carry-out and overflow
no carry-out but overflow
no carry-out and no overflow
Notes: With one caveat: since computer numbers have a finite number of bits,
the results of addition can exceed the maximum number that can be represented.
With only 4 bits, that’s very easy.
Of course, we could just use 8, 16, or even 32 bits to make overflow less likely.
But even with 64 bit numbers, overflow is possible.
Let’s look at a few examples, for signed and unsigned integers. We again stick to just 4 bits to make everything fit on the page and in our heads.
For unsigned numbers it’s easy: the carry-out indicates overflow.
For signed numbers that’s not the case. Actually, it’s not immediately obvious how to detect overflow for addition of two’s complement numbers.

## Slide 45: Overflow Detection 4-bit Example
Unsigned
Carry-out indicates overflow
Signed (Two’s Complement)
Overflow if
  Signs of operands are equal
  AND
  Sign of result differs from sign of operands
No overflow when signs of operands differ
Overflow rules depend on operands (signed vs unsigned)
Notes: A little more investigation shows that the rules are not really complicated …
But we must remember that they are DIFFERENT for unsigned and signed numbers!
Acceptable tradeoff for making addition simple and fast

## Slide 46: Sign Extension
Decimal | Binary |  | 
 | 4-bit | 8-bit | 32-bit
3ten | 0011two | 0000 0011two | 0000 0000 0000 0011two
-3ten | 1101two | 1111 1101two | 1111 1111 1111 1101two
Why is this relevant?
Assignment differs for signed (above) and unsigned numbers
  Compiler knows (from type declaration)
  Different assembly instructions for copying signed/unsigned data

## Slide 47: Your Turn
Which range of decimals can be expressed with a 6-bit two’s complement number?
Answer | Range
A | -32 … 32
B | -64 … 63
C | -31 … 32
D | -16 … 15
E | -32 … 31

## Slide 48: Answer
Which range of decimals can be expressed with a 6-bit two’s complement number?
Answer | Range
A | -32 … 32
B | -64 … 63
C | -31 … 32
D | -16 … 15
E | -32 … 31

## Slide 49: And In Conclusion … (1/2)
CS61C:
  Higher speed performance + better energy efficiency by leveraging computer architecture:
    Strength and weaknesses (e.g. cache)
    Performance features (e.g. parallel instructions)
  Learn C and assembly facilitate access to machine features
Basis: five great ideas in computer architecture
  Abstraction: Layers of Representation/Interpretation
  Moore’s Law
  Principle of Locality/Memory Hierarchy
  Parallelism
  Dependability via Redundancy
Performance Measurement and Improvement

## Slide 50: And In Conclusion … (2/2)
Everything is a Number!
  Collections of bits can store and communicate arbitrary digital data
  Even programs are represented by bits
Two’s complement representation avoids special rules for addition of negative numbers